## Slide 1: Trace gas algorithms for TEMPO
G. Gonzalez Abad1, X. Liu1, C. Miller1, H. Wang1, C. Nowlan2 and K. Chance1
1Harvard-Smithsonian Center for Astrophysics
2Dalhousie University
ggonzale@cfa.harvard.edu

## Slide 2: Overview
TEMPO trace gas requirements
Generic trace gas algorithm framework
  Slant column retrieval
  Vertical column determination
Current examples of working or in development algorithms at SAO: H2CO, SO2 ,C2H2O2, BrO and OClO for low earth orbit platforms OMI and GOME-2
Future studies for algorithm upgrades

## Slide 3: TEMPO trace gas requirements
Standard products: H2CO, SO2 and C2H2O2
Secondary products, BrO, H2O, OClO and plume height-resolved volcanic SO2

## Slide 4: TEMPO trace gas requirements

## Slide 5: TEMPO trace gas requirements
Best fitting to date:
2.0×10-4 full-scale radiance
(Instrument vs. algorithm: Tied! S/N drives instrument if meas. requirements can be met

## Slide 6: Generic algorithm framework
Two step approach
  Direct fitting of radiance spectra to obtain slant columns + Air Mass Factors (AMFs) to convert to vertical columns
One step approach
  Target molecule cross sections are multiplied by wavelength-dependent AMFs for direct retrieval of vertical columns.

## Slide 7: Generic algorithm framework
AMF calculations
  Scattering weights + shape factors (Palmer et al., 2001)
  Shape factors to be obtained from model climatology, i.e., GEOS-Chem
  Scattering weights from VLIDORT:

## Slide 8: Generic algorithm framework
AMFs for partially cloudy pixels, single pixel approximation (Martin et al., 2002)
Cloudy SZA: 28°
Clear SZA: 24°
Clear VZA: 2.7°
Cloudy VZA: 16°
Clear cloud fractions: 0.01
Cloudy cloud fraction: 0.2

## Slide 9: Generic algorithm framework
Scattering weights lookup table:
  VLIDORT calculations from 300 to 500 nm
  Find compromises between resolution and computing performance.
  Parameterization on albedos and relative azimuth angles of radiance and Jacobians (Bhartia & Wellemeyer, 2001):

## Slide 10: Generic algorithm framework
AMF sensitivity to O3 concentration

## Slide 11: Generic algorithm framework
AMF sensitivity to O3 concentration

## Slide 12: Generic algorithm framework
AMF sensitivity to O3 concentration

## Slide 13: Generic algorithm framework
AMF sensitivity to NO2

## Slide 14: Generic algorithm framework
Typical retrieval flow chart for two step retrieval
L1 data
Auxiliary data
Read L1 data
Read auxiliary data
Wavelength calibration using high resolution solar spectrum
Compute AMFs
Compute I0 correction
Compute common mode spectrum
Compute undersampling spectrum
Direct fitting of slant columns
Read loo up tables & climatology
Compute vertical columns
Compute Ring spectrum
Post processing (if needed)
Lookup tables and climatology for AMF calculation

## Slide 15: Working algorithms from SAO
OMI operational H2CO
Fitting window | 327.5 – 356.5 nm
Baseline polynomial | 3rd order
Scaling polynomial | 3rd order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar reference spectrum | Chance and Spurr, 1997
H2CO cross sections | Cantrell et al., 1990; 300K
O3 cross sections | Malicet et al., 1995; 228K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 16: OMI operational HCHO

## Slide 17: Working algorithms from SAO
OMI C2H2O2
Fitting window | 431.5 – 469.5 nm
Baseline polynomial | 4th order
Scaling polynomial | 3rd order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar reference spectrum | Chance and Spurr, 1997
C2H2O2 cross sections | Volkamer et al., 2005; 296K
O3 cross sections | Malicet et al., 1995; 228K
NO2 cross sections | Vandaele et al., 1998 220K
O2-O2 cross sections | Hermans BISA, 2006; 294K
H2O cross sections | HITRAN 2008, 280K
Liquid H2O cross sections | Pope and Fry, 1997
IO cross sections | Spietz et al., 2005; 298K
Vibrational Raman spectrum | Chance and Spurr, 1997
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 18: OMI CHOCHO

## Slide 19: Working algorithms from SAO
OMI operational BrO
Fitting window | 319.0 – 347.5 nm
Baseline polynomial | 4rh order
Scaling polynomial | 4th order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar reference spectrum | Chance and Spurr, 1997
HCHO cross sections | Cantrell et al., 1990; 300K
O3 cross sections | Malicet et al., 1995; 218K; 295K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
O2-O2 cross sections | Hermans BISA, 2006; 294K
SO2 cross sections | Hermans et al., 2009; 295K
OClO cross sections | Kromminga et al,. 2003; 213K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 20: OMI operational BrO

## Slide 21: Working algorithms from SAO
OMI operational OClO
Fitting window | 358.5 – 392.0 nm
Baseline polynomial | 3rd order
Scaling polynomial | 3th order
Instrument slit function | Hyper-parameterization of pre-flight measurements
Wavelength calibration | Spectral shift (no squeeze)
Solar reference spectrum | Chance and Spurr, 1997
O3 cross sections | Malicet et al., 1995; 228K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
O2-O2 cross sections | Hermans BISA, 2006; 294K
OClO cross sections | Kromminga et al,. 2003; 213K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 22: Working algorithms from SAO
GOME-2 SO2
Fitting window | 312.0 – 330.0 nm
Baseline polynomial | 3rd order
Scaling polynomial | 3rd order
Instrument slit function | Asymmetric Gaussian fitted online
Wavelength calibration | Spectral shift (no squeeze)
Solar reference spectrum | Chance and Spurr, 1997
SO2 cross sections | Bogumil et al., 2003; 293K
HCHO cross sections | Meller and Moortgat et al., 2000; 298K
O3 cross sections | Brion et al., 1993; 218K, 273K
NO2 cross sections | Vandaele et al., 1998 220K
BrO cross sections | Wilmouth et al., 1999; 228K
Molecular Ring cross sections | Chance and Spurr, 1997
Sampling correction | Computed on-line
Residual common mode spectrum | Computed on-line

## Slide 23: Future studies for algorithm upgrades
O2-O2 spectroscopy
Continue with sensitivity studies for wavelength dependent AMF one step retrievals of SO2 and H2CO
OMI H2CO retrieval upgrade
C2H2O2 operational OMI retrieval (C. Miller)
H2O operational OMI retrieval (H. Wang)
Volcanic SO2 plume height-resolved optimal estimation retrieval (Nowlan et al. 2011)

## Slide 24: SO2 plume height-resolved OE retrieval
Cloud fraction < 0.2, Solar Zenith Angle < 70°, no ice- or snow-covered pixels

## Slide 25: OMI water vapor
July 14, 2005
Retrieval Window: [430, 480]nm
Relative uncertainty: 12%

## Slide 26
Thank you!!