## Slide 1: Global and regional air quality forecasting and assimilation relevant to the TEMPO mission
Richard Ménard, Didier Davignon*, Christ McLinden, Jean de GrandPré,
Yves Rochon, Alain Robichaud, and several others
Air Quality Research Division, (*) Canadian Meteorological Center
1st TEMPO Application Workshop, University of Alabama, Hunstville, June 12, 2016

## Slide 2: Modeling and assimilation approach used in Canada
Use an integrated / unified modeling and assimilation approach for meteorology and chemistry
Same model that is used for meteorology and chemistry
Same model that is used for global and regional applications
The assimilation system (EnVar: hybrid) used for
meteorology and for chemistry is similar
Present : Chemistry: static covariances
    Meteorology : hybrid (static + EnKF 256 members 512
  Future (4 years) :
  Chemistry long-lived (CO2, linearized chemistry) : hybrid (static + EnKF)
  Chemistry short-lived: hybrid (static + climatological ensembles)
Harmonize the remote sensing with our modeling and assimilation components (e.g. AMF from GEM-MACH)

## Slide 3
Ensembles: transport of tracer : Correlation after 5 days
N = 20

## Slide 4
Ensembles: transport of tracer : Correlation after 5 days
N = 100

## Slide 5
Ensembles: transport of tracer : Correlation after 5 days
N = 500

## Slide 6: GEM Canadian NWP model GEM-MACH GEM with online chemistry
SRPDQA-016
GEM-Regional
Grid projection | Rotated Lat/Lon
Time step | 300 s for meteorology; 900 s for chemistry
Horizontal grid-spacing | Δx=10 km (528x708)
Model top | 80 vertical levels to 0.1 hPa (~60 km)
Meteorological model GEM (25 km)
regional 10 km

## Slide 7: Overview of current systems
GEM-MACH Regional (10 km) - Operational
  Operational AQ forecasting
  Wildfire emissions
  Air Quality Health Index (AQHI)
  Analyses using AirNow observations, derived AQHI maps
  Long-term analysis and its effect on human health
  AQ Analyses at 2.5 km (operational for the PanAm games)
GEM Global NWP (25 km) – Operational in 2017
  Linearized ozone chemistry online (strato only) with NWP model.
  with/without radiative coupling
  UV-Index forecasting
GEM-MACH Global (100km) – In R&D
  Tropo-strato version of the GEM-MACH regional but with linearized O3
  chemistry in the stratosphere

## Slide 8: GEM-MACH10 – Regional Air Quality Deterministic Prediction System
(GEM-regional)
GEM-MACH
Model Output:
48-h forecast
O3, NO2, PM2.5 SO2, NO, PM10
+
Meteorological
fields
r100/r112
Piloting fields
(meteorology)
Chemical initial conditions
(from previous gm)
SMOKE
(emission
processing)
Pre-calculated
Emissions
database
gm00/gm12
Execution of 00, 12 UTC runs
Notes: What’s important to note b/w these 2 slides is that:
1- We are not proposing a chnage to the regional model. Still a separate run.
2- Most of the pieces of the puzzle will change so this is major change in infrastructure.

## Slide 9: GEM-MACH Wildfire Project
FireWork framework (Pavlovic et al. 2016, JA&WMA)
Weather model output (GEM)
Fire Information from AVHRR/MODIS
Emissions (SMOKE)
GEM-MACH
CWFIS
(Cdn Wildland
Fire Information
System)
USA
Canada
BlueSky FEPS only
BlueSky FEPS only
CWFIS
(Cdn Wildland
Fire Information
System)

## Slide 10
June 29th,2015
Source: NASA Earth Observatory
http://earthobservatory.nasa.gov
Le 29 juin, une "rivière de fumée" a été observée entre le NO du Canada et le centre des ÉU. FireWork a bien performé pour prévoir la région affecté.
Contribution des feux de forêt aux PM2.5 à la surface , prévue par FireWork 2015-06-28 12utc
valide à 29 juin à 12UTC.
Edmonton, AL
(averaged of 9 stations)
Prince Albert, SK
(station ID 80402)
June 24th – July 15th 2015 Case
Validation against observation
Contribution to surface

## Slide 11: FireWork partners/clients
US Air
Resource Advisors
SUPREME Système de surveillance et de prévention des impacts sanitaires des événements météorologiques extrêmes
Canadian Wildland Fire Information System
BlueSky Team

## Slide 12: Canadian Air Quality Health Index (AQHI) (Stieb et al. 2008, JA&WMA)
Ten year old program that has evolved from an O3-only forecast in Eastern Canada to a Canada-wide O3, NO2, PM2.5 forecast program
Forecast is communicated in most areas as an Air Quality Health Index (AQHI)
  10 point scale that links air quality to the health risk associated with exposure to a 3 pollutant mixture
  Developed by Health Canada (Stieb et al., 2008, JA&WMA ) from Canadian multi-city mortality/morbidity studies of short term health effects and AQ data from the Canadian National Air Pollution Surveillance Network (NAPS)
AQHI = 10/10.4100[(exp(0.000871[NO2])-1)
+(exp(0.000537[O3]) -1)+(exp(0.000487[PM2.5]) -1)]
Notes: Canadian program is a 10 year old program that has evolved from an O3 only forecast to a Canada-wide forecast for 3 smog related pollutants
In most areas, the AQ forecast is communicated through an index which was designed by Health Canada based on Canadian mortality/morbidity studies of short-term health effects.
It combines information on the 3 pollutants: O3, PM2.5 and NO2, to provide a forecast of the integrated health risk of exposure to the pollutant mix.

## Slide 13: AQHI products
Monitoring – based on observations of O3, NO2, and PM2.5
Forecast at observation sites. GEM-MACH forecast corrected by model output statistics.
Maps of AQHI based on analyses of O3, NO2, and PM2.5
(Robichaud et al. 2015, Air Qual Atmos Health, DOI 10.1007/s11869-015-0385-9

## Slide 14: Optimum Interpolation AQ analyses
Operational since 2013 (experimental since 2003)
(Ménard and Robichaud 2005, ECMWF Proceedings)
  O3 and PM2.5
  In April 2015 we added NO, NO2, SO2, and PM10
Optimum interpolation (OI) currently
  Uses a local Hollingsworth-Lönnberg fitting to obtain error variance
  Uses a parametrization of error statistics for isolated stations
  Has a seasonal bias correction, based on four large regions
Next release
  Maximum likelihood estimation of correlation length
  Use compact support correlation models
  (Ménard et al. 2016, JA&WMA)
  Use hybrid error statistics. Locally averaged H-L or Desroziers in
  observation space and ensemble of model runs
  Run in assimilation mode for (at least) verification

## Slide 15: Applications : Health effects
10 year AQ analyses using AirNow CHRONOS and GEM-MACH
Robichaud et Ménard, 2014, Atmos. Chem. Phys., 14, 1769-1800
Ambient PM2.5, O3, and NO2 Exposures and Associations
with Mortality over 16 Years of Follow-Up in the
Canadian Census Health and Environment Cohort (CanCHEC)
Crouze et al. (2015), Environ. Health Perspect., 123, 1180-1186
The Canadian Urban Environmental (CANUE) Health Research Consortium
Jeff Brook (PI) (ECCC and UofT) with 15 Canadian Universities,
Federal, Provincial and Local Governments.
Develop an easy access geospatial data server (e.g. Google Earth)
to support quantitative research on the effect urban environment
on health. Data linked to postal codes will contain information
on numerous metrics, NDVI, local climatic zones, building density, land use,
noise level, air pollution, greenspace, walkability. Data from 1980’s up to now.
GEM 10 km reanalysis since 1979. AQ rerun with GEM-MACH and AQ OI
(going back at least 2001) is being considered

## Slide 16: 2.5 km AQ analyses (PanAm Games)
GM
OA
AI
OBS
ozone

## Slide 17: GEM NWP Global with LINOZ
LINOZ is a linearized ozone chemistry (McLinden et al. 2000, JGR)
3D-Var-Chem
  Spectral formulation as in meteorology
  Could use hybrid error covariances from ensembles
  Estimation of error variances
  based on Desroziers
Real time observation
  GOME2, OMPS
Produces UV Index
Assimilation of total column GOME2 O3 at 33 km

## Slide 18
Verification of the maximum UV Index in a day against Brewers
Clouds from model GEM
UV index based on
radiative calculation
using 4 broad bands
UV-B (280-294)
(294-310)
UB-A (310-330)
(330-400)

## Slide 19
GEM MACH Global
comparison with MACC-II
Column NOx
Surface NOx

## Slide 20
Where we are heading for 2020
To consolidate the 3 main systems into an hybrid EnVar
framework and port to operations
  AQ applications using an hybrid with climatological ensemble of model output
  NWP application using and hybrid with an Ensemble Kalman filter
The OI will be replaced by LAM spectral formulation for the static
The global NWP model will be running at 10 km
The global GEM-MACH will be running at 40 km with assimilation
of aerosols
The regional AQ model will run at 10 km with 2.5 km windows
over populated areas
Conduct an AQ reanalysis at 10 km resolution since 2001
Integrate the remote sensing for assimilation and for a correction on bottom-up emissions

## Slide 21
SO2 emission retrieved from OMI (McLinden et al 2016)

## Slide 22: What do you want from TEMPO? – responses from Cdn forecasters / scientists
Surface concentrations, especially for O3, NO2, PM2.5, at highest spatial resolution possible
  Also VCD / AOD products, trop/strat components, O3 profiles (also: uncertainties, averaging kernels, detection limits, cloud information, dust, fine/coarse mode))
  Multiple temporal scales (hourly, daily mean, monthly mean, annual mean)
NRT (<3 hour preferred) access to level 1 data, level 2 products; available from ECCC servers
Multiple data formats: BUFR, netcdf, ascii, kml, GIS layers; ingestible by current ECCC tools; software to read/manipulate data
Online visualization tools (e.g., https://worldview.earthdata.nasa.gov/)
  Straightforward ways to present data so non-specialists can interpret
Wild fire data, hotspots and plumes updated in real time
  plume heights
  merged with fire products from GOES-R
Emissions at high spatial resolution

## Slide 23
Thanks for your attention

## Slide 24: Forecast Guidance – Objective Analysis http://aqhi.cmc.ec.gc.ca
**developed at AQRI & CMC/CMDA by A. Robichaud, R. Ménard, Y. Zaitseva
Products are hourly surface analyses for O3 and PM2.5 (eventually NO2)
Generated using an improved optimum interpolation technique
  Observations from Canadian networks (direct from providers) and U.S. networks (from EPA/AIRNow)
  Forecasts from GEM-MACH10 as background
=> Combining together model forecasts and observations provide our best knowledge of the state of the atmosphere.
Ozone
PM2.5

## Slide 25
Comparison of annual mean NO2 analyses with OMI
(From Lamsal et al., 2010)
Need to correct for NOz interference in surface measurements

## Slide 26: Objectives of the Canadian operational air quality forecast program
The Air Quality Health Index or (AQHI) is a scale designed in Canada to help understand the :
Impact of air quality on health.
It is a health protection tool used to make decisions to reduce short-term exposure to air pollution by adjusting activity levels during increased levels of air pollution.
The Air Quality Health Index also provides advice on how to improve air quality by proposing behavioral change to reduce the environmental footprint.
This index pays particular attention to people who are sensitive to air pollution. It provides them with advice on how to protect their health during air quality levels associated with low, moderate, high and very high health risks.

## Slide 27: AQ Processes in GEM-MACH
gas-phase chemistry (ADOM-II mechanism)
Particles formation (CAM): natural emissions, nucleation, condensation, coagulation, activation, dry deposition, wet deposition
  2 size bin allowed for particle size (PM2.5 et PM10)
aqueous-phase chemistry (chemistry in cloud droplets)
heterogeneous inorganic chemistry (HETV)
secondary organic aerosol formation(IAV)
dry and wet deposition of gaseous species and particles
vertical diffusion of chemical species

## Slide 28: AQ Processes in GEM-MACH
input and injection of anthropogenic surface emissions and elevated emissions (incl. plume rise)
calculation and injection of biogenic emissions (BEIS3)
chemical lateral boundary conditions (for LAM)
chemical upper boundary conditions (model top)
initialization of chemical species (including cycling of chemical tracers from day to day)

## Slide 29
Observation minus 240-hr forecast (O-F) global mean differences (solid) and standard deviations (dashed) against radiosondes for the period Jan 1st to Feb 28th 2009 for the zonal wind component (top left), meridional wind component (top right), geopotential height (bottom left), and temperature (bottom right). Results from non-interactive (blue) and interactive (red) ensemble ozone forecasts have been launched from Y3H9CN13 analyses in which MLS std. ozone measurements have been assimilated. The squares on the left and right axis indicate respectively the levels of significance for the differences of the means and standard deviations at the level of 90 % or more.
Linearized chemistry (LINOZ)
800x600 (50 km)
Jan-Feb 2009
Cooling (~.5°)

## Slide 30
October 2020
GEM-MACHv2, 10km, 96hr forecast (pilot GDPS 10 km) with updated particulate matter (i.e., aerosol) module, chemical boundary conditions from a global air quality deterministic prediction system (GAQDPS)
FireWork, 10km, 72 hr - Regional air quality assimilation using the EnVar in 3D model;
Assimilation of satellite and surface observations
Global Air Quality Deterministic Prediction System at 40 km based on GEM-MACH-Global with LINOZ - Global assimilation of aerosol optical depth, ozone, and NO2.
High-resolution 2.5km model, 24/36 hour forecast (pilot RAQDPS 10 km) - Objective analysis at 2.5 km - GEM-LINOZ as part of GEM version used for the GDPS and applied to ozone interactive forecasting;
Additional forecasting of GHGs (CH4 and N2O) if not already done. - Assimilation of ozone and GHG satellite data as part of the GDPS assimilation system with chemical data assimilation in 3D mode