## Slide 1: Moving from interannual analyses to day-to-day (and even glimpsing minute-to-minute) NO2 variations
Luke Valin, LDEO - Columbia University, EPA/ORD
Arlene Fiore (LDEO), Jim Szykman (EPA/ORD)
ACAM data
Scott Janz
Matt Kowalewski
Jay Al-Saadi
PANDORA data
Jay Herman
Elena Spinei
Nadar Abuhassan

## Slide 2
Long-term averages provide detailed information on the spatial pattern of NOX emission sources.
                OMI NO2 Column - 1:30 PM daily measurement
                June- August; 2005 – 2012;
                N ≈ 150 cloud-free measurements per site

## Slide 3
OMI Monthly NO2 Columns (×1015 mol. cm-2) East U.S. (36 – 40°N; 70 – 75°W) Lamsal et al., 2015
Monthly, regional-averaged NO2 columns observed by Aura/OMI are
1) consistent year to year (high precision) + trend
2) in agreement with trends observed at the surface
E.g., Lamsal et al., 2015; Duncan et al., 2013; Russell et al., 2010
See airquality.gsfc.nasa.gov for trends near you

## Slide 4
Tuesday, 29 Jul 2008
Jun-Aug 2005-2012
Due-West Winds (u>0; |v|<1 m s-1)
N=38 cloud-free measurements
Ameren Missouri-Labadie Plant, Labadie, MO
~50 km west of central St. Louis
NEI2011: 52nd largest point source of NOX (9891 tons / yr)
~ 1.7×1015 molecules cm-2
Application: Can OMI measure the influence of power plants on NO2 in my city?
σ(N=1) = 1.0×1015 molecules cm-2
σ(N=38) = 0.16×1015 molecules cm-2
No
Yes
Notes: Abs(V-component; 3x3 box average) <1 m s-1; U-component; 3x3 box average > 0 m s-1

## Slide 5
Tuesday, 29 Jul 2008
Jun-Aug 2005-2012
Due-West Winds (u>0; |v|<1 m s-1)
N=38 cloud-free measurements
Ameren Missouri-Labadie Plant, Labadie, MO
~50 km west of central St. Louis
NEI2011: 52nd largest point source of NOX (9891 tons / yr)
~ 1.7×1015 molecules cm-2
Can OMI measure the influence of power plants on NO2 in my city?
σ(N=1) = 1.0×1015 molecules cm-2
σ(N=38) = 0.16×1015 molecules cm-2
Will increase for TEMPO: variation will not be averaged over as large of footprint
Will decrease for TEMPO: ~100x increase in N
Notes: Abs(V-component; 3x3 box average) <1 m s-1; U-component; 3x3 box average > 0 m s-1

## Slide 6
There is incredibly detailed information on daily variation E.g., OMI NO2 columns over NYC
Stagnant conditions
SW winds
Strong NW winds
NE winds
SSE winds
Wed., 20 July 2011
Thur., 25 Aug 2005
Wed., 8 June 2005
Tue., 26 July 2005
Sat., 23 July 2007

## Slide 7
NOx Emission
NO2 Columns
NOx removal
+NO3 PM
Ozone production
VOC, oxidant
chemistry
13 km hr-1
Wednesday 20 July 2011
NO2 column provides information on precursor emissions and transport: Poughkeepsie O3 at 3PM - 120 ppb, NYC ~ 60 ppb
-- Identify high priority data segments (geographic, spectral) necessary to generate near real time NO2 products for use in statistical or dynamical O3 forecast models

## Slide 8
Ozone production (PO3) depends on
1) NOx
2) VOC (correlated with temperature)
More VOC
Biogenic VOC ~ Temperature
What information can currently available measurements of NO2 columns provide on surface O3 exposure?

## Slide 9
NYC– stagnant winds, large NO2 columns, Hot temperatures: slow net PO3 in NYC, fast PO3 at edge
6 km hr-1
T1PM = 31° C

## Slide 10
3 km hr-1
T1PM = 28° C
NYC – stagnant winds, intermediate NO2 columns, warm temperatures: very fast local PO3

## Slide 11
4 km hr-1
T1PM=19° C
NYC– stagnant winds, large NO2 columns, cold temperatures: slow local PO3, net local O3 destruction

## Slide 12: DISCOVER-AQ: Initial glimpses at the monitoring network of the future

## Slide 13
ACAM (“TEMPO flight simulator”)
Bakersfield, January 2013
Bakersfield
Bakersfield
Bakersfield
Data courtesy of NASA-GSFC (S. Janz)
Wind
Morning
Mid-day
Afternoon
SW transport of high NO2 over Bakersfield site between morning and mid-day with steep gradients (~0 – 2×1016 molecule cm-2)

## Slide 14
P3B integrated spirals
PANDORA NO2
Surface NO2 (scaled)
PANDORA NO2 columns (●) and integrated P3B NO2 profiles (▼) are consistent with ACAM slant NO2 observations.
The relationship of column (●) and surface NO2 ( —, scaled) highlights impacts of boundary layer growth.
Data courtesy of USEPA (R. Long), NCAR (A. Weinheimer) and NASA‑GSFC (J. Herman)

## Slide 15
Morning
Mid-day
Afternoon
Bakersfield
Bakersfield
Bakersfield
Data courtesy of NASA-GSFC (S. Janz)
Wind
Bakersfield
Bakersfield
Bakersfield
CMAQv5.1/4km
CMAQv5.1/4KM does not capture spatial variation
-- NO2 columns provide extremely detailed information on pollutant transport
-- Need to combine chemical and met reanalysis?
Courtesy of EPA/NERL/CED

## Slide 16
Highlights the limitations of evaluating model performance using surface data alone (top), particularly in conditions where mixing (or lack of mixing) are difficult to simulate
Simulated
Observed
Simulated
Observed

## Slide 17
ACAM NO2 Column
10 – 10:15 AM
P3B in situ NO2 spiral scaled to column (ppbx3e15)
10 – 10:15 AM
~30 minute NO2 column enhancement
observed by PANDORA over Essex at 10:15 AM
ACAM NOx Emission/transport monitoring capabilities can go down to minute-to-minute time scale.
Essex, MD, DAQ-Maryland
Tuesday, 5 July 2011
A data-driven phonebook? Local AQ managers are provided an automated list of potentially relevant stakeholders based on TEMPO measurements
Essex site
Essex site

## Slide 18
Conclusions
Air quality managers want information on causes of exceedance events - daily variations, local scales
  See aqast.wisc.edu for AQAST engagement of AQ managers with current resources on East US pollution episodes
DISCOVER-AQ ground and satellite simulator resources provide an initial glimpse of monitoring network of future - column, surface and model needs
Met reanalysis/forecast systems are not optimized for scales of observations that will be available

## Slide 19
Recommendations to data providers
Include measurements and expected values of well understood species (e.g., O4 column, O2 column, Ring “column”) in trace gas level 2 and 3 products.
Identify high priority data segments for faster response forecasting needs.
Compute column quantities of NO2 and HCHO (including loss and production terms) as standard suite of model results

## Slide 20: Extras

## Slide 21
Local Standard Time
PANDORA NO2 column
EPA CAPS NO2
Data courtesy of USEPA (R. Long) and NASA-GSFC (J. Herman)
DISCOVER-AQ Houston
What is the relationship between surface exposure and column concentrations?

## Slide 22
What is the relationship of NO2 column (molecules cm2) to NOX emissions (tons / day)?
Labadie PP: 27 tons/day * (2000 lbs/tons) / (2.2 lbs/kg) / (0.044 kg/mole) * (6.02e23 molecules/mole) / (1e10 cm^2/ km^2) / (24 hours/day) / (50x50 km^2) * (4 hour lifetime) *0.75 NO2:NOx
~ 1.7 × 1015 molecules cm2
OMI daily measurement 1σ Noise:
~ 1× 1015 molecules cm2

## Slide 23
2008
NASA Standard Product
vs INTEX-B NO2
Slope: 0.86
Y-intercept: 0.14 × 1016 cm-2
DOMINO
vs INTEX-B NO2
Slope: 1.68
Y-intercept: -0.59 × 1016 cm-2
OMI NASA-SP and DOMINO Validation:
One possible stakeholder takeaway:
Factor of 2 “uncertainty”

## Slide 24
Bucsela et al., 2013 ( panel c – latest version)

## Slide 25
Russell et al., 2011 ( before SP and DOMINO updates)