## Slide 1: TEMPO Applications to Emissions Quantification and Understanding
Greg Frost
NOAA Earth System Research Laboratory
Acknowledgements to Si-Wan Kim (NOAA/U Colorado), NASA GEO-CAPE Atmospheric Composition Science Working Group, and NASA AQAST

## Slide 2: Need for Top-Down Methods for Quantifying Emissions
Actions about the atmosphere focus on emissions. Emission inventories are critical for understanding emissions in the past, present and future.
Inventories are inherently complex and therefore uncertain, and these uncertainties are difficult to quantify.
X±? ton/yr
Top-down methods based on observations can provide objective tests of inventories and help improve the scientific basis of emissions.
Bottom-Up Inventories
Top-Down Approaches
Reconciliation
Synthesis to Benefit Stakeholders
Improvement
Rapid societal development results in new challenges to emissions understanding. Similarly, efforts to circumvent controls may be difficult to detect.
W. Steffen et al., The Anthropocene Review, 2015
We cannot manage what we can’t measure – John Burrows

## Slide 3
TEMPO will provide observational constraints on emissions, atmospheric transport and chemical processes
TEMPO will be part of an integrated observing strategy employing complementary approaches

## Slide 4
TEMPO NO2 will help constrain NOx emissions trends
A. R. Russell et al., Atmos. Chem. Phys., 2012
BEHR OMI NO2
Summer
2005
2011
Ohio River Valley: Satellite (GOME/SCIA)
Ohio River Valley: Inventory
Northeast US: Satellite (GOME/SCIA)
Northeast US: Inventory
SCIAMACHY
Summer 2004
S.-W. Kim et al., Geophys. Res. Lett., 2006

## Slide 5: TEMPO offers improved emissions constraints compared to LEO platforms
TEMPO’s hourly sampling and high spatial resolution will enable it to…
Evaluate temporal variations, spatial mapping, and sector-specific emissions in unprecedented ways
Resolve daytime cycles in emissions and chemistry
Improve detection of lower frequency variations in emissions and processes
Kelly Chance and Jay Al-Saadi
Fishman et al., BAMS, 2008

## Slide 6: TEMPO can spatially resolve urban emissions & chemistry
LAX
Pasadena
Fontana
Irvine
Ontario
Riverside
17 PST
(1015 molec. cm-2)
Si-Wan Kim et al.
Kim et al., JGR, 2016
Model
NO2
Aircraft
NO2
08 PST
Field observations provide test of air quality model
NO2 columns modeled at approximate TEMPO resolution

## Slide 7: TEMPO will resolve day of week variations with much fewer samples than LEO platforms
Weekend
Weekday
Pollack et al., JGR, 2012
Thu Fri Sat Sun Mon Tue Wed
S.-W. Kim et al., JGR, 2009
SCIAMACHY NO2 (U. Bremen), May-Sept 2003-2007
Selected Western US Cities
NO2 Column (cm-2)

## Slide 8: TEMPO will be useful for monitoring complex source regions
Satellite (OMI) vs. Model (WRF-Chem) NO2
Aircraft (WP-3D) vs. Model (WRF-Chem) NO2
S.-W. Kim et al., Atmos. Chem. Phys., 2011
OMI NO2 columns indicate overestimate of NOx emissions by inventory in Houston
Aircraft data reveal that inventory overestimates result from biases in port and industrial point sources while motor vehicle emissions are well represented by inventory
Higher resolution satellite data like those of TEMPO may be allow similar source separation
TEXAQS, Summer 2006

## Slide 9: TEMPO could help to characterize emissions from evolving sources, such as oil and natural gas basins
Duncan et al., JGR, 2016
Changes in OMI NO2 columns, 2005-2014
COLORADO
Frank Keutsch, Mitchell Thayer, et al.

## Slide 10: TEMPO HCHO may provide constraint on urban VOC emissions
Si-Wan Kim et al.
Comparisons of WRF-Chem Model to CalNex 2010 observations in Pasadena
Long-path DOAS and Model HCHO
Model VOCs/GC-MS VOCs
Field observations and surface monitoring provide complementary information for sorting out VOC sources and their impact on HCHO

## Slide 11: TEMPO may help assess control strategies
Natural VOCs from trees are so high in the East that ozone production is primarily controlled by reducing NOx emissions.
Ozone production is controlled by reducing VOC emissions in downtown LA.
Reduce NOx Emissions
Reduce VOC Emissions
Transition
Duncan et al., Atmos. Environ., 2010
OMI
HCHO/NO2
HCHO/NO2 columns used to explore sensitivity of ozone formation to changes in VOC and NOx emissions
Indicator ratios will vary with time of day, day of week, and temperature, reflecting emissions source mixtures and chemistry

## Slide 12: TEMPO’s high-resolution retrievals require high resolution inputs
  Quantify high-resolution inputs to air mass factor: vertical profiles, terrain height
  Use field campaign data and regional model to understand sensitivities
Si-Wan Kim et al.
Ratio of AMFs
Ratio of HCHO AMFs = Default AMF/WRF-Chem AMF

## Slide 13: Retrieval uncertainties can impact absolute emissions estimates
North Valmy
Intermountain
Hunter /
Huntington
Mohave
Navajo
Four Corners/
San Juan
Cholla/Coronado/ Springerville
Bonanza
Craig/Hayden
Jim Bridger/
Naughton
Dave Johnston/
Laramie River
Colstrip
Reid Gardener
US power plants directly monitor their emissions (CEMS)
Leverage power plant satellite signals to understand retrieval uncertainties
S.-W. Kim et al., J. Geophys. Res., 2009

## Slide 14: TEMPO in global GEO monitoring constellation
Courtesy Jhoon Kim,
Andreas Richter
GEMS
Sentinel-4
TEMPO
Policy-relevant science and environmental services enabled by common observations
Improved emissions at common confidence levels over Northern Hemisphere
Improved air quality forecasts and assimilation systems
Improved assessment of impacts
Spatial coverage of funded GEO spectrometers 2018-2020

## Slide 15: Constraints on methane from proposed GEO IR instrument
Wecht et al., ACP, 2014
GEO measurements, particularly multi-spectral (TIR+SWIR), constrain CH4 emissions better than comparable LEO observations
Increased frequency of GEO sampling allows shorter averaging periods to be used and CH4 emissions to be studied on finer timescales
Bousserez et al., Atmos Chem Phys, 2016
30 days
3 days

## Slide 16
Azimuthal
Scan
FTIR Spectrometer
Pointing Mirror
1.7 km a.s.l.
California Laboratory for Atmospheric Remote Sensing (CLARS)
K. W. Wong, 2015; D. Fu, 2014
GEO IR instrument as an urban CH4 monitor

## Slide 17: Lessons learned from AQAST: How to convey science to EPA, States, local agencies
http://aqast.org

## Slide 18
Bringing TEMPO products to international partners in research, regulation, and policy
National/Regional Working Groups
www.igacproject.org
GEIA member(s)
SSC member(s)
1800+
http://www.geiacenter.org/
GEIA Working Groups: China, Latin America and Caribbean,
VOCs, Urban Areas

## Slide 19: More Information
Bousserez, N. et al. (2016) Atmos. Chem. Phys., doi:10.5194/acp-16-6175-2016
Duncan, B. N., et al. (2010) Atmos. Environ., doi: 10.1016/j.atmosenv.2010.03.010
Duncan, B. N., et al. (2016) J. Geophys. Res., doi:10.1002/2015JD024121
Fishman, J., et al. (2008) Bull. Am. Meteor. Soc., doi: 10.1175/2008BAMS2526.1
Fu, D., et al. (2014), Atmos. Meas. Tech. 7: 713-729. 10.5194/amt-7-713-2014 Kim, S.-W., et al. (2006) Geophys. Res. Lett., doi: 10.1029/2006GL027749
Kim, S.-W., et al. (2009) J. Geophys. Res., doi: 10.1029/2008JD011343
Kim, S.-W., et al. (2011) Atmos. Chem. Phys., doi: 10.5194/acp-11-11361-2011
Kim, S.-W., et al. (2016) J. Geophys. Res., doi: 10.1002/2015JD024292
Pollack, I. B., et al. (2012) J. Geophys. Res., doi: 10.1029/2011JD016772
Russell, A. R., et al. (2012) Atmos. Chem. Phys., doi: 10.5194/acp-12-12197-2012
Steffen, W., et al. (2015) The Anthropocene Review, doi: 10.1177/2053019614564785
Streets, D. G., et al. (2013) Atmos. Environ., doi: 10.1016/j.atmosenv.2013.05.051
Wecht, K. J., et al. (2014) Atmos. Chem. Phys., doi: 10.5194/acp-14-8173-2014
Wong, K. W., et al. (2015) Atmos. Chem. Phys., doi: 10.5194/acp-15-241-2015
Greg Frost: gregory.j.frost@noaa.gov, http://www.esrl.noaa.gov/csd/staff/gregory.j.frost/