## Slide 1: Using TEMPO to Evaluate the Impact of Ozone on Agriculture
Denise L. Mauzerall
Princeton University
TEMPO Applications Workshop
Shelby Center for Science and Technology
Huntsville, AL
July 12, 2016

## Slide 2
Negative Effect of Ozone (O3) Pollution on Agricultural Yields
Reductions in O3 result from controls on:
- Nitrogen oxides (NOx)
  Carbon monoxide (CO)
  Hydrocarbons
  Methane (CH4)
Challenge: Need to double global grain production by 2050 while reducing environmental footprint of agriculture.
Reducing surface ozone concentrations increases agricultural yields and improves public health.

## Slide 3: O3 Pollution and Crop Yield Reductions
Large-scale, open top chamber (OTC) studies have been used to derive concentration:response functions to predict the relative yield (RY) of a crop at a given O3 level during the growing season.
  U.S. National Crop Loss Assessment Network (NCLAN) study in 1980s
  European Open Top Chamber (EOTC) program in 1990s
  Smaller-scale studies in Asia and other developing countries
Notes: While O3 has been studied in field-level experiments, at the time of commencement of my research projects, global scale estimate of O3 impact did not exist

## Slide 4
Mauzerall and Wang, 2001
O3 Exposure Metrics
Seasonal Mean or Cumulative Hourly Exposure Metrics are used.

## Slide 5: Global Estimates of O3 Damage use Models with Integrated Assessment Approach
Intermediate Outcome | Method
1) Surface O3 concentrations | Simulated using MOZART-2 CTM in 2000 and 2030 according to IPCC SRES A2 and B1 scenarios (Horowitz et al., 2006)
2) Plant Exposures to O3 | Calculated using various metrics for each scenario derived from field studies
3) Yield Loss | Estimated using concentration:response functions obtained from the US NCLAN study and Mills et al. (2007), convert to crop production loss (soybean, maize, wheat)
4) Economic Valuation | Estimated value of lost production based on producer prices in 2000
[Avnery et al., 2011a, 2011b]

## Slide 6: Simulate O3 Concentrations using Global Atmospheric Chemistry Transport Model MOZART-2 Simulations
Resolution: 2.8˚ lat x 2.8˚ lon; 34 sigma levels (surf.– 40 km)
Timestep: 20 minutes
Winds: MACCM (climatological)
Photochemistry: 63 chemical species (O3, NOx, hydrocarbon)
Present-day surface emissions (EDGAR v2.0):
  Anthropogenic fossil fuel combustion
  Biomass burning
  Biogenic emissions
  Soil emissions
  Oceanic emissions
  Lightning: NOx source in convective clouds
Transport: Advection and Convection
Dry and wet deposition
Notes: Transport – wind, turbulence
Chemistry – production and loss
Deposition – wet and dry

## Slide 7: Crop Production - 2000
Global crop distribution dataset (Monfreda et al., 2008; Ramankutty et al., 2008) for soybean, maize, and wheat
5 min horizontal resolution based on combining agricultural inventory data with satellite imagery from 1998-2002
Notes: MODIS-derived land cover product aboard AQUA satellite and the SPOT VEGETATION GLC2000 data set

## Slide 8: Year 2000 AOT40 O3 Exposure Calculated from MOZART-2
[Avnery, Mauzerall et al., 2011a]
Soybean
Maize
Wheat
Notes: Growing season data compiled from USDA and other sources, 95% of produciton
O3 exposure higher in NH, coincidence of soybean and maize growing seasons coincide with peak summer O3 concentrations
In SH, wheat and maize growing seasons in Brazil, and DRC respectively coincide with biomass burning seasons
M12 – 40-60 ppb, locally higher, AOT40 above 3 ppmh critical level in much of the world, 5-15 ppmh, higher eastern china, brazil, india, central US

## Slide 9
Calculated Crop Yield Loss in 2000
Global year 2000 yield losses are 4-15% for wheat, 9-14% soybean, 2-6% for maize
Crop production losses ~80-120 Mt worth $11-18 billion USD2000 annually
Avnery, Mauzerall et al., Atmospheric Environment (2011a)
Soybean
Maize
Wheat
Notes: Calculated RYL in each grid cell weighted by production to get national RYL
Distribution reflects:
Coincidence of O3 exposure during crop growing seasons & at specific locations where crops are grown
For AOT40, threshold dependent metric – differences in hourly O3 concentrations of only a few ppb around 40 ppb threshold generates significant difference in exposure
Soybean and maize appears more sensitive according to M12, wheat according to AOT40. This could be an artifact of statistical analysis used, or could be that wheat is more sensitive to higher O3 and this is captured better by AOT40 than mean.
Cumulative metrics more accurately predict

## Slide 10: Optimistic and Pessimistic O3 Precursor Emission Scenarios for 2030
Emissions from the IPCC SRES A2 and B1 scenarios
  Represent lower- and upper-boundary projections of O3 precursor emissions
  Difference between A2 and B1 simulations indicates potential decreases in O3 and associated crop yield benefits of reducing emissions of air pollutants.
http://sedac.ciesin.columbia.edu/ddc/sres/

## Slide 11
Yield Loss in 2030 (A2 – High emissions)
Soybean
Maize
Wheat
Avnery, Mauzerall et al., (2011b)
Global 2030 A2 yield losses range from 5-26% (+2-10%) for wheat, 15-19% (+1-11%) for soybean, and 4-9% for maize (+2-3%)
Crop production losses 120-230 Mt worth $17-35 USD2000 (+$6-17 billion) annually
Soybean
Maize
Wheat
[Avnery et al., 2011b]
Notes: wheat ranges from 5.4-26% (a change of +1.5-10% from year 2000 values), 15-19% for soybean (+0.9-11%), and 4.4-8.7% for maize (+2.1-3.2%)

## Slide 12
Yield Loss from Ozone Exposure (%)
Soybean
Maize
Wheat
Global year 2000 yield losses 4-15% for wheat, 9-14% soybean, 2-6% for maize
Crop production losses ~80-120 Mt worth $11-18 billion USD2000 annually
Global year 2030 yield losses potentially increase to 5-26% for wheat, 15-19% for soybean, 4-9% for maize.
Crop production losses 120-230 Mt worth $17-35 USD2000 (+$6-17 billion) annually
(Avnery, Mauzerall, et al. 2011a)
(Avnery, Mauzerall, et al. 2011b)
2000
2030 (High: A2)
Soybean
Maize
Wheat
Notes: Calculated RYL in each grid cell weighted by production to get national RYL
Distribution reflects:
Coincidence of O3 exposure during crop growing seasons & at specific locations where crops are grown
For AOT40, threshold dependent metric – differences in hourly O3 concentrations of only a few ppb around 40 ppb threshold generates significant difference in exposure
Soybean and maize appears more sensitive according to M12, wheat according to AOT40. This could be an artifact of statistical analysis used, or could be that wheat is more sensitive to higher O3 and this is captured better by AOT40 than mean.
Cumulative metrics more accurately predict

## Slide 13: Benefits of Reducing Conventional Ozone Precursors
Compare losses of high pollution (A2) and low pollution (B1) scenarios
Improving air quality through reductions in conventional ozone precursors increases crop yields.
Choosing O3 resistant crop cultivars can reduce losses.
India, U.S., and China experience greatest gains >$1.5 billion each
Change in EL (Million USD2000)
Change in 2030 EL (2030A2 – 2030B1)
Notes: ~30% reduction in NOx & NMVOC, 50% CO, 20%CH4

## Slide 14: TEMPO Provides Opportunities to Improve Agricultural Yields
TEMPO hourly 5-10km horizontal resolution data can be used to calculate local crop yield losses using a variety of cumulative exposure metrics. Spatial and inter-annual variability as well as trends in losses can be estimated.
TEMPO will help identify regions where use of O3 resistant cultivars is particularly valuable.
TEMPO NOx measurements can characterize NOx emissions from fertilizer applied to agricultural fields including spatial and temporal variability depending on farmers practices (eg. autumn vs. spring application, varying fertilizer types and application rates, etc.). This will facilitate an evaluation of potential benefits for surface O3 concentrations of improved nitrogen use efficiency in fertilizer application.