## Slide 1: Principal Component Analysis SO2 Retrieval Algorithm – Potential Application to TEMPO
Can Li
NASA GSFC Code 614 & ESSIC, UMD
Email: can.li@nasa.gov
Joanna Joiner, Nick Krotkov, Yan Zhang, Simon Carn, Chris McLinden, Vitali Fioletov
TEMPO Science Team Meeting
June 2, 2016
Washington DC

## Slide 2: Take home message
SO2 has come down in the TEMPO domain, but TEMPO SO2 data may still be of science value;
PCA algorithm – data driven, straightforward to implement, now produces operational OMI PBL SO2 product with good data quality
Application to TEMPO – feasible, given PCA approach’s speed, and ability to produce consistent retrievals between instruments
May be implemented with GEMS

## Slide 3: Background and Motivation
Motivation: Band Residual Difference (BRD) algorithm fast and sensitive, but large noise and artifacts (only 3 pairs of wavelengths)
Objective: develop an innovative approach to utilize the full spectral content from OMI while maintaining computational efficiency
Previous Version OMI PBL SO2 (Sept. 2004 – Feb. 2008)

## Slide 4: Basis – Spectral fitting algorithms
First look at the DOAS Equation:
Measured sun-normalized radiances
Various gas absorbers (O3, SO2 etc.)
Rayleigh and Mie scattering, surface reflectance etc.
The Ring effect
Plus additional measurement artifacts terms (e.g., wavelength shift, stray light, etc.) and/or radiance data correction schemes
Utilization of the full spectral content, but some terms are difficult to model (e.g., RRS)

## Slide 5: Methodology (Framework): PCA
Instead of explicit modeling of ozone, RRS, and other instrumental features, we use a data-driven approach based on principal component analysis (PCA) with spectral fitting
Measured N-value spectrum
PCs from SO2-free regions, (O3 absorption, surface reflectance, RRS, measurement artifacts etc.) other than SO2 absorption
Pre-calculated SO2 Jacobians (assuming O3 profiles, albedo, etc.)
SO2 column amount
Fitting of the right hand side to the spectrum on the left hand side -> SO2 column amount and coefficients of PCs
(See Guanter et al., 2012; Joiner et al., 2013; Li et al., 2013)

## Slide 6: Principle Components and Residuals
(a-c) First few PCs
Blue line: scaled reference Ring spectrum
(d) Least squares fitting residuals for a pixel near Hawaii
(Var.% 99.8492)
(Var.% 0.1264)
Example PCs from entire row # 11, Orbit 10990
(Var.% 0.0217)
(Var.% 5.32E-5)
(Var.% 4.79E-5)
PC #1: Mean spectrum
PC #2: O3 absorption
PC #3: Surface reflectance (also Ring signature)
PCs #4 and #5: likely measurement artifacts, noise (>99.99% variance explained)
Smaller residuals with SO2 Jacobians fitted

## Slide 7: Results: noise and artifact reduction
PCA algorithm reduces retrieval noise by a factor of two as compared with the BRD algorithm
SO2 Jacobians for PCA algorithm calculated with the same assumptions as in the BRD algorithm
August, 2006
OMI BRD SO2
OMI BRD
OMI PCA
Instantaneous FOV

## Slide 8: When combined with wind data and careful, innovative data analysis …
An independent “top-down” global SO2 emission inventory [McLinden et al., 2016];
Annual emissions quantified for ~500 large sources, ~40 missing or unreported in “bottom-up” inventories, or ~6-12% of the total anthropogenic sources;
Emissions quantified for 75 volcanoes – large differences between OMI measurements and the Aerocom database.

## Slide 9: SO2 change over the U.S. during the OMI era
OMI
Inventory
OMI PCA SO2 retrievals suggest large decrease of SO2 over the eastern U.S., in agreement with emission inventory;
Currently emissions barely detectable by OMI – requires averaging of large dataset;
More frequent measurements by TEMPO will help to continue the monitoring.
[Krotkov et al., 2016]

## Slide 10: Outside contribution to air pollution over the western North America?
An important science question of the GEO-CAPE mission is to assess the impact of inter-continental transport on air quality;
The planned CO product for GEO-CAPE could have served as a tracer for pollutant inflow, as demonstrated with AIRS CO data by Lin et al. [2012]

## Slide 11: A transpacific transport episode in Oct. 2006 detected with OMI SO2 Data [Hsu et al., 2012]
OMI SO2
Tracer SO2
AIRS CO
Among the species of that can be retrieved with TEMPO, SO2 may serve as a tracer for transpacific transport:
Longer lifetime than other TEMPO species (rapid LRT events)
Characteristics of Asian emissions

## Slide 12: Volcanic SO2 retrievals for aviation safety applications
New OMI operational volcanic SO2 product assuming 3 km plume height [Li et al., 2016, in prep]
August 11, 2008
August 12, 2008
A number of volcanoes in or just outside of the TEMPO domain may pose threat to aviation safety or even human lives;
Frequent TEMPO SO2 measurements may help to mitigate these threats.

## Slide 13: Execution Speed of the PCA SO2 Algorithm
~4 min per OMI orbit (~70,000 pixels) using simplified SO2 Jacobians LUT ;
5 days used for reprocessing 10-year OMI data for the current operational PBL product;
~65 min per OMI orbit using full LUT - can be reduced to ~10 min if cross-section is used in fitting for SCD and then converted to VCD using AMF;
~20 s per OMPS orbit (~10,000 pixels) using simplified SO2 Jacobians LUT

## Slide 14: Good consistency between OMI and OMPS Annual Mean PBL SO2 Retrievals for 2012
OMI
OMPS
[Zhang et al., 2016, in prep]

## Slide 15: Daily regional SO2 loading over Mexico (PBL retrievals)
[Zhang et al., 2016, in prep]

## Slide 16: Daily OMI/OMPS regional volcanic SO2 loading near Hawaii (PCA 3-km retrievals)
Daily spatial correlation
[Li et al., 2016, in prep]

## Slide 17: Implementation with TEMPO
PCA conducted for the same group of CCD pixels along the direction of scan (similar to the OMI algorithm);
Take advantage of natural variability due to clouds, O3, reflectivity and also observational difference such as different viewing zenith angles;
Data over ocean are important – offers variability for PCA analysis, also coverage for pollution inflow
For final SO2 product, needs L2 O3 and cloud products as input (no need for NRT product);
Uses L1B data as is (may sample multiple days for PCA), but may benefit from instrument characterization done for other algorithms.

## Slide 18: Conclusions
The PCA SO2 retrieval approach – data-driven, good quality, straightforward to implement.
If implemented with TEMPO may provide science return in 1) remaining large SO2 sources; 2) inflow of Asian pollution; 3) aviation safety.
If implemented with both GEMS and TEMPO may help to establish source-receptor relationship between two continents.