## Slide 1
Updating a Fuel-based Inventory of Vehicle Emissions
for Chemical Transport Modeling during LISTOS
TEMPO Science Team Meeting (June 6, 2019)
Brian C. McDonald, Ph.D.
Acknowledgments: Meng Li (CIRES/NOAA), Stuart McKeen (CIRES/NOAA), Luke Valin (EPA)

## Slide 2
~600 coal-fired power plants
~1700 natural-gas plants
Current US Budget of Nitrogen Oxides Emissions (2018)
Highway Vehicles
Off-Highway
Vehicles
Power
Plants
~230 million cars +
~3 million freight trucks
~33%
~25%
~10%
Mobile Sources
Industrial Facilities
Stationary Sources
~30%
Source: EPA Emissions Trend Report

## Slide 3
Summer Field Studies Suggest Mobile Source NOx Overestimated in NEI
Year | Region | Measurement | Findings
2011 | Baltimore/DC | Aircraft (DISCOVER-AQ) | Mobile sources overestimated by 50-70% [Anderson et al., Atmos. Environ. 2014]
2013 | Southeast | Aircraft (SEAC4RS) | Reduce mobile and industrial sources by 30-60% [Travis et al., Atmos. Chem. Phys. 2016]
2013 | Urban Texas | Satellite Inversion (DISCOVER-AQ) | Reduce mobile, area, point sources by 30-60% [Souri et al., Atmos. Env. 2016]
2013 | Southeast | Aircraft (SENEX) | Mobile sources overestimated by ~30% [McDonald et al., Environ. Sci. Technol. 2018]

## Slide 4
Research Objectives
  Update mobile source NOx emissions using a fuel-based approach for recent field campaigns (e.g., LISTOS)
  Utilize regional chemical transport model and evaluate with TROPOMI and Pandora NO2 column data
What can TEMPO data provide that helps improve bottom-up emission inventories?

## Slide 5
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
Trends in U.S. Mobile Source Activity (Fuel Use)
Fuel Use (t/d)
Year
Fuel sales based on
US DOT and DOE surveys
reported annually by state

## Slide 6
Gasoline EF
within ~20%
Trends in Mobile Source NOx Emission Factors Updated to 2018
Diesel EF
within ~30%
NOx EF (g/kg fuel)
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
Year
(default from MOVES shown)

## Slide 7
Updated US NOx Emissions Inventory from 2013 to 2018
Total U.S. NOx emissions decreases by ~3.5% y-1
Updated mobile sources with FIVE
~60% of decrease
(2) Updated power plants with CEMS
~40% of decrease
(3) Updated other point sources to NEI14
Updated inventory (4 km x 4 km) for NOx, CO, VOCs will be made publicly available

## Slide 8
WRF-Chem Model Comparison of NO2 with TROPOMI (July 2018)
Tropospheric NO2 (molec. cm-2)
WRF-Chem (12 km x 12 km)
Meng Li (NOAA)
Recalculated AMF for TROPOMI NO2 retrieval
allows for more “apples-to-apples” comparison

## Slide 9
Tropospheric NO2 (molec. cm-2)
WRF-Chem Model Comparison of NO2 with TROPOMI (July 2018)
Tropospheric NO2 (molec. cm-2)
TROPOMI (12 km x 12 km)
WRF-Chem (12 km x 12 km)

## Slide 10
NO2 (molec. cm-2)
WRF-Chem – TROPOMI
Model Results Generally Consistent with TROPOMI NO2
TROPOMI NO2 (molec. cm-2)
WRF-Chem NO2 (molec. cm-2)
Slope = 0.99
r = 0.91

## Slide 11
Sharper Spatial Features in Model and TROPOMI NO2 Columns
NO2 (molec. cm-2)
NO2 (molec. cm-2)
WRF-Chem (4 km x 4 km)
TROPOMI (4 km x 4 km)
I-95
I-95
NY Thruway
NY Thruway

## Slide 12
NO2 (molec. cm-2)
TROPOMI NO2 (molec. cm-2)
WRF-Chem NO2 (molec. cm-2)
Slope = 1.09
r = 0.84
Model NO2 Higher in Cities and Lower in Rural Areas
WRF-Chem – TROPOMI

## Slide 13
Long Island Sound Tropospheric Ozone Study (LISTOS 2018)

## Slide 14
WRF Model Evaluation of NO2 with Pandora Data in NYC Region
Acknowledgments: Luke Valin and Jim Szykman (EPA), Bob Swap, Nader Abuhassan, Alexander Cede (NASA)

## Slide 15
WRF Model Evaluation of NO2 with Pandora Data in NYC Region
Acknowledgments: Luke Valin and Jim Szykman (EPA), Bob Swap, Nader Abuhassan, Alexander Cede (NASA)

## Slide 16
Summary
  Differences in 2018 mobile source NOx emission inventories (MOVES2014b vs. FIVE) relatively small compared to previous years
    No longer factor of ~2 difference in on-road gasoline emission factor
  Updated 2018 NOx emissions over Eastern US consistent with TROPOMI and Pandora NO2 levels
    Magnitude of model NO2 within 0-30% of retrievals
  (3) Observations raise potential issues with emissions and modeling
    Is New York City plume being transported precisely?
    Spatial and temporal allocation of emissions?