## Slide 1
Image Navigation and Registration (INR)
James L Carr, Co-I (INR)
May 21, 2013
(301).220.7350
jcarr@carrastro.com

## Slide 2: INR System Objectives
Provide geographic
coordinates for all
pixels in the data cube.
Control the Line-of-Sight for:
(a) Spatially Uniform Sampling
< 82 mrad uncertainty (3s) everywhere.
Maps to 4km at center of Greater North America (GNA) for a satellite at -100° longitude.
< 10% of a
pixel (3s)
(b) Gapless Coverage of GNA
25%
Overlap >0 (3s)
Column N
Column N+1
Binned Pixel

## Slide 3: Level-1 INR Product
290-490 nm
Radiances
Metadata per scan:
UTC Date/Time String (t0)
Band
540-740 nm
Radiances
l
l
x
x
y
y
Metadata per column (temporal):
Time (t - t0)
Satellite x, y, z
Sun x, y, z
Moon x, y, z
Metadata per pixel:
 | Center | Corners
Latitude | 1 | 4
Longitude | 1 | 4
Ellipsoid Altitude | 1 | 4
Cov(EW,NS) | 3 | -
INR Data Quality Flag | 1 | 
INR Software in Science Data Processing Center (SDPC) at SAO applies spatial metadata
Real-Time (R/T) with Coarse and Post-R/T with Refined INR
Encapsulated in HDF5
Styled after GOME
WGS84 geographic coordinates
Blue: Spatial Metadata
Gold: Radiometric Data
Data >> Metadata

## Slide 4: TEMPO INR Challenge
Instrument
Ground
System
Spacecraft
INR
TEMPO Ground System
Navigates (geolocates) Pixels
Algorithms Designed for TEMPO
Control with SW Requirements
Host Spacecraft (S/C)
Attitude Control
Orbit Determination
Gyroscopes
Constrain with Spec
TEMPO Instrument
Creates L0
Scan Mechanism
Control with Spec
Opportunity (Maximize)
Build for
Purpose
INR Solution must be Low Cost,
Flexible, and Robust!
Gyros

## Slide 5: Systems Engineering Status
Passed Systems Requirements Review (SRR)
  INR Requirements allocated to L4
  INR Kalman Filter-Smoother
  approach based on U.S. Patent
  developed for TEMPO
  INR Error Budgets
  INR Simulation
  Key Technology Demonstration
Preliminary Design Review on track
for Summer 2014
4 Requirements
8 Requirements
≈80 Requirements
L1
L2
L3
L4

## Slide 6: INR Enabled by Tie-Points
GOES-E
TEMPO
GOES-W
Height

## Slide 7: INR Simulation
Solar Zenith Angle < 70°
All Solar Zenith Angles
No VIS Tie-Points to Earth,
uncompensated gyro random walk
VIS Tie-Points to Earth,
compensated gyro random walk
Spec
Geolocation Requirement is Satisfied with Margin