## Slide 1
Minimum TEMPO cal/val requirements from PLRA
Dave Flittner and Jay Al-Saadi
May 21-22, 2014
TEMPO Science Team Meeting
National Institute for Aeronautics
Hampton, VA

## Slide 2
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
PLRA Table 1
Minimal set of products sufficient for constraining air quality
Across Greater North America (GNA): 1819°N to 5857.5°N near 100°W, 67°W to 125°W near 42°N (worst case combo of instrument and host pointing; best case still 18-58)
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of Field Of Regard (FOR)
  Threshold ≤ 300 km2 at center of FOR
Temporal scales to resolve diurnal changes in pollutant distributions
Collected in cloud-free scenes
Geolocation uncertainty of less than 4 km
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months
Implementation of SO2, C2H2O2, and aerosols delayed until instrument cost and schedule risks retired
Likely ~October 2015
Derived UVB also delayed
All still ready for launch if successful
Clouds being implemented at present
PLRA 4.1.1 and 4.1.2 Baseline and threshold data products

## Slide 3: PLRA Section 4.1.1.b Baseline Cal/Val
Purpose: identify and correct regional-scale and diurnal systematic biases in the space-based products and demonstrate required precisions in polluted clear-sky scenes to the levels listed in Table 1.
Approach: Compare space-based and ground-based retrievals of products using correlative data collected from:
  daytime (solar zenith angles <70° for all products) observations
  at least one month each season
  from at least three (3) ground validation sites in the US
At the validation sites, Pandora solar spectral-radiometer measurements will be the primary source of correlative data for trace gas column densities.
Ozonesondes will contribute to the validation of the O3 mixing ratio on a best effort basis.

## Slide 4: Pandoras in TEMPO Field of Regard
Current Pandora Sites:
  GSFC, MD
  NASA HQ, DC
  SERC near the Chesapeake Bay
  LaRC, VA
  Four Corners, NM
  Boulder, CO
  Houston, TX
Future Sites:
  Boston, St. Louis, Wallops Island