## Slide 1
A Discussion on TEMPO Draft
CH2O Validation Plan
Jim Szykman, Jay Herman,
& all interested in CH2O
May 27-28, 2015
3rd TEMPO Science Team Meeting
UAH-NSSTC
Huntsville, AL

## Slide 2: Proposed Approach for validation (presented at 1st STM)
Validation conducted from commissioning till end of Phase E (end of operations)
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months
Level | Product Definition |  | Approach | 
0 | Raw instr. Sci. and HK data |  | Quality flags for duplicates, missing files, checksums | 
1b | Level 1 geo-located, calibrated spectral radiances |  | Comparisons with measured and modeled radiances based on coincident column measurements | 
2 | Retrieved gas columns and profiles, aerosol, clouds, UVB |  | Comparisons with ground-based, balloon-borne, sub-orbital, and satellite remote-sensed products | 
2 NRT | Retrieved gas, aerosols, clouds, UVB |  | Comparison with L2 normal delivery products | 
3† | Gridded monthly means of L2 data |  | Comp. with correlative measurements and climatologies | 

## Slide 3
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
PLRA Table 1
Across Greater North America (GNA): 19°N to 57.5°N near 100°W, 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of Field Of Regard (FOR)
  Threshold ≤ 300 km2 at center of FOR
Temporal scales to resolve diurnal changes in pollutant distributions
Collected in cloud-free scenes
Geolocation uncertainty of less than 4 km
PLRA 4.1.1 and 4.1.2 Baseline and threshold data products

## Slide 4: Validation Challenges
Validation challenges for TEMPO CH2O column measurements:
Adequacy (or lack) of correlative measurements - vertical distribution (especially within the BL)
Impact a priori vertical diurnal profiles
Aerosols and clouds
Albedo changes and spatial gradients
Sources of independent sources of CH2O measurements:
Satellite data sets from independent sensors: TropOMI
Aircraft observations; GCAS, GeoTASO, Aircarft in-situ profiles
Ground-based measurements; Pandora
For CH2O a-priori vertical profile shapes have the largest systematic impact on the satellite column errors due to the strong decrease of the satellite UV measurement sensitivity near the surface.

## Slide 5: DISCOVER-AQ P-3 Median CH2O Profiles
5

## Slide 6: Daily CH2O P-3 Spirals (Profiles) DISCOVER-AQ Baltimore, MD July 2011