## Slide 1: TEMPO Validation Capabilities Pandora NO2
Total and tropospheric columns of NO2 from direct sun measurements -> column along a narrow cone (0.5o), actual spatial coverage depends on solar azimuth and zenith angles for tropospheric and stratospheric column
Tropospheric NO2 column from MAX-DOAS measurements -> averaged column along viewing horizontal direction (1-10 km), actual spatial coverage depends on aerosol loading conditions and viewing azimuth direction.
Near surface concentration -> averaged concentrations along 1-10 km in horizontal direction and 100-200 m in vertical direction; actual spatial coverage depends on aerosol loading conditions and viewing azimuth direction.
Profile information is limited -> averaged profile along 1-10 km in horizontal direction and 1-2 km in vertical direction; actual spatial coverage depends on aerosol loading conditions and viewing azimuth direction. A narrow slice of the atmosphere.

## Slide 2: Pandora TEMPO validation capabilities
Three products will be available from the MAX-DOAS data:
  Real time near surface concentrations
  Total tropospheric columns
  Profile information of NO2, HCHO, O3, SO2, H2O
Fast azimuthal scans can provide “areal” view with a diameter of 2-20 km
Deploying multiple Pandoras at the same location will increase temporal resolution

## Slide 3
Pandora Inversion Algorithms for MAX-DOAS interpretation
Aerosols/clouds impact light path  retrieval of trace gases depends on “correct” aerosol/cloud representation
ΔSCD: NO2, HCHO, O3, SO2, H2O and O2O2
Combination of different elevation angle measurements (1, 2, 15, 20, 30, 90o)

Near surface concentrations, tropospheric total columns, some profile information
Optimal estimation using on-line radiative transfer calculations (VLIDORT)

Aerosol Ext. Coef. Profile,
SSA, ASY factor,
Surface Albedo
Trace gas profiles
2. Intensity fitting
1. Real time

## Slide 4: Pandora Validation
PANDORA MAX-DOAS data need further validation (spatial averaging, trace gas spatial gradients, aerosol loading)
DISCOVER-AQ demonstrated that the real situation is more complicated than expected.
Not well represented by model studies
More complex measurement strategies are needed to validate Pandora near surface NO2 concentrations and profiles, especially during high emission periods with large temporal and special heterogeneity.
Need to account for azimuthal inhomogeneity and different profile shapes

## Slide 5: Pandora validation: better designed experiments are needed to understand and validate MAX-DOAS spatial coverage: - multiple in-situ measurements - long pass DOAS - mobile measurements
In-situ near the Pandora
In-situ at surface, 1 km away from Pandora
In-situ 3 km away from Pandora
In-situ at 50 m
In-situ at 100 m
In-situ at 150 m
In-situ at 200 m
In-situ mobile
Tethered
Balloon at 400m
NO2 Sonde instrument
NO2 Sonde instrument
LP-DOAS and mobile: Up to 10 km travel along the view direction

## Slide 6: Near surface O3 volume mixing ratios at Moody Tower (preliminary)