## Slide 1: Funded tropospheric chemistry mission parameters (as of 4/2015)
 | Europe Sentinel 4 | USA TEMPO | Korea GEMS | Europe Sentinel 5 Precursor TROPOMI
Orbit | Geostationary | Geostationary | Geostationary | Low-Earth
Domain | Europe and surrounding | North America | Asia-Pacific | Global
Revisit | 1 hour | 1 hour | 1 hour | 1 day
Status | Detailed Design, Phase C | Instrument CDR July 2015 | Instrument CDR complete | Instrument delivery 2015
Launch | 2021 (Flight Acceptance Review first instrument) | No earlier than 11/2018 No later than 11/2021 | 2019 | Early 2016
Payload | UV-Vis-NIR 305-500, 750-775 nm | UV-Vis 290-490, 540-740 nm | UV-Vis 300-500 nm | UV-Vis-NIR-SWIR 270-500, 675-775, 2305-2385 nm
Products | O3, trop. O3, NO2, SO2, HCHO, AAI, AOD, height-resolved aerosol | O3, trop. O3, 0-2km O3, NO2, HCHO, SO2, CHOCHO, AOD, AAI | O3, NO2, SO2, HCHO, AOD | O3, NO2, SO2, HCHO, AAI, AOD, height-resolved aerosol, CO, CH4
Spatial Sampling | 8 km x 8 km at 45N | ≤ 2.22 km N/S x 5.15 km E/W @35N | 3.5 km N/S x 8 km E/W @38N | 7 km x 7 km nadir
Nominal product resolution | 8.9 km N/S x 11.7 km E/W @40N | ≤ 8.88 km N/S x 5.15 km E/W @35N | 7 km N/S x 8 km E/W @38N (gas), 3.5 km N/S x 8 km E/W @38N (aerosol) | 7 km x 7 km nadir
Notes | Two instruments in sequence on MTG-S; use TIR sounder on MTG-S (expected sensitivity to O3 and CO). Synergy with imager on MTG-I w.r.t. aerosol and clouds. | GEO-CAPE precursor or initial component of GEO-CAPE. Synergy with GOES-R/S ABI w.r.t. aerosol and clouds. | Synergy with AMI and GOCI-2 instruments w.r.t. aerosol and clouds. | In formation with S-NPP for synergy w.r.t. clouds and O3.
Notes: The limitation of GEO view is the lack of a global perspective
This can be mitigated through international cooperation to form a constellation from GEO
Timing and payloads demonstrate that threshold capability is ready
N. America-Europe-Asia covers the three primary economic/population/emissions regions

## Slide 2: Air Quality Constellation Targets: Harmonization to improve data product quality and usage
During 2013, the CEOS* ACC** AQ Constellation leads developed recommendations for harmonization to mutually improve data quality and facilitate widespread use of the data products (see next slide)
Includes LEO and GEO: LEO observations are a common transfer standard to link the GEO observations
Progress to date includes:
  Sharing of instrument requirements influenced instrument specifications, which may facilitate harmonization of data products
  Advocating open data policy (including L1B) with common formats to facilitate broad usage
  Sharing L1B and L2 format specifications to easily exchange data
  Establishment of new GSICS UV-Vis subgroup
  AQ Constellation “Geophysical Validation Needs” document is in preparation
*CEOS = Committee on Earth Observation Satellites **ACC = Atmospheric Composition Constellation

## Slide 3: Open Data Policy and Common Cal/Val Standards: Recommendations
  Apply best practices (lessons learned) for UV-Vis spectrometer calibration, characterization, and validation
    Share calibration/characterization plans and invite cross participation in reviews of such plans
    Develop longer term recommendations for common post-launch cal/val strategies (e.g. supersite instrumentation round-robins, joint airborne campaigns)
  Radiometric consistency
    Pre-launch: highest priority is per-instrument calibration/characterization as completely as possible (common absolute radiance calibration is secondary)
    Post-launch: more work needed on approaches (eg LEO vicarious intercalibration or Earth scenes)
  Sharing and consistency of data products (format, content, metadata)
    Share specification documents
    Share instrument characterization/calibration databases and Level 1-b data, in a common format, to allow wide application of algorithms to all datasets
    Identify and produce common constellation data products (may differ from standard products)
  Consistency in retrieval algorithms
    Cross participation in ATBD reviews
    Jointly improve retrieval algorithms by conducting inter-comparisons on common radiances
  Consistency of spectroscopy
  Support scientific collaboration

## Slide 4
Thanks to Ben Veihelmann & Jean-Christopher Lambert for initial draft
Identification of Common Parameters in L1b and L2 Products
Lessons Learned from LEO heritage missions
Common Geophysical Validation Needs (by mission phase)
Inter-Mission Geophysical Validation Needs (by mission phase)
Development Needs for New Validation Infrastructure or Approaches
“Geophysical Validation Needs” document outline

## Slide 5
Complete the GEO Geophysical Validation Needs (GV) document
  Draft 1 in 6 Months, Finalisation 6 months prior to GEMS and TEMPO instrument deliveries, May 2017
  Test flow of 1 case-study product e.g. Trop NO2
  Check status/need to address GMAP-ASIA, Chinese FY4
  Address DSCVR
Agree to an initial subset of constellation products, and target performance requirements (timeframe? After individual mission L2 processing is defined)
Identify aspects that require harmonization, report on status at next CEOS meeting
Identification of possible additional GV infrastructure / standards needed to demonstrate/achieve intermission consistency
Assess feasibility of an Air Quality “Data-Quality Traceability Framework” (e.g., the ESA QA4ECV currently in progress)
  Expect update (case study for NO2) at ACC-12
Action Items & Recommendations from 4/2015 CEOS ACC-11 Meeting (1 of 2)

## Slide 6
ACTION: ALL to Evaluate adoption of data file conventions as being implemented by S-5P team as an AC missions convention
  P. Veefkind to provide current S5P format specs to CEOS-ACC
  Involve relevant teams at the respective agencies
  Goal to select/endorse convention at ACC-12 meeting
  Formulate meta-data guidelines sufficiently open for AC missions
Hold next OSSE workshop (preferably at ECMWF, TBC)
Explore feasibility of extending measurements from KORUS-AQ ground sites to overlap with S-5P initial operations. (POCs at NIER and NASA) By S5PVTeam workshop
Begin planning/advocacy for a post-launch integrated geophysical validation (GV) campaign
  Pan-mission GV infrastructure
  Collaborative planning and implementation of an around-the-world airborne + ground+ modeling campaign
Action Items & Recommendations from 4/2015 CEOS ACC-11 Meeting (2 of 2)

## Slide 7: Level 2 Products: Potential Constellation Products (as of 4/2015)
 | Europe Sentinel 4 | USA TEMPO | Korea GEMS | Europe Sentinel 5 Precursor TROPOMI
Tropospheric O3 | Standard | Standard | Possible | Standard
Total O3 | Standard | Standard | Standard | Standard
Total NO2 | Standard | Possible | Standard? | Standard
Tropospheric NO2 | Standard | Standard | Standard? | Standard
Tropospheric H2CO | Standard | Standard | Standard | Standard
Total SO2 | Standard | Likely | Standard | Standard
AOD | Standard | Likely | Standard | Standard
Potential common products include the standard products common to all missions
Notes: The limitation of GEO view is the lack of a global perspective
This can be mitigated through international cooperation to form a constellation from GEO
Timing and payloads demonstrate that threshold capability is ready
N. America-Europe-Asia covers the three primary economic/population/emissions regions

## Slide 8: Level 2 Products: Potential Constellation Products (as of 4/2015)
Challenges for common constellation products
Differing instrument specifications
  Differing fields of regard and viewing geometries => direct inter-calibration and inter-validation of L1b is not possible
  Differing radiometric performance
  Differing native horizontal resolutions (spatial representativeness)
Differing retrieval algorithms
  Different approaches in standard algorithms
  Probably different methods for total/troposphere separation
  Differences in standard cloud/aerosol screening (e.g., S-4 & S-5P will make use of NIR)
  TEMPO Trop O3 will make use of visible band
Etc. Etc.
What products, to what accuracies (precisions?), validated how?

## Slide 9: Summary: Ongoing Activities
Data harmonization activities are underway
  Mission leads have been sharing specifications
  Pre-launch instrument characterization requirements necessarily vary by instrument
  GSICS UV-Vis working group is off to a good start
AQ Constellation Geophysical Validation Document is being prepared with the goal of guiding mission specific requirements being developed by the respective agencies
  Next step: identify goals/approaches for common constellation products and their validation
Past and upcoming airborne field campaigns offer potential for ongoing collaborative GEO mission preparation and possibly early S-5P cal/val
  AROMAT Romania 2015, 2016 (ESA)
  KORUS-AQ Korea 2016 (Korea NIER, US NASA)
An AQ Constellation session has been proposed for the Dec 2015 Fall AGU Meeting, to include all aspects of preparation