## Slide 1: Geolocation improvement for EPIC/DSCOVR
Víctor Molina García, Ronny Lutz, Diego Loyola
German Aerospace Center (DLR)
Earth Observation Center (EOC)
Institut für Methodik der Fernerkundung
Joint Geostationary Science Team Meeting
Harvard-Smithsonian Center for Astrophysics
Cambridge, MA, USA
26-27 September 2019

## Slide 2: Introduction
Mission:
  Satellite: DSCOVR (Deep Space Climate Observatory)
    Launch date: 11th February 2015
    Arrival to destination: 8th June 2015
    Location: Lagrangian point L1 (approx. 1.5 million km distance to the Earth)
  Sensor: EPIC (Earth Polychromatic Imaging Camera)
    10 channels UV / VIS / NIR
    1 image every 2 hours (2048 x 2048 pixels)
    12 x 12 km2 pixel size (subsatellite point)
2015/07/16
© NASA: https://www.nasa.gov/sites/default/files/styles/full_width/public/thumbnails/image/dscovrepicmoontransitfull.gif?itok=m-pCEXqi

## Slide 3: Motivation – OCRA/ROCINN Cloud Products from EPIC/DSCOVR
2023+
1995
GOME/ERS-2
1995-2011
SCIAMACHY/ENVISAT
2002-2012
GOME-2/MetOp-A since 2007
GOME-2/MetOp-B since 2012
TROPOMI/Sentinel-5P since 2017
GOME-2/MetOp-C since 2018
UVN/Sentinel-4 from 2023
Status: operational cloud products for many UVN sensors
Goal: generate cloud products also for EPIC/DSCOVR

## Slide 4: Motivation – Cloud Retrieval with OCRA & ROCINN
ROCINN
(CRB+CAL)
RGB color space
UV VIS NIR
O2 A-Band, NIR
OCRA
Cloud fraction
Cloud-top pressure/
Cloud-top height
Optical thickness/
Cloud albedo
forward model
neural network

## Slide 5: Motivation – Cloud Products for EPIC/DSCOVR
  Problem encountered:
  Misalignment of EPIC L1B images between the arrays of Earth coordinates and the arrays storing the actual measurement images
  E.g. ocean pixels could be wrongly regridded into a land cell when constructing the clear-sky composite map
  Proposed solution:
  Develop an automated registration correction

## Slide 6: Automatic EPIC registration correction
Current state of EPIC registration quality:
  Misalignment of EPIC L1B images between the arrays of Earth coordinates and the arrays storing the actual measurement images
  Scientific issues for any development in which the arrays of Earth coordinates are required
    Selection of surface albedo from a reference map
    Generation of EPIC product mean maps
Assumptions to fix the EPIC registration issue:
  The misalignment between the arrays of coordinates and the arrays of measurements is not extreme
  The correction can be performed by a specific transformation on the arrays of measurements, while keeping the arrays of coordinates unmodified
EPIC L1B 2016/03/20 18:36:56 UTC (v02)
Credit: NASA

## Slide 7: Automatic EPIC registration correction
How to select pairs of misaligned and correct pixels:
  Generate the theoretical coastline mask with the arrays of latitudes and longitudes
  Generate the radiometric coastline mask with the arrays of true reflectances
    Canny edge detector
    Polluted with the cloud borders
  Detect and describe features in the theoretical and radiometric coastlines by using the computer vision algorithm ORB (Oriented FAST and Rotated BRIEF)
  Find matching features from both images using a Brute Force Matcher and filter the results based on descriptor distance and pixel distance
Theoretical features (yellow circles) and radiometric features (green circles)

## Slide 8: Automatic EPIC registration correction
How to fix the EPIC registration issue:
  Misregistration model that describes how a pixel location is degradated by specific sensor or algorithm issues
    Radial distortion correction around a center of distortion
    Rotation around a center of rotation
    Shift
  Gauss-Newton optimisation with regularisation term (Tikhonov) over the transformation parameters when used for the pairs of matching features found by using the computer vision techniques
    A priori knowledge from image inspection

## Slide 9: Automatic EPIC registration correction
Basic conclusions from EPIC registration correction:
  The radial distortion parameter does not change significantly over the images, and is approximately equal to (barrel distortion)
  The rotation angle does not change significantly over the images, and is approximately equal to
  The shift is image-dependent but it shows an oscillating behaviour whose period is similar to DSCOVR Lissajous orbit period around the Lagrangian point L1
Performance of EPIC registration correction:
  Misalignment before correction: ~5.0 pixels
  Misalignment after correction: ~1.5 pixels
  Computation time per image: ~15 seconds
EPIC L1B 2016/03/20 18:36:56 UTC (v02)
Credit: NASA

## Slide 10: OCRA/ROCINN: Retrieval of Cloud Properties from EPIC
EPIC L1B 2018/01/30 05:32:37 UTC (v02)
Credit: NASA
OCRA radiometric cloud fraction
ROCINN cloud optical thickness
ROCINN cloud-top height / km

## Slide 11: Reference for further reading

## Slide 12: Additional slides

## Slide 13: Additional slide – EPIC channels
Channel description:
  2 channels in the oxygen B-band (absorption peak plus reference)
  2 channels in the oxygen A-band (absorption peak plus reference)
Estimation of cloud properties:
  Cloud optical thickness
  Cloud-top height
  Cloud fraction
Band | Central wavelength / nm | Band width / nm | Use
1 | 317.5 ± 0.1 | 1.0 ± 0.2 | Ozone, sulphur dioxide
2 | 325.0 ± 0.1 | 2.0 ± 0.2 | Ozone
3 | 340.0 ± 0.3 | 3.0 ± 0.6 | Ozone, aerosols, clouds
4 | 388.0 ± 0.3 | 3.0 ± 0.6 | Aerosols, clouds
5 | 443.0 ± 1.0 | 3.0 ± 0.6 | Aerosols
6 | 551.0 ± 1.0 | 3.0 ± 0.6 | Aerosols, vegetation
7 | 680.0 ± 0.2 | 3.0 ± 0.6 | Aerosols, clouds, vegetation
8 | 687.75 ± 0.20 | 0.80 ± 0.20 | Aerosols, clouds, vegetation
9 | 764.0 ± 0.2 | 1.0 ± 0.2 | Clouds
10 | 779.5 ± 0.3 | 2.0 ± 0.4 | Clouds, vegetation
Oxygen B-band
Oxygen A-band