## Slide 1: From Aerosol Optical Centroid Height (AOCH) to aerosol vertical profile retrieval: TEMPO’s advancement
Jun Wang
James E. Ashton Professor
College of Engineering, The University of Iowa
Many thanks to:
Zhendong Lu, Xi Chen, Hyerim Kim, Univ. of Iowa
Shobha Kongdragunta, NOAA NESDIS
Xiong Liu, Kelly Chance, Smithsonian Astrophysical Observatory
Omar Torres, NASA Goddard Space Flight Center
Acknowledgements: TEMPO and RST/NASA; MURI/NRL, and NOAA

## Slide 2: AOCH was proposed as part of GEO-CAPE and TEMPO original concept
Fishman et al. 2012. GEO-CAPE, BAMS
Chance, Liu et al. 2012, TEMPO proposal

## Slide 3: Our 16-year journey of passive sensing of AOCH
2008, High-spectral resolution simulation of polarization of skylight: sensitivity to aerosol vertical profile, GRL, Zeng, Wang, & Han.
2014, A numerical testbed for remote sensing of aerosols, and its demonstration for evaluating retrieval synergy from a geostationary satellite constellation of GEO-CAPE and GOES-R, JQSRT, Wang et al.
2016, Polarimetric remote sensing in O2 A and B bands: Sensitivity study and information content analysis for vertical profile of aerosols, AMT, Ding, Wang et al.
2017, Passive remote sensing of altitude and optical depth of dust plumes using the oxygen A and B bands: First results from EPIC/DSCOVR at Lagrange-1 point, GRL, Xu, Wang, et al.,
2019, Detecting layer height of smoke aerosols over vegetated land and water surfaces via oxygen absorption bands: Hourly results from EPIC/DSCOVR satellite in deep space
First retrieval of absorbing aerosol height over dark target using TROPOMI oxygen B band, RSE, Chen, Wang et al.
Hourly Mapping of the Layer Height of Thick Smoke Plumes Over the Western U.S. in 2020 Severe Fire Season, FRS, Lu, Wang, et al.,
Can multi-angular polarimetric measurements in the oxygen-A and B bands improve the retrieval of aerosol vertical distribution? JQSRT, Chen, Wang, et al.
2021
Passive remote sensing of aerosol height, in Remote Sensing of Aerosols, Clouds, and Precipitation, Xu, Wang, et al. in Remote Sensing of Aerosols, Clouds, and Precipitation
2023
First Mapping of Monthly and Diurnal Climatology of Saharan Dust Layer Height Over the Atlantic Ocean From EPIC/DSCOVR in Deep Space, GRL., Lu Wang et al.
Thanks to NASA, NOAA, ONR …
2024
PACE O2 bands for ALH over ocean, JRS, Xu et al.

## Slide 4: Oxygen absorption bands vs. surface reflectance spectra
O2-O2 477 nm
O2 B-band has moderate absorption, stronger than O2-O2 at 477 nm and weaker than O2 A. O2 B-band also has very low surface reflectance, comparable if not lower than blue bands, due to Chlorophyll-a absorption.
Blue band
Xu et al., 2019

## Slide 5
https://asdc.larc.nasa.gov/project/DSCOVR/DSCOVR_EPIC_L2_AOCH_01
Level-2 data product:
DSCOVR_EPIC_AOCH_01 data production in ASDC/LaRC.
Thanks to Marshall Sutton and EPIC project team in GSFC to make the RTO happen.

## Slide 6: Development/Results with primary use of TROPOMI O2 B-band
Chen, Wang, et al., 2021, RSE
VIIRS
This study
KNMI
CALIOP

## Slide 7
FILDA2 MCE
SD
WA
MT
OR
SD
WA
MT
OR
SD
WA
MT
OR
OR
SD
WA
MT
AQ Applications
August 16, 2023
TROPOMI AOCH
TROPOMI AOD

## Slide 8: Retrieval AOD and AOCH from TEMPO preliminary results; overall consistent with TROPOMI But, TEMPO provides much more dense observations

## Slide 9: Diurnal variation of the TEMPO AOCH and surface PM2.5
08/16/2023 19:00 UTC 20:00 UTC 21:00 UTC

## Slide 10: Zoom-in view at regional/community scale
08/16/2023 19:00 UTC 20:00 UTC 21:00 UTC

## Slide 11: New development: toward retrieval of aerosol vertical profile
PCA of CALIOP aerosol vertical profiles; obtain the major modes in the variation of aerosol vertical distribution
Retrieval the weights for each major modes, which can be then used to construct the aerosol vertical profile.

## Slide 12: Preliminary Results From TEMPO 16 Aug. 2023

## Slide 13: Summary
AOCH is an optical parameter that is well defined with mathematical rigor and can be derived from and validated with the aerosol extinction profile measured by lidar measurements.
Passive sensing retrieval of AOCH from TEMPO have its unique advantage in spatial and temporal coverage, providing rich context and quantitative information to link AOD to surface PM2.5.
It appears promising to use UV, blue and O2-B band from TEMPO (and future GEO-XO ACX) to retrieve aerosol extinction profile.
Passing sensing of aerosol vertical distortion is urgently needed, considering (a) large fires can inject aerosols into middle troposphere and above; (b) no CALIOP-like instrument is now planed in the coming 10 years.
ACX, TEMPO, and TROPOMI can fill in this critical need and data gap to quantify aerosol vertical profile with large spatial coverage and hourly temporal resolution.

## Slide 15
16 March 2023

## Slide 16: Retrieve only 2 EOF weights: vertical aggregation
First 2 EOFs explain ~82% of total variability in the vertical.
It is feasible to retrieve the Saharan dust profiles using PCA technique.
Each CALIOP aerosol extinction profile is normalized and aggregated to 600 m vertical resolution.
Notes: 13 years of CALIOP L3 data (daytime) are involved: Jun. 2006 – Jun. 2019
Each CALIOP aerosol extinction profile is normalized by its AOD and aggregated to 600-m vertical resolution before conducting PCA

## Slide 17: Improvement on prediction and analysis
false alarm!
MERRA-2
MERRA-2 Corrected by AOCH

## Slide 18: Large uncertainty in aerosol vertical profile
Annual- and zonal-mean mass-weighted mean pressure level (vertical center of mass in pressure coordinates)
Latitude
Pressure
Sulfate Sea Salt Black Carbon
Organic Mineral dust
Kipling et al., 2016;
ACP. AeroCOM-II

## Slide 19: New Development/Results with primary use of TROPOMI O2 B-band
Deriving Aerosol Optical Centroid Height (AOCH) and AOD by primarily using 420, 680, and 688 nm
Surface reflectance from MODIS climatology and ASTER/USGS spectral reflectance library
Aerosol optical properties derived from AERONET climatology (varying with region)
Quasi-Gaussian distribution for the shape of aerosol vertical extinction profile
Compared with CALIOP data for many many cases
Chen, Wang, et al., 2021, RSE

## Slide 20: AQ Applications
http://fireaq.uiowa.edu for weekly briefing of FireAQ in 2023
useful
SD
WA
MT
OR
MT
August 16, 2023