## Slide 1
Kyunghwa Lee, Jaehoon Jeong, Goo Kim, Minseok Nam,
Jeonghyeon Seo, Mijeong Kim, Dongwon Lee
Myung Soo Yoo
Current Status and Future Plans
for the Geostationary Environment Monitoring Spectrometer (GEMS) Operations
2024 TEMPO/GEMS Joint Science Team Workshop
Environmental Satellite Center (ESC)
Climate and Air Quality Research Department
National Institute of Environmental Research (NIER)

## Slide 2
Data processing (L0-L4) & analyzing
Validation
Data back-up & archiving
Receiving
Distribution
Monitoring
Universities
Institutes
Public service
(http://nesc.nier.go.kr)
Air Quality Forecasting Center
Roles of the Environmental Satellite Center (ESC) in GEMS operations
Oct. 2020
IN-Orbit Test (IOT)
Distribution of image files
8 Mar. 2020
LEOP
Now
19 Feb. 2020
Launch
L2 production / Validation
Mar. 2021
Jun., Nov., 2022
Distribution of NC files
ESC
Introduction of ESC

## Slide 3
Month | 07:45 | 08:45 | 09:45 | 10:45 | 11:45 | 12:45 | 13:45 | 14:45 | 15:45 | 16:45 | #
1 | - | - | HE | HK | FC | FW | FW | FW | - | - | 6
2 | - | - | HE | HK | FC | FW | FW | FW | FW | - | 7
3 | - | HE | HK | FC | FC | FW | FW | FW | FW | - | 8
4 | HE | HK | FC | FC | FC | FW | FW | FW | FW | FW | 10
5 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
6 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
7 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
8 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
9 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
10 | - | HE | HK | FC | FC | FW | FW | FW | FW | - | 8
11 | - | - | HE | HK | FC | FW | FW | FW | - | - | 6
12 | - | - | HE | HK | FC | FW | FW | FW | - | - | 6
Half Korea
(HK)
Full West
(FW)
Half East
(HE)
Full Central
(FC)
Month | 07:45 | 08:45 | 09:45 | 10:45 | 11:45 | 12:45 | 13:45 | 14:45 | 15:45 | 16:45 | #
1 | - | - | FC | FC | FC | FC | FW | FW | FW | - | 7
2 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
3 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
4 | HE | HK | FC | FC | FC | FC | FW | FW | FW | FW | 10
5 | HE | HK | FC | FC | FC | FC | FW | FW | FW | FW | 10
6 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
7 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
8 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
9 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
10 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
11 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
12 | - | - | FC | FC | FC | FC | FW | FW | - | - | 6
Reschedule of GEMS observation since 1 FEB 2024
+
-
Change
Current status of GEMS

## Slide 4
Current status of GEMS
Operation success rates
☯ Operation success rates
Nearly 100% for production/distribution & 98.9% for receiving GEMS data in 2024
Jan.
Plan/Real | 232/232 | 232/231 | 232/231 | 232/231 | 232/232 | 232/232
Success rate(%) | 100.0 | 99.6 | 99.6 | 99.6 | 100.0 | 100.0
Feb.
Plan/Real | 248/248 | 248/246 | 248/246 | 248/246 | 248/248 | 248/248
Success rate(%) | 100.0 | 99.2 | 99.2 | 99.2 | 100.0 | 100.0
Mar.
Plan/Real | 300/300 | 300/297 | 300/297 | 300/297 | 300/300 | 300/300
Success rate(%) | 100.0 | 99.0 | 99.0 | 99.0 | 100.0 | 100.0
Apr.
Plan/Real | 310/310 | 310/305 | 310/305 | 310/305 | 310/310 | 310/310
Success rate(%) | 100.0 | 98.4 | 98.4 | 98.4 | 100.0 | 100.0
May
Plan/Real | 1317/1317 | 1317/1303 | 1317/1303 | 1317/1303 | 1317/1317 | 27657/27657
Success rate(%) | 100.0 | 98.9 | 98.9 | 98.9 | 100.0 | 100.0
AVG.
Category | Earth Obs. | Receiving | L1A | L1B | L1C | L2
Plan/Real | 232/232 | 232/231 | 232/231 | 232/231 | 232/232 | 232/232
Success rate(%) | 100.0 | 99.6 | 99.6 | 99.6 | 100.0 | 100.0

## Slide 5
Current status of GEMS
Data distribution
Download from the ESC website (nesc.nier.go.kr)
Anyone can download GEMS data without logging in
Up to 20 GB and 40 files
SFTP service (A written application form required)
An account is issued for the user’s public IP address, which is allowed to pass through the ESC’s Web Application Firewall (WAF)
Log in to the SFTP server using the account and download data

## Slide 6
Current status of GEMS
Data distribution
Open-API (JUN 2023 - present)
The Open-API service requires a user key
Go to Open-API Key Issuance and request a key
Once your request is complete, your key code will be sent to you via email
You can use the key to create a URL for data download at the Create Open-API URL

## Slide 7
SFTP
ESC website
OPEN-API
China
S. Korea
Belgium
Japan
United States
Taiwan
Others
Germany
Current status of GEMS
Data distribution
☯ Average number of downloads for each method and country (JAN 2023 – JUN 2024)
Total #: 5,254,431 including 98% of NetCDF and 2 % of image files (> 40 countries)
Download method
Top 7 countries

## Slide 8
Current status of GEMS
Data distribution
☯ Average search number for each species (JAN 2023 – JUN 2024)
2023
2024

## Slide 9
Current status of GEMS
Data distribution
☯ Average number of downloads for each species (JAN 2023 – JUN 2024)
2023
2024
Image downloads
Data downloads

## Slide 10
Current status of GEMS
Monitoring long-term GEMS data
☯ Telemetry
Seasonal & stable variability meets requirements
Variability of the Charge-coupled device (CCD) temperature is < 0.3 °C
Focal plane electronics (FPE) temperature meets the criteria of -35°C to +65°C, but it has gradually increased
Image credit: BATC
Image credit: BATC
2020
2024
2020
2024

## Slide 11
15
16
17
18
Current status of GEMS
Monitoring long-term GEMS data
☯ Telemetry
Stable temperature for the telescope
Image credit: BATC
2020
2024
2020
2024
2020
2024
2020
2024

## Slide 12
13
19
22
21
Current status of GEMS
Monitoring long-term GEMS data
☯ Telemetry
Stable temperature for the telescope
Image credit: BATC
2020
2024
2020
2024
2020
2024
2020
2024

## Slide 13
Monitoring and maintaining calibration
Observation |  | Frequency | Time | Comments
Earth |  | Avg. 8/day | HH:45 min – HH+1 hr:15 min (duration: 30 min) | CMA position: Open Schedule considering SKM, WOL
Solar | WSD | 1/day | Perform before/after local midnight at a sun-diffuser normal angle of 30.5° | CMA position: WD or RD Reschedule after midnight (16 – 17 UTC) if SKM is overlapped on regular observation time (13 – 14 UTC)
 | RSD | 2/year |  | 
Dark | Normal | 2/day (180 images) | Right before/after daytime Earth observation | CMA position: Close Normal: Additional observation after SKM, WOL
 | Solar | 1/day (2 images) | Right before solar observation | 
 | LED | 1/week (42 images) | Right after LED observation | 
LED |  | 1/week (17 UTC on Sunday) | After dark imaging and prior to solar calibration | CMA position: Close Observations at multiple integration times
Thermally-Controlled Composite Structure
Radiator Assembly
Aperture
Calibration Mechanism Assembly
Scene Selection Wheel
Image credit: BATC
Transmissive
Diffusers
Current status of GEMS
WSD: Working solar diffuser
RSD: Reference solar diffuser
CMA: Calibration mechanism assembly
LED: Light emitting diode
CCD: Charge-coupled device (a light-sensitive integrated circuit)

## Slide 14
Monitoring long-term GEMS data
☯ WSD (APR 2020 – JUL 2024)
N, 300nm
S, 500nm
Current status of GEMS
2020
2024
2020
2024
2020
2024
2020
2024
CCD

## Slide 15
-0.48%
-0.43%
-0.25%
-0.57%
-0.35%
-0.45%
Current status of GEMS
Monitoring long-term GEMS data
☯ Degradation of L0 RSD
Exposure to the sun was conducted 11 times, resulting in a degradation of about 1%
Vernal
equinox day
Autumnal
equinox day
Digital count
Differences
2021
2022
2023
2024
2022 - 2021
2023 - 2022
2024 - 2023

## Slide 16
Current status of GEMS
Monitoring long-term GEMS data
☯ LED
Linearity of the CCD by using LED signals
Increasing Integration time
Reference

## Slide 17
Current status of GEMS
Inter-comparison between GEMS and the Advanced Meteorological Imager (AMI)
☯ Spatiotemporal collocation
Temporal collocation: Using AMI data -10, 0, + 10 min from GEMS observation time
Spatial collocation: AMI 1 km by 1 km → 3.5 km by 8 km (to GEMS domain)
Image credit: Ewha Womans University

## Slide 18
Current status of GEMS
☯ Spectral collocation
Collocation of GEMS data using AMI SRF to compare with AMI VIR004 band (central wavelength at 470 nm)
Inter-comparison between GEMS and AMI
Image credit: Ewha Womans University

## Slide 19
Current status of GEMS
☯ Cloud effect removal
Comparison by considering clear pixels using cloud mask
Inter-comparison between GEMS and AMI
Collocated AMI cloud
Collocated radiance diff. w/ cloud
Collocated radiance diff. w/o cloud
2023.01.01 02:45
2023.01.01 02:45 GEMS - AMI
2023.01.01 02:45 GEMS - AMI

## Slide 20
Current status of GEMS
☯ Geometric differences (JAN – DEC 2023)
Almost 1-2 pixels difference in RMSE analysis
Sometimes, a reversal trend occurs after rebooting GEMS
Inter-comparison between GEMS and AMI
w/o cloud mask
w/ cloud mask
E-W
E-W
N-S
N-S
JUL 17 2023
SEP 24 2023
DEC 10 2023
JAN 4 2023

## Slide 21
Current status of GEMS
☯ Geometric differences (JAN – MAY 2024)
Almost 1-2 pixels difference in RMSE analysis
GEMS did not require a reboot as no issues were encountered
Inter-comparison between GEMS and AMI
w/o cloud mask
w/ cloud mask
N-S
N-S
E-W
E-W
N-S
N-S

## Slide 22
Current status of GEMS
☯ Radiometric difference (JAN 2023 – MAY 2024)
Dramatic change in correlation coefficient and bias after rebooting GEMS
Inter-comparison between GEMS and AMI
JAN 4 2023
JUL 17 2023
SEP 24 2023
DEC 10 2023
w/o cloud mask
w/ cloud mask

## Slide 23
Future plans
To achieve 100 % success rates in receiving and retrieving GEMS data
To monitor and analyze GEMS telemetry, solar observations, and L1 data
To conduct intercomparison with other satellites (GEO-GEO, GEO-LEO)

## Slide 24
Thank you for your attention.
2024 TEMPO/GEMS Joint Science Team Workshop