## Slide 1: Current status of GEMS VOCs and their future development plan
Rokjin J. Park1), Gitaek T. Lee1), Eunjo S. Ha1), Yoonbae Chung 1), Hyeong-Ahn Kwon2), Isabelle De Smedt3), Michel Van Roozendael3), and Jhoon Kim4)
1)School of Earth and Environmental Sciences, Seoul National University, Republic of Korea
2)Department of Environmental & Energy Engineering, University of Suwon, Republic of Korea
3)Belgian Institute for Space Aeronomy, Brussels, Belgium
4)Department of Atmospheric Sciences, Yonsei University, Seoul, Republic of Korea
Atmospheric Chemistry Modeling Group,
Seoul National University
2024.08.29. TEMPO-GEMS joint science team workshop
Notes: Today, I will speak about the GEMS VOCs status and our future development plan. If time allows, I will switch gear to talk about NO2 retrieval using the SNU algorithm for ASIA-AQ.

## Slide 2: GEMS VOCs retrieval algorithm
[Configurations of GEMS VOCs v3]
[GEMS VOCs version history]
v1 (initial)  v2 (operational)  v3 (scheduled to be reproduced soon)
Modified GEMS scan schedule (2020.10.01. ~)
[Lee et al., 2023, ACP]
 | HCHO | CHOCHO
Fitting window (calibration window) | 329.3-358.6 nm (326.3-361.0 nm) | 433-461.5 nm (431-463.5 nm)
Fitting method | Direct fitting [González Abad et al., 2015] | 
Absorption cross-sections | HCHO, , Br, , Ring effect, polarization sensitivity | CHOCHO, , , (vapor), (liquid), Ring effect, polarization sensitivity
Polynomials | Third order | Third order
Reference spectrum | 120-150∘E three-day running mean zonal mean radiances (cloud fraction < 0.4) | 
A priori profile | GEOS-Chem 0.25∘ x 0.3125∘ Monthly mean hourly HCHO/CHOCHO | A priori profile
Background correction | Variable background concentrations in the radiance reference sector | 
Surface reflectance | GEMS L2 BSR | 
 | HCHO | CHOCHO
Fitting window (calibration window) | 329.3-358.6 nm (326.3-361.0 nm) | 433-461.5 nm (431-463.5 nm)
Fitting method | Direct fitting [González Abad et al., 2015] | 
Absorption cross-sections |  | 
Polynomials | Third order | Third order
Reference spectrum | 120-150∘E three-day running mean zonal mean radiances (cloud fraction < 0.4) | 
A priori profile | GEOS-Chem 0.25∘ x 0.3125∘ Monthly mean hourly HCHO/CHOCHO | A priori profile
Background correction | Variable background concentrations in the radiance reference sector | 
Surface reflectance | GEMS L2 BSR | 
*Red: Changes in v3
Poster by Gitaek Lee
Evaluation of GEMS formaldehyde vertical column densities during ASIA-AQ
Poster by Eunjo Ha
Analysis of drought effects on VOC emissions in Asia using GEMS products
Notes: Currently, version 2 products are open to the public and will be updated to version 3 later this year so I will show how much improvement we can get in v3 compared to v2.
For both HCHO and CHOCHO, the most significant change is the background correction. In v3, we use model values in the region where we calculate the radiance reference.

## Slide 3
GEMS HCHO v3 reduced negative NMBs with TROPOMI, compared to v2
HCHO VCDs comparison: GEMS v3 vs. TROPOMI
[GEMS]
Final algorithm flags: “Good”
Cloud fraction < 0.4
[TROPOMI]
QA value < 0.5
Cloud fraction < 0.4
Monthly mean field for
TROPOMI overpass time (13:30 LT)
Average of correlation coefficients(R) | FOR | Northeast Asia
v2 | 0.59 | 0.70
v3 | 0.58 | 0.68
NMB [%]
Northeast Asia (110-130∘E, 20-45∘N)
Notes: Ok, this is a comparison of GEMS HCHO VCDs with TROPOMI for 2023.
Top panel shows NMBs over the filed of regard and bottom is for north east asia for each month.
Black indicates NMB of v2 and red is version 3.
NMB are significantly reduced in v3 compare to v2.

## Slide 4: HCHO validation results: GEMS v3 vs. Pandora
GEMS HCHO shows strong agreement (r ~ 0.76) across East Asia.
*statistics: daily mean data
January 2022 ~ May 2024
Notes: This is a comparison of gems with pandora. You have already seen this kind of comparison in the poster presentations. In summary, gems hcho shows a strong agreement with pandora across east asia.

## Slide 5
Underlying issue for GEMS HCHO (PEGASOS report)
Background correction contributes ~70% of total VCDs for the eastern part of the scan domain
  Radiance reference sector partially includes some of East China, Korean Peninsula, and Japan
  Model-dependent value should be reduced
SE: Southeast Asia
NE: Northeast Asia
VCD0 = dSCD/AMF
Relative contributions of dSCD to VCD in GEMS v3 and TROPOMI for 2023
Notes: However, there is still an issue, which is raised by the pegasos report that background correction contributes too much in gems vcds.
For example, individual bards are hcho vcds at major cities in asia. Left is gems and right is tropomi. And black and dark grey indicate how much of vcds are contributed from background correctior I show say model values. As you can see gems vcds are too much dependent on a model and this is especially true in east asia where getting clean radiance references is quite limited.

## Slide 6
dSCDs retrieved using irradiance references are by ~70 % higher than those using radiance references.
dSCDs comparison: irradiance vs. radiance reference
dSCD가 더 크다 = dSCD 기여율이 커진다
dSCD ↑, background VCD ↓
R=0.94
March 2021, 09:45 ~ 15:45 KST
(a) GEMS HCHO v3
(irradiance reference)
(b) GEMS HCHO v3
a - b
*Background corrections are performed using minimum background concentrations (143~150E)
Notes: So in order to address this issue, we plan to use irradiance in the retrieval. Left panel shows gems hcho using irradiance reference and the middle is version 3 based on radiance references.
Overall, we have a similar value in the field of regard.

## Slide 7: Relative contributions of dSCDs in VCD calculation
GEMS HCHO VCDs using irradiance references show about 2~6 times higher dSCD contributions.
dSCD contributions of GEMS over India are consistently lower than those of TROPOMI.
*VCD0 (VCD without background correction)= dSCD/AMF
[March 2021]
GEMS v3
GEMS v3
(irradiance reference)
TROPOMI
Contribution of dSCDs to VCDs
[VCD0/VCD]
Notes: Moreover, dscd contribution to vcd becomes larger in our new product based on irradiance reference compared to the product using radiances.
This is especially true in north east asia.

## Slide 8: Impact of irradiance reference retrieval on background contributions
*VCD0 (VCD without background correction)= dSCD/AMF
Relative contributions of dSCD to VCD in GEMS v3 and TROPOMI (March 2021)
SE: Southeast Asia
NE: Northeast Asia
Notes: Less model dependency is also clearly shown in this comparison. So we have bigger blue bars. I think this improvement is very promising.

## Slide 9: Improvement in GEMS CHOCHO
[Lerot et al., 2021]
Period: December, 2022
CHOCHO VCDs (GEMS- TROPOMI)
GEMS NO2 VCDs
Empirical correction as a function of NO2 SCDs
  CHOCHO retrieval is significantly affected by the strong absorption of NO2.
  GEMS CHOCHO SCDs are empirically corrected using the regression line used to correct TROPOMI CHOCHO SCDs.
    Regression line:
Notes: For chocho, the most significant change is empirical correction as function of NO2 scd following the way done for tropomi.

## Slide 10: Seasonal variation before the NO2 correction
Period: 2020/8 ~ 2022/12
High bias in Northeast Asia (Korea, NCP, YRD) in winter (The Region and season in which NO2 concentration is high).
NCP: North China Plain
YRD: Yangtze River Delta
PRD: Pearl River Delta
Notes: This shows monthly variation of chocho at major cities in asia. Black is gems and red is tropomi.
As you can see that gems chocho is much higher than tropomi especially in wintertime.

## Slide 11: Seasonal variation after the NO2 correction
Period: 2020/8 ~ 2022/12
Increase of the correlation coefficients in Northeast Asia.
NCP: North China Plain
YRD: Yangtze River Delta
PRD: Pearl River Delta
Notes: After we perform an empirical correction based on the no2 vcds. The agreement is a lot better.

## Slide 12
Comparison of GEMS and TROPOMI CHOCHO
: statistics before and after the NO2 correction
Period: 2021 – 2022
More consistent NMB across the seasons
Higher R
Slope closer to 1
Notes: This is clearly shown in the statistics. For northeast asia with high NO2 concentration. Nmb for djf season show much lower values after the correction.

## Slide 13: Influence of the polluted radiance reference
(A) 120-133°E: the narrow reference sector limited by the FW scan, frequently conducted after the IOT
(B) 120-150°E: the reference sector that could be obtained by nominal scan conducted during the IOT
The current polluted reference spectrum could reduce the retrieved CHOCHO VCDs and inhibit the accurate representation of temporal variation.
Scan areas have shifted eastward since 2024, enabling the use of a cleaner reference spectrum.
Sensitivity test for the radiance reference sector
NMB=-22%
Period: August, 2020

## Slide 14
Period: August, 2020
NMB = 8.8%
xCHOCHO >1.2 ppt
Screened regions over the reference sector (>120 E)
Increase of CHOCHO VCDs when screening is applied
Screening with simulated glyoxal concentration (column-averaged mixing ratio)
xCHOCHO >1.5 ppt
xCHOCHO >1.8 ppt
NMB = 6.8%
NMB = 5.4%
Effect of screening polluted regions in the reference sector

## Slide 15
Model Updates
NO2 and SO2 show a decreasing trend in East Asia. In China, NO2 concentration has decreased from 16.9 ppb to 12.5 ppb (-25.8%) and SO2 concentration was reduced from 10.0 ppb to 3.2 ppb (-67.8%) from 2015 to 2023.
For accurate satellite retrievals, it is crucial that we update our CTM to reflect recent changes. The CTM results are used as a priori information to calculate the air mass factor (AMF).
Poster by Yoonbae Chung
Update of a priori profiles and its effect on GEMS observations
Yearly Average Surface Mixing Ratio
 | GEOS-Chem (Prior) | GEOS-Chem (Update)
Resolution | 0.25º x 0.3125º, 47 layers | 
Meteorological data | GEOSFP 0.25º x 0.3125º | 
Target period | 2020.08 ~ 2021.07 | 2023.02
Anthropogenic emission | KORUSv5 (2015) | AQNEAv3 (2019)

## Slide 16: Configuration of GEMS (SNU) NO2 retrieval algorithm
 | GEMS official NO2 | GEMS (SNU) NO2
Version | v2 (operational)  v3 (Preliminary) | -
Fitting window | 432.0-450.0 nm | 405.0-465.0 nm
Reference spectrum | Irradiance | Irradiance
Absorption cross-sections | NO2 at 220K (Vandaele et al., 1998) O3 at 243 K and 293 K (Bogumil et al., 2000) O4 (Thalman and Volkamer, 2013) H2O (HITRAN 2012 data) | NO2 at 220 K (Vandaele et al., 1998) O3 at 243 and 293 K (Serdyunchenko et al., 2014) O4 at 293 K (Thalman and Volkamer, 2013) H2O (HITRAN 2012 data) Polarization sensitivity
Ring efffect | Chance and Spurr (1997) | 
Polynomial | 2nd order | 3rd order
A priori profile | GEOS-Chem 0.25∘ x 0.3125∘ Monthly mean hourly NO2 for 2021 | GEOS-Chem 0.25∘ x 0.3125∘ Monthly mean hourly NO2 for 2021
Notes: Ok how much time do I have? Ok..
Let me switch gears to talk about our pet project about no2 retrieval using our snu algorithm, which uses slightly different configuration from the official gems no2 algorithm.
we used this to produce no2 vcds for aisa-aq campaign which occurred feb-march this year.

## Slide 17
NO2 VCD comparison: GEMS (SNU) vs. GEMS (NIER)
*NO2 total column
Feb. 2024, 11:45 ~ 15:45 KST
GEMS (SNU) NO2
GEMS NO2 v3
GEMS NO2 v2
TROPOMI
Notes: This is monthly mean no2 vcds for feb this year. As you noted that gems no2 v3 is lower than v2.
But our snu no2 show a bit lower values compared to both gems v2 and v3.

## Slide 18
NO2 VCD comparison: GEMS (SNU) vs. GEMS (NIER)
vs. GEMS NO2 v2
vs. GEMS NO2 v3
vs. GEMS (SNU) NO2
February 2024, 11:45 ~ 15:45 KST
*NO2 total column
GEMS (SNU) NO2
NO2 VCDs [molec. cm-2]
GEMS NO2 v3
NO2 VCDs [molec. cm-2]
GEMS NO2 v2
NO2 VCDs [molec. cm-2]
Notes: This is clearly shown tin this scatter plot comparison against tropomi. Gems operation products are higher than tropomi but snu vcds are slightly lower.

## Slide 19
GEMS (SNU) shows good consistency in tropospheric NO2 VCD with TROPOMI
Tropospheric NO2 VCD comparison: GEMS (SNU) vs. TROPOMI
(a) GEMS (SNU) NO2
(b) TROPOMI NO2
(a - b)/b
February 2024, 11:45 ~ 15:45 KST
GEMS (SNU) NO2
NO2 VCDs [molec. cm-2]
Notes: We also calculated tropospheric no2 vcd and compared them against tropomi. Again our snu no2 vcds show good agreement with tropomi.

## Slide 20: Tropospheric NO2 validation results: GEMS (SNU) vs. Pandora
GEMS (SNU) tropospheric NO2 shows strong agreement (r ~ 0.93) across East Asia.
NO2 VCDs
[molec. cm-2]
February 2024
Notes: We have compared agaist pandora across asia and correlations are relatively high.

## Slide 21: Tropospheric NO2 validation results: GEMS (SNU) vs. DC-8 during ASIA-AQ
GEMS (SNU) NO2 shows good agreement with DC-8 observations during ASIA-AQ
  DC-8 observations are 30~40% higher than GEMS over SMA
GEMS: tropospheric NO2 VCDs
DC-8: 10 minutes mean NO2 VCDs below 2km
GEMS (SNU) vs. DC-8: Korea
DC-8 NO2: Courtesy of Alessandro Franchin (NCAR)
franchin@ucar.edu
DC-8 vs. GEMS (SNU)
Notes: Finally, we have compared our no2 vcds with dc-8 observations. So this is an apple and orange comparison because dc-8 did not measure column amount
But we want to focus on spatial variability, and in the future, we have to compare against geo-taso observations.
Anyhow, we find that gems and dc-8 are well correlated in Korean peninsula during the campaign.

## Slide 22: Tropospheric NO2 validation results: GEMS (SNU) vs. DC-8 during ASIA-AQ
GEMS: tropospheric NO2 VCDs
DC-8: 10 minutes mean NO2 VCDs below 2km
GEMS (SNU) vs. DC-8: Philippines
DC-8 vs. GEMS (SNU)
Notes: And this is spatial variability of gems and dc-8 over philippines, scatter is shown on the right.

## Slide 23: Tropospheric NO2 validation results: GEMS (SNU) vs. DC-8 during ASIA-AQ
GEMS: tropospheric NO2 VCDs
DC-8: 10 minutes mean NO2 VCDs below 2km
GEMS (SNU) vs. DC-8: Taiwan
DC-8 vs. GEMS (SNU)
Notes: This is Taiwan.

## Slide 24: Tropospheric NO2 validation results: GEMS (SNU) vs. DC-8 during ASIA-AQ
GEMS (SNU) vs. DC-8: Thailand
GEMS: tropospheric NO2 VCDs
DC-8: 10 minutes mean NO2 VCDs below 2km
DC-8 vs. GEMS (SNU)
Notes: Finally, over Thailand.

## Slide 25
HCHO
  GEMS HCHO strongly correlates with TROPOMI and Pandora but shows high contribution of model background HCHO in the eastern scan domain.
  Irradiance references partially reduce model contributions, but further improvements are needed to address fitting residuals and advanced de-striping algorithm.
  GEMS (SNU) NO2 align closely with TROPOMI and DC-8 observation during ASIA-AQ
CHOCHO
The seasonal variations of GEMS and TROPOMI measurements become more consistent after applying the NO2 correction.
CHOCHO VCDs decrease when the radiance reference is polluted, particularly in latitudes above 28 N. This issue can be partly resolved by screening polluted regions in the reference sector using simulated glyoxal concentrations.
DC-8 and GEMS observed similar spatial distributions of CHOCHO concentrations during the ASIA-AQ campaign, with elevated concentrations in SMA and Daegu.
Summary
Notes: Ok this is summary slide which I am not going to read. Thanks!

## Slide 26
Thank you