## Slide 1: Changes to TEMPO for ACX
Dennis Nicks, BAE Systems, Space & Mission Systems

## Slide 2: Comparison of GEMS, TEMPO and ACX
Parameters | GEMS | TEMPO | ACX
Mass | 145 kg | 137 kg | 157 kg (CBE)
Volume (x,y,z) meters | 1.0 x 1.1 x 0.87 | 1.4 x 1.1 x 1.2 | 1.4 x 1.1 x 1.2
Average Operational Power | 155 W | 139 W | 145.3 W (CBE)
Field of Regard | 7.8° N/S x 11.2° E/W | 4.76° N/S x 8.95° E/W | 4.76° N/S x 8.95° E/W
Ground Sample Distance | 6 km x 8 km (N/S x E/W) | 2.2 km x 5 km (N/S x E/W) | 2.2 km x 5 km (N/S x E/W)
Spectral Range | 300-500 nm | 290-490 nm, 540-740 nm | 300-500 nm, 540 – 740 nm
Spectral Bandwidth | 0.6 nm | 0.6 nm | 0.6 nm
Status | 2/2020 launch / 128° E | 4/2023 launch / 91° W | In development

## Slide 3: ACX will build on TEMPO & GEMS success
GEMS and TEMPO were the First Ever Geostationary UV/Vis Hyperspectral Imagers
TEMPO was an aggressive development for a NASA Earth Venture Instrument (EVI) budget
      TEMPO & GEMS are first ever geostationary UV/Vis hyperspectral imagers
      NASA LaRC, SAO and BAE made lots of concessions to get there
      Co-development with GEMS was critical for success
      Overall successful developments, with some lessons learned
  ACX allows us to build on TEMPO success
      Modernize focal plane subsystem
      Improve optical performance
      Improve calibration performance and stability

## Slide 4: ACX requires higher dynamic range
ACX scene radiance is >> than TEMPO scene radiance
      Will minimize saturation during observations
Requires larger pixel well depth, faster frame rate, or both
      TEMPO max frame rate ~9 Hz
      Nominal ACX frame rate ~ 30Hz
ACX utilizes a digital CMOS focal plane
      Monolithic 3k x 3k detector
      Pros: higher frame rate, lower noise than TEMPO CCD
      Pros: Additional operational capabilities (programmable gain stages)
      Cons: lower QE than TEMPO CCD

## Slide 5: Improved slit for spectral bandpass
TEMPO slit varied ~4 μm over slit length
      Caused non-compliance in spectral bandpass
New silicon slit width variability is better than 0.5 um
      Provides better precision and uniformity
55 μm
TEMPO: 52 μm

## Slide 6: More stringent polarization sensitivity
TEMPO Polarization Sensitivity:
      < 5% from 240 – 490 nm
      < 20% from 540 – 740
GEMS Polarization Sensitivity
      < 2% from 310 – 500 nm
ACX Polarization Sensitivity
        < 5% from 300 – 500 nm, 540 – 740 nm
  ACX achromatic waveplate design provides improved polarization sensitivity
        Early risk reduction testing completed

## Slide 7: Improvements in Stray Light Performance
TEMPO stray light model did not predict performance well
      Diffraction grating scatter not well modelled
      Did not predict non-compliance at 290 – 307 nm
        Caused by light > 500 nm, so not seen by GEMS
      Primary stray light source is the grating
ACX changes
      Incorporate a low-pass filter over UV channel
      Further characterize flight grating and update stray light model
      Use updated stray light model for additional mitigation
order-sorting long-pass filter
ACX to incorporate short-pass filter over UV channel
TEMPO FPA

## Slide 8: Updated solar calibration diffuser based on GEMS/TEMPO experience
Updates to TEMPO & GEMS ground fused silica transmissive diffuser plates for improved stability and bidirectional transmission distribution function (BTDF) performance
New ACX material has more uniform BTDF over large angles
      BTDF measured during ACX study
Will conduct UV exposure testing to validate on-orbit life

## Slide 9: Summary
BAE continues to innovate atmospheric composition remote sensing instruments
      TEMPO and GEMS first ever Geostationary UV/Vis Hyperspectral imagers
ACX highly leverages GEMS & TEMPO instrument design
      Same spectral and spatial performance
      Adds modern, digital, focal plane subsystem
      Improved optical performance
      Improved solar calibrator