## Slide 1
Enhancing Atmospheric Composition Forecasting over continental United States: Assimilating TEMPO data in Regional Air Quality Models with the ETKF method
Chengzhe Li1, Jun Wang1, Huanxin (Jessie) Zhang1
1. Department of Chemical and Biochemical Engineering, Center for Global & Regional Environmental Research, The University of Iowa, Iowa City, 52240, Iowa, United States.
Motivation and Research Goal
Case Study: April 2024
Atmospheric chemical transport models (CTMs), such as the Unified Inputs (Initial and Boundary Conditions) Weather Research and Forecasting model coupled with Chemistry (UI-WRF-Chem), can simulate and forecast aerosol and trace gases distribution, capturing these diurnal variations effectively.
Overall goal:
Enhance UI-WRF-Chem simulation of the diurnal variation of aerosol and trace gas concentrations and aerosol properties (including vertical and size distribution) in the United States through data assimilation (DA) of aerosol and trace gases products from TEMPO.
Update the existing anthropogenic emission inventory of trace gases and aerosols by assimilating TEMPO observation into WRF-Chem.
Contact: Jun Wang(jwang-6@uiowa.edu), Chengzhe Li(chengzli@uiowa.edu)
This work is supported by This work was supported by in part by NASA’s ACMAP, HAQ and HAQAST program.
Acknowledgement
Flow chart of WRF-Chem-ETKF method
Domain | Boston-NY
Time Period | April 2024
Domain size | 10°×14°
# of grid box | 108×116
Resolution | 9km×10km
Emission inventory | NEI 2017
Vertical layer | 48
Aerosol chemical scheme | RADM2/MADE/SORGAM
UI-WRF-Chem setting
Methodology
△ = 6.45%
Errors in Diurnal Pattern would lead to false air quality alarm
How to decrease the error from diurnal profile of emission inventory?
Period 1: 202304-07, 484 ozone exceedance days
Period 2: 202308-10, 14 ozone exceedance days
Period 3: 202404-06, 13 ozone exceedance days
TEMPO observation available
Ensemble Transfer Kalman Filter (ETKF) utilizes a linear transformation matrix to avoid direct computation of high-dimensional error covariance matrices by using the ensemble error covariance matrix instead, and update the state vector (here as NO2 concentration or emissions).
Performing DA of TEMPO NO2 VCD every three hours during the daytime (marked by dashed lines in figure (i)) improves the alignment of the WRF-Chem ozone diurnal pattern with EPA observations.
Here we shows the WRF-Chem ozone spatial pattern at 11 AM (ET) April 07th 2024 , which also better matches EPA observations, as shown by the colored dots in figures (k) and (l).
Comparison between WRF-Chem and AQS O3 ground diurnal variation
（d）
（e）
（f）
（g）
（h）
（i）
（j）
（k）
（l）