## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
TEMPO Mission Status
Xiong Liu1, K. Chance1, C.R. Nowlan1, G. Gonzalez Abad1, R. Suleiman1, J. Houck1, J. Davis1, H. Wang1, H. Chong1, W. Hou1, J. Park1, J. Bak1, L. Carpenter1,
C. Chan Miller1, J. Fitzmaurice1, A. Oppenheimer1, E. O’Sullivan1,
K. Daugherty2, D.E. Flittner2, C. Fenn2, D. Rosenbaum2, C. Brown2, N. Mishra2,
R.T. Neece2 , E. Roback2, J. Strickland2, L. Judd2, P. Rawat2, K. Travis2, J. Carr3,
J. Szykman4, B. Henderson4, L. Valin4, J. Joiner5, Z. Fasnacht5, S. Frith5,
D. Haffner5, E. Knowland5, N. Kramarova5, N. Krotkov5, C. Li5, W. Qin5,
G. Jaross5, C. Seftor5, A. Vasilkov5, E.-S. Yang5, J. Ziemke5, M. Newchurch6,
Naeger6, R. Cohen7, J. Geddes8, J. Herman9, B. Pierce10, R. Spurr11,
S. Kondragunta12, J. Wang13, O. Torres5, H. Zhang12, P. Ciren12,
X. Zhao14, and the TEMPO Team
1Smithsonian Astrophysical Observatory (SAO), CfA
2NASA LaRc 3Carr Astro. 4EPA 5NASA GSFC 6UAH 7UCB
8BU 9UMBC 10UWM 11RT Sol. Inc 12NOAA 13UI 14ECCC
TEMPO/GeoXO ACX Joint Science Team Workshop
Cambridge, MA
August 19-22, 2025

## Slide 2: Tropospheric Emissions: Monitoring of Pollution
NASA’s first Earth Venture Instrument (EVI-1), selected in 2012
Led by Smithsonian Astrophysical Observatory (SAO) in partnership with NASA LaRC, with instrument built by Ball Aerospace (now part of BAE Systems)
NASA’s first GEO & host payload, launched on board Intelsat-40e in April 2023 on to the GEO at 91 ∘ W
Hourly daytime air pollution over North America at neighborhood scale (2x4.75 km2 at the center of the field of regard)
Global Geostationary Air Quality Constellation along with GEMS (2020) and Sentinel-4 (7/2025)
Credit: NASA’s Scientific Visualization Studio
TEMPO first light RGB and examples of spectra
Credit: Heesung Chong
293-494 nm
538-741 nm

## Slide 3: TEMPO Scanning
Nominal scans: hourly, 2.4M pixels
  2035 North/South pixels
  1181 East/West steps per hour
  2 x 4.75 km2 at center of field of regard
Optimized scans
  Higher temporal resolution scans in early AM and late PM over coasts (40 mins)
Twilights scans (science bonus & discovery)
  Performed during darkness (~Aug. 15-Apr. 15)
  City lights, moonlights, Aurora, airglow, gas flaring, lightning, fires
Special observations to support TEMPO Green Paper: 21 days in 2025 for wildfires, prescribed burning, lightning NOx, CO Front Range field campaigns, CAL/VAL
  High-time scans (5-10 mins) over selected regions (alternate hourly scan /
  1 hour high-time scans)
  Lunar collect (4/9/2025)
  RRV 2024/2025 (side slither)
Request special observations at TEMPO Early Adopter Website
Credit: NASA’s Scientific Visualization Studio
Radiance derivation  Post-processing (de-speckling, de-streaking, etc.)  Composite
Clearest-Sky City lights Composite 1–12 February 2024
Credit: Jim Carr

## Slide 4: TEMPO Timeline & Status
Successful TEMPO commissioning and nominal operation, instrument performing very well
Date | Details
7 April 2023 | Launch
June-July 2023 | TEMPO power on + dry-out, cool down, etc.
2 August 2023 | First light
19 October 2023 | Nominal operations
18 June 2025 | Baseline mission ends (end of prime mission review on 10 Oct. 2025)
September 2026 | First extended mission ends, further extension by NASA senior reviews (next in March 2026)
Credit: Heesung Chong & Dave Flittner
Very small degradation in 2 years even for short UV, correctable in future versions.

## Slide 5: TEMPO Data Products Public Release NASA’s Atmospheric Science Data Center (ASDC)
Public Release | Date | Details
V01 | Feb. 2024 | Limited 3 weeks released
V02 | Feb. 2024 | Level 1 (spectra) released
V03 | May 2024 | L1 updated, Level 2/3 cloud, NO2, HCHO, total O3 V3 O3 profile (ASDC June 9, 2025, not for the public)
V04 | 9/15/2025 | Release ozone profile, update L1 + other L2/L3
NRT V02 | 9/15/2025 | L1, Level 2/3 cloud, NO2, HCHO (funded by SNWG)
TEMPO data now publicly available at NASA’s ASDC (~6 hours latency).
Multiple tools:
  Earthdata Search, OPeNDAP
  NASA Worldview: all data products (L2+L3)
  ArcGIS services: currently L3 NO2 +
  HCHO new + total ozone new
  RSIG (EPA)
  TEMPO-Lite (CfA CosmicDS): L3 NO2
  NASA SPoRT Viewer
  Google Earth Engine (L3 NO2 & HCHO) new
For more information check out:
  User Guides (known issues)
  Daily operation & commissioning logs
  Validation reports (coming soon)
  ATBD (drafts available upon request for L0-1, L2 ATBDs released for cloud, NO2, & HCHO)
V3 download metrics (May 2024-Aug 12, 2025)
2.8 PB (1st instrument to reach 2 PB within 1 year)
101M files
890 unique users
ASDC TEMPO

## Slide 6: Baseline TEMPO Data Products
*Beta: “minimally validated”, publication “not recommended and highly discouraged”
*Provisional: “performance demonstrated”, "suitable for scientific publication”
The data products are upgraded to provisional status after the validation team approval in Dec. 2024!
Level | V3 Product | Validation Status
L1 | Irradiance | Provisional
 | Radiance | Provisional
 | Radiance (twilight – city lights) | Provisional
L2 | Clouds | Provisional
 | NO2 | Provisional
 | HCHO | Provisional
 | O3 (total) | Provisional
 | O3 (profile) | Beta, June 9, 2025
L3 | L2 gridded to 0.02° × 0.02° | Provisional
Level | V4 Product | Validation Status
L1 | Irradiance | Provisional
 | Radiance | Provisional
 | Radiance (twilight – city lights) | Provisional
L2 | Clouds | Provisional
 | NO2 | Provisional
 | HCHO | Provisional
 | O3 (total) | Provisional
 | O3 (profile) | Beta
L3 | L2 gridded to 0.02° × 0.02° | Provisional

## Slide 7: Baseline TEMPO Data Products + SNWG TEMPO NRT + TEMPO Enhanced
Level | Product | Developer
L1 | Irradiance | SAO
 | Radiance NRT | SAO
 | Radiance (twilight – city lights) | SAO
L2 | Cloud NRT | SAO/GSFC
 | NO2 NRT | SAO
 | HCHO NRT | SAO
 | O3 (total) | SAO/GSFC
 | O3 (profile) | SAO
 | TEMPO/GOES-R synergy aerosol product NRT | NOAA (released 1 yr data)
 | C2H2O2 | SAO
 | H2O | SAO
 | BrO | SAO
 | SO2 NRT | NASA GSFC (under develop.)
 | UVAOD | NASA GSFC (under develop.)
 | Aerosol layer height | U. Iowa (under develop.)
 | UVB | NASA GSFC (under develop.)
Baseline Products
Satellite Needs Working Group (SNWG)
Cycle 3 NRT Products (~2-3 hours)
Public release (Sep. 15, 2025)
SNWG Cycle 4
TEMPO Enhanced Products
To be funded ~Q3 2025 (?)
Research Products
  Ocean color (funded by ROSES TEMPO/ACX)
  Vegetation (GPP)
  City lights/lighting types
  HNO2
  Free tropospheric NO2
  Surface concentrations
  Emissions
  Surface albedo
  IO
  NO3
  Solar induced fluorescence

## Slide 8
Algorithm Updates for TEMPO V4 (NRT V2)
GEOS-CF (meteorology / a priori): V1  V2
L1b: Improve absolute calibration (~10% overestimation in normalized radiance)
  Update BTDF by ~cos(30°) and scattering angle dependence, update to radiometric calibration coefficients based on ABI/VIIRS comparison
  Improve straylight correction (over correction in V3): improve PSF + background correction + reconstruct saturated pixels
  Improve wavelength calibration, and wavelength grid for rad. cal. coefficients
  Improve INR (geolocation)
Trace gases and clouds
  NO2 / O2-O2 de-striping
  Greatly Improved GLER surface albedo climatology (fix RAA clipping & BRDF clipping)
  Fix surface pressure anomaly (index shift by 1 in GEOS-CF surface pressure)
  Include clear-sky AMF & scattering weights for NO2/HCHO
TEMPO V3 in NASA ASDC
histogram peaks at ECF ~ 0.05,
suggesting an overestimate.
20240601 all scans
TEMPO V4*
20240601 all scans
ECF histogram peaks ~0.0, primary
due to L1b update & GLER
Histogram of Effective Cloud Fraction (ECF)

## Slide 9
Total O3: L1b improvement and
  Update LUTs with average on-orbit slit functions
  Perform additional soft calibrations using NPP OMPS data
  Quality flag updates.
Profile O3 : L1b improvement and
  Additional soft calibration
  Optimization in a priori, surface albedo, and measurement error constraint
Algorithm Updates for TEMPO V4
7/26/2024
V3: TEMPO-NPP
V4*: TEMPO-NPP
UVAI bias reduced from -2 in V3 to 0 in V4* (mostly from L1b)
Lat. depen. reduced from soft cal.
V3 soft cal.
7/26/2024
V4* soft cal.
7/26/2024
6/12/2024 S006
8/08/2024 S008
V4*: This version is subject to change before public release of V4.
Credit: Matthew Johnson

## Slide 10
TEMPO AGU Special Collection
Call for Papers
TEMPO Data Products, Science, and Applications
Submission Deadline: December 31, 2025
Currently, 21 papers were submitted and 5 papers were published.

## Slide 11: Summary and Outlook
TEMPO operations are nominal, and instrument is performing very well.
Mission extended to September 2026, further extension via Senior Review
V3 L1b, cloud, NO2, HCHO, total O3 are publicly available and upgraded to provisional status. O3 profile product is operationally produced.
Significantly improved V4 data products including ozone profile and V2 NRT products will be released in mid-September 2025
Many more TEMPO products to come!
AGU Special Collection “TEMPO data products, science and applications” are open until 12/31/2025.
Thank you!
Acknowledgements: Funding from NASA (TEMPO, NNL13AA09C; SNWG TEMPO NRT, 80MSFC24CA004)