## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
TEMPO Level 1 Status
Heesung Chong1, X. Liu1, D.E. Flittner2, J. Houck1, J. Carr3, W. Hou1, J. Park1, G. González Abad1, C.R. Nowlan1, H. Wang1, L. Flynn4, S. Marchenko5, J. Joiner5, J. E. Davis1, R. M. Suleiman1, J. Fitzmaurice1, L. Yatsuhashi1, K. Chance1, B. Baker6, C. Seftor5, G. Jaross5, J. O. Robaidek7, X. Wu4, H. Xu4, B. Basnet4, Y. Bai4, C. Cao4, D. Doelling2
1SAO, CfA 2NASA LaRC 3Carr Astro. 4NOAA/NESDIS 5NASA GSFC 6BAE 7UW–Madison
August 19, 2025

## Slide 2: Updates in Version 4
Major updates
  Absolute calibration
  Stray light correction
  Spectral calibration
Additional updates
  Diffuser goniometry correction
  Etalon fringe correction
  Smear correction

## Slide 3: Absolute calibration
Issue to resolve in Version 3: Positive bias in Sun-normalized radiance (on the order of 10%)
Approach: Adjust the solar diffuser transmittance.
(Earth radiance)
(Solar irradiance)
(Sun-normalized radiance) =
(Earth-radiance electric current) * (Calibration coefficient)
(Solar-irradiance electric current) * (Calibration coefficient) / (Diffuser transmittance)
=

## Slide 4: Absolute calibration
1024th spatial index
2023/08/01 (first-light)
(Solar irradiance) = (Solar-irradiance electric current) * (Calibration coefficient) / (Diffuser transmittance)
(Earth radiance) = (Earth-radiance electric current) * (Calibration coefficient)
(TEMPO Version 3 irradiance) – (TSIS-1 reference irradiance)
Why did the transmittance bias not appear in Version 3?  Biases in calibration coefficients
How to verify the hypothesis?  Earth radiance

## Slide 5: Absolute calibration
Applying in Version 4 will decrease Sun-normalized radiances by ~13.4%.
Solar diffuser
Definition of BTDF at GSFC during on-ground calibration
Definition of BTDF in TEMPO algorithm
Update in BTDF (Bidirectional Transmittance Distribution Function) data interpretation
Use of in TEMPO algorithm - Version 3: - Version 4:

## Slide 6: Absolute calibration
In Version 4, the UV and visible calibration coefficients will be reduced by 11% and 7%, respectively.
Earth radiance intercomparison (TEMPO vs. ABI vs. VIIRS)
Example: 470 nm (UV), GOES-19

## Slide 7: Absolute calibration
Version 3
*Note: Spectral-independent, constant surface albedo (0.074) was used.
[Credit: Junsung Park]
2023/11/06, scan 009, granule 02
Sun-normalized radiance (Version 3  Version 4)
Updated
Most significant outcome: Cloud fraction bias will be significantly reduced.
(For details, see Huiqun (Helen) Wang’s presentation at 14:00 today.)
Ratio: TEMPO / VLIDORT simulation

## Slide 8: Stray light correction
Issues to resolve in Version 3:
Overcorrection at short wavelengths
Background stray light remaining in the UV channel
Most significant outcome: Ozone profile retrieval will be stabilized.
(For details, see Junsung Park’s presentation at 14:30 today.)
Approach 1
Update PSFs (Point Spread Functions).
Approach 2
Implement a background stray light correction.
Before
(308.03 nm)
After
(308.03 nm)
VIS PSF

## Slide 9: Stray light correction
Before reconstruction
After reconstruction
Approach 3: Reconstruct radiances for CCD pixels with signal saturation.
Without reconstructing these flat-tops, stray light is underestimated.
Most significant outcome: Positive biases in formaldehyde retrieval over cloudy pixels will be mitigated.
(For details, see Gonzalo González Abad’s presentation at 14:20 today.)

## Slide 10: Spectral calibration
Issue to resolve in Version 3: Spatial variability (North-South) in wavelength registration
Approach: Remove the slit-function asymmetry factor from the fitting to increase stability.
[Image credit: Gonzalo González Abad]
NO2 fitting window
HCHO fitting window
Spectral shift [nm]
Spectral shift [nm]
NO2 fitting window
HCHO fitting window
CCD spatial index (North ➝ South)
CCD spatial index (North ➝ South)
Version 3
Updated
(For details, see Weizhen Hou’s poster tomorrow.)
Most significant outcome: The Level 1 calibration will capture spectral changes with enhanced accuracy.

## Slide 11: Summary
For Version 4, we have enhanced
  the Sun-normalized radiance absolute calibration
  the stray light correction
  the spectral calibration
  the diffuser goniometry correction, etalon fringe correction, and smear correction.
Calibration work will continue.

## Slide 12
Thank you for your attention!