## Slide 1
Developing Atmospheric Composition Validation Networks and Methods for GeoXO Era using TEMPO
August 20, 2025
Mina Kang, Mitch Goldberg, Shobha Kondragunta, Hai Zhang, Fred Moshary, Ruben Delgado, Yonghua Wu, Barry Baker, Wei Li
Postdoctoral Researcher
The City Collegee of New York
A National Oceanic and Atmospheric Administration (NOAA) Educational Partnership Program with Minority Serving Institutions (EPP/MSI) Cooperative Science Center (CSC) since 2016 (#NA22SEC4810016)
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)

## Slide 2
Joint Collaborative Research and Development Project (JCRDP)
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
    Develop a satellite-based atmospheric composition (AC) validation system through collaboration between CESSRST-II and NCAS-M researchers and students, with guidance from experts at NOAA, NASA, and EPA.
NCAS-M
Ground-based observing instruments deployed at CCNY
Smoke layers observed by the CCNY CHM15k ceilometer, June 3–6, 2025

## Slide 3
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
TEMPO L2 Product
(O3T, NO2, HCHO,
AOD, ALH, PM2.5)
Forecast Model
(NOAA-NAQFC,
ECMWF-CAMS)
Ground-based Observations
(PGN, AERONET, UCN, AQS)
Collocation
Hourly Stats
Weekly/Monthly/Yearly Stats
Vertical Cross Section
j
Conceptual Framework
This system will enhance NOAA’s AerosolWatch and provide additional independent functionality.
*NAQFC: NOAA Air Quality Forecast Capability
*CAMS: Copernicus Atmosphere Monitoring Service Global Atmospheric Composition Forecasts
*UCN: Unified Ceilometer Network
*AQS: Air Quality System from the U.S. EPA

## Slide 4
j
Seasonal Mean AOD (Aug. 2023 – Jul. 2024)
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
Land-only AOD with high quality retrieval and without high SZA, sunglint, or snow/ice contamination
CONUS
Major Cities
Notes: the surface in the Salt Lake City area is very bright, and VIIRS also has difficulty retrieving data in that region.

## Slide 5
j
Case Study
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
Smoke plume from the Jones Road Fire in New Jersey at 13:45 UTC on April 22, 2025
Notes: The fire ignition time of the Jones Road Wildfire (Ocean County Fire) was at 9:45 AM EDT (1:45 PM UTC) on April 22, 2025, near 39.95°N, 74.35°W

## Slide 6
j
Case Study
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
Downwind Impacts: Smoke-Related PM2.5 and High Ozone Event (April 22–24, 2025)
See also: Dr. Moshary, “Synergistic observation of ozone and aerosol vertical distribution, transport, and application to air quality by ground-based lidar and satellite in New York City area” (Aug 20, 4:50 p.m.)

## Slide 7
j
AOD Validation
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
TEMPO AOD: 0.76
AERONET AOD: 0.07
Outliers are dominated by cloud-/snow-contaminated pixels and bright-surface hotspots.
Notes: most of the outliers are due to cloud contamination and hotspots over bright surfaces . Higher TOA reflectance is associated with positive bias
.

## Slide 8
CAMS
NAQFC
TEMPO
Ground Meas
HCHO
NO2
O3T
AOD
PM2.5
Monthly Average for August 2023
(Resampled to CAMS Resolution)
Trop.
Trop.
Notes: Cams no2 clound 0.3 & quality flag AOD quality flag / sunglint, high sza vza /

## Slide 9
CAMS
NAQFC
TEMPO
Ground Meas
HCHO
NO2
O3T
AOD
PM2.5
Monthly Average for August 2023
(Resampled to CAMS Resolution)
Tot.
Tot.

## Slide 10
HCHO
NO2
O3T
AOD
PM2.5
Bias Relative to Pandora, AERONET, and AQS Observations – August 2023
CAMS
NAQFC
TEMPO
HCHO | Corr | MB | RMSE
CAMS | 0.82 | -0.13 | 0.35
NAQFC | 0.76 | -0.17 | 0.43
TEMPO | 0.86 | 0.03 | 0.30
NO2_tot | Corr | MB | RMSE
CAMS | 0.72 | 0.24 | 0.30
TEMPO | 0.84 | -0.09 | 0.16
NO2_trop |  |  | 
NAQFC | 0.87 | -0.16 | 0.21
TEMPO | 0.87 | -0.01 | 0.12
O3T | Corr | MB | RMSE
CAMS | 0.88 | -4.40 | 6.29
TEMPO | 0.84 | -0.32 | 5.17
AOD | Corr | MB | RMSE
CAMS | 0.77 | 0.07 | 0.09
NAQFC | 0.72 | 0.03 | 0.06
TEMPO | 0.71 | 0.02 | 0.08
PM2.5 | Corr | MB | RMSE
CAMS | 0.41 | 2.45 | 4.58
NAQFC | 0.55 | -0.25 | 3.43
TEMPO | 0.84 | 1.61 | 2.71
[1016 molecules/cm2]
[1016 molecules/cm2]
[1016 molecules/cm2]
[DU]
[µg/m3]
Tot.
Tot.

## Slide 11
HCHO
NO2
O3T
AOD
PM2.5
Bias Relative to Pandora, AERONET, and AQS Observations – August 2023
CAMS
NAQFC
TEMPO
HCHO | Corr | MB | RMSE
CAMS | 0.82 | -0.13 | 0.35
NAQFC | 0.76 | -0.17 | 0.43
TEMPO | 0.86 | 0.03 | 0.30
NO2_tot | Corr | MB | RMSE
CAMS | 0.72 | 0.24 | 0.30
TEMPO | 0.84 | -0.09 | 0.16
NO2_trop |  |  | 
NAQFC | 0.87 | -0.16 | 0.21
TEMPO | 0.87 | -0.01 | 0.12
O3T | Corr | MB | RMSE
CAMS | 0.88 | -4.40 | 6.29
TEMPO | 0.84 | -0.32 | 5.17
AOD | Corr | MB | RMSE
CAMS | 0.77 | 0.07 | 0.09
NAQFC | 0.72 | 0.03 | 0.06
TEMPO | 0.71 | 0.02 | 0.08
PM2.5 | Corr | MB | RMSE
CAMS | 0.41 | 2.45 | 4.58
NAQFC | 0.55 | -0.25 | 3.43
TEMPO | 0.84 | 1.61 | 2.71
[1016 molecules/cm2]
[1016 molecules/cm2]
[1016 molecules/cm2]
[DU]
[µg/m3]
Trpp.
Trpp.

## Slide 12
    The atmospheric composition validation networks and procedure have been developed
    For NO₂ and HCHO, TEMPO shows high correlations and low biases, so they can serve as reliable references for models.
    For AOD, performance is similar to the models, but we expect further improvements once cloud screening is refined
    TEMPO shows strong agreement with ground-based observations, offering reliable validation for models today and key insights for future missions like GeoXO-AC
j
Summary
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
Notes: most of the outliers are due to cloud contamination and hotspots over bright surfaces . Higher TOA reflectance is associated with positive bias
.

## Slide 13
Questions
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
Thank you

## Slide 14
CENTER FOR EARTH SYSTEM SCIENCES & REMOTE SENSING TECHNOLOGIES (CESSRST-II)
Weekday-Weekend NO2 Variation
Monthly Validation of O3 Total Column
j
Application of Conceptual Framework