## Slide 1: Assessing Ozone Dynamics During the 2023 Summer STAQS Field Campaign Using Synergistic Observations and Model Simulations
TEMPO/GeoXO ACX Joint Science Workshop August 2025
Claudia M. Bernier
NASA Ames Center, Earth Science Division

## Slide 2
Key Configurations for WRF-Chem v4.2 Simulation | 
Period ran | 2023-07-23 00:00 – 2023-08-18 00:00 UTC
Horizontal | nested domains: 12, 4, 1.33 km
Vertical | 47 levels; surface - 50 hPa
Anthropogenic | NEMO based on US EPA NEI 2019 (1 km)
Initial/boundary | Meteorology: GFS (0.25°), Chemical: WACCM (1° x 1°)
Chemistry | Gas scheme: MOZART-T1, Aerosol scheme: GOCART
Other emissions | Fire: FINNv2.5, Biogenic: MEGAN
Parameterizations | Thompson, Modified Tiedtke, RRTMG, YSU, revised Monin-Obukhov, Noah, full TUV, Lightning-NOx
AGES+ campaign & model setup
Domain setup:
Instruments used:
subregions: urban, Long Island coastal, CT coastal

## Slide 3
Surface model vs. observations: O3 & NO2
Evaluating model performance
O3: higher biases overnight & daytime peaks
  R = 0.74, MB = 4.4 ppb, NMB = 12.5%
NO2 : underestimated peaks
  R = 0.56, MB = -1.4 ppb, NMB = -19.1%
Subregions:
  Urban region: best performance (higher correlation, lowest biases)
  LI & CT coastal: moderate - low correlation, higher biases (especially CT coastal)
Wind speed:
  R = 0.68, MB = 0.7 m/s, NMB = 27.0%
Wind direction:
  R = 0.73, MB = -5.2°, NMB = 4.7 %
Subregions:
  Urban region: weaker correlation, higher RMSE due to calmer/more variable winds
  LI & CT coastal: slightly better performance

## Slide 4
R: 0.81, NMB:-14.5%
R: 0.80, NMB:-3.6%
R: 0.10, NMB: 46.1%
R: 0.03, NMB: 38.4%
08/05
08/09
08/05
08/09
Evaluating TEMPO with GCAS data
NO2
  TEMPO generally agrees with GCAS
  Largest underestimation over Staten Island & overestimation over Manhattan & west LI (Queens/Brooklyn)
    Could be due to retrieval over water/land, reflectivity assumptions
HCHO:
  TEMPO shows poor spatial correlation & high bias due to background noise sensitivity

## Slide 5
Evaluating TEMPO at Pandora sites
Urban Sites
  Good agreement/moderate - strong correlation overall
  NO2 by sites:
    All positive biases except New Brunswick & Bayonne (transitional urban/rural sites)
    TEMPO can resolve urban fringes to some extent but overestimates how steeply NO2 decreases between areas
    TEMPO retrieval may be overestimating background NO2
R = 0.71
NMB = 2.9%
RMSE = 3.3e+15 (molec/cm2)
R = 0.43
NMB = -8.0%
RMSE = 5.5e+15 (molec/cm2)
R = 0.25
NMB = -12.6%
RMSE = 4.7e+15 (molec/cm2)
R =. 0.17
NMB = 43.2%
RMSE = 1.5e+15 (molec/cm2)
Coastal Sites
  Weaker agreement/correlation overall
  NO2 by sites:
    Positive biases
    Lower/background NO2 concentrations => lower signal
    Poorer performances due to retrieval accuracy at land-water interfaces
  HCHO by sites:
    weaker correlations & negative biases
    more missing data
    correlations vary
Retrieval challenges:
  Vertical sensitivity
  A priori vertical profiles
  Clouds, aerosols, & surface reflectance
Urban Sites
Coastal Sites
NO2
HCHO

## Slide 6
DC8 Instrument Flight Path Overlayed on TEMPO retrieval
08/09
19:00
20:00
21:00
08/16
19:00
20:00
21:00
General agreement, especially over urban NYC, further evidence TEMPO can capture urban/rural or coastal gradients
Some discrepancies (e.g., near Flax Pond on Aug 16) highlight how rapid plume evolution & vertical distribution differences can affect alignment between column & in situ measurements

## Slide 7: Integrated multi-platform analysis of pollution events during STAQS
Use integrated approach from multiple observational platforms to analyze O₃ dynamics & chemical characteristics during STAQS:
  TOLNet lidars stationed along the LIS
  Doppler wind lidars co-located at select sites
  Satellite, airborne, & ground-based column measurements of NO2 & HCHO from TEMPO & GCAS
  Use WRF-Chem outputs to bridge gaps between measurements
Focus on unique cases during high, moderate, & low pollution conditions:
    July 26 & 28
    August 5, 9, 11, & 12

## Slide 8
07/26: surface O3 & winds
Defining O3 Dynamics: high pollution days
07/28: surface O3 & winds
Max O3 (104 ppb) at 19 UTC on CT coastline
Land/sea breeze circulation: W  S shift
Lower early urban O3 (< 65 ppb)
Max O3 (94 ppb) at 17 UTC along southern LI coast
Land/sea breeze circulation: NW/W  SW/S shift
07/26: lidars
NYTOLS lidar
TROPOZ lidar
TOPAZ lidar
BRONX
STONY BROOK
YALE COASTAL
BRONX
WANTAGH
STONY BROOK
YALE COASTAL
07/28: lidars
NYTOLS lidar
TROPOZ lidar
TOPAZ lidar

## Slide 9
07/26
07/28
14:00 – 17:00 UTC
17:00 – 20:00 UTC
07/26
07/28
14:00 – 17:00 UTC
17:00 – 22:00 UTC
07/26
07/28
14:00 – 17:00 UTC
17:00 – 20:00 UTC
Spatiotemporal ozone precursor characterization
GCAS
NO2 VCDs
GCAS
HCHO VCDs
GCAS HCHO / NO2

## Slide 10
Defining O3 Dynamics: moderate & low pollution days
Max daily observed O3 reaching 72/76 ppb at 18:00/19:00 UTC on Staten Island
Max daily observed O3 reached only 49 ppb
08/05: surface O3 & winds
08/09: surface O3 & winds
BRONX
STONY BROOK
YALE COASTAL
08/09: lidars
NYTOLS lidar
TROPOZ lidar
TOPAZ lidar
LMOL lidar
08/05: lidars
NYTOLS lidar
TROPOZ lidar
TOPAZ lidar
STATEN ISLAND
BRONX
YALE COASTAL

## Slide 11
08/05
08/09
14:00 – 17:00 UTC
17:00 – 20:00 UTC
TEMPO
14:00 – 17:00 UTC
17:00 – 20:00 UTC
GCAS
08/05
08/09
14:00 – 17:00 UTC
17:00 – 22:00 UTC
TEMPO
14:00 – 17:00 UTC
17:00 – 22:00 UTC
GCAS
08/05
08/09
14:00 – 17:00 UTC
17:00 – 20:00 UTC
TEMPO
14:00 – 17:00 UTC
17:00 – 20:00 UTC
GCAS
GCAS & TEMPO
NO2 VCDs
GCAS & TEMPO
HCHO VCDs
GCAS & TEMPO HCHO / NO2
Spatiotemporal ozone precursor characterization

## Slide 12
Defining O3 Dynamics: moderate pollution days
Max daily observed O3 reaching 77 ppb in afternoon
> 70 ppb for 4 consecutive hours after along CT coastline
Max daily observed O3 reaching 78/ 73 ppb at 18/19 UTC north of NYC
~ 69 ppb in Manhattan at 17 UTC
08/11: surface O3 & winds
08/12: surface O3 & winds
08/11: lidars
NYTOLS lidar
TROPOZ lidar
LMOL lidar
STONY BROOK
YALE COASTAL
TOPAZ lidar
TOPAZ lidar
08/12: lidars
BRONX
SUFFERN
TROPOZ lidar

## Slide 13
14:00 – 17:00 UTC
17:00 – 20:00 UTC
14:00 – 17:00 UTC
17:00 – 22:00 UTC
08/11
08/12
08/11
08/12
08/11
08/12
14:00 – 17:00 UTC
17:00 – 20:00 UTC
TEMPO
NO2 VCDs
TEMPO
HCHO VCDs
TEMPO HCHO / NO2
Spatiotemporal ozone precursor characterization

## Slide 14
Conclusions & Future Work
STAQS campaign captured wide range of pollution events (high, moderate, low) driven by varying meteorological & chemical conditions across NYC/LIS region
Multi-platform approach (surface monitors, lidar profiles, model output, Pandora, GCAS, TEMPO) provided comprehensive understanding of O3 dynamics
Intercomparisons between datasets filled temporal/spatial gaps & emphasized importance of resolving sub-grid variability in complex coastal and urban–rural interface regions
GCAS & TEMPO VCDs revealed key insights into NO2 & HCHO influences on coastal O3 formation
Although TEMPO not operational during highest O3 days, GCAS showed value of high-resolution VCDs for diagnosing coastal pollution accumulations
When available, TEMPO effectively captured sharp spatial/temporal gradients in NO2 & HCHO, supporting its value for forecasting and air quality mitigation planning
Future work:
  incorporate TEMPO O3 products (0 – 2km), assess performance at urban–rural & land–water interfaces
  evaluate effects of a priori profiles
  further investigation impact of land cover, land use maps, urban heating as drivers of BL evolution, sea breeze development, & O3 formation in modeling (WRF)
contact: claudia.m.bernier@nasa.gov

## Slide 15: Extra slides/info

## Slide 16
Table S2. Mean surface statistics model vs. observations |  |  |  | 
a) full domain |  |  |  | 
 | R | MB (ppb) | NMB (%) | RMSE (ppb)
O3 | 0.73 | 4.4 | 12.5 | 10.6
NO2 | 0.56 | -1.4 | -19.1 | 4.0
 | R | MB (m/s, °) | NMB (%) | RMSE (m/s, °)
wind speed | 0.68 | 0.7 | 27.0 | 1.4
wind direction | 0.73 | -5.2 | 4.7 | 57.8
By sub regions |  |  |  |  |  |  | 
 | R | MB (ppb) |  | NMB (%) |  | RMSE (ppb) | 
O3 |  |  |  |  |  |  | 
urban | 0.74 | 1.8 |  | 5.0 |  | 10.3 | 
LI coastal | 0.60 | 3.5 |  | 9.2 |  | 12.0 | 
CT coastal | 0.66 | 5.0 |  | 13.6 |  | 13.0 | 
NO2 |  |  |  |  |  |  | 
urban | 0.55 | -0.2 |  | -2.4 |  | 5.3 | 
LI coastal | 0.39 | -0.6 |  | -27.5 |  | 1.6 | 
CT coastal | 0.26 | -4.2 |  | -62.8 |  | 6.4 | 
 | R | MB (m/s, °) |  | NMB (%) |  | RMSE (m/s, °) | 
wind speed |  |  |  |  |  |  | 
urban | 0.52 | 0.5 |  | 13.4 |  | 1.82 | 
LI coastal | 0.63 | 0.9 |  | 31.9 |  | 1.78 | 
CT coastal | 0.55 | 0.9 |  | 35.5 |  | 1.76 | 
wind direction |  |  |  |  |  |  | 
urban | 0.68 | -4.1 |  | -1.1 |  | 65.5° | 
LI coastal | 0.77 | -5.7 |  | -1.6 |  | 54.1° | 
CT coastal | 0.76 | 0.2 |  | 0.0 |  | 56.1° | 
Evaluating model performance

## Slide 17
Evaluating model performance across domain resolutions
 | R |  |  | MB |  |  | NMB (%) |  |  | RMSE |  |  | MAE |  | 
 | d01 | d02 | d03 | d01 | d02 | d03 | d01 | d02 | d03 | d01 | d02 | d03 | d01 | d02 | d03
a) Domain average full campaign period: 0726 – 0816 (11 – 23 UTC) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
O3 | 0.77 | 0.76 | 0.75 | 4.8 | 4.2 | 4.5 | 14.2 | 12.4 | 13.4 | 10.0 | 9.4 | 9.7 | 8.0 | 7.6 | 2.8
NO2 | 0.64 | 0.62 | 0.57 | -0.1 | -0.1 | -0.1 | -2.0 | -1.4 | -1.1 | 3.5 | 3.9 | 4.2 | 2.5 | 7.7 | 2.9
Domain average one day: 0726 (11 – 23 UTC) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
O3 | 0.92 | 0.88 | 0.86 | 4.7 | 0.6 | 0.3 | 9.4 | 1.3 | 0.7 | 10.2 | 10.4 | 11.3 | 8.5 | 9.7 | 10.4
NO2 | 0.95 | 0.96 | 0.92 | 0.4 | 0.1 | 0.2 | 4.6 | 1.4 | 2.4 | 2.6 | 3.0 | 2.9 | 2.1 | 2.6 | 2.3
Domain average one day: 0802 (11 – 23 UTC) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
O3 | 0.99 | 0.99 | 0.98 | 1.8 | 1.1 | 1.1 | 5.4 | 3.3 | 3.5 | 2.3 | 1.8 | 1.9 | 1.9 | 1.3 | 1.3
NO2 | 0.86 | 0.91 | 0.91 | 0.6 | 0.5 | 0.1 | 14.1 | 10.6 | 2.9 | 1.4 | 1.0 | 0.83 | 1.0 | 0.8 | 0.7
Benefit of higher resolution not necessarily linear finer grid sizes & also varies by day
Resolution might not significantly improve predictions, but better captures spatial distributions
Detailed spatiotemporal info important in complex regions with fine meteorological processes & emissions
O3 0802 (19:00 UTC)
d03
d02
d01

## Slide 18
WSPD > 3
WSPD < 3
WSPD > 3
WSPD < 3
WSPD > 3
WSPD < 3
 | WSPD | WDIR
Mean Bias | 0.7 | -6.6
Normalized Mean Bias | 30.1 | 5.9
R Correlation | 0.63 | 0.69
Root Mean Squared Error | 1.5 | 60.3
Mean Absolute Error: | 1.2 | 41.8
 | WSPD | WDIR
Mean Bias | 0.7 | -5.7
Normalized Mean Bias | 25.5 | 5.1
R Correlation | 0.67 | 0.72
Root Mean Squared Error | 1.4 | 58.5
Mean Absolute Error: | 1.2 | 40.0
 | WSPD | WDIR
Mean Bias | 0.7 | -5.2
Normalized Mean Bias | 27.0 | 4.7
R Correlation | 0.68 | 0.73
Root Mean Squared Error | 1.4 | 57.8
Mean Absolute Error: | 1.1 | 39.4
D02
Statistically wind speed & direction improve with finer simulations
Winds tend to be more variable at lower speeds
If we filter out winds less than 3 m/s we get a better correlation
This shows how the model is better able to capture wind direction at higher speeds
D03
WSPD
WDIR
D01
Evaluating model performance across domain resolutions
Domain average winds overall stations: 07/26 – 08/16 (11:00 – 23:00 UTC)
D01
D02
D03

## Slide 19
Evaluating model spatiotemporal performance
~ using TOLNet
model - NYTOLS lidar
model - TROPOZ lidar
model - TOPAZ lidar
model - NYTOLS lidar
model - TROPOZ lidar
model - TOPAZ lidar
model - NYTOLS lidar
model - TROPOZ lidar
model - TOPAZ lidar
model - LMOL lidar
Different results depending on the type of pollution day
07/26: high pollution day (sea breeze) model peaks earlier than observed
08/05: moderate pollution day better but mixed model performance
08/09: low pollution day good model performance in lower 2000 m (except right at surface for NYTOLS lidar)
07/26:
08/05:
08/09:

## Slide 20
Table 1. Pandora vs. TEMPO average campaign VCD statistics |  |  |  |  |  |  |  | 
 | NO2 |  |  |  | HCHO |  |  | 
Site | R | NMB (%) | RMSE (molec/cm2) | Mean Pandora (molec/cm2) | R | NMB (%) | RMSE (molec/cm2) | Mean Pandora (molec/cm2)
New Brunswick | 0.58 | -6.9 | 2.0e+15 | 4.0e+15 | 0.29 | -1.6 | 6.2e+15 | 1.3e+16
Bayonne | 0.63 | -5.4 | 4.6e+15 | 1.0e+16 | 0.42 | -8.4 | 5.1e+15 | 1.3e+16
Queens | 0.64 | 0.8 | 3.2e+15 | 7.9e+15 | 0.51 | -13.3 | 5.5e+15 | 1.5e+16
Manhattan-CCNY | 0.73 | 3.8 | 2.8e+15 | 7.5e+15 | 0.82 | 6.2 | 5.8e+15 | 1.3e+16
Bronx | 0.55 | 26.0 | 3.3e+15 | 5.6e+15 | -- | -- | -- | --
Old Field | -0.04 | 77.7 | 1.8.e+15 | 1.6e+15 | -- | -- | -- | --
Westport | 0.16 | 49.5 | 1.6e+15 | 1.9e+15 | 0.23 | -17.4 | 5.2e+15 | 1.3e+16
New Haven | 0.20 | 16.9 | 1.3e+15 | 2.2e+15 | -- | -- | -- | --
Madison | 0.17 | 41.6 | 1.3e+15 | 1.4e+15 | 0.14 | -7.6 | 4.3e+15 | 1.0e+16
Evaluating TEMPO performance

## Slide 21
a) 07/26: O3 averages
b) 07/28: O3 averages
c) 08/05: O3 averages
d) 08/06: O3 averages
e) 08/11: O3 averages
f) 08/12: O3 averages
h) 08/09: O3 averages
g) 08/02: O3 averages
Average O3 by cases

## Slide 22
a) 07/26: Wind averages
b) 07/28: Wind averages
urban
LI coastal
CT coastal
c) 08/05: Wind averages
d) 08/06: Wind averages
urban
LI coastal
CT coastal
e) 08/11: Wind averages
f) 08/12: Wind averages
urban
LI coastal
CT coastal
g) 08/02: Wind averages
h) 08/09: Wind averages
urban
LI coastal
CT coastal
Average winds by cases