## Slide 1: Evaluating TEMPO and quantifying NOx with AMAX-DOAS in the Colorado Front Range
Clara Lietzke*, Sunil Baidar, Jan-Lukas Tirpitz, Ruby Burgess, Robert G. Ryan, Alan Brewer, Steve Brown, Xinrong Ren, Rainer Volkamer*
*Dept. of Chemistry & CIRES, CU Boulder
TEMPO/GeoXO ACX Joint Science Team Workshop – Aug 2025

## Slide 2: Outline
Ozone formation and NOx sensitivity in the Colorado Front Range
AMMBEC 2024 aircraft campaign
CU AMAX-DOAS measurements and mass balance approach
NOx emissions
  Concentrated animal feeding operation (CAFO)
  Oil and gas basin (Denver-Julesburg Basin)
TEMPO NO2 over Denver
Outlook and synergies with TEMPO

## Slide 3: Ozone formation in the CO Front Range
High summertime ozone with “serious” classification by EPA
Much of the region is NOx-sensitive1
Necessary to quantify and reduce NOx emissions from shared land use (O&G, agriculture, transportation)
Previous work found that concentrated animal feeding operations (CAFOs) have the potential to double NOx in remote areas2
NO
NO2
RO2
RO
OH
HO2
RH
O3
N
20 km
Urban area, NOx-saturated
Rural area, NOx-sensitive
Denver-Julesburg oil & gas basin
+ agriculture
Denver
Boulder
Image Landsat/Copernicus

## Slide 4: Airborne Methane Mass Balance Emissions in Colorado (AMMBEC) campaign in summer 2024
AMAX-DOAS: NO2, HCHO, O4 columns
Radiometers: surface albedo
In situ monitors: NO2, NOy (+ O3, GHGs)
Scanning Doppler lidar: 3-D wind and aerosol profiles, boundary layer height
NOAA Twin Otter aircraft payload

## Slide 5: CU AMAX-DOAS Airborne Multi-AXis Differential Optical Absorption Spectroscopy
Motion stabilized, rotated prism telescope
Fixed, cloud-free, high-altitude (~2200 m agl; above boundary layer) zenith reference spectrum recorded during the same flight
Stratospheric NO2 correction
Geometric air mass factor1,2
NO2 fit window (425 – 490 nm)
Cross sections:
  NO2 (298 K; Vandaele et al., 1998)
  O3 (223 K; Serdyuchenko et al., 2014)
  O2-O2 (293 K; Thalman & Volkamer, 2013)
  H2O (296 K; HITEMP 2010; Rothman et al., 2010)
  Rotational Raman (250 K; Chance & Kurucz, 2010)
5th order polynomial and constant intensity offset
HCHO fit window (328.5 – 346 nm)
Cross sections:
  HCHO (297 K; Meller & Moortgat, 2000)
  O3 (223 K; Serdyuchenko et al., 2014)
  O2-O2 (293 K; Finkenzeller & Volkamer, 2022)
  NO2 (298 K; Vandaele et al., 1998)
  Rotational Raman (250 K; Chance & Kurucz, 2010)
5th order polynomial and constant intensity offset
We measure in the same geometry as TEMPO
TEMPO
AMAX-DOAS
Top of atmosphere
Boundary layer
Surface
Albedo, forward off-axis angles support RTM and are well-suited to evaluate TEMPO measurements and a priori!

## Slide 6: AMAX-DOAS measurements & mass balance approach
Measurements used for mass balance analysis meet the following criteria:
Nadir spectra measuring columns below the aircraft
  Apply geometric AMF to convert slant columns to VCDs
SZA < 60°
  Suitable for stratospheric NO2 correction and geometric AMF approximation
Measurements used for TEMPO evaluation include additional criteria:
Within 30 minutes of TEMPO overpass
Legs above the boundary layer (>1500 m agl)
  Free tropospheric column above the aircraft (determined from TEMPO a priori) is added
Sum NO2 flux, F, along a closed path, S, to get emission rate, Q
S
source area
F1
F2
F3 …
Fn
DOAS VCD & Lidar wind
In-situ conc. & Lidar wind + BLH
or

## Slide 7: NOx emissions from a CAFO
Only some CAFOs are explicitly included in emissions inventories
Between 3 flights and 6 loops, we observe an average NOx emission rate of 9 kg hr-1
AMAX-DOAS NO2 VCDs
NO2 flux around CAFO
wind
Factor of 1.2 to account for NOx (NO + NO2) photostationary state

## Slide 8: NOx emissions from an O&G basin
Suitable wind conditions + accounting for NOx photostationary state and NOy chemistry1
Between 2 flights and 4 loops, we observe average NOx emissions of 2.5 – 3.6 MT hr-1
30-90% higher than in state-of-the-art GRA2PES emission inventory
6-hr Hysplit backtrajectories
Doppler lidar boundary layer and wind

## Slide 9: TEMPO captures NO2 plumes over Denver

## Slide 10: TEMPO captures NO2 plumes over Denver
Sub-pixel
variability

## Slide 11: Summary & Outlook
Synergies between DOAS, Doppler lidar, and in situ measurements allow for quantification of NOx emissions from small (individual CAFO) and large (basin-wide) source areas
NOx emissions are underestimated in emissions inventories
TEMPO captures NO2 plumes over Denver
Synergies with TEMPO & future opportunities
  Evaluate TEMPO’s ability to quantify NOx emissions
  RTM using albedo and off-axis angles (+ expand to low altitude legs)
  Evaluate TEMPO a priori
  Evaluate TEMPO HCHO
  RFN and O3 photochemistry
State of Colorado contract #2025*0297
Surface albdeo
HCHO VCD [molec cm-2]
Forward off-axis angles supporting RTM

## Slide 12: Extra slides

## Slide 13: Mass balance approach
Net source strength
(1)
(2)
Sum NO2 flux, F, along a closed path, S, to get emission rate, Q
S
source area
F1
F2
F3 …
Fn
in situ
DOAS VCD
Doppler lidar wind perpendicular to flight path
Doppler lidar
Assume negligible change in pollutant concentration and chemistry (or apply correction factor)
Need to assume steady-state winds and negligible wind divergence (choose suitable flights for analysis or apply correction)

## Slide 14: Between 2 flights and 4 loops, we observe average NOx emissions of 2.5 – 3.6 MT hr-1
NOx (NO + NO2) photostationary state
Flight Information |  |  | Doppler Lidar Meas. Mean (Std Dev) |  |  | DOAS NO2 Meas. |  | 
Date Leg | # | Loop | Wind Speed [m s-1] | Wind Direction [°] | BLH [m agl] | NO2 Flux [MT hr-1] | NOx Flux [MT hr-1] | NOx Flux [MT hr-1]
29-Jun L2 | F03 | 1+2 | 5.0 (1.5) | 146 (15) | 1558 (117) | 1.95 | 2.34 | 3.34
 |  | 2 | 5.1 (1.3) | 140 (13) | 1615 (78) | 2.25 | 2.70 | 3.86
02-Jul L2 | F05 | 1 | 5.7 (2.9) | 258 (75) | 1575 (439) | 1.75 | 2.10 | 3.0
 |  | 1+2 | 6.0 (2.3) | 279 (54) | 1766 (481) | 2.34 | 2.81 | 4.0
Average ± Std Dev |  |  |  |  |  | 2.1 ± 0.3 | 2.5 ± 0.3 | 3.6 ± 0.5
Flight Information |  |  | Doppler Lidar Meas. Mean (Std Dev) |  |  | DOAS NO2 Meas. |  |  | In situ NOy Meas.
Date Leg | # | Loop | Wind Speed [m s-1] | Wind Direction [°] | BLH [m agl] | NO2 Flux [MT hr-1] | NOx Flux [MT hr-1] | NOx Flux [MT hr-1] | NOx Flux [MT hr-1]
29-Jun L2 | F03 | 1+2 | 5.0 (1.5) | 146 (15) | 1558 (117) | 1.95 | 2.34 | 3.34 | 2.18 – 2.63
 |  | 2 | 5.1 (1.3) | 140 (13) | 1615 (78) | 2.25 | 2.70 | 3.86 | 2.98 – 3.57
02-Jul L2 | F05 | 1 | 5.7 (2.9) | 258 (75) | 1575 (439) | 1.75 | 2.10 | 3.0 | 2.22 – 3.12
 |  | 1+2 | 6.0 (2.3) | 279 (54) | 1766 (481) | 2.34 | 2.81 | 4.0 | 2.36 – 3.01
Average ± Std Dev |  |  |  |  |  | 2.1 ± 0.3 | 2.5 ± 0.3 | 3.6 ± 0.5 | 2.4 – 3.1 (± 0.4)
Flight Information |  |  | Doppler Lidar Meas. Mean (Std Dev) |  |  | DOAS NO2 Meas. |  |  | In situ NOy Meas. | GRA2PES
Date Leg | # | Loop | Wind Speed [m s-1] | Wind Direction [°] | BLH [m agl] | NO2 Flux [MT hr-1] | NOx Flux [MT hr-1] | NOx Flux [MT hr-1] | NOx Flux [MT hr-1] | NOx Flux [MT hr-1]
29-Jun L2 | F03 | 1+2 | 5.0 (1.5) | 146 (15) | 1558 (117) | 1.95 | 2.34 | 3.34 | 2.18 – 2.63 | 1.63
 |  | 2 | 5.1 (1.3) | 140 (13) | 1615 (78) | 2.25 | 2.70 | 3.86 | 2.98 – 3.57 | 
02-Jul L2 | F05 | 1 | 5.7 (2.9) | 258 (75) | 1575 (439) | 1.75 | 2.10 | 3.0 | 2.22 – 3.12 | 2.17
 |  | 1+2 | 6.0 (2.3) | 279 (54) | 1766 (481) | 2.34 | 2.81 | 4.0 | 2.36 – 3.01 | 
Average ± Std Dev |  |  |  |  |  | 2.1 ± 0.3 | 2.5 ± 0.3 | 3.6 ± 0.5 | 2.4 – 3.1 (± 0.4) | 1.9 ± 0.3
Loss to NOy1
Correction for bkgd NOy (0.2 – 0.8 ppb) in airflux
State of the art emission inventory
Our measurements of NOx emissions are 30-90% higher than in the inventory
Notes: Dix et al – using TROPOMI, NOx lifetime ~4.5 hr

## Slide 15: Ongoing work: evaluating TEMPO HCHO