## Slide 1
TEMPO cloud-sliced NO2 observations：
Implications for sources and chemistry of free tropospheric NOx
Ruijun Dang
Harvard University
Daniel J. Jacob, Yujin Oak, Laura Yang (ACMG, Harvard)
Helen Wang, Caroline R. Nowlan, Gonzalo Gonzalez Abad, Heesung Chong, Xiong Liu (Harvard-SAO)
Viral Shah (NASA GMAO), Drew W. Rollins (NOAA CSL), James H. Crawford (NASA Langley)
Eloise A. Marais, Rebekah P. Horner (UCL)
TEMPO/GeoXO ACX, August 22, 2025

## Slide 2
Free Troposphere
Boundary layer
~2 km
Tropopause
FT NOx is a major driver of global oxidant chemistry.
The importance of Free Tropospheric (FT) NOx
FT NO2 contributes a background column that must be accounted for when interpreting satellite data for surface NOx emissions.
Uncertainties remain in lightning source and organic nitrate reservoirs
But we lack observations!
North America
65% in summer
25% in winter
winter
summer
Shah et al. (2023)
Lightning, Aviation
Surface uplift
Nitrate
reservoirs

## Slide 3
50km
50km
300 hPa
Cloud pressure
700 hPa
450 hPa
Measured above-cloud NO2 VCD
TOA
Using cloud-slicing technique to derive FT NO2 for TEMPO
Above cloud NO2 VCD
Cloud pressure
TOA
Observing columns over adjacent fully cloudy scenes with different cloud pressures
Inferring NO2 concentration from the regression slope between NO2 VCD and cloud pressure
High observation density from TEMPO enables effective cloud slicing

## Slide 4
Consistency between the two products
correlation coefficient (r): 0.30-0.73
regression slope: 1.1-1.3
TEMPO - with denser sampling - provides
significantly more data samples (3x more)
a smoother background
a better coverage (e.g., western US; winter)
with only 1 year of data
Free tropospheric NO2 from TEMPO: comparison to TROPOMI
DJF
TEMPO (2023-2024, 1-year)
MAM
JJA
SON
FT NO2 (ppt)
TROPOMI (2018-2021, 4-year)
FT NO2 (ppt)
Dang et al., (in review)
Seasonal 700-300 hPa NO2 on 2° x 2.5° grid
seasonal: reversed pattern compared to the surface
spatial: weaker gradient than at surface

## Slide 5
Validation with vertical profiles from aircraft campaigns
Aircraft campaigns averaged on the 2° x 2.5° grid:
INTEX-B, ARCTAS, DC-3, SEAC4RS, DISCOVER-AQ, FRAPPE, WINTER, AEROMMA campaigns
PSS NO2 inferred from observations of NO, O3, J(NO2), HO2
Aircraft observations show:
higher values in spring and summer over the eastern US
TEMPO captures the observed variability
does better than TROPOMI
Conservative error estimation
14% accuracy and 50% precision in TEMPO product
TEMPO vs. aircraft
TROPOMI vs. aircraft
Dang et al., (in review)

## Slide 6
TEMPO enables the first diurnal observations of FT NO2
Flat in winter
A midday minimum in spring-fall
Diurnal variation of FT NO2 over North America
TEMPO diurnal FT NO2 (700-300 hPa)
TEMPO
Sampled GEOS-CF
DJF
MAM
JJA
SON
Local time
Local time
Dang et al., (in review)

## Slide 7
TEMPO + Geostationary Lightning Mapper (GLM)
reveal large errors in GEOS-CF lightning NOx emissions
Dang et al., (in review)
1. CTH-based flash rate parameterization needs improvement
land-ocean contrast and diurnal variation
2. NOx-yield per flash needs to be lowered
GEOS-CF
TEMPO
FT NO2
500 mol N flash-1
260 mol N flash-1
FT NO2

## Slide 8
DJF
TEMPO
MAM
JJA
SON
FT NO2 (ppt)
FT NO2 (ppt)
GEOS-Chem Yield_150
Dang et al., (in prep.)
Constraining lightning NOx emissions using TEMPO and GLM
For flash rates ⇢ prescribed hourly GLM
For NOx yield per flash ⇢ adjust yield to best match TEMPO FT NO2 observations
Constraining lightning emissions
TEMPO-model difference has been reduced to 0-2 ppt
Good agreement in diurnal cycle
A yield of 150 mol N flash-1 appears most reasonable for North America

## Slide 9
Emission (70%) + convection (10-20%) account for 80-90% of total FT NOx sources.
Aviation dominants in winter (up to 40%);
Lightning dominants in other seasons (up to 60% in summer).
Convection contribution is strongest in summer
For entire TEMPO FOV
Dang et al., (in prep.)
NOx family: NO + NO2 + NO3 + 2N2O5 + HONO + HNO4
Budget analysis – contributions of individual processes to FT NOx

## Slide 10
Winter FT NO2:
- NOx is flat;
- NO2/NOx is the main driver (changes in NO-NO2-O3 PSS throughout the day)
Summer FT NO2:
- Both NOx and NO2/NOx contribute
- Chemical loss together with lightning emissions drives a noontime NOx minimum
- NO2+OH → HNO3 is the major NOx chemical loss
Budget analysis – what drives the FT NO2 diurnal shape
Local time, hours
Local time, hours
DJF
JJA
FT NOx conc. (ppt)
NO2/NOx (mol/mol)
NOx tendencies
(105 kgN h-1)
(Transport + mixing)
For entire TEMPO FOV
Dang et al., (in prep.)
Notes: More active photochemistry in summer than in winter

## Slide 11
TEMPO product shows improved performance than TROPOMI.
TEMPO + GLM reveal large errors in modeled lightning NOx emissions.
We develop a new TEMPO cloud-sliced FT (700-300 hPa) NO2 product
with unique diurnal resolution.
Takeaways
We use improved GEOS-Chem to better understand sources and chemistry of FT NOx.
A NOx yield of 150 mol N flash-1 enables model to best match the TEMPO FT NO2 observations
Lightning is the leading FT NOx source in all seasons except winter.
The diurnal variation of FT NO2 is mainly driven by NO-NO2-O3 photochemical steady state, with additional contribution from midday NOx loss in summer (NO2+OH).
Contact: rjdang@g.harvard.edu