## Slide 1
Leveraging Observations of Remotely Sensed HCHO Column to Assess Surface Ozone
prajjwal.rawat@nasa.gov
1NASA Langley Research Center, Hampton, VA, USA
2Environmental Protection Agency, NC, USA
3NASA Goddard Space Flight Center, Greenbelt, MD, USA
4Harvard-Smithsonian Center for Astrophysics, Cambridge,
Massachusetts, USA
Prajjwal Rawat1, James H. Crawford1, Katherine R. Travis1, Laura M. Judd1, Mary Angelique G. Demetillo1, Tabitha C. Lee1, James J. Szykman2, Lukas C. Valin2, Barron Henderson2, Eric Baumann2, Thomas F. Hanisco3, Gonzalo Gonzalez Abad4

## Slide 2
Surface Ozone and Signature/Observations from Space
Anthropogenic, biogenic, fire, etc.
Nitrogen oxides, CO, VOCs
hn
Ozone (O3)
hn, H2O
HOx
Emissions
Non-linear photochemistry
Ground ozone monitors are sparse across many regions and potentially miss small-scale air quality events.
Satellite observations can help fill these gaps in unmonitored regions, but near-surface ozone retrieval remains challenging due to optical interference from clouds, aerosols, and stratospheric ozone.
The formation of peroxy radicals during the secondary production of HCHO makes it a helpful indicator for surface ozone.
[Schroeder et al., 2016]
Despite decades of declines in precursors, many U.S. cities still exceed the EPA 8-hour ozone NAAQS.

## Slide 3
Column HCHO can indicate surface ozone variability/tendencies
Observations of column (Ω) HCHO and surface ozone during different field campaigns show ΩHCHO as a valuable indicator of surface ozone variability.
Ozone (ppb)
Ozone (ppb)
[Schroeder et al., 2016]
[Travis et al., 2022]
DISCOVER-AQ campaign
KORUS-AQ campaign
LISTOS campaign
Long Island Sound
[Travis et al., 2022]
Olympic Park, S Korea
Maryland
GCAS airborne

## Slide 4
O3:HCHO Relationship with TEMPO as good as with Pandora in NY- NJ
Pandora DS
Pandora SS
TEMPO
DS
SS
TEMPO
Months
Months
Months
Months
Months
Months
Daily average surface ozone and ΩHCHO during Jun to Sep 2024 (10 – 18 LT)
R2=0.55
R2=0.45
R2=0.49
R2=0.39
R2=0.65
R2=0.49
Bayonne Pandora site
Manhattan Pandora site
TEMPO shows similar or stronger O₃–HCHO relationships across other NY ozone monitoring sites.
Cloud Screened quality flagged data

## Slide 5
DS
SS
TEMPO
Months
Months
Months
Pandora and TEMPO ΩHCHO relationship with surface ozone over Boston MA, New Haven CT, and Bristol PA
DS
SS
TEMPO
Months
Months
Months
R2=0.67
R2=0.61
R2=0.54
R2=0.38
BristolPA Pandora site
BostonMA Pandora site
R2=0.54
R2=0.67
Both Pandora and TEMPO capture the O₃–HCHO relationship well, though TEMPO shows slightly lower correlation.
The O₃–HCHO relationship can be used to assess the accuracy and reliability of Pandora DS and SS observations.
DS
SS
TEMPO
Months
Months
Months
R2=0.32
R2=0.43
R2=0.56
New HavenCT Pandora site

## Slide 6
DS
SS
TEMPO
DS
SS
TEMPO
Months
Months
Months
Months
Months
Months
Pandora Shows better O₃–HCHO Relationship than TEMPO in Atlanta
Overall, TEMPO shows difficulty in capturing the ozone–HCHO relationship; however, good correlations are seen in individual months, except June.
Atlanta GT Pandora site
Atlanta SD Pandora site
R2=0.58
R2=0.39
R2=0.23
R2=0.39
R2=0.30
R2=0.40
Cloud influence may explain the larger uncertainty, while V4 retrievals could yield improved relationships.

## Slide 7
TEMPO Underestimation at Higher Columns Likely Reduces Correlation
DS
SS
TEMPO
DS
SS
TEMPO
Months
Months
Months
Months
Months
Months
R2 =0.55
R2 =0.51
R2 =0.35
R2 =0.57
R2 =0.31
HoustonTX Pandora site
Houston-SanJacinto Pandora site
R2 =0.53
TEMPO underestimates (-20%) at higher columns, weakening the ozone–HCHO relationship at elevated ozone levels, whereas Pandora captures the full dynamic range.
Validation Results Presented in our Poster

## Slide 8
DS
SS
TEMPO
DS
SS
TEMPO
Months
Months
Months
R2=0.57
R2=0.57
R2=0.51
R2=0.47
R2=0.45
DS
SS
TEMPO
R2 =0.58
R2 =0.55
R2 =0.37
TurlockCA Pandora site
ChicagoIL Pandora site
KenoshaWI Pandora site
R2=0.60
Pandora and TEMPO HCHO capture surface ozone dynamics well.
Daily TEMPO ΩHCHO offers great potential for mapping ozone exceedance days.
Long-term HCHO averages can reveal photochemical hotspots: Useful for identifying potential high-ozone regions and guiding monitoring and air quality strategies within cities.
Pandora and TEMPO ΩHCHO relationship with surface ozone over Chicago-Kenosha and Turlock

## Slide 9
TEMPO Observations Highlight a Strong Spatial O₃–HCHO Link in New York
It shows how well the ozone monitoring network covers the possible ozone exceedance regions.
NO₂ reveals emission hotspots, while TEMPO HCHO captures ozone tendency well.
Over the NY region, ΩHCHO shows a good spatial link to ozone (r2 ≈ 0.5), and monitoring strategies capture photochemical hotspots well.
TEMPO HCHO distribution
Spatial relationship
0.7 DU
Jun to Sep
1✕1km2 map

## Slide 10
Houston Shows Robust O₃–HCHO Relationship, Yet Some High HCHO Areas Are Unmonitored
Spatial relationship
TEMPO HCHO distribution
Over the Houston region, ΩHCHO shows a good spatial link to ozone (r2 ≈ 0.63), However monitoring strategies missing some photochemical hotspots or potential high ozone regions.
Unmonitored region
Jun to Sep
1✕1km2 map
0.7 DU

## Slide 11
Strong O₃–HCHO Correlation Despite Small HCHO Variability in Atlanta
0.6 DU
TEMPO HCHO distribution
Spatial relationship
Over the Atlanta region, ΩHCHO shows a good spatial link to ozone (r2 ≈ 0.6), and monitoring strategies capture photochemical hotspots well.
Atlanta shows lower NO2 column and HCHO column are relatively uniform.
0.7 DU
Jun to Sep
1✕1km2 map

## Slide 12
Frequent Fire Events Disrupt O₃–HCHO Linkage in LA, While PM₂.₅ shows Good Correlation Spatially
PM2.5
Frequent fire events disrupt the relationship between ozone and ΩHCHO due to ozone titration, primary HCHO emissions, lesser photochemistry but PM2.5 correlates well.
Ozone
Monitoring strategies capture high ozone hotspots well.

## Slide 13
Summary
Pandora and TEMPO ΩHCHO observations show strong spatial and temporal relationships with surface ozone.
Daily TEMPO ΩHCHO offers great potential for mapping ozone exceedance days.
The spatial–temporal correlation will improve understanding of surface ozone distribution in air quality models.
The ozone–HCHO relationship further validates the scientific value of TEMPO ΩHCHO.
Findings have important implications for air quality monitoring and policy at local and regional scales.
Future work
TEMPO sub-column ozone retrievals will be evaluated against surface ozone observations, with a focus on their coherence with TEMPO ΩHCHO in active urban photochemical regions.
Thank You
prajjwal.rawat@nasa.gov

## Slide 14
Higher ozone over different regions is associated with higher ΩHCHO as seen by TEMPO.
Intensity of ΩHCHO increases along with ozone and shows the regions of active photochemical activity.
Many regions with high HCHO, indicating potential high ozone, remain unmonitored.
Mapping potential surface ozone exceedances using daily TEMPO ΩHCHO observations.
New York
Atlanta
Houston
CloudF<0.2

## Slide 16
Michigan Lake area, HCHO column and surface ozone during Jun – Sep 2024
O3 nonattainment areas
TEMPO HCHO distribution
Spatial relationship
Over the Michigan Lake region, ΩHCHO shows a moderate spatial link to ozone (r ≈ 0.38), and monitoring strategies capture photochemical hotspots well.

## Slide 18
Surface Ozone Signature/Observations from Space: utilization of Geostationary satellite
Ozone sensitivity NASA
AIRS/Aqua satellite
Efforts to observe near-surface ozone directly from space are hindered by the limited sensitivity of ozone satellite retrievals to the lower troposphere.
Lower stratosphere
InfraRed
Ozone sensitivity
TEMPO UV and UV-VIS

## Slide 19
05, 09 Aug GCAS
05, 09 Aug TEMPO

## Slide 20
TEMPO v3 HCHO column agrees well with Pandora
Oversampled Map of TEMPO
Direct sun
Pandora DS shows R2 about 0.63 to 0.84.
Histogram of difference between TEMPO and Pandora HCHO column.
TEMPO required precision
(1 × 1016)
Local time
Normalized Total Column HCHO
TEMPO and Pandora HCHO Columns Exhibit Similar Diurnal Patterns
At most PGN sites, TEMPO and Pandora HCHO show similar diurnal patterns.
Normalized Median
TEMPO PANDORA
Robust agreement between TEMPO and Pandora ΩHCHO highlights its value for investigating surface ozone dynamics and other air quality studies.