## Slide 1: Copernicus Sentinel-4
Ben Veihelmann, ESA Mission Scientist for Sentinel-4 and Sentinel-5
Thanks to
  S4 Teams at ESA, EUMETSAT, DLR,
  Consortium led by Airbus, EC, CAMS
  TEMPO-DART, 15 June 2026, SRON, Leiden, Netherlands

## Slide 2
Sentinel-4
Sentinel-5P
TEMPO
GEMS
Sentinel-5
Consistency Targets |  | 
O3 | Total column | 1%
 | Stratospheric | 5%
 | Tropospheric | 20%
NO2 | Total column | 1×1015 molec/cm2
 | Tropospheric | 1×1015 molec/cm2
SO2 |  | 1×1016 molec/cm2
HCHO |  | 1×1016 molec/cm2
CHOCHO |  | 4×1014 molec/cm2
AOD |  | 0.05 @ 440 nm
Earth radiance |  | 2-5%
Solar irradiance |  | 1-2%
Reflectance |  | 2-5%
AC-VC whitepaper on
GeoAQ Validation Needs
2000 + | 17 |  | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |  | 26 | 27 | 28 | … |  | 
S5P |  |  |  |  |  |  |  |  |  |  |  |  |  | … |  |  | 
GEMS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | … | 
TEMPO |  |  |  |  |  |  |  |  |  |  |  |  |  |  | … |  | 
S4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | … | FM2 | 
S5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | … | FM2 | FM3

## Slide 3: Copernicus Sentinel-4
For observing air quality over Europe with hourly revisit time
on a long-term operational basis
UV-Vis-NIR (UVN) Imaging Spectrometers on MTG-S series
Built under the responsibility of ESA
  Instruments and L1 Prototype Processor by a consortium led by Airbus
  L1 Reference Processor by Huld
  L2 Operational Processor by a consortium led by DLR
Operated by EUMETSAT
Hourly coverage of Europe enabled by geostationary orbit
Mission lifetime of >16.5 years: two S4 in sequence
Copernicus Atmosphere Monitoring Service (CAMS) is committed to exploit S4 data for operational information services

## Slide 4: Copernicus Sentinel-4
Sentinel-4
Proto Flight Model
Launch of MTG-S1 with a Falcon 9
1 Juli 2025
Sentinel-4 on MTG-S1 satellite

## Slide 5: Copernicus Sentinel-4
Proto Flight Model on MTG-S1
Launched with a Falcon 9 on 1 July 2025
Switched on 15 September
Nominal acquisitions since mid November
S4/UVN Commissioning Results Review January 2026
In-flight commissioning of L1 and L2
Ongoing tests: full disc, fast scans, PICS, planets
Re-location 3.6⁰W to final position 0⁰E
Next steps
Hand-over to EUMETSAT
Cal/Val start first batch September
Public release of data products in staggered approach
Flight Model 2
On-ground characterization & calibration completed April 2026
Outlook: tests at satellite level, long-term storage, re-calibration
UV-Vis
NIR
Earth Radiance 8 Oct 2025
Earth Radiance RGB
8 Oct 2025

## Slide 6: S4/UVN Instrument and Level-1 Products
S4 Proto Flight Model is behaving well in flight
L1 radiometric, spectral, geometric performances are overall very good
Ongoing work on remaining smaller features
warm
cold
... after solving an issue
radiometric degradation and evolving pseudo-noise
due to molecular contamination of detectors
fixed by operating the instrument with a higher detector temperature, February 2026

## Slide 7: S4 Level-2 Products
L2 processor developed by a consortium lead by DLR

## Slide 8: S4 Level-2 Products
Cloud Fraction
Cloud Height
Surface Reflectance

## Slide 9: S4 Level-2 Products
Total Ozone
Tropospheric Ozone
NO2
SO2

## Slide 10
Sentinel-4 on MTG-S1 and -S2
UV-Vis-NIR Imaging Spectrometer
Geostationary orbit  hourly Europe
Air quality
Sentinel-5 on MetOp-SG-A1, -A2, -A3
Morning
Sentinel-5 Precursor
TROPOMI
Early afternoon
Image: ESA
O3
NO2
SO2
Aerosol
HCHO
CHOCHO
CH4
CO
UV-Vis-NIR-SWIR Imaging Spectrometer
Polar orbit  daily global
Air quality, climate, ozone & UV
End of presentation
Thank you
Questions?