## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
TEMPO Total-Ozone and Ozone-Profile Algorithm: Current Status, Updates, and Evaluation
Junsung Park1, Xiong Liu1, Juseon Bak2, Heesung Chong1, Kelly Chance1, Weizhen Hou1, John Houck1, Gonzalo González Abad1, Caroline R. Nowlan1, Huiqun Wang1, Kai Yang3, Lawrence E. Flynn4, Dave P. Haffner5, David E. Flittner6, Matthew Johnson7, John Sullivan5, Laura Judd6, Mary Angelique G. Demetillo6, K. Emma Knowland8, Viral Shah5, Pamela Wales5, Arthur Mizzi7, Stacey M. Frith5, Jay Herman5, Jerry R. Ziemke5, Natalya Kramarova5, Michael J. Newchurch9, Robert Spurr10, Xiaoyi Zhao11, Can Li5, Kanghyun Baek5, and the TEMPO Team
1Center for Astrophysics | Harvard & Smithsonian (SAO), 2Busan National University, 3University of Maryland, 4NOAA/NESDIS,
5NASA Goddard Space Flight Center, 6NASA Langley Research Center, 7NASA Ames Research Center, 8NASA Headquarters, 9University of Alabama in Huntsville, 10RT Solutions Inc.,
and 11Environment and Climate Change Canada
TEMPO DART Team Meeting
June 15–18, 2026, in Iowa City, Iowa

## Slide 2: Summary of the V04 TEMPO O3TOT algorithm updates
TEMPO O3TOT (total column ozone) algorithm
  OMTO3 V8.5 (TOMS V8.5) based algorithm
  Uses two wavelength pairs: (317.62 and 331.34 nm) and (331.34 and 360.15 nm)
  Total O3, UVAI, and cloud fraction with spatial resolution of 2.0 km 4.75 km
Applied filtering: quality_flag < 4096, SZA < 80, VZA < 80, and CF < 0.5
Applied filtering: quality_flag = 0 and 1, SZA < 80, VZA < 80, and CF < 0.5
TEMPO O3TOT V03
TEMPO O3TOT V04
Publicly released on Sep 17, 2025
Publicly released on May 20, 2025
Update Quality_Flag
Improve latitudinal-dependent bias in total column ozone.
Update LUTs using the on-orbit slit function and the BDM ozone cross-section
In prep. Park et al. (TEMPO O3TOT)

## Slide 3: Summary of the V04 TEMPO O3TOT algorithm updates
-1%
3
Implemented BTDF update in TEMPO L1B + bump correction + 360nm adjustment
Bump correction
Updated
V03
BTDF correction update
bump correction
360nm adjustment
V03 exhibits significant latitudinal-dependent bias against OMPS NPP (+6% in low-latitude regions and - 2% in high-latitude regions).
V04 shows improved stability with a small bias (mostly within ±1%).
A slight positive bias (+2%) remains only in very low-latitude regions.
Applied filtering: quality_flag < 4096, SZA < 80, VZA < 80, and CF < 0.5
Applied filtering: quality_flag = 0 and 1, SZA < 80, VZA < 80, and CF < 0.5
In prep. Park et al. (TEMPO O3TOT)

## Slide 4: Evaluation of V04 TEMPO O3TOT: V04 TEMPO vs. OMPS NPP
4
Co-location: Temporal: 13:30 pm ± 30 minutes
TEMPO Data Filtering: Cloud Fraction < 0.5, SZA & VZA < 80°, Quality_Flag = 0
OMPS Data Filtering: Cloud Fraction < 0.5, SZA & VZA < 80°, AlgorithmFlags = 1
In prep. Park et al. (TEMPO O3TOT)
V04 TEMPO O3TOT vs. OMPS NPP
Available data between 2023 and 2026
The summer season data only came from 2023, 2024, and 2025.
The spring season data came from 2024, 2025, and 2026.

## Slide 5: Evaluation of V04 TEMPO O3TOT: V04 TEMPO vs. OMPS NPP
5
Co-location: Temporal: 13:30 pm ± 30 minutes
TEMPO Data Filtering: Cloud Fraction < 0.5, SZA & VZA < 80°, Quality_Flag = 0
OMPS Data Filtering: Cloud Fraction < 0.5, SZA & VZA < 80°, AlgorithmFlags = 1
In prep. Park et al. (TEMPO O3TOT)
V04 TEMPO O3TOT vs. OMPS NPP
Available data between 2023 and 2025
The winter season data only came from 2025 and 2026.
The autumn season data came from 2023, 2024, 2025, and 2026.

## Slide 6: Evaluation of V04 TEMPO O3TOT: V04 TEMPO O3TOT vs. Pandora
6
Co-location: Temporal: ±15 minutes, Spatial: Radius ≤ 5 km
TEMPO Data Filtering: Cloud Fraction: ≤ 0.5, SZA & VZA: ≤ 80°, Quality_Flag: 0
Pandora Data Filtering: Quality Flag: 0 & 10
V04 TEMPO O3TOT vs. Pandora
Available data between 2023 and 2026
In prep. Park et al. (TEMPO O3TOT)

## Slide 7
V05 Update Plan:
Low-bias due to the Instrument degradation and high geometry angles
Instrument degradation correction
Geometry angle dependence correction
V04 operational product
Improved version
V04 operational product

## Slide 8: Summary of the V04 TEMPO O3PROF algorithm updates
TEMPO O3PROP (ozone profile) algorithm
  Adopted from the Optimal Estimation (OE) method-based SAO OMI ozone profile algorithm (UV only)
    Proposed using UV (293-340 nm) and VIS (540-650 nm)
    The publicly released V04 TEMPO O3PROF algorithm is UV only (308-340 nm) algorithm
    The VIS channel, which can improve low-tropospheric ozone sensitivity, will be implemented in a future version.
  Retrieve Ozone profile at 24 layers
  A prior
    Combination of V2 GEOS-CF (ozone profile) and TB (tropopause-based) Climatology, TB climatology (error)
UV & VIS, @0.6 nm, 0.2nm/pixel Optimal estimation approach based
  Including total, stratospheric, tropospheric, and 0–2 km ozone
  Spatial resolution: 8.0 km 4.75 km, with 4-pixel coadding in the North-South direction, mostly due to the limitation in computational resources.

## Slide 9: Evaluation of V04 TEMPO O3PROF: V04 TEMPO vs. TOLNet
Using all available TEMPO and TOLNet observations from 2023 to 2026
Co-location
  Temporal: ±30 minutes
  Spatial: Radius ≤ 5 km
TEMPO Data Filtering
  Cloud Fraction: ≤ 0.5
  SZA & VZA: ≤ 80°
  Quality_Flag: 0
  1 ≤ exit_status ≤ 99
  avg_residual ≤ 0.3
  fit_RMS ≤ 3.0
In prep. Park et al. (TEMPO O3PROF)
Matthew’s Oral presentation “TEMPO Ozone Profile Validation in the Troposphere using TOLNet”: Today, 5:30 PM

## Slide 10: Evaluation of V04 TEMPO O3PROF: V04 TEMPO vs. TOLNet
Using all available TEMPO and TOLNet observations from 2023 to 2025
Co-location
  Temporal: ±30 minutes
  Spatial: Radius ≤ 5 km
TEMPO Data Filtering
  Cloud Fraction: ≤ 0.5
  SZA & VZA: ≤ 80°
  Quality_Flag: 0
  1 ≤ exit_status ≤ 99
  avg_residual ≤ 0.3
  fit_RMS ≤ 3.0
In prep. Park et al. (TEMPO O3PROF)
Matthew’s Oral presentation “TEMPO Ozone Profile Validation in the Troposphere using TOLNet”: Today, 5:30 PM

## Slide 11: Evaluation of V04 TEMPO O3PROF: V04 TEMPO vs. Ozonesonde
Using all available TEMPO and Ozonesonde observations from 2023 to 2026 at Boulder
In prep. Park et al. (TEMPO O3PROF)

## Slide 12: V04 TEMPO O3PROF: Evaluation profile using Ozonesonde
In prep. Park et al. (TEMPO O3PROF)

## Slide 13: V04 TEMPO O3PROF: Evaluation STO using MLS
Co-location:
SZA, VZA ≤ 80 CF ≤ 0.5
1 ≤ Exit_status ≤ 99
Avg_residual ≤ 0.3
Fit_rms ≤ 3.0 Temporal ±30 minutes
Spatial ≤ 50 km
TEMPO and MLS show strong agreement at three pressure levels (1, 100, and 200 hPa) for a specific date in each season.
Successfully captured latitudinal variations in ozone distribution from each season.
In prep. Park et al. (TEMPO O3PROF)

## Slide 14: V04 TEMPO O3PROF: Evaluation STO using MLS
Co-location:
SZA, VZA ≤ 80 CF ≤ 0.5
1 ≤ Exit_status ≤ 99
Avg_residual ≤ 0.3
Fit_rms ≤ 3.0 Temporal ±30 minutes
Spatial ≤ 50 km
Demonstrated high agreement between TEMPO and MLS profiles at the Stratosphere (10-260 hPa).
However, the TEMPO stratospheric has a systematic low bias (V04 known issue).
It could be caused by differences between the a priori profiles used in the soft calibration calculation and in the retrieval.
We plan to improve these in the next version (V05).
In prep. Park et al. (TEMPO O3PROF)

## Slide 15: Summary
TEMPO O3TOT product
  Total column ozone from V04 TEMPO O3TOT products shows a strong correlation with both ground-based and other satellite observations.
  The known issue of latitudinal-dependent bias has been mitigated in V04.
  Known issues: Instrument degradation and viewing/solar zenith angle-dependent bias
TEMPO O3PROF product
  Tropospheric and 0−2 km ozone from V04 TEMPO O3PROF show great agreement with ground-based TOLNet observations.
  Ozone profiles demonstrate good agreement with the ozonesonde observations.
  Known issues: Stratospheric column ozone shows a systematic low bias compared to MLS observations.

## Slide 16: TEMPO DART team meeting
Thank you for your attention!