## Slide 1: The NASA GEOS Composition Forecasting system (GEOS-CF)
Fei Liu, Viral Shah, Pam Wales, Carl Malings, Maryam Abdi-Oskouei, Joe Ardizzone, Nikolay Balashov, Jerome Barré, Sourish Basu, Michael Long, Rob Lucchesi, Retha Mecikalski, Sandra Roberts, Tommy Tobin, Kris Wargan, Brad Weir, Emma Knowland, Christoph Keller, Lesley Ott, Steven Pawson

## Slide 2: GEOS-CF is widely used for research and mission support
NASA’s Composition Forecasting system
Version 2 released last year and used in TEMPO V04
Global Coverage | 25km resolution worldwide
Real-Time Information | Daily NRT estimates + 5-day forecasts
Open Science | Collaborative development + public data & software
NASA Mission Support | TEMPO • TolNet • Field Campaigns
Research Applications | Atmospheric chemistry + air quality and health
Air Quality Monitoring | Supporting communities in the US and globally
Keller et al., 2021, JAMES; Knowland et al., 2022, JAMES, Malings et al., 2026, BAMS

## Slide 3: Engaged with a broad user community
User survey feedback
Strengths:
Global coverage, low latency, multi-pollutant forecasts
Multiple access options (direct file access, API, OPeNDAP, GEE)
Features most desired:
Finer spatial resolution, especially over US
Malings et al., 2026, BAMS

## Slide 4: GEOS-CF version 2 marks a major advance for the system
HTAP → CEDS
Updated fire emission factors & lightning NOx emissions
Assimilation of ozone column and profile data from OMPS/OMI and MLS/OMPS-LP
Model components
Emissions
Data assimilation
GEOS 10.23 & GEOS-Chem 14.0
CO2 and CH4 forecasts
Replay to GEOS-IT

## Slide 5: Updated emissions improve NO2 in GEOS-CF version 2
Results for 2023
TROPOMI NO2 (trop columns, annual mean)
GEOS-CF-2 – TROPOMI
GEOS-CF-1 – TROPOMI
Winter NOx lifetime in model too long, and high retrieval uncertainties
Updated BB emissions
TEMPO NO2 (V04) (trop columns, Aug-Sept)
GEOS-CF-2 – TEMPO
GEOS-CF-1 – TEMPO
Within NO2 retrieval uncertainties
Soil NOx emissions overestimated in the model
Improved anthro. emissions

## Slide 6: GEOS-CF-2 NO2, NOy profiles more consistent with aircraft observations over the US
NO2 profiles during AEROMMA: July-Aug ‘23
NOy profiles during MAGEQ: July ‘25
Figure courtesy of Nikolay Balashov
NO2 & NOy measurements from NOAA (CSL)
Obs
CF-1
CF-2
CF-1
CF-2

## Slide 7: Surface PM2.5 is much improved in GEOS-CF-2
Observations
GEOS-CF-2
µg m-3
µg m-3
CF-1
CF-2
Observations
CF-1
CF-2
Observations
Monthly cycle
Annual mean PM2.5
US
China
Results for 2023

## Slide 8: Ozone data assimilation improves tropospheric ozone in GEOS-CF-2
Ozonesonde observations are from the SHADOZ, WOUDC, and NOAA networks
Ozone (ppbv)
No DA
Tropospheric profiles
Obs
CF-2
CF-1
Results for 2023
Columns (sfc-300 hPa)
Mean bias: 0.9 DU
r: 0.98
Improvement in free tropospheric ozone; but mixing in the boundary layer may be too fast

## Slide 9: Surface ozone improves with updated NOx and VOC emissions, but some bias remains over US
Annual 95th percentile MDA8 ozone
Obs
CF-2
CF-1
Observations
GEOS-CF-2
Results for 2023

## Slide 10: Conclusions & outlook
GEOS-CF is a state-of-the-science, versatile tool for atmospheric chemistry research and applications
v2 of the system includes major updates and improvements; targeted research on ozone profiles in the PBL
v3 would include new model physics & chemistry, better vertical resolution, advanced data assimilation & modernized workflow
Launching soon: GEOS Composition Reanalysis (2009–18 in phase I)