## Slide 1: Updates and activities with Pandora and GCAS Thomas Hanisco, NASA GSFC
TEMPO DART
University of Iowa
15-June, 2026

## Slide 2: NASA GSFC Pandora Operations and Calibrations Team
Tom Hanisco, PI
Nader Abuhassan,
Operations Lead
Bryan Place
Calibrations &
Analysis
Apoorva Pandey
Calibrations & Analysis
Nicholas Lombel
Operations & Calibrations
Ksanet Zecharias
Operations & Calibrations
Jonguk Park
Calibrations & Analysis
Soojin Park
Calibrations & Analysis
Chris Rader
Operations & Maintenance

## Slide 3: Research programs
NASA IPMSI – 13 instruments at colleges and universities with minimal prior NASA funding
  Completed 12/13 installations.
  Ongoing research programs developed by the IPMSI institutions
    Focus on student training with instruments and classroom instruction on remote sensing
TEMPO DART (PI: Pandey)
  Use Pandora measurements to improve TEMPO Formaldehyde retrievals
NASA Satellite needs Working Group (SNWG)
  10 US department of Agriculture rural sites – 9/10 installed
  20 US State Department embassy locations – 5/20 installed
  16 Fire locations “Smoky Pandoras” beginning in 2027
Notes: Shobha Kondragunta at NOAA Bojan Bokov at Eumetsat

## Slide 4: IPMSI
Planned
Complete

## Slide 5: SNWG Agriculture
Planned
Complete

## Slide 6: SNWG Agriculture
Planned
Complete
Chaco, NM
Palo Duro, TX
Ames, IA
Luke Valin, EPA

## Slide 7: NASA Research & Analysis Program
Planned
Complete

## Slide 8: SNWG Embassies 2025-2026
Planned
Complete

## Slide 9: SNWG Embassies 2025-2026
Planned
Complete
Nairobi, Kenya
Skopje, Macedonia
Guatemala City
Kigali, Rwanda
Ashgabat, Turkmenistan

## Slide 10: PGN 2026
211+ active sites
70+ in TEMPO FOR

## Slide 11
Pandora HCHO profiles* and MAX-DOAS columns reproduce aircraft measurements across regimes and altitudes
*new version
Ongoing work: the effect of profile shape factor on the scatter and slope between HCHO columns from TEMPO and Pandora MAX DOAS (Jin Liao)
June 2025
June 2024
Formaldehyde Profiles – TEMPO DART (PI: Apoorva Pandey)

## Slide 12
Professor Yonjoo Choi, Gyeol Lee

## Slide 13: Ansung (winter)
Ansung (37.00 °N, 127.24 °E)
  2025-11-15 ~ 16 (three times in a day; AM. noon, PM)
  Variation in NO2 layer depending on PBL height
2026-11-15
2026-11-16

## Slide 14
Chuncheon (spring)
@춘천
2026-04-25/26
강원대학교 춘천캠퍼스
강원권
대기환경연구소
~ 1.9 km
2026-04-18/19
Chuncheon (37.87 °N, 127.75 °E)
  2026-04-18,19,25,26 (sunrise to sunset; 8 to 19 LST)
  Diurnal variation in NO2 and PBL height in urban scale

## Slide 15: NASA GCAS Team
Tom Hanisco, PI
Laura Judd
Retrievals and Flight Planning
Sam Xiong
Calibrations &
Operations
Apoorva Pandey
Calibrations & Analysis
Scott Janz (Ret)
Calibrations & Analysis &
Engineering
Jonguk Park
Calibrations & Analysis
Zane McBride
Operations and Engineering

## Slide 16
Nagoya raster
GCAS flights during the Tokyo-FC campaign
Spectral resolution | 0.6 nm | 
Spectral sampling | 0.2 nm | 
Nominal spatial resolution * at nadir, alt=41,000 ft ** Flight speed=420 NM/hr | x-track: | 320 m*
 | a-track: | 500 m**
NO2 fitting window | 430 – 460 nm | 
2-σ detection limit | 1.6e15 molecules cm-2 | 
People working on GCAS
(GSFC) Tom Hanisco, Jonguk Park, Apoorva Pandey, Scott Janz, Zane McBride, Sanxiong Xiong
(LaRC) Laura Judd
Total 11 Science Flights (40 hrs)
Tokyo: Mar 11, 14, 24, 29
Nagoya: Mar 8
Nagoya-Osaka: Mar 12, 17, 27
Hokkaido: Mar 20, 25
Survey (Kyushu): Mar 21
NASA LaRC G-Ⅲ
GCAS (NO2; GSFC), AVIRIS-5 (CH4, CO2; JPL)
Campaign period
Mar 8 – Mar 29, 2026 (flights)
Japan King Air
JAMSTEC NO2 Imager (NO2)
Mission objectives
Validation of recently launched GOSAT-GW data (GHG, NO2)
Nagoya-Osaka raster
Kyushu survey
Hokkaido
Tokyo raster
Pandora

## Slide 17
GCAS flights during the SARP2026 campaign
Spectral resolution | 0.6 nm | 
Spectral sampling | 0.2 nm | 
Nominal spatial resolution * at nadir, alt=33,000 ft | x-track: | 250 m*
 | a-track: | 250 m
NO2 fitting window | 430 – 460 nm | 
2-σ detection limit | 1.6e15 molecules cm-2 | 
Science Flight hours: 42 hrs (planned)
Dallas/Fort Worth: June 3
Atlanta: June 4
Permian basin: June 4, 7
Survey (Mississippi/Memphis): June 5
Survey (Houston): June 10
NASA LaRC G-Ⅲ
GCAS (NO2; GSFC), AWP (3-D wind profile; LaRC)
Campaign specifics
June 3 – June 14, 2026 / Houston, TX
Other aircrafts
JSC G-V (HSRL2), Dynamic B200 (AVIRIS-3), NOAA P-3 (in-situ; TexAQS)
GCAS Instrument
Wind profile curtain plot from AWP
Permian basin
June 7, am flight
June 7, pm flight
Atlanta
Pandora

## Slide 18: Future Projects
2026-2027 Apply SNWG/GMAO air quality forecasts to US embassy and US rural/agricultural sites
2026-2027 Support the NASA FarmFlux Earth Venture suborbital campaign to measure agricultural nitrogen fluxes
2028 HAMAQ Pandora and GCAS
2028-2029 SNWG install Pandoras at US Forestry service locations to sample forest fire plumes.

## Slide 19: Future Projects
New PanCam concept will provide MAX-DOAS profiles of the horizon
New GCAS with CMOS camera and improved HCHO