## Slide 1
Tianlang Zhao1, Jingqiu Mao1*, Xiaoyi Zhao2*, Martina M Friedrich3, Debora Griffin2, Ramina Alwarda4, Kimberly Strong4, William R Simpson1, Martin Tiefengraber5, Manuel Gebetsberger5, Alexander Cede5, Elena Spinei6, Apoorva Pandey6,7, Viral Shah6,8, Pamela A. Wales6,8 , K. Emma Knowland6,8,9, Thomas F Hanisco6
1 University of Alaska Fairbanks 2 Environment Canada, 3 BIRA-IASB, 4 University of Toronto, 5 LuftBlick, 6 NASA GSFC, 7 University of Maryland Baltimore County , 8 Morgan State University, 9 NASA Headquarter
This work is supported by UAF Troth Yeddha’ fellowship and NASA HAQAST grant
* Corresponding authors
Optimal-Estimation Pandonia Global Network (PGN) Formaldehyde (HCHO) Profile Retrievals across North America

## Slide 2: Quick introduction: what are Pandora and PGN?
Pandora is a ground-based sun/sky/moon viewing UV-Vis spectrometer system
Pandora has two operation mode: direct-sun and sky-scan (MAX-DOAS)
Direct-sun: derive total column (widely used for satellite validation)
Sky-scan: derive vertical profile
PGN: Pandonia Global Network, the global network of Pandora instrument
Notes: There are currently over 180 quasi-autonomous Pandora instruments deployed and operationally live as part of the Pandonia Global Network (PGN).

## Slide 3: Model has correlated biases in surface ozone and HCHO column
Slope = 2.8, intercept = 3.8
Slope = 2.6
These biases are likely related to chemical production, especially during heatwaves
(ppb O3,sfc / 1015 molec cm-2 HCHO)
(ppb O3)
(Submitted to ES&T)
(Travis et al, 2022)
Black dots: 17 SLAMS ozone monitor locations during LISTOS campaign
Notes: Positive bias in surface ozone in eastern US is a common issue in atmos chemistry models.
In GEOSCF , we find that HCHO trop column bias has a similar spatial distribution with surface ozone bias.
They are showing a correlation across the five regions of contiguous US, and both increase with temperature.
The regression slope of biases is very similar to the slope of O3 and HCHO during LISTOS campaign.

## Slide 4: Model shows a stronger PBL mixing than PGN
Surface T in 25-30°C
Northeast Coastal US, HCHO profile, July-August 2022, 12-15LT average
GEOS-CF
Surface T in 35-40°C
PGN sky-scan L2
GEOS-Chem
(PBLH x 1.25)
GEOS-Chem
(PBLH x 0.5)
PGN sky-scan L2
GEOS-CF
GEOS-Chem
(PBLH x 1.25)
GEOS-Chem
(PBLH x 0.5)
HCHO (ppb)
HCHO (ppb)
Altitude (km)
Surface T
PGN HCHO trop column
(~0-3km)
GEOS-CF HCHO trop column
PGN shows a different HCHO profile shape than GEOS-CF, including a stronger vertical gradient, and an aloft layer within PBL*
Excessive PBL mixing could potentially lead to overestimation in HCHO and O3
*Zhao et al,. 2025 GRL

## Slide 5: We present a new retrieval of PGN HCHO profiles using MMF* optimal estimation (OE) algorithm
PGN L1 data
HCHO, O4 dSCDs
QDOAS fitting
HCHO 324.5-359nm
O4 425-490nm
Elevation angle sequence: 1,2,3,4,5,6,7,8,9,10,15,20,30,90
Remove blocked elevation angles;
Apply HCHO and O4 fitting RMS filter (RMS < 1e-3)
Filtered HCHO, O4 dSCDs
PGN MMF HCHO profiles
MMF profiling
Quality-controlled PGN MMF HCHO profiles, aerosol extinction profiles,
averaging kernel, DOF…
QA flag
HCHO concentration (molec cm-3)
A priori profile
(constant, exponential decay, scale height=1km)
*MMF: Mexican MAX-DOAS Fit (Friedrich et al., 2019)

## Slide 6
HCHO tropospheric column (HCHOtrop) from PGN MMF retrieval, across the contiguous US
PGN MMF HCHO profile retrieval is performed at 76 sites, during 2023-2025 summers
MMF HCHOtrop show a similar spatial pattern as previous satellite retrieval reported
(Zhu et al 2017, ES&T)

## Slide 7: MMF HCHOtrop vs TEMPO and PGN L2 data
TEMPO HCHO trop column
(1016 molecules cm-2)
MMF HCHO
trop column
(molec cm-2)
PGN direct-sun
total column
(1016 molecules cm-2)
PGN sky-scan
trop column
(1016 molecules cm-2)
MMF HCHOtrop agrees well with PGN sky-scan L2 trop column;
MMF HCHOtrop shows a negative bias relative to PGN direct-sun and TEMPO HCHO columns, likely because the profile retrieval has a limited sensitivity to HCHO above ~3 km.

## Slide 8: MMF median HCHO profile in five regions of US, during 2023-2025 summers
MMF HCHO profiles indicate that HCHO may be not well-mixed in PBL, especially during heatwaves.
During heatwaves, MMF show a more clear HCHO aloft layer than PGN L2 data. They are similar in other cases.
Local time (hour)
PGN sky-scan L2 at Southeast US
Altitude (km)
Heatwaves
Non-heatwaves
Western US
Southern US
Southeast US
Northeast Coastal
Great Lakes
Heatwaves
Non-heatwaves
Local time (hour)
MMF HCHO
Local noon (12-15 LT)
MMF
PGN L2
Notes: Add PBLH from GEOSCF and ERA5 and Ceilometer
Potentially more Ceilometers

## Slide 9
AEROMMA HCHO profiles also show a non-well-mixed PBL under high surface temperature,
Elevated HCHO aloft during heatwaves: real signal or artifact?
CO mixing ratio (ppb)
HCHO mixing ratio (ppb)
NYC
Los Angeles
But AEROMMA-PGN collocated observations are likely influenced by fire smokes, so we need more evidences
AEROMMA aircraft campaign,2023

## Slide 10
Azimuth Viewing Angle
1.3 miles
A case study at Toronto St George site,
during 2024-2025 summers
Pandora 243
Toronto-CNTower
Pandora 170
StGeorge
Local hour
Altitude (km)
There are two Pandoras, nearly collocated horizontally, but has ~150m vertical gap.
The difference in direct-sun total column, and MMF profiling, can be independent constraint on HCHO abundance within the layer.
Also, there is a mini Micro Pulse LiDAR (MPL) at the StGeorge site, run by Dr. Debra Wunch.
miniMPL
CNTower
StGeorge
Notes: We use a case study to validate the aloft layer in the afternoon. There are two Pandora at downtown Toronto, the StGeorge P170, CNTower P243, they are horizontally collocated, but has a vertical gap of 150m. Also there is a mini micro Pulse lidar at the StGeorge site to provide boundary layer height measurements. Direct-sun, sky-scan , miniMPL there are three independent measurements.

## Slide 11
Local hour
StG - CNTower
PGN direct-sun
HCHO total column difference
HCHO total column
And
MMF trop column
(StGeorge)
MMF HCHO
Vertical profile
(StGeorge)
Heatwaves
Non-Heatwaves
Pandora direct-sun HCHO VCD at StGeorge P170 is increasing from 12 to 16 LT.
This is consistent with the MMF HCHO trop column diurnal cycle.
Difference of Pandora direct-sun HCHO VCD at StGeorge P170 and CNTower P243 is decreasing from 12 to 16 LT.
This is consistent with the MMF HCHO profile diurnal cycle near the surface.

## Slide 12
8 selected days at StGeorge P170 in 2025 summer
MMF
GEOSCF
HCHO VCD
PGN direct-sun
MMF
HCHO VCD
difference
miniMPL
miniMPL PBLH is consistent with the upper bound of HCHO aloft layers from MMF, providing independent evidence of the accuracy of MMF retrieval
When there is aloft layer in the afternoon, HCHO column increases, but surface HCHO reduces.

## Slide 13: Takeaways
We successfully retrieved HCHO profiles at 76 PGN sites across North America using MMF OE profiling algorithm, which are consistent with satellite and PGN level-2 column products.
MMF HCHO profiles show elevated HCHO aloft during heatwaves, which GEOS-Chem and GEOS-CF does not capture.
A case study using dual Pandora with an altitude gap, and collocated miniMPL provides independent evidence that support the existence of aloft layers. However, more measurements are needed to verify the MMF profiles.
Thank you for your attention!

## Slide 15
AEROMMA vs MMF aerosol extinction coefficient profile (477nm)
The Pandora instruments are selected because they are located within 50km distance from AEROMMA profiles. Only profiles with DOFS>1.5 are selected. Then the profiles are grouped by cities.
QA flag and DOFS are listed on each panel.
At Toronto, the MMF and AEROMMA have the best agreement in aerosol profiles.