## Slide 1: Advancing TEMPO NO2 Utilization: 4DEnVar Data Assimilation, Emission Inversion, and Near Real-Time Forecast Monitoring with GEOS-CF/JEDI
Maryam Abdi-Oskouei, Jérôme Barré, Viral Shah, Pam Wales, Fei Liu, Michael Anstett, Doruk Ardag, Furkan Goktas, Ricardo Todling, Emma Knowland, Steven Pawson
TEMPO DART Team Meeting, Iowa City, IA
June 16, 2026

## Slide 2: JEDI-based 4DEnvar system for TEMPO NO2 assimilation
Abdi-Oskouei et al. (2026), 10.1029/2025MS005482
TEMPO
JEDI (Joint Effort for Data assimilation Integration) is a generic and modular data assimilation framework that supports various DA methodology such as 4D methodology for atmospheric composition

## Slide 3: JEDI-based 4DEnvar system for TEMPO NO2 assimilation
Abdi-Oskouei et al. (2026), 10.1029/2025MS005482
TEMPO
JEDI (Joint Effort for Data assimilation Integration) is a generic and modular data assimilation framework that supports various DA methodology such as 4D methodology for atmospheric composition
Experiment design:
GEOS-CF interfaced with JEDI
EDA 4DEnVar with 32 members for Aug 2023.
  Deterministic C360 (0.25o) resolution
  Ensemble C90 (1o) resolution
Assimilation observations:
  TEMPO tropospheric NO2 (SZA < 70o, CF < 0.15)
  TROPOMI tropospheric NO2 (qa > 0.75, -65o < lat < 65o)
Independent observations:
  Pandora total column NO2
  AirNow surface NO2 and O3
  AEROMMA and STAQS field campaigns
Hourly NO2 increment at surface
Notes: CEDS emissions, replay of meteorology to FP

## Slide 4: Obs-space: fit to TEMPO obs
Abdi-Oskouei et al. (2026), 10.1029/2025MS005482
OmA < OmB shows DA functioning correctly
Strongest fit improvement in early morning
4DEnVar propagates obs influence across full 6-hr window

## Slide 5: Validation against independent observation
Rural and Suburban: improved total column NO2 in morning. Urban: mixed
Indirect ozone improvement

## Slide 6: Emission perturbations and adjustment
Gamma random Perturbation generator per sector
https://github.com/jeromebarre/perturbator
HEMCO perturbation scaling factors
on emissions
GEOS-CF concentration to emission
Jacobians/sensitivities - increments
JEDI DA perturbation scaling factors adjustment
+
temporal harmonization smoothing

## Slide 7: Concentration vs emission constraints
[Surface, 800hPa] NOx partial column: August 4, 2023
Concentration analyses vs control (noDA)
Replay of emission analyses vs control (noDA)

## Slide 8: End-to-end GEOS-CF monitoring system using TEMPO NO2 observation powered by JEDI and SWELL workflow
GEOS-CF v3 data assimilation component will be JEDI-based
The end-to-end monitoring system provides an opportunity to test JEDI and SWELL workflow in NRT before the release of GEOS-CF v3
Continuous comparison between GEOS-CF and TEMPO can provide information about the performance of the system

## Slide 9: Summary
We assimilated TEMPO NO₂ using a 4DEnVar approach with EDA methodology in a JEDI/GEOS-CF system.
Results show a better fit to the observations, with strong increments during the morning.
Constraining NO₂ concentrations in the system improved the representation of surface O₃.
We are currently working to expand the system to constrain anthropogenic NOₓ emissions.
We are also setting up an end-to-end GEOS-CF monitoring system using TEMPO NO₂ observations with JEDI and the SWELL workflow in preparation for GEOS-CF v3.

## Slide 10: backup

## Slide 11: Emission increments