## Slide 1
High-resolution Column NO2 from GCAS:
Implications and Synergy with Pandora and Satellite Observations
Jonguk Park, Tom Hanisco, Apoorva Pandey, Bryan Place
and GCAS team
TEMPO DART Team Meeting
June 17, 2026

## Slide 2
Weight (dimensions) | 80 lbs, 19”×19”×18”
Spectral resolution | 0.6 nm
Spectral sampling | 0.2 nm
Spectral range | 300 – 490nm
FOV (iFOV) | 45° (0.8 mrad)
Native detector (spectral × spatial) | 1072 × 1024
SNR | 600 (340 nm) 900 (440 nm)
GEO-CAPE Airborne Simulator (GCAS)
specification (AQ)
Nominal spatial resolution * at nadir, alt=33,000 ft ** Typical, with sampling cadence ≈ 2.3 s | x-track: | 250 m*
 | a-track: | 250 m**
NO2 fitting window | 430 – 460 nm | 
2-σ detection limit | 1.6e15 molec cm-2 | 
Airborne GCAS observations during the STAQS campaign
OC
AQ
STAQS
(Synergetic TEMPO Air Quality Science)
GCAS flew over major U.S. cities
17 flight days × maximum 3 rasters/day
Chicago (5 days), Toronto (1), NYC (4), California (7)
JSC G-V: ~ Aug 15 (13 flights) / with HSRL-2
LaRC G-Ⅲ: Aug 22~ (4 flights) / with HALO
Campaign period
June – August 2023 (GCAS flights)
Mission objectives
Integrate TEMPO satellite observations with traditional air quality monitoring to improve understanding of air quality science and increase social benefit

## Slide 3
TROPOMI
TEMPO
GCAS
20230823 California
Airborne GCAS observations during the STAQS campaign
20230802 Chicago
Notes: Virtue of high-resolution observations

## Slide 4
Ray-tracing
Calculating synthetic GCAS data along the line of sight (LOS) of Pandora measurements
Conventional co-location
(single pixel, spatial window)
Methods to co-locate GCAS and Pandora for intercomparison
It is more intuitive (physical) to compare ground-based Pandora observations with raytraced synthetic GCAS data
 |  | Method (how)
Conventional | Pixel | GCAS (satellite) pixel containing the ground-based instrument location
 | Spatial average | 3×3 mean (mean of the 9 nearest pixels)
Ray-tracing | Accumulated SCD along the LOS “n(z)-stacked VCD” | Create 3-D number-density field based on model profiles scaled to match GCAS VCD. Integrate n·ds along the solar LOS (zenith=SZA, az=SAA) from ground to the aircraft altitude; report SCD and SCD·cosSZA as a below-aircraft VCD-equivalent.
 | n(z)-weighted LOS pixel-VCD “n(z)-weighted VCD” | Walk the LOS, weight each probed pixel's retrieved VCD by the local model number density n(z); report the weighted mean. DS uses SAA/SZA; sky uses VAA / VZA=75°. Sky also reports the unweighted simple mean.
Notes: Used number densities of target species along the line of sight (LOS) based on a priori model profiles used in GCAS retrievals

## Slide 5
Ray-tracing slightly improves TEMPO–Pandora intercomparison score, but not significantly
GCAS has significantly higher spatial resolution than TEMPO (×~10)
  Raytracing can significantly reduce artifacts in GCAS–Pandora intercomparison by matching the air-mass they are measuring as close as possible to each other
Ray-tracing vs conventional: TEMPO–Pandora intercomparison
Greenbelt (MD), year 2024
During STAQS & in STAQS domain
Pandora NO2 VCD [DU]
TEMPO NO2 VCD [DU]
Pixel
3×3
n(z)-stacked
n(z)-weighted
* TEMPO NO2 VCDs in this figure are V3
* TEMPO NO2 VCDs in this figure are V4

## Slide 6
Temporal co-location window:
GCAS overpass ± 5 min
Ray-tracing vs conventional: GCAS–Pandora intercomparison
1 pixel
spatial average (9 pix)
n(z)-stacked
n(z)-weighted
LOS-tracing
Conventional

## Slide 7
GCAS compared with TEMPO and TROPOMI (NO2 VCDTrop)
The temporal disparity may contribute to the spatially random differences between satellite (TEMPO, TROPOMI) and GCAS NO2
Satellite–GCAS are temporally co-located by: Satellite overpass ± 30 min
August 25, 2023
GCAS
TEMPO
TROPOMI
ΔNO2 (TEMPO-GCAS)
ΔNO2 (TROPOMI-GCAS)
Notes: Now we know that GCAS observations conforms with Pandora direct-sun measurements, which can be an indicative of its high accuracy.
It is hard to narrow down temporal co-location window for satellite-GCAS comparison. (Maybe higher temporal res TEMPO measurements during the GCAS flights?)

## Slide 8
Aug 2, Chicago
NO2 VCD (GEOS-CF)
NO2 VCD (WRF-Chem)
AMF (GEOS-CF)
AMF (WRF-Chem)
GEOS-CF: 0.25° (~ 25 km)
WRF-Chem*: 4 km
ΔNO2 VCD (WRF–GEOS)
GCAS NO2 VCD retrieval sensitivity on input model (GEOS-CF, WRF-Chem)
Higher-resolution model a priori yields spatially more continuous (physically reasonable) GCAS NO2 VCD field
*Special Thanks to:
Brad Pierce (UW-Madison)
Jerrold Acdan (NCAR, previously at UW-Madison)

## Slide 9
GCAS NO2 VCDs retrieved with GEOS-CF and WRF-Chem agreed well (R > 0.98, MAE < 0.015 DU), but with greater deviation at higher NO2
GCAS NO2 VCD retrieval sensitivity on input model (GEOS-CF, WRF-Chem)

## Slide 10
Higher-resolution model a priori does not necessarily guarantee better accuracy
Regardless of the input model resolution, GCAS accurately captures most of the spatial information (e.g., spatial inhomogeneity)
Temporal co-location window: GCAS overpass ± 5 min
GCAS NO2 VCD retrieval sensitivity on input model (GEOS-CF, WRF-Chem)
GCAS (GEOS-CF)
GCAS NO2 VCD (by method) [DU]
Pandora NO2 VCD [DU]
Pixel
3×3 pixels
LOS: n(z)-stacked
LOS: n(z)-weighted
Pixel
3×3
n(z)-stacked
n(z)-weighted
GCAS (WRF-Chem)
GCAS NO2 VCD (by method) [DU]
Pandora NO2 VCD [DU]
Pixel
3×3 pixels
LOS: n(z)-stacked
LOS: n(z)-weighted
Pixel
3×3
n(z)-stacked
n(z)-weighted

## Slide 11
Tokyo-FC campaign
Total 11 Science Flights (40 hrs)
Tokyo: Mar 11, 14, 24, 29
Nagoya: Mar 8
Nagoya-Osaka: Mar 12, 17, 27
Hokkaido: Mar 20, 25
Survey (Kyushu): Mar 21
Campaign period
Mar 8 – Mar 29, 2026 (flights)
Mission objectives
Validation of recently launched GOSAT-GW data (GHG, NO2)
GCAS data (dSCD) are preliminary
Pandora
Nagoya, March 12
Tokyo, March 24

## Slide 12
Tokyo-FC campaign – wildfire plume!
March 24
Wildfire occurred around the time we approached Tokyo area
wind
March 14
Plume advected S–SW
Advantages of GEO!

## Slide 13
GCAS is actively enrolled in recent field campaigns and will continue to make high-res NO2 column measurements in upcoming ones!
GCAS team is seeking a way to improve HCHO column measurements
 coincident high-res NO2 and HCHO observations
Summary and Remarks
Ray-tracing (consideration of Pandora viewing LOS) effectively reduces the artifact when comparing high resolution GCAS data against ground-based Pandora observations.
The highly variable nature of NO2 can introduce (random) biases when a larger temporal co-location window is employed for GCAS – TEMPO (satellite) intercomparisons, which warrants further investigation.
Higher-resolution model a priori yields spatially more continuous (physically reasonable) GCAS NO2 VCD field but does not necessarily guarantee better accuracy.
GCAS accurately captures most of the spatial information (e.g., spatial inhomogeneity) in general, even with the coarse model input (e.g., GEOS-CF)
 High-res observations (e.g., GCAS) have standalone significance!
+ and more!