## Slide 1: Closing the spatial gap in ozone monitoring with TEMPO and machine learning
Dan Anderson, Doyeon Ahn, Bryan Duncan
TEMPO DART Meeting, Iowa City, IA
17 June 2026

## Slide 2: Limitations of the current surface ozone monitoring system
EPA O3 Monitors
O3 monitors provide highly accurate observations but are sparsely distributed.
Air quality models often have significant biases
Evaluation of the NASA GEOS-CF model with surface observations
Satellites don’t provide surface concentrations
TEMPO total column O3 (15Z May 1, 2024)
Keller et al, 2021, Description of NASA GEOS CF, JAMES
Tools are needed to constrain O3 elsewhere.

## Slide 3: TEMPO and ML can fill in the gaps
Recent advances in machine learning (ML) and the launch of TEMPO present an opportunity to improve our ability to constrain diurnal O3 outside monitoring sites.
Project goal:
  Satellite-constrained, near real time surface O3 at derived from machine learning, satellite data, and in situ observations.
  Ideal is to provide product at hourly resolution across the TEMPO domain.
Work closely with air quality managers/stakeholders to make product as useful as possible.
Results shown today are preliminary and will likely change.

## Slide 4: Machine learning framework
Training Targets (Surface O3)
Trop. Column NO2 & HCHO
Total Column O3
Viewing Geometry
Reflectivity
T, P, Humidity
Wind speed
TEMPO
HRRR Meteorology
Wind direction
PBL Height
Other
Population
Month, Hour
Road Density
EPA Ozone Monitoring (824 Sites)
Test model performance at 114 independent EPA O3 sites
Day of Week
NDVI
Latitude
Gradient Boosted Regression Tree Model Training
ML Model Inputs
TEMPO data are V3, Level 2 and have been cloud filtered.
Trained on data from May – Aug. 2024.
O3 product is hourly at the TEMPO pixel resolution.

## Slide 5: TEMPO-derived surface O3 reproduces variability of surface monitors
Satellite data can constrain surface O3 variability over many regions of the continental US (median r2 = 0.70).
Correlation between EPA and TEMPO-Derived O3
Results are preliminary and may change.
Bias between EPA and TEMPO-Derived O3
TEMPO O3 at individual sites is generally within 5 ppb of EPA.

## Slide 6: TEMPO-derived captures diurnal variability but often misses peak O3
O3 variability at UW – Milwaukee EPA site
Results are preliminary and may change.
Shading indicates nighttime (8pm – 7am), and numbers indicate number of TEMPO-Derived observations per day.
O3 variability at DC Takoma Rec Center EPA site
TEMPO-derived product captures high O3 (O3 > 60 ppb) 70% of the time.

## Slide 7: Performance declines at some sites near land/water interface
O3 variability at UW – Milwaukee EPA site
Results are preliminary and may change.
Shading indicates nighttime (8pm – 7am), and numbers indicate number of TEMPO-Derived observations per day.
O3 variability at Edgewood EPA site
TEMPO-derived product captures high O3 (O3 > 60 ppb) 23% of the time.

## Slide 8: Consistent low bias at high O3 across sites
Results are preliminary and may change.
Near term focus is improving ML model performance for these high O3 cases.
Bias in ML O3 when EPA monitor > 60 ppb
Bias in ML O3 when ML O3 > 60 ppb

## Slide 9: Capturing O3 exceedances in metro Atlanta
TEMPO-derived O3 qualitatively captures the regional nature of air quality episodes.
TEMPO-Derived (background) and EPA monitor (circles) O3 in northern Georgia on June 14, 2024, a day with several exceedances.
10:00 AM
2:00 PM
Metro
Atlanta
Results are preliminary and may change.
12:00 PM

## Slide 10: Capturing O3 exceedances in metro Atlanta
TEMPO-derived O3 qualitatively captures the regional nature of air quality episodes.
10:00 AM
12:00 PM
2:00 PM
TEMPO-Derived (background) and EPA monitor (circles) O3 in northern Georgia on June 14, 2024, a day with several exceedances.
Results are preliminary and may change.

## Slide 11: Evaluating regional performance
Results are preliminary and may change.
10:00 AM
1:00 PM
TEMPO-Constrained O3
NOAA AQ Forecast Model
Difference (TEMPO – NOAA)
EPA monitor (triangles). June 14, 2024. TEMPO data have been gridded to NOAA grid.
Goal is to have TEMPO-constrained product to perform better than AQ forecasts.

## Slide 12: Evaluating regional performance
Results are preliminary and may change.
TEMPO-constrained product performs better for O3 < 60 ppb, suggesting potential utility of product.
TEMPO-Constrained O3
EPA O3
EPA O3
Data from metro Atlanta for June 1 – 14, 2024.
NOAA AQ Model O3

## Slide 13: Conclusions and future work
Results are preliminary and may change.
Strong performance at many sites for O3 < 60 ppb
Qualitatively captures regional O3 issues
Many potential air quality applications for AQ management: informing O3 events in NRT, siting future monitors, understanding exceptional events, etc.
Future:
  Improving performance at high O3
  Understanding reasons behind poor performance at some sites.
  Case studies: wildfires, stratospheric intrusions
  Short-term O3 forecast
  Evaluation of TEMPO 0 – 2 km product
Contact: daniel.c.anderson@nasa.gov

## Slide 14: Current model relatively insensitive to TEMPO NO2 and HCHO
Results are preliminary and may change.
Goal is to develop methods to increase model sensitivity to chemical inputs (e.g., spatial averaging, shape factors to estimate surface values).
Absolute difference in TEMPO-derived O3 when indicated ML input was perturbed by 10% for 6/14/24 in metro Atlanta.
Total Column O3
Trop. Column NO2
Trop. Column HCHO