## Slide 1
Modeling of Radiative Transfer Illuminated by Moon: Uncertainty Analysis and Applications
Jun Wang
Lichtenberger Family Chair Professor
College of Engineering
TEMPO DART Meeting
June 17, 2026
Notes: Thanks to the meeting organizers for giving me an opportunity to talk about our most recent work to detect nighttime global fire phase from space.

## Slide 2: Measurements of Moonlight
It is deemed that moonlight is a stable source of illumination; that is why many remote sensing instruments use moonlight to do calibration. Is it true?
Beers-law technique in clean & stable atmosphere
Satellite measurement and aircraft measurements
Full Moon of 2020 April 08
Cave Creek Observatory, AZ
Fred Espenak
The Arcstone observatory
350 nm to 2300 nm
Kouyama et al., 2016
ASTER April 14, 2003
Launched in June 23, 2025

## Slide 3: Moonlight Polarization
The DOLP of moonlight is nearly zero at full moon(regardless of wavelength) and can be 5–20% for wavelengths in the UV (0.3 4μm) to the green part of the visible spectrum (0.51 μm) when the moon phase angle is 100°–120°; the longer the wavelength and the smaller the phase angle, the smaller is the DOLP.
Higher DoLP for waning
phases (max 8.3%) than for waxing (max 6.8%),
Venkatesulu and Shaw, 2024.
Pellicori 1971

## Slide 4: Shortwave radiative transfer model in conditions illuminated by moonlight, fire light and city light
Wang, J., M. Zhou*, X. Xu, S. Roudini*, S. Sander, T. Pongetti, S. Miller, J. Reid, E. Hyer, R. Spurr, Development of a nighttime shortwave radiative transfer model for remote sensing of nocturnal aerosols and fires from VIIRS, Remote Sensing of Environment, 241, 111727, 2020.

## Slide 5: Moonlight illumination model
Spectrally-resolved moon-phase dependent lunar irradiance model:
Solar spectral irradiance database
geometric lunar spectral albedo (averaged over the whole disk) as a function of phase angle; in full conditions, 0.116 integrated over 0.4 and 0.7 μm
Other factors (variation of distance from the Sun, opposition surge effect, etc).
Existing models:
1) ROLO model
2) RIMO (ROLO Implementation for Moon's Observation) Correction Factor (RCF)
3) Steve & Miller model (S&M): data base that includes calculations of moon phase angle for any given time and location
To our knowledge, none of these models has been integrated with a vector RTM, with consideration of polarization.

## Slide 6: UNL-VRTM: new development for lunar illumination
Wang et al., 2014; 2020.
Xu & Wang, 2019.
Unified Linearized Vector Radiative Transfer Model: aiming to a testbed for remote sensing of atmosphere, land, and ocean.
May (Zhixin) Xue
U. Iowa
Meng Zho
U. Iowa

## Slide 7: Development of moonlight radiative transfer model validation: comparison with surface moonlight measured at night at red bands
JPL’s Facility in Table Mountain, California
Wang et al., RSE, 2020.

## Slide 8: Overall uncertainty
MPA = 0
MPA = 20
5 solar irradiance database + 3 lunar spectral albedo = 15 ensemble members
The overall uncertainty is 7% except in the full-moon conditions, it can be up to 17% for wavelength from UV to 1000 nm.
Large relative uncertainties in UV and blue wavelength, and wavelength longer more than 1000 nm

## Slide 9: Application to Nighttime Aerosol Retreivals Nighttime Ocean AOD Retrieval Algorithm (NOARA)
Wang, J., M. Zhou, X. Xu, S. Roudini, S. Sander, T. Pongetti, S. Miller, J. Reid, E. Hyer, R. Spurr, Development of a nighttime shortwave radiative transfer model for remote sensing of nocturnal aerosols and fires from VIIRS, Remote Sensing of Environment, 241, 111727, 2020.
Zhou, M., J. Wang, X. Chen, X. Xu, P. R. Colarco, S. D. Miller, J. S. Reid, S. Kondraguntah, D. M. Gilese, and B. Holben, Nighttime smoke aerosol optical depth over U.S. rural areas, first retrieval from VIIRS moonlight observations, Remote Sensing of Environment, 112717, 2021.
Zhou, M., J. Wang, X. Chen, Y. Wang, P. Colarco, R. Levy, and S. Miller, First lunar-light mapping of nighttime oceanic aerosol optical depth from space, in review.
Meng Zhou
U. Iowa

## Slide 10: First mapping of nighttime visible AOD climatology over the ocean
DNB AOD from VIIRS
IASI IR AOD at 10 um
Vandenbussche et al., 2013
JJA 2021
VIIRS Dart-target Deep Blue
Sampling rate: 6-10 days/month; 1 km res.
Night
Day
12 × 12 km @ nadir
39 × 20 km @ edge
Visible AOD

## Slide 11: Food of thoughts for TEMPO
UNL-VRTM low-light component can be used
  together with TEMPO night measurements for quantitative remote sensing of fires and aerosols from
  together with TEMPO night measurement for nighttime NO2 and other gas retrievals.
  to help AEROENT and PANODRA nighttime retrievals.
  to help bring calibration with lunar measurements into the uncertainty analysis of Level-2 data product.

## Slide 12
Thank you !

## Slide 13: Solar spectral irradiance uncertainty
Smithsonian Astrophysical Observatory (SAO) solar irradiance spectrum – resolution of 0.01nm
Kurucz solar irradiance spectrum – resolution up to 0.004nm
American Society for Testing and Materials (ASTM) solar irradiance spectrum – resolution up to 1~2nm (ASTM, 2000)
TSIS
NOAA CDR
Largest uncertainty (30-60%) in UV and shorter wavelength
Up to 10-20%% at some other wavelengths, but overall, it is less 5%
1 nm resolution

## Slide 14: Lunar spectral albedo model uncertainty
Beyond 1640 nm, the M&T model gives negative albedo
ROLO model is the only model that simulates the albedo beyond 1640 nm.
The uncertainty increases with wavelength, and large differences can be found beyond 1000 nm.
Overall uncertainty is about 6% for wavelengths less than 1640 nm.
Large uncertainty of 15% in full moon conditions.
M&T model doesn’t consider opposition effect, it seems that.

## Slide 15: First mapping of nighttime visible AOD over the ocean
August 22 – 27, 2021; 0.75 km spatial resolution
Dust front can transport at 50-80 km/hr
Much less is known about dust IR impact and nighttime transport.
CALIPSO footprint is color coded with AOD
Nighttime Daytime

## Slide 16: Validation with AERONET & CALIPSO AOD

## Slide 17: Number of Days available for retrieval
DNB AOD from VIIRS
IASI IR AOD at 10 um
Vandenbussche et al., 2013
JJA 2021
Sampling rate: 6-10 days/month
Night
Day
VIIRS DB

## Slide 18: Case Study
(a) VIIRS 09-29-2020 Daytime
(b) VIIRS 09-29-2020 Nighttime
(d) VIIRS 09-30-2020 Nighttime
(c) VIIRS 09-30-2020 Daytime
(e) MODIS AOD
(f) DNB AOD
(h) DNB AOD
(g) MODIS AOD
2020 Fire case – Day and Night AOD Map
Interpolation

## Slide 19: Case Study
(a) VIIRS 09-29-2020 Daytime
(b) VIIRS 09-29-2020 Nighttime
(d) VIIRS 09-30-2020 Nighttime
(c) VIIRS 09-30-2020 Daytime
(e) MODIS AOD
(f) DNB AOD
(h) DNB AOD
(g) MODIS AOD
2020 Fire case – Day and Night AOD Map
AERONET Daytime Site
AERONET Nighttime Site

## Slide 20: What is the retrieval uncertainty?
EE%: 52.381%
EE%: 44.44%
EE%: 86.25%
EE%: 62%
EE%: 69%
EE%: 33.33%
±(0.085 + 10% AOD)
MERRA-2
DNB

## Slide 21: Summary & Outlook
Moon-light vector radiative transfer model at night is developed and validated with the limited data.
We assessed the uncertainty of lunar irradiance model. Overall, 7%, but it varies with wavelength and moon-phase angle. Shorter wavelength and smaller moon-phase angle have larger uncertainty.
We demonstrated that AOD can be retrieved with good accuracy at night from reflected moon light.
The nighttime AOD product MAY provide equally important information as daytime product to understand the smoke and dust transport processes and for data assimilation.
There is a critical need to sample AOD and aerosol property change around the clock from space. A small-satellite mission with multiple spectral channels focusing on low light imaging is warranted for aerosol studies, fire studies, and light pollution studies.

## Slide 22: User Community
Being used for remote sensing of aerosol, gas, cloud, and surface
User feedbacks are important sources to improve the model
Routinely maintained by Dr. Xiaoguang Xu, UMBC and research team in U. Iowa.
Xiaoguang Xu

## Slide 23: Moonlight
The Moon rotates once every 27.3 days, which is the same amount of time it takes for the Moon to orbit our planet. So, we always see the same side of the Moon
It is deemed that moonlight is a stable source of illumination; that is why many remote sensing instruments use moonlight to do calibration.
However,
Due to moonlight libration, the moon surface facing the Earth is not necessarily the same all the time.
Interaction of moonlight with Earth and atmosphere depends lunar zenith angle and the moon phase angle.
Moonlight can be seen in daytime as well. RTM?
Various phase of the moon seen in daytime
View at EarthSky Community Photos. | Meiying Lee
Notes: the Moon rotates once every 27.3 days, which is the same amount of time it takes for the Moon to orbit our planet. The result? On Earth we always see the same side of the Moon

## Slide 24: Definition of phase angle
As seen from moon, the angle between the directions to the Sun and the observer (Earth). Phase angle: 0, full moon; 180 new moon.
180o
0o
Lyot 1929.
This is different from other fields, where angle is defined as seen from the Earth!