## Slide 1
http://tempo.si.edu/
Data Product Overview & Use Case Demonstration
Aaron Naeger
& TEMPO Team
NASA Marshall Space Flight Center, Huntsville, AL

## Slide 2
How Does TEMPO Observe Pollutants?
2
2
Vertical Column Density (VCD)
Slant Column Density (SCD)
Trace Gas Absorption (NO2)
Surface Reflectance
UV-VIS Radiation
UV-VIS Spectrometer
TEMPO
Vertical Column Density (VCD)
Slant Column Density (SCD)
Cloud Reflectance
TOA Radiances
Aerosol Absorption/Scattering
TOA = Top-Of-Atmosphere
TEMPO’s trace gas retrievals are based on multi-step approach.
  Derive slant column densities (SCD) via spectral fitting to measured TOA radiances in known trace gas absorption windows
  Calculation of vertical column densities (VCDs) using Air Mass Factors (AMF) calculated offline with a radiative transfer model accounting for surface, atmospheric, and viewing geometry conditions
  For NO2 retrieval, perform Stratosphere-Troposphere separation for retrieving tropospheric NO2 VCDs
Aerosol effects are not explicitly treated in the retrieval

## Slide 3: TEMPO Data Product Updates

## Slide 4
TEMPO Products: SAO Baseline + SNWG NRT + NOAA Aerosol
4
4
4
Level | Product | Filename | Developer | Notable File Variables | Validation Status | Resolution (km2)
L1 | Radiance | RAD | SAO + SNWG | Radiances | Provisional | 2.0 x 4.75
 | Radiance (twilight) | RADT | SAO | Radiances | Provisional | 2.0 x 4.75
L2 | Cloud | CLDO4 | SAO/GSFC + SNWG | Cloud Fraction, Cloud Pressure | Provisional | 2.0 x 4.75
 | Ozone Total Column | O3TOT | SAO/GSFC | Total Column O3, UV Aerosol Index | Provisional | 2.0 x 4.75
 | Nitrogen Dioxide | NO2 | SAO + SNWG | Tropospheric VCD, Total VCD | Provisional | 2.0 x 4.75
 | Formaldehyde | HCHO | SAO + SNWG | Total VCD, Cloud Fraction | Provisional | 2.0 x 4.75
 | Ozone Profile | O3PROF | SAO | O3 Profile, Tropospheric O3 column | Beta | 8.0 x 4.75
 | AOD & ALH | AODALH | NOAA | AOD 550 nm, ALH | N/A | 2.0 x 4.75
 | Aerosol Detection Product (ADP) | ADP | NOAA | Dust/Smoke Discrimination, UV Aerosol Index | N/A | 2.0 x 4.75
L3 | Same as L2 | Same as L2 | SAO/GSFC + SNWG | Same Variables as L2 | Same as above | 0.02°x 0.02°
L4 | Surface PM2.5 | PM25 | NOAA | Hourly PM2.5 Estimation | N/A | 2 km x 2 km
*
AOD: Aerosol Optical Depth
ALH: Aerosol Layer Height
*
33.7°N, 91.7°W
@Center of Field of Regard
*
SNWG: Satellite Needs Working Group - near real-time products (~2-3 hours) – public release Sept. 17, 2025
O3PROF L3 Product  0.04 x 0.04° Resolution
*
NOAA: National Oceanic and Atmospheric Administration
SAO: Smithsonian Astrophysical Observatory
Latest product versions: Version 4 (standard) & Version 2 (NRT)
Notes: The level 3 product provides the same type of product variables as the level 2 product except the level 3 product is on a standard, regular grid of 0.02 degrees or about 2 km across the TEMPO Field of Regard. The level 3 product essentially stitches together the level 2 granules (9 granules or slices across the full TEMPO Field of Regard) and uses an area-weighted re-gridding method to remap the level 2 data onto the regular 0.02 degree grid of the level 3 product.

## Slide 5
Future TEMPO Products: SNWG NRT & Enhanced
5
These products have no formal release date yet but are officially funded for the TEMPO mission
UVB (Ultraviolet B) radiation retrievals support analyses on UV exposure trends, human health risks (skin cancer), and environmental impacts such as ecosystem damage.
Glyoxal forms from vegetation and wildfires with human activities (i.e., fossil fuels burning) contributing smaller amounts
Sources of bromine include volcanic emissions, biomass burning, industrial emissions, and marine processes
Level | Product | Filename | Source | Key Product Variables | Resolution (km2)
L2 | Glyoxal (C2H2O2) | GLYX | SNWG Enhanced | Total VCD, Cloud Fraction | 2.0 x 4.75
 | Water Vapor (H2O) | H2O | SNWG Enhanced |  | 2.0 x 4.75
 | Bromine (BrO) | BRO | SNWG Enhanced |  | 2.0 x 4.75
 | Sulfur Dioxide (SO2) | SO2 | SNWG NRT | Total VCD | 2.0 x 4.75
 | UVAOD | TBD | SNWG Enhanced | AOD 354, 388, 500 nm | 2.0 x 4.75
 | ALH | TBD | SNWG Enhanced | ALH | 2.0 x 4.75
 | UVB | TBD | SNWG Enhanced | UVB | 2.0 x 4.75
@Center of Field of Regard
33.7°N, 91.7°W
*
Notes: Note the SO2 product will be a near real-time product with < 2 hour data latency.

## Slide 6
TEMPO Product Release & Tools
6
Public Release | Date | Details
V01 | 2/5/2024 | Limited 3 weeks released
V02 | 2/26/2024 | Level 1 (spectra) released
V03 | 5/20/2024 | L1, L2/3 cloud, NO2, H2CO, total O3 (provisional) V3 O3 profile (ASDC 6/9/2025, not for the public)
V04 | 9/17/2025 | Ozone Profile (beta), L1 + other L2/L3 (provisional) Reprocessing starting this week
NRT V02 | 9/17/2025 | L1, L2/3 cloud, NO2, H2CO (funded by SNWG)
TEMPO data publicly available at NASA’s ASDC (~6 hours latency, NRT with 2-3 hours latency).
Wealth of tools:
  Earthdata Search
  NASA Worldview
  NASA ArcGIS services
  RSIG (EPA)
  TEMPO-Lite (SAO)
  NASA SPoRT Viewer
  Google Earth Engine
TEMPO website for data access, visualization tools, and user guides links
Worldview for visualizing TEMPO
NASA SPoRT Viewer for NRT imagery
Notes: Graphic to stress the point that TEMPO makes atmospheric column measurements, rather than surface-level measurements, and relies on complex retrievals that account for surface and atmospheric conditions and TEMPO viewing geometry, which leads to important errors / uncertainties that users must consider.

## Slide 7
TEMPO L2 Data Across Field of Regard (FoR)
7
7
VCDs – total amount of trace gas in the vertical column of air directly above a specific area of Earth’s surface to the top of the atmosphere
  molecules cm-2 - total number of gas molecules found in the vertical column of air
  Dobson Units (DU) – measures thickness of a gas layer if compressed to sea-level pressure
Tropospheric NO2 VCDs
Total HCHO VCDs
Total O3 columns
0-2 km O3 columns

## Slide 8: Data Filtering for Version 4 Products

## Slide 9
Data Filtering Guidance – NO2 & HCHO
9
9
QA Parameter | Variable (group) | Range | Qualitative Use (Worldview) | Quantitative Use
Effective Cloud Fraction (ECF) | eff_cloud_fraction (support_data) | 0 – 1.0 | > 0.5 | > 0.1
Solar Zenith Angle (SZA) | solar_zenith_angle (geolocation) | 0 – 90° | > 80° | > 70°
Main Data Quality Flag (QF) | main_data_quality_flag (product) “0” = High-quality “1” = Suspect due to AMF & viewing geometry “2” = Outlier retrievals or no successful AMF calculation | 0 to 2 | ≠ 2 | > 0
Users must apply data filtering for both Level 2 and Level 3 NO2 and HCHO products
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 10
May 4, 2026 NO2 Example
10
10
ECF > 0.1
SZA > 70°
QF > 0
ECF > 0.5
SZA > 80°
QF ≠ 2
GOES ABI True Color ~1250 UTC
No data due to SZA > 70°
= 2.116
= 2.086
SZA > 80°
QF ≠ 2
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 11
No data due to SZA > 70°
11
11
ECF > 0.1
SZA > 70°
QF > 0
ECF > 0.5
SZA > 80°
QF > 0
GOES ABI True Color ~1250 UTC
May 4, 2026 NO2 Example
= 2.086
SZA < 80°
QF < 2
= 2.116
Limited QF impact
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 12
May 4, 2026 NRT NO2 Example
12
12
ECF > 0.1
SZA > 70°
QF > 0
ECF > 0.5
SZA > 80°
QF ≠ 2
GOES ABI True Color ~1250 UTC
No data due to SZA > 70°
= 2.088
= 2.067
SZA < 80°
QF < 2
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 13
13
13
ECF > 0.1
SZA > 70°
QF > 0
ECF > 0.5
SZA > 80°
QF ≠ 2
GOES ABI True Color ~1250 UTC
No data due to SZA > 70°
May 4, 2026 HCHO Example
= 6.859
= 5.555
SZA < 80°
QF < 2
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 14
14
14
ECF > 0.1
SZA > 70°
QF > 0
ECF > 0.5
SZA > 80°
QF ≠ 2
GOES ABI True Color ~1250 UTC
No data due to SZA > 70°
May 4, 2026 NRT HCHO Example
= 8.378
= 7.005
SZA < 80°
QF < 2
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 15
TEMPO L2 Data Across Field of Regard (FoR)
15
15
VCDs – total amount of trace gas in the vertical column of air directly above a specific area of Earth’s surface to the top of the atmosphere
  molecules cm-2 - total number of gas molecules found in the vertical column of air
  Dobson Units (DU) – measures thickness of a gas layer if compressed to sea-level pressure
Tropospheric NO2 VCDs
Total HCHO VCDs
Total O3 columns
0-2 km O3 columns

## Slide 16
Data Filtering Guidance – O3 Total
16
16
QA Parameter | Variable (group) | Range | Qualitative Use (Worldview) | Quantitative Use
Quality Flag | quality_flag (product) 0 = highest-quality 1 = Glint contamination 2 = SZA > 84° 5 = SO2 present <1024 = ONLY disregard radiance/irradiance data which are missing or contain errors | 0 to 32768 | ≠ [0, 1, 2, 5] (adequate) | > 0 (best)
Effective Cloud Fraction (ECF) | fc (product) | 0 – 1.0 | No Filter | > 0.5
Solar Zenith Angle (SZA) | solar_zenith_angle (geolocation) | 0 – 90° | > 80° | > 80°
Viewing Zenith Angle (VZA) | viewing_zenith_angle (geolocation) | 0 – 90° | > 80° | > 80°
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 17
May 4, 2026 O3 Total Example
17
17
ECF > 0.5
ZA > 80°
QF > 0
NO ECF
ZA > 80°
QF ≠ 0,1,2,5
GOES ABI True Color ~1250 UTC
= 385.02
= 385.52
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 18
May 4, 2026 O3 Total Example
18
18
ECF > 0.5
ZA > 80°
QF ≠ 0,1,2,5
NO ECF
ZA > 80°
QF ≠ 0,1,2,5
GOES ABI True Color ~1250 UTC
= 385.02
= 385.52
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 19
O3 Total Column – Level 3 Product
19
19
When regridding TEMPO Level 2 data to the regular 0.02° Level 3 grid, data filtering is used during the procedure
  “Best” Quality flag (QF = 0)
  Solar (SZA < 80°) & viewing zenith angles (VZA < 80°)
Effective cloud fraction is NOT used for filtering when producing the O3 Total Column product
Users need to apply fc (effective cloud fraction) variable for filtering clouds from Level 3 O3 Total Column product
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 20
Data Filtering Guidance – O3 Profile
20
20
QA Parameter | Variable (group) | Range | Quantitative Use
retrieval exit status | exit_status (qa_statistics) 0 = not converged 1-99 = converged 100-110 = converged but with negative O3 value | (-10) – 110 | < 1 or > 99
ratio of fitting residual to measurement error | fit_RMS (qa_statistics) | 0 - 100 | > 3
average fitting residuals | avg_residuals (qa_statistics) | 0 - 100 | > 0.3
Effective Cloud Fraction (ECF) | eff_cloud_fraction (support_data) | 0 – 1.0 | > 0.5
Solar Zenith Angle (SZA) | solar_zenith_angle (geolocation) | 0 – 90° | > 80°
Viewing Zenith Angle (VZA) | viewing_zenith_angle (geolocation) | 0 – 90° | > 80°
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 21
May 4, 2026 O3 Profile Example
21
21
ECF > 0.5
SZA > 80°
VZA > 80°
fit_RMS > 3
avg_residual > 0.3
exit_status < 1 or > 99
0-2 km O3
Tropospheric O3
Total O3
Data filtering recommendation
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 22: TEMPO Nominal “Standard” Operations July 23, 2024 West U.S. Wildfires

## Slide 23
L2 NO2 Product Animation – July 23, 2024
23
23
Filter using
Cloud Fraction < 50%
SZA < 80°
Nominal operations consist of standard (hourly) daytime scans over full FoR and optimized (~30-40 minute) scans over daylight portions of the FoR during the morning and afternoon
Filter using
Cloud Fraction < 50%
SZA < 80°
2 x 4.75 km2 @ center of FoR
Notes: Animation showing one day in the life of TEMPO as it scans east to west across the TEMPO FoR, showing large tropospheric NO2 columns from urban areas like Chicago and Los Angeles, NO2 plumes related to wildfires in the western U.S. especially in California, and notable NO2 columns over the Permian Basin.

## Slide 24
L2 O3 Profile Product Animation – July 23, 2024
24
24
Nominal operations consist of standard (hourly) daytime scans over full FoR and optimized (~30-40 minute) scans over daylight portions of the FoR during the morning and afternoon
Filter using
Cloud Fraction < 50%
SZA < 80°
VZA < 80°
8 x 4.75 km2 @ center of FoR
Notes: Animation showing one day in the life of TEMPO as it scans east to west across the TEMPO FoR, showing large tropospheric NO2 columns from urban areas like Chicago and Los Angeles, NO2 plumes related to wildfires in the western U.S. especially in California, and notable NO2 columns over the Permian Basin.

## Slide 25
TEMPO NO2, HCHO, UVAI - West U.S. Zoom
25
25
ECF > 0.5
SZA > 80°
QF > 0
No ECF
SZA > 80°
VZA > 80°
Tropospheric NO2 VCDs
Total HCHO VCDs
UV Aerosol Index
TEMPO observed large NO2 and HCHO plumes associated with the wildfire smoke plumes
Elevated HCHO columns within the smoke plumes transported further downwind
The absorbing smoke aerosols lead to the strongly positive UV Aerosol Index values
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 26
TEMPO NO2 & ECF - West U.S. Zoom
26
26
No ECF
SZA > 80°
VZA > 80°
UV Aerosol Index
Using ECF > 0.1 for data filtering removes the vast majority of NO2 within the smoke plumes
Using ECF > 0.2 retains slightly more NO2 within the smoke plumes
Tropospheric NO2 VCDs
ECF > 0.1
ECF > 0.2
Notes: TEMPO validation against the Pandora ground-based network using the latest Version 3 TEMPO data shows overall good results for NO2 and HCHO. The maps show correlation and normalized mean bias (in percent) for TEMPO NO2 and HCHO versus Pandora NO2 and HCHO at each of the Pandora sites across the TEMPO Field of Regard. Key point is TEMPO NO2 and HCHO compares well to the Pandora sites, with overall better performance of the TEMPO NO2 product. The good validation results led to the previous ‘beta’ version of TEMPO products being upgraded to ‘provisional status’, indicating TEMPO data products are suitable for scientific research. Note these validation results were done using the strictest quality assurance thresholds to retain the highest quality TEMPO data.

## Slide 27: August 2, 2023 Canadian Wildfires

## Slide 28
TEMPO Aerosol Data – AOD & Aerosol Layer Height (ALH)
Large smoke plumes were transported from Canada over the eastern U.S. in early August 2023
TEMPO AOD observed values exceeding 1 within much of the transported smoke plume
TEMPO ALH showed the variability of smoke plume height with generally lower heights (smoke plume closer to the surface) as the smoke was transported farther downwind from the source
TEMPO AOD
TEMPO Aerosol Layer Height
MODIS Terra True Color

## Slide 29
Thank You!
aaron.naeger@nasa.gov
NASA SPoRT Viewer
TEMPO Operations Log