## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
A New Era of Air Quality Monitoring from Space over North America with TEMPO: Commissioning and Early Nominal Operation Results
Xiong Liu1, Kelly Chance1, Raid Suleiman1, John Houck1, John Davis1,
Kevin Daugherty2, David Flittner2, David Rosenbaum2, Crystal Fenn2,
Gonzalo Gonzalez Abad1, Caroline Nowlan1 , Huiqun Wang1, Heesung Chong1, Weizhen Hou1, Junsung Park1, Christopher Chan Miller1, Juseon Bak1, Jim Carr, James Szykman, Mike Newchurch, Aaron Naeger,Ronald Cohen,Zolal Ayazpour1,
Christopher Brown2, Zachary Fasnacht, Marcellin Feasson1, Jean Fitzmaurice1, Jeffrey Geddes, David Haffner, Jay Herman, Joanna Joiner, Laura Judd,
Emma Knowland, Xuming Lei, Nischal Mishra2, Robert Neece2, Ewan O'Sullivan1,
Brad Pierce, Wenhan Qin, Eric Roback2, Justin Strickland2, Robert Spurr,
Luke Valin, Alexander Vasilkov, Eun-Su Yang, and the TEMPO Team
1CfA | Harvard & Smithsonian
San Francisco, CA, December 11, 2023
A13F-01A

## Slide 2: Introduction to TEMPO
NASA’s first Earth Venture Instrument (EVI) selected in 2012
PI: Kelly Chance, Smithsonian Astrophysical Observatory (SAO): Science team, ground systems, science data processing center
Instrument Project Management: NASA LaRC  SAO (Phase E)
Instrument Development: Ball Aerospace
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, UAH, U Iowa, Sitting Bull College, RT Solutions, Carr Astronautics
International collaboration: Mexico, Canada, Cuba, Korea, U.K., ESA, Spain
NASA’s first host payload
  Mission Project Management: NASA LaRC
  Host Satellite Provider: Maxar Technologies
  Satellite Host: Intelsat (IS-40e)
  Launch: SpaceX
TEMPO: It’s about Time!

## Slide 3: TEMPO Commissioning
Launch
TEMPO
Power On
First Light
TEMPO Commissioning
S/C Activity (TEMPO Off)
Activation
Outgassing
Instrument Characterization and Analysis
PLAR
Nominal Operations
L+61 days (6/7/23)
L+115 days (7/31-8/2/23)
L+194 days
(10/19/23)
L+0 (4/7/23)
TEMPO commissioning: SAO + LaRC + Intelsat + Maxar + Ball + Carr Astronautics
  TEMPO power on 6/7
  Dry out (6/9-7/9) and cool down (7/10-7/12)
  First light (7/31-8/2): working/reference diffuser solar & Earth imaging
  Instrument Characterization and Analysis (ICA) activities
  Coordinate with AGES+ campaigns in Aug. and Coastal Texas Air Quality Field Campaign in Sep. (no Earth imaging for only 6 days, special observations over LA and Texas)
Nominal operation: started on 10/19 after successfully passing the Post Launch Acceptance Review (PLAR) on 10/18-19
A13F-02, Suleiman et al.

## Slide 4: Plan for Nominal Operation & Public Release
Data Product | Description | Time beyond On-Orbit Checkout (OOC) to deliver initial data | Maximum data latency after first release for ≥ 80% of products
Level 0 | Reconstructed, Unprocessed Instrument Data | 2 months | Within 2 hours of receipt at SAO
Level 1b | Calibrated, Geolocated Radiances | 4 months | Within 3 hours of Level 0 and ancillary data receipt at SAO
Level 2 | Derived Geophysical Data Products | 6 months | Within 24 hours of production of Level 1 at SAO
Level 3 | Derived Gridded Geophysical Data Products | 6 months | 1 month after completion of data accumulation required for individual geophysical products
Baseline mission (Phase E, 20 months, 10/2023-6/2025), NASA senior/extension review
Data products sent to ASDC for archival and distribution
Early access to data ASDC have been provided to TEMPO Science and Validation Teams
Plan for initial public release of baseline products at ASDC after algorithm verification, product validation, algorithm optimization/improvement: ~2/2024 for L1b, ~4/2024 for L2/L3

## Slide 5: TEMPO Instrument & First Light (8/1-2/2023)
Imaging spectrometer measuring solar irradiance and solar backscattered Earth radiance
First Light Earth 8/2/2023 @11:13-17:16 ET
RGB Images
First Light Solar
8/1/2023 @12:18 am ET
~293-494 nm
~538-741 nm
A11L-2151, Chong et al.
A11L-2150, Hou et al.

## Slide 6: TEMPO Operation
Nominal: Scan Field of Regard (FOR) in 1 hour
  ~ 2K N/S pixels ~1200 steps/hr
  2 4.75 km2 @center of FOR
Optimized scan: in the early morning and late afternoon, daylight portion, higher temporal resolution (~30 mins)
Special Observations (up to 25%):
  High-time scan: selected portion at higher temporal res. (e.g., <= 10 mins)
  Oversample to effectively increase spatial resolution
  Change FOR
Field of regard is optimized to cover both Puerto Rico and Canadian tar sands.
S5p-TROPOMI NO2 product oversampled by Kang Sun.
  Operate on geostationary communications satellite Intelsat 40e (IS-40e) at 91 ∘ W
A11L-2148, Naeger et al.
https://weather.ndc.nasa.gov/tempo/green_paper.html
Request special observation

## Slide 7: Field of Regard
First light 8/2 field of Regard: 62.7 mins
(100 ms integration time, 26 coadds, 61.5 µrad)
Fields of regard characterization (FOR mapping) with different N-S SMA angles
Requirement
Performance
Optimized field of Regard in late Sep.: 59.75 mins
(100 ms integration time, 26 coadds, 64 µrad)

## Slide 8: Baseline and Threshold Measurements Requirements
* # of hourly measurements to be averaged to achieve required precision
Mission duration: 20 months for baseline, 12 months for threshold
Spatial resolution: < 60 km2 for baseline (4 native pixels coadded), < 300 km2 for threshold
Species/Products | Required Precision | Temporal Revisit*
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour

## Slide 9: TEMPO Data Products Baseline + SNWG TEMPO NRT
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted digital counts |  | 2.0 x 4.75 | Daily/hourly
L1-b | Irradiance NRT | SAO L0-1 | Calibrated & quality flags |  |  | daily
 | Radiance NRT | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule
L2 | Cloud NRT | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | Climatology+GEOS-CF | >= 8.0 x 4.75** | Hourly, granule
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule
 | NO2 NRT | SAO trace gas, BU strat./trop. sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | HCHO NRT | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 5 x 5 2 x 2 | Hourly, scan
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
Satellite Needs Working Group (SNWG) will fund TEMPO NRT products (L2 products < 3 hours from observation time): 1/1/2023-12/31/2025, NOAA GeoXO team to produce TEMPO/GOES-R NRT aerosol products
A11L-2154, Ciren and Kondragunta
A41O-2839, Zhang, Kondragunta, et al.

## Slide 10: Algorithm/Data Product Status
First Light NO2 Images Release (8/24): updates to pre-launch (SDPC v4.0) for (offline/development):
  Use initial wavelength grid for radiance from calibrated first light working solar irradiance
  No straylight correction and polarization correction
  Specialized Image Navigation and Registration (INR)
  Optimization to clouds & NO2 algorithms
First SDPC update: SDPC v4.1 approved on 10/16, operational on 10/17, L0-1b, cloud, NO2, HCHO, total O3 produced and sent to ASDC
  INR: working well meeting science requirements.
  L0-1b: gain/non-linearity, bad pixel map, improved saturation flagging, Octant phase (odd/even)
  Further optimization in cloud and NO2
  Major changes to HCHO: radiance reference, and background/reference correction
  O3 profile not ready due to absolute radiometric calibration
SDPC v4.2: approved on 11/17, operational on 11/18
  INR: remove UV/Visible biases, accurate at subpixel level, tested to work for special observation
  Data processing pipeline: more robust, automatically recover from INR crash, other minor updates
  Used to reprocess TEMPO commissioning observations

## Slide 11: First Light NO2 (2 August 2023)
Credit: NASA Scientific Visualization Studio
A13F-03, Nowlan et al.
Notes: Caroline
- First mention these are from first-light. Got a lot of media attention.
I will talk about first light and describe the sources of NO2 as I go along on this slide: transportation, fires, lightning, soils
Mention how we can’t measure below clouds
Will point out these data are novel because we can measure every hour

## Slide 12: First Light HCHO (2 August 2023)
A13F-04, Gonzalez Abad et al.

## Slide 13: NO2 Tropospheric Column & HCHO Column Uncertainties
TEMPO NO2 & HCHO meets requirement for >90% of cloud-free scenes with no pixel coadding!
NO2 Median uncertainty = 0.46 × 1015 molecules/cm2 (SZA < 70°, all clouds)
Requirement
Coadd 4 pixels
Aug. 29-Sep. 1
SZA < 70°
All cloud fractions
All scans
Single pixel performance
Requirement
Coadd 12 pixels
Aug. 29-30
SZA < 70°
All cloud fractions
All scans
Single pixel performance
HCHO Median uncertainty = 5.5 x 1015 molecules/cm2 (SZA < 70˚, all clouds)

## Slide 14
Cloud fraction
Cloud pressure
Cloud Products (29 September 2023)
Saturation causes no retrieval under very cloudy conditions.
A11L-2149, Wang et al.

## Slide 15
First Light Total Ozone (02 August 2023)
TEMPO
OMPS
Similar spatial distribution with OMPS total ozone
Total ozone will be further improved with improved radiometric calibration (e.g., image processing, straylight correction)

## Slide 16
First Light H2O SCD (2 August 2023)

## Slide 17
TEMPO AOD vs ABI AOD in the VA fire region
Credits: NOAA GeoXO Team, Pubu, Hai, Zigang and Shobha

## Slide 18: Ongoing and Forward Work
TEMPO Cal/Val activities are ongoing with bi-weekly Cal/Val meeting (led by Jim/Brad)
Two more updates before public release: 1 before L1b release in February 2024, and another before L2/3 release in April 2024
  L0-1: BTDF correction, reference BTDF, improved wavelength calibration, improved CCD image processing steps (electronic offset correction, smear correction, dark current correction after accounting for temperature dependence), straylight correction
  Improvements to cloud, NO2 and HCHO algorithms
  Updates to O3 profile retrieval (very likely using UV only) and release the data product
  Change L3 resolution from to
  Address Feedback from ASDC, TEMPO validation and science teams
After public release --- end of baseline mission:
  Updates to science algorithms as needed based on validations and feedback
  Release O3 profile retrieval with UV/Visible to improve retrieval sensitivity to 0-2 km O3.
A11L-2151, Chong et al.
A11L-2150, Hou et al.

## Slide 19: Summary
Started nominal operation on Oct. 19 after a successful TEMPO commissioning phase and Post Launch Acceptance Review (PLAR)
TEMPO is providing revolutionary hourly daytime atmospheric pollution measurements at high spatial resolution over North America
Most data products (L1b, cloud, NO2, HCHO, total O3) are in good quality at this early stage, showing that the TEMPO instrument and science algorithms are working very well
We have a good understanding about the improvements needed for the ozone profile product before the public release
Calibration and validation activities are being conducted to validate and improve the data products

## Slide 22: TEMPO Software/Algorithm Teams
Operational Algorithm | Personnel
Instrument Operation Center (IOC) including Raw-L0 | John Davis
L0-1b | Heesung Chong, John Houck, Weizhen Hou, Xiong Liu, Dave Flittner, Jim Carr
Ozone profile | Xiong Liu, Junsung Park
Total ozone | GSFC / Xiong Liu
Nitrogen dioxide | Caroline Nowlan, Gonzalo González Abad
Formaldehyde | Gonzalo González Abad, Caroline Nowlan
Clouds | Huiqun (Helen) Wang, Eun-Su Yang, Alexander Vasilkov, Joanna Joiner
Science Data Processing Center Operational Implementation & Processing Pipeline | John Houck

## Slide 23: Science Algorithms
Launch-ready Science Data Processing Center (SDPC) V4 software completed in Mar 2023
Algorithm mostly based on OMI heritage algorithms except for new L0-1b processor including Imaging Navigation and Registration (INR) using GOES-R by Carr Astronautics
SAO trace gas algorithm (HCHO, NO2): spectral fitting to derive Slant Column Densities (SCDs), calculate air mass factor (AMFs) and derive Vertical Column Densities (VCDs)
  NO2 requires stratospheric/tropospheric separation based on spatial filtering method (Geddes et al., 2018)
Cloud algorithm: SAO O2-O2 fitting + NASA GSFC’s O2-O2 cloud at ~477/466 nm
Total ozone algorithm: heritage TOMS V8.5, using ozone absorbing and non ozone absorbing pairs to derive total ozone column
Ozone profile algorithm: heritage SAO OMI O3 profile, using 290-340, 540-650 nm, retrieve O3 profile at 24 layers, including total, stratospheric, tropospheric, and 0-2 km O3
Main L1-2 algorithms updates include:
  NASA GMAO’s GEOS-CF trace gas profiles and meteorology
  Hourly resolved monthly mean Geometry-dependent Lambertian Equivalent Reflectivity (GLER) climatology

## Slide 24: TEMPO and TROPOM HCHO (29-30 August 2023)
Google Engine S5P HCHO 0829
Google Engine S5P HCHO 0830
TEMPO HCHO 0829-0830 (scans close to S5P overpass)
TEMPO vs TROPOMI shows spatial agreement in HCHO columns. TEMPO shows small noise and almost no striping. Systematic biases are expected associated with AMF, radiance reference and background corrections.

## Slide 25: Including Visible to Improve Tropospheric Ozone Retrieval Sensitivity
This example is for solar zenith angle =25, viewing zenith angle 45, relative azimuthal angle 86, Signal to noise Ratio (SNR) with 4 pixels coadded
Add visible to improve retrieval sensitivity in the lower troposphere and help separate free tropospheric O3 from boundary layer O3
Under ideal conditions: 3-5 total Degree of Freedom for Signal (DFS) with up to ~1.5 in the troposphere, and up to ~0.5 DFS in 0-2 km
Adapted from OMI (Liu et al., 2010): Spectral fitting + VLIDORT + Optimal Estimation (OE) from Fitting windows: 293-345 nm, 540-650 nm
Retrieve partial O3 columns at ~24 layers (bottom layer is 0-2 km above the surface) as well as total, stratospheric, and tropospheric O3 columns, other trace gases, and auxiliary parameters.
A priori: a combination of tropopause-based climatology (Bak et al., 2013) with diurnally-resolved GEOS-CF data

## Slide 26
Ozone profile algorithm has been tested and we know how to improve the data product!
Total Ozone from Ozone Profile Product:
UV (8/28) vs. UV/VIS (8/29)
Large total ozone bias due to large positive biases (~20-30%) in radiance below ~305 nm, and the fitting of a first-order wavelength dependent surface albedo. Necessary to improve UV radiometric calibration (e.g., solar diffuser BTDF, image processing, straylight correction) and derive soft calibration
Less stable with UV/VIS retrievals than UV only retrievals. In addition, need to improve VIS spectral dependence of surface albedo and UV/VIS radiometric calibration consistency.
Ozone Profile (UV/VIS)
on 8/29
Ozone Profile (UV only) on 8/28

## Slide 27: Calibration and L1b Validation
Verify and update image correction steps in the L0-1 processing during Commissioning Phase and Nominal Operation
  System linearity, zero-input, relative gains, saturation blooming, dark current variation and temperature-dependent correction, check quality flags, evolution of solar diffuser, noise calculation, straylight
Assess wavelength calibration and its performance
  Will assess performance of routine processing (wavelength calibration in both L0-1b & L1-2 via high-resolution solar reference and atmospheric absorption)
  Pre-launch measured instrument line shape will be compared with that derived from solar irradiance
Assess radiometric calibration using a multi-pronged approach
  Internal assessment of images, assess performance of routine processing
  Comparison solar irradiance with solar reference and correlative contemporaneous sensors (e.g., OMPS, TROPOMI, GOME-2, EPIC, MODIS, VIIRS)
  Comparison with radiative transfer simulation
Assess and improve INR accuracy
  Alignment issue, ephemeris reliability, IRU time synchronization, scan tailoring verification
  Different configuration for special observation

## Slide 28: TEMPO Level 2 Data Products Validation Plan
TEMPO PLRA validation requirements: 3 Pandoras, 1 month per season
Jim Szykman has led the development of best-efforts basis validation plan: beta, provisional, full
Use satellite observations (i.e., LEO and EPIC/DSCOVR) for cross validations
Pandora & Pandonia Global Network (PGN): validate NO2, HCHO, total O3 and diurnal variation
TOLNet: 8 LIDAR instruments by time of launch to validate tropospheric O3 & 0-2 km O3 and diurnal variation
Airborne instruments: GEO-TASO, GCAS, HSRL-2, IAGOS, SeaRey UAV
Other instruments: ozonesonde, Dobson/Brewer, MAXDOAS, FTIR, AERONET, …
Planned flight campaigns AGES+ (e.g., STAQS, AEROMMA+CUPiDS, GOTHAAM) during Aug 2003, provide integrated approaches linking TEMPO science, applications, and validation
Indirect evaluation with chemistry transport models and data assimilation
www-air.larc.nasa.gov/missions/TOLNet/
Nowlan et al. (2018) GCAS, DISCOVER-AQ, Texas, Sep 2013
https://www.pandonia-global-network.org/
~60 PGNs in TEMPO FoR, ~20 to add in 2 years