## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
A New Era of Air Quality Monitoring from Space over North America with TEMPO: Commissioning and Early Nominal Operation Results
X. Liu1, K. Chance1, R. Suleiman1, J. Houck1, J. Davis1, G. Gonzalez Abad1,
C.R. Nowlan1, H. Wang1, H. Chong1, W. Hou1, J. Park1, J. Bak1, L. Carpenter1,
C. Chan Miller1, J. Fitzmaurice1, A. Oppenheimer1, E. O’Sullivan1, Z. Ayazpour1,
K. Daugherty2, D.E. Flittner2, C. Fenn2, D. Rosenbaum2, C. Brown2, N. Mishra2,
R.T. Neece2 , E. Roback2, J. Strickland2, L. Judd2, P. Rawat2, K. Travis2, J. Carr3,
X. Lei3, J. Szykman4, B. Henderson4, L. Valin4, J. Joiner5, Z. Fasnacht5,
S. Frith5, D. Haffner5, E. Knowland5, N. Kramarova5, W. Qin5, C. Seftor5,
Vasilkov5, E.-S. Yang5, J. Ziemke5, M. Newchurch6, A. Naeger6, R. Cohen7,
J. Geddes8, J. Herman9, B. Pierce10, R. Spurr11, S. Kondragunta12,
H. Zhang12, P. Ciren12, J. Wang13, Ivan Orteg14, and the TEMPO Team
1SAO, CfA 2NASA LaRc 3Carr Astro. 4EPA 5NASA GSFC 6UAH
7UCB 8BU 9UMBC 10UWM 11RT Solutions Inc 12NOAA 13UI 14UCAR
17th HITRAN Database Conference
June 24, 2024

## Slide 2: Outline
Introduction
TEMPO Science Overview
TEMPO Instrument and Operation
TEMPO Data Products
Commissioning/Early Nominal Operation & Validation Results
Summary and Outlook

## Slide 3
Notes: Before we jump in, I want to ask us all to take a minute to think about the air quality in your neighborhood, your community, your state?
What do you know about the air quality where you live?
For some of us, lucky enough to live in areas with good air quality, this may be the first time you’re taking the time to consider this question, but for some of you I imagine you’ve often wondered what am I breathing in?

## Slide 4: Why Does Air Quality Matter in the USA?
  Climate change is making the job of cleaning up the air more difficult
  1 in 3 Americans lives with unhealthy levels of air pollution
People of color are 3.7x as likely to live in areas of unhealthy air pollution
Notes: Health:
- Increases risk of COPD, lung cancer, asthma, respiratory infections, pre-term birth, heart disease, stroke, diabetes and dementia.
- Strongest links with fine particulate matter, ozone, nitrogen dioxide (NO2) and sulfur dioxide (SO2)
Ecosystems:
Loss of biodiversity due to excess nitrogen added to soil and water. This can cause certain plants to thrive, and also algae blooms.
An example of acidification is acid rain
Economic impacts from crop damage

## Slide 5: Surface Pollution Monitoring
EPA air quality system NO2 monitors

## Slide 6: Satellite Remote Sensing
Satellites can provide continuous mapping
UV/visible/near-infrared instruments are sensitive to pollutants in the lower atmosphere
Low Earth Orbit (LEO): global coverage
  Eight UV/Vis instruments in LEO
  Spatial resolutions ~3.5 × 5.5 km2 to ~50 × 80 km2
  Measure a location typically once per day
TROPOMI NO2, ESA
6

## Slide 7: Why geostationary? High temporal and spatial resolution
Hourly NO2 surface concentration and integrated column calculated by CMAQ air quality model: Houston, TX, June 22-23, 2005
June 22
Hour of Day (UTC)
June 23
LEO observations provide limited information on rapidly varying emissions, chemistry, & transport
GEO will provide observations at temporal and spatial scales highly relevant to air quality processes
NRC’s 2007 Earth Science Decadal Survey recommended Geostationary Coastal & Air Pollution Events (GEO-CAPE) mission: GEO-CAPE mission studies (2009-2018)
[Fishman et al., 2008]

## Slide 8
NASA’s first Earth Venture Instrument (EVI) selected in 2012
PI-led at Smithsonian Astrophysical Observatory (SAO): Science team, instrument operation center (IOC), science data processing center (SDPC)
Instrument Project Management: NASA LaRC  SAO (Phase E)
Instrument Development: Ball Aerospace (now part of BAE Systems, Inc.)
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, UAH, U Iowa, Sitting Bull College, RT Solutions, Carr Astro.
International collaboration: Mexico, Canada, Cuba, Korea, U.K., ESA, Spain
NASA’s first host payload
  Mission Project Management: NASA LaRC
  Host Satellite Provider: Maxar Technologies
  Satellite Host: Intelsat (IS-40e)
  Launch: SpaceX
TEMPO Early Adopter Program at UAH/NASA MSFC (funded by NASA Applied Science): ~600 early adopters
TEMPO: It’s about Time!
The TMEPO Mission

## Slide 9: Geostationary Air Quality Constellation
Launch Feb 2020
Launch 2025
Launch April 2023
Image Credit: NASA LaRC
MEASMA (hourly)

## Slide 10: TEMPO (GEO-CAPE) Science Questions
What are the temporal and spatial variations of emissions of gases and aerosols important for air quality and climate?
How do physical, chemical, and dynamical processes determine tropospheric composition and air quality over scales ranging from urban to continental, diurnally to seasonally?
How does air pollution drive climate forcing and how does climate change affect air quality on a continental scale?
How can observations from space improve air quality forecasts and assessments for societal benefit?
How does intercontinental transport affect air quality?
How do episodic events, such as wildfires, dust outbreaks, and volcanic eruptions, affect atmospheric composition and air quality?

## Slide 11: TEMPO Timeline
1/2013 | TEMPO project kick off
11/2018 | Instrument delivered
07/2019 | Host provider Maxar selected
02/2020 | Host Intelsat 40e (IS-40e) selected
02/2023 | TEMPO integration tested with IS-40e
4/07/2023 | Launch
6/7/2023 | TEMPO power on
8/1-2/2023 | TEMPO first light
10/19/23 | TEMPO nominal operation
2/2024 | Release L1 data products to the public
5/2024 | Release L2/3 data products to the public
6/2025 | End of Baseline Mission Extended via NASA extension/senior review
Credit: Ball, Instrument Delivery 11/2018
Credit: Maxar, TEMPO integrated & tested on 3/2023
Photo Credit: Carey Plemmons

## Slide 12: TEMPO Commissioning and Early Nominal Operation
Launch
TEMPO
Power On
First Light
TEMPO Commissioning
S/C Activity (TEMPO Off)
Activation
Outgassing
Instrument Characterization and Analysis
PLAR
Nominal Operations
L+61 days (6/7/23)
L+115 days (7/31-8/2/23)
L+194 days
(10/19/23)
L+0 (4/7/23)
TEMPO commissioning: SAO + LaRC + Intelsat + Maxar + Ball + Carr Astronautics
  Coordinate with AGES+ campaigns in Aug. and Coastal Texas Air Quality Field Campaign in Sep. (no Earth imaging for only 6 days, special observations over LA and Texas)
Nominal operation: after the Post Launch Acceptance Review (PLAR) on 10/18-19/2023
  Weekly commanding, no special observations before L2/3 public release
  Optimize off-nominal twilight observations: city lights=>lighting types, Aurora
  Overall, very smooth operation
Baseline mission (Phase E, 20 months until 6/18/2025): extended via NASA extension/senior review
Successful TEMPO commissioning and early nominal operation!

## Slide 13: TEMPO Instrument First Light (8/1-2/2023)
First Light Solar
8/1/2023 @12:18 am ET
First Light Earth 8/2/2023 @11:13-17:16 ET
RGB Images
[Credit: Heesung Chong]
Imaging spectrometer measuring solar irradiance and solar backscattered Earth radiance
[Credit: John Davis]

## Slide 14
Credit: NASA Science Visualization Studio

## Slide 15: TEMPO Scanning
Nominal scans
  2048 North/South pixels
  1181 East/West steps per hour
  2 x 4.75 km2 at center of field of regard
Optimized scans
  Higher temporal resolution AM and PM scans over coasts (40 minutes)
Twilight scans (city lights)
  Performed during darkness
Special observations: can be requested with strong science justification
  High-time scans (5-10 mins) over selected longitudes
  Oversampling in the E/W
  Slightly change of field of regard
  Operate on Intelsat 40e (IS-40e) at 91 ∘ W

## Slide 16: Ground System Architecture Review

## Slide 17: Baseline and Threshold Measurements Requirements
* # of hourly measurements to be averaged to achieve required precision
Mission duration: 20 months for baseline, 12 months for threshold
Spatial resolution: < 60 km2 for baseline (4 native pixels coadded), < 300 km2 for threshold
AOD, SO2, and CHOCHO removed at KDP-C.
Species/Products | Required Precision | Temporal Revisit*
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Reduced list of baseline data products due to cost cap!

## Slide 18: TEMPO Data Products Release Timeline
Public Release | Details
V01 | Limited 3 weeks released in February 2024
V02 | Level 1 (radiances) released in February 2024
V03 | Level 1 updated, Level 2/3 NO2, HCHO, total O3 released May 2024 Currently 13 May 2024 onwards; reprocessing has begun.
Data products sent to ASDC for archival & distribution before nominal operation
Early access to TEMPO Science and Validation team members in November 2023.

## Slide 19: Baseline TEMPO Data Products
Level | Product | Validation Status
L1 | Irradiance NRT | Beta
 | Radiance NRT | Beta
 | Radiance (twilight – city lights) | Beta
L2 | Clouds NRT | Beta
 | NO2 NRT | Beta
 | HCHO NRT | Beta
 | O3 (total) | Beta
 | O3 (profile) | Production/Release on hold
L3 | L2 gridded to 0.02° × 0.02° | 
*Beta: “minimally validated”, publication “not recommended and highly discouraged”
 Hope to go to provisional status after validation team approval
Satellite needs working group has funded TEMPO NRT products (expect in 2025)
NOAA to product NRT aerosols
Research products:
Aerosols, SO2, ocean color, city lights
Future SAO products:
H2O vapor, glyoxal, BrO, HNO2

## Slide 20: Getting TEMPO Data
TEMPO data now publicly available through NASA Atmospheric Science Data Center
  13 May 2024 onward
  Now reprocessing from August 2023
Multiple tools:
  Earthdata Search, OPeNDAP
  NASA Worldview: all data products
  ArcGIS services: currently NO2
  RSIG (EPA)
  TEMPO-Lite (CfA): currently NO2
For more information check out:
  User Guide
  Daily log
  Validation plan
  Validation reports (coming soon)
  Algorithm Theoretical Basis Documents (drafts available upon request, not yet reviewed)
NASA Webinar recording for new users: https://youtu.be/meySKqVuVT0?si=uiLTRXsgtKIGS_OT
Notes: Update with real Worldview data

## Slide 21: TROPOMI and TEMPO NO2
[Credit: Caroline Nowlan]

## Slide 22: TEMPO and TROPOMI HCHO (29-30 August 2023)
Google Engine S5P HCHO 0829
Google Engine S5P HCHO 0830
TEMPO HCHO 0829-0830 (scans close to S5P overpass)
TEMPO vs TROPOMI shows spatial agreement in HCHO columns. TEMPO shows small noise and almost no striping. Systematic biases are expected associated with AMF, radiance reference and background corrections.
[Credit: Gonzalo Gonzalez Abad]

## Slide 23
Cloud fraction
Cloud pressure
Cloud Products (29 September 2023)
Saturation causes no retrieval under very cloudy conditions.
[Credit: Huiqun Wang]

## Slide 24: Pandora and TROPOMI Comparisons (V02)
HCHO
NO2
[Credit: Barron Henderson, Luke Valin, Jim Szykman]
* TROPOMI comparisons are for ozone non-attainment areas

## Slide 25: FTIR HCHO Comparisons (V2)
Courtesy of Ivan Ortega et al. (UCAR/NCAR, UNAN, ECCC)

## Slide 26: Pandora NO2 Comparisons (V1)
November 23-Jan 20
Courtesy of Prajjwal Rawat (NASA LaRC), Katherine Travis (NASA LaRC), James Szykman (EPA)

## Slide 27: NO2 Tropospheric Column & HCHO Column Uncertainties
TEMPO NO2 & HCHO meets requirement for >90% of cloud-free scenes with no pixel coadding!
NO2 Median uncertainty = 0.46 × 1015 molecules/cm2 (SZA < 70°, all clouds)
Requirement
Coadd 4 pixels
Aug. 29-Sep. 1
SZA < 70°
All cloud fractions
All scans
Single pixel performance
Requirement
Coadd 12 pixels
Aug. 29-30
SZA < 70°
All cloud fractions
All scans
Single pixel performance
HCHO Median uncertainty = 5.5 x 1015 molecules/cm2 (SZA < 70˚, all clouds)

## Slide 28
TEMPO Total Ozone (V2):
Comparison with OMPS and OMI
Credit: Jerry Ziemke & Stacey Frith, NASA GSFC
OMPS and OMI within ±3 hr overpass with TEMPO with all data binned to 1o × 1o daily averages
20240328, S008
V2
V3
V3 – V2
CF < 0.3

## Slide 29: TEMPO O3PROF (UV Only) (3/29/2024 Scan 006)
Tropospheric O3 from TEMPO O3PROF
Tropospheric O3 from GEOS-CF
Tropospheric O3 from TROPOMI
Tropospheric O3 from EPIC
PRELIMINARY!
Note different tropopause pressure from OMI/EPIC/TROPOMI!
[Credit: Junsung Park]
[Credit: Jerry Ziemke]
[Credit: Juseon Bak]
Tropospheric O3 from OMI

## Slide 30
TEMPO O3PROF (UV/Visible) Retrieval
Benefits of visible fitting (Natraj et al., 2011; Zoogman et al., 2017)
- UV + visible to help distinguish boundary layer O3 from free tropospheric O3.
Challenges of visible fitting
Weak O3 absorption, strong interferences from surface reflectance & aerosols/clouds, and O4, O2, H2O
Need accurate radiometric calibration across the spectral range
Expensive RTM calculations at ～800 (line-by-line calculations at 0.002 nm in the visible)

## Slide 31
TEMPO Aerosol Retrieval
Credits: NOAA GeoXO Team, H. Zhang, P. Ciren, Z. Wei and S. Kondragunta

## Slide 32
City Lights & Aurora
[Credit: Jim Carr]
Radiance derivation  Post-processing (de-speckling, de-streaking, etc.)  Composite
Clearest-Sky Composite 1–12 February 2024
Oxygen at 558 nm

## Slide 33
City Lights Spectral Classification
[Credit: Jim Carr]
Miami, Fl
Offshore Flaring
~1200 K Blackbody

## Slide 34
TEMPO Spectroscopic Needs
O3 cross section: ESA SEOM-IAS BW (Birk & Wagner, 2018), only covers 244-346 nm, no visible
O2-O2 cross section and its temperature dependence: (Finkenzeller and Vaolkamer, 2022), only covers 297-500 nm at 223, 263, 293 K.
O2-B, O2-O2-accuracy and temperature dependence
Surface albedo spectra especially in the visible:
Need aerosol optical properties' information at fine enough spectral resolution, and often have to make assumptions about wavelength dependence - for example refractive index information as a function of wavelength (S. Kondragunta).
Lightning spectra: currently using NOAA NCEI laboratory spectra (coarser spectral resolution than TEMPO) (J. Carr)
Liquid water / sea water: For multiple molecules, liquid water is most likely the reason that we get different structures and amplitudes in residuals between the land and ocean (H. Wang)
Other species:

## Slide 35: Summary and Outlook
TEMPO commissioning and nominal operation have gone on very well.
Most data products (L1b, cloud, NO2, HCHO, total O3) are publicly available.
Validation team starting to examine V03
Priorities for V04:
  Radiances  improve absolute calibration, include polarization correction, advance validation to provisional
  NO2 , HCHO, cloud  improve surface albedo, cloud fraction bias, HCHO background correction
  Total O3  latitude-dependent bias
  Continued development and release of O3 profile product
Near-real time products estimated for middle of 2025
Thank you!
Acknowledgements: Funding from
NASA (Contract No. NNL13AA09C )

## Slide 38
First Light H2O SCD (2 August 2023)
[Credit: Huiqun Wang]

## Slide 39: Princeton fire, British Columbia
TEMPO HONO from Fire
PRELIMINARY!
Credits: N. Theys, BIRA-IASB

## Slide 40: TEMPO Data Products Baseline + SNWG NRT + SNWG NRT/Enhanced
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted digital counts |  | 2.0 x 4.75 | Daily/hourly
L1-b | Irradiance NRT | SAO L0-1 | Calibrated & quality flags |  |  | daily
 | Radiance NRT | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule
 | City lights | SAO L0-1 | Geolocated & calibrated |  | 2.0 x 4.75 | Variable, granule
L2 | Cloud NRT | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3, errors, a priori, AKs | Clim. + GEOS-CF | >= 8.0 x 4.75** | Hourly, granule
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule
 | NO2 NRT | SAO trace gas, BU strat/trop sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | HCHO NRT | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | C2H2O2 | SAO trace gas |  | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | H2O | SAO trace gas |  | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | HNO2 | SAO trace gas |  | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | BrO | SAO trace gas |  | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | Aerosol NOAA NRT | OMAERUV/UI AOCH | AAI, UVAOD, UVSSA, AOCH, VISAOD |  | 8.0 x 4.75 | Hourly, granule
 | SO2 NRT | OMSO2 PCA | SCD, VCD (PBL,TRL,TRM,TRU,STL) |  | 2.0 x 4.75 | Hourly, granule
 | TEMPO/GOES-R Synerg. product | GOES-R products on TEMPO pixels | Radiance, aerosol, cloud & mask, fire/hotspot, snow/ice, rainfall, precipitable water, land/sea surface T, lightning |  | 2.0 x 4.75 | Hourly, granule
 | Vegetation/Ocean color | GSFC GOME2/TROPOMI ML | Vegetation indices, ocean color, Growth Primary Productivity (GPP), Solar Induced Fluorescence (SIF), ocean color |  | 2.0 x 4.75 | Hourly, granule
 | UVB | GEMS/GSFC UVB | UV irradiance, erythemal irradiance, UVI |  | 2.0 x 4.75 | Hourly, scan
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 2 x 2 | Hourly, scan
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
Satellite Needs Working Group (SNWG) will fund TEMPO NRT products (L2 products < 3 hours from observation time): 3/26/2024-3/25/2026
SNWG 2022 Survey has selected to produce TEMPO NRT/Enhanced Productions starting in 2026

## Slide 41: TEMPO Data Products Baseline + SNWG TEMPO NRT
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size | Val. Status (5/20/2024)
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted DN |  | 2.0 x 4.75 | Daily/hourly | 
L1 | Irradiance NRT | SAO L0-1 | Calibrated & quality flags |  |  | weekly | Beta
 | Radiance NRT | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule | Beta
 | City lights | SAO L0-1 | Geolocated & calibrated |  | 2.0 x 4.75 | Variable, granule | Beta
L2 | Cloud NRT | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule | Beta
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | Climatology+GEOS-CF | >= 8.0 x 4.75** | Hourly, granule | Not released due to building cooling
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule | Beta
 | NO2 NRT | SAO trace gas, BU strat./trop. sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule | Beta
 | HCHO NRT | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule | Beta
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 2 x 2 | Hourly, scan | 
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
Research aerosols, SO2, ocean color products
Satellite Needs Working Group (SNWG) funded TEMPO NRT products (L2 products < 3 hours from observation time): 3/26/2024-3/25/2026, NOAA GeoXO team to produce TEMPO/GOES-R NRT aerosol products

## Slide 42: Field of Regard
First light 8/2 field of Regard: 62.7 mins
(100 ms integration time, 26 coadds, 61.5 µrad)
Fields of regard characterization (FOR mapping) with different N-S SMA angles
Requirement
Performance
Optimized field of Regard in late Sep.: 59.75 mins
(100 ms integration time, 26 coadds, 64 µrad)
[Credit: Heesung Chong]

## Slide 43
TEMPO AOD vs ABI AOD in the VA fire region
Credits: NOAA GeoXO Team, Pubu, Hai, Zigang and Shobha

## Slide 44: TEMPO Operation
Nominal: Scan Field of Regard (FOR) in 1 hour
  ~ 2K N/S pixels ~1200 steps/hr
  2 4.75 km2 @center of FOR
Optimized scan: in the early morning and late afternoon, daylight portion, higher temporal resolution (~40 mins)
Special Observations (up to 25%):
  High-time scan: selected portion at higher temporal res. (e.g., <= 10 mins)
  Oversample to effectively increase spatial resolution
  Change FOR
  No Special observations before April release
Field of regard is optimized to cover both Puerto Rico and Canadian tar sands.
S5p-TROPOMI NO2 product oversampled by Kang Sun.
  Operate on geostationary communications satellite Intelsat 40e (IS-40e) at 91 ∘ W
https://weather.ndc.nasa.gov/tempo/green_paper.html
Request special observation

## Slide 45: TEMPO Software/Algorithm Teams
Operational Algorithm | Personnel
Instrument Operation Center (IOC) including Raw-L0 | John Davis
L0-1b | Heesung Chong, John Houck, Weizhen Hou, Xiong Liu, Dave Flittner, Jim Carr
Ozone profile | Junsung Park, Xiong Liu
Total ozone | Junsung Park, Xiong Liu, GSFC
Nitrogen dioxide | Caroline Nowlan, Gonzalo González Abad
Formaldehyde | Gonzalo González Abad, Caroline Nowlan
Clouds | Huiqun (Helen) Wang, González Abad, Caroline Nowlan, GSFC
Science Data Processing Center Operational Implementation & Processing Pipeline | John Houck

## Slide 46: Science Algorithms
Launch-ready Science Data Processing Center (SDPC) V4 software completed in Mar 2023
Algorithm mostly based on OMI heritage algorithms except for new L0-1b processor including Imaging Navigation and Registration (INR) using GOES-R by Carr Astronautics
SAO trace gas algorithm (HCHO, NO2): spectral fitting to derive Slant Column Densities (SCDs), calculate air mass factor (AMFs) and derive Vertical Column Densities (VCDs)
  NO2 requires stratospheric/tropospheric separation based on spatial filtering method (Geddes et al., 2018)
Cloud algorithm: SAO O2-O2 fitting + NASA GSFC’s O2-O2 cloud at ~477/466 nm
Total ozone algorithm: heritage TOMS V8.5, using ozone absorbing and non ozone absorbing pairs to derive total ozone column
Ozone profile algorithm: heritage SAO OMI O3 profile, using 290-340, 540-650 nm, retrieve O3 profile at 24 layers, including total, stratospheric, tropospheric, and 0-2 km O3
Main L1-2 algorithms updates include:
  NASA GMAO’s GEOS-CF trace gas profiles and meteorology
  Hourly resolved monthly mean Geometry-dependent Lambertian Equivalent Reflectivity (GLER) climatology

## Slide 47: Including Visible to Improve Tropospheric Ozone Retrieval Sensitivity
This example is for solar zenith angle =25, viewing zenith angle 45, relative azimuthal angle 86, Signal to noise Ratio (SNR) with 4 pixels coadded
Add visible to improve retrieval sensitivity in the lower troposphere and help separate free tropospheric O3 from boundary layer O3
Under ideal conditions: 3-5 total Degree of Freedom for Signal (DFS) with up to ~1.5 in the troposphere, and up to ~0.5 DFS in 0-2 km
Adapted from OMI (Liu et al., 2010): Spectral fitting + VLIDORT + Optimal Estimation (OE) from Fitting windows: 293-345 nm, 540-650 nm
Retrieve partial O3 columns at ~24 layers (bottom layer is 0-2 km above the surface) as well as total, stratospheric, and tropospheric O3 columns, other trace gases, and auxiliary parameters.
A priori: a combination of tropopause-based climatology (Bak et al., 2013) with diurnally-resolved GEOS-CF data

## Slide 48
TEMPO Observation of Solar Eclipse
[Credit: Heesung Chong]

## Slide 49: Algorithm/Data Products Development Timeline
First Light NO2 Images Release (8/24): updates to pre-launch (SDPC v4.0) (offline/development):
  Use initial wavelength grid for radiance from calibrated first light working solar irradiance
  No straylight correction and polarization correction
  Optimized Image Navigation and Registration (INR) for first light
  Optimization to clouds & NO2 algorithms
First official SDPC update: SDPC v4.1 (V1 data products) approved on 10/16, operational on 10/17, L0-1b, cloud, NO2, HCHO, total O3 produced and sent to ASDC
  INR: working well meeting science requirements.
  L0-1b: gain/non-linearity, bad pixel map, improved saturation flagging, Octant phase (odd/even)
  Further optimization in cloud and NO2
  Major changes to HCHO: radiance reference, and background/reference correction
  O3 profile not ready due to absolute radiometric calibration
SDPC v4.2 (V1): approved on 11/17, operational on 11/18
  INR: remove UV/Visible biases, accurate at subpixel level, tested to work for special observation
  Data processing pipeline: more robust, automatically recover from INR crash, other minor updates
  Used to reprocess TEMPO commissioning observations

## Slide 50
SDPC v4.3 (V2) & Level 1 release: approved on 2/23/2024, operational 2/26/2024
  Level 1 Beta Public Release:
    Scattering angle dependent BTDF correction, removing time- and across-track dependent biases
    Improved CCD image processing steps (electronic offset correction, smear correction, dark current correction after accounting for temperature dependence)
    Improved solar wavelength calibration, use latest solar irradiance wavelength for radiance
Algorithm/Data Products Development Timeline
  Critical updates to NO2, HCHO, and cloud algorithms: GLER interpolation issues, snow/ice, missing data due to cloud radiance wavelength calibration failure, NO2 tropopause layer selection bug, temperature correction in total NO2 AMF
  Change L3 resolution from to
[Credit: David E. Flittner]

## Slide 51
SDPC v4.4 (V3) & Level 2-3 release: May 20, 2024
  Improved Level 1 & new Level 1 city lights
    Add nominal geolocations for city lights & Improve the robustness for INR
    Improve FPA temperature sampling and temperature-dependent dark current correction
    Add straylight correction (1-D PSF)
    Add radiance wavelength calibration
  Improved Level 2 & 3 for public release except for ozone profile (UV only) product
    Update GLER (v6.0->v6.1, snow free + 100% snow, quality flag 2-> 5, fill in gaps via interpolation)
    Perform retrievals up to SZA 90
    Update main data quality flag (AMF > 6 as suspect), Revisit convergence flag & AMF diagnostic flag
    Add temperature profile to output (for AMF)
    Cloud: SCD fitting optimization, SCD T correction, ECF/OCP iteration, wavelength shifts to ECF
    Ozone profile: Update the use of GEOS-CF meteorology and ozone profile + Derive soft calibration
After the May 2024 L2/3 public release --- end of baseline mission:
  Reprocessing for all data products (except for ozone profile product)
  Release O3 profile retrieval with UV only in ~2 months
  Release UV/Visible to improve retrieval sensitivity to 0-2 km O3 at the end of baseline mission
  Updates to science algorithms & calibrations as needed based on validations and feedback
Algorithm/Data Products Development Timeline
Power/cooling issues at our data center

## Slide 52: Pandora NO2 Comparisons (V2)
52
Courtesy of Barron Henderson, EPA
Overall, TEMPO tropospheric NO2 agrees well with Pandora.
Larger negative TEMPO bias over high NO2 site.
Biases between products can be due to differences in AMF inputs
Pandora Sites

## Slide 53: TROPOMI NO2 Comparisons (V2)
53
Courtesy of Barron Henderson, EPA
Overall, TEMPO tropospheric NO2 agrees well with TROPOMI
Positive biases at eastern sites and negative biases at western sites.
Biases between products can be due to differences in AMF inputs
Pandora Sites
Nonattainment Areas

## Slide 54: Pandora/TROPOMI HCHO Comparisons (V2)
54
Courtesy of Barron Henderson, EPA
Pandora
TROPOMI