## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
A New Era of Air Quality Monitoring from Space over North America with TEMPO: Commissioning Results
Xiong Liu1, Kelly Chance1, Raid Suleiman1, John Houck1,
John Davis1, Kevin Daugherty2, David Flittner2, Caroline Nowlan1,
Gonzalo Gonzalez Abad1, Huiqun Wang1, Heesung Chong1,
Weizhen Hou1, Jean Fitzmaurice1, Jim Carr3,
Christopher Chan Miller1, Juseon Bak1, Marcellin Feasson1,
Zolal Ayazpour1, and the TEMPO team
1CfA | Harvard-Smithsonian 2 NASA LaRc 3 Carr Astro.
14th GEMS Workshop
September 7, 2023

## Slide 2: TEMPO Commissioning
Launch
TEMPO
Power On
First Light
TEMPO Commissioning
S/C Activity (TEMPO Off)
Activation
Outgassing
Instrument Characterization and Analysis
PLAR
Nominal Operations
L+61 days (6/7/23)
L+115 days (7/31-8/2/23)
L+194 days
(10/19/23)
L+0 (4/7/23)
TEMPO is GEMS’s sister instrument also built by Ball:
  UV + visible bands: ~293-494 nm, ~538-741 nm
  Operate at 91 ∘ W, with 2x4.75 km2 at the center of field of regard
TEMPO commissioning (6/7-10/18/2023): no major issues to prevent us from nominal operations
  TEMPO power on 6/7
  Dry out and cool down (6/9-7/13):
  Additional activation: scan mirror tuning, command load testing, etc.
  First light (7/31-8/2): solar measurements with working/reference diffuser & Earth imaging
  23 Instrument Characterization and Analysis (ICA) activities.
  Coordinate with AGES+ campaign: (no Earth imaging only on 8/3,8/10, 8/13, 8/14, 8/24, 10 mins special observation on 8/23, 10 mins+1hr FOR on 8/27, twilight on 8/30 for supermoon)
We are here!

## Slide 3: First Light: Working Diffuser Solar @12:18 am ET, August 1, 2023
Synthetic Data

## Slide 4: Wavelength Shift from Pre-launch
Large wavelength shifts from pre-launch characterization.

## Slide 5: First Light: Reference Diffuser Solar @12:18 am ET, August 2, 2023
Difference mainly caused by using the same BTDF

## Slide 6: First Light: Earth Imaging Started @11:13 ET, August 2, 2023

## Slide 7: TEMPO Baseline Data Products
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted digital counts |  | 2.0 x 4.75 | Daily/hourly
L1-b | Irradiance | SAO L0-1 | Calibrated & quality flags |  |  | daily
 | Radiance | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule
L2 | Cloud | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | Climatology+GEOS-CF | >= 8.0 x 4.75** | Hourly, granule
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule
 | NO2 | SAO trace gas, BU strat./trop. sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | HCHO | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 2 x 2 (?) | Hourly, scan
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2

## Slide 8: First Light: Nitrogen Dioxide
Credit: NASA Scientific Visualization Studio
Notes: Caroline
- First mention these are from first-light. Got a lot of media attention.
I will talk about first light and describe the sources of NO2 as I go along on this slide: transportation, fires, lightning, soils
Mention how we can’t measure below clouds
Will point out these data are novel because we can measure every hour

## Slide 9: Nitrogen Dioxide
Credit: NASA Scientific Visualization Studio
August 2, 2023
12:14 PM
4:24 PM
Typical fitting uncertainty for clear sky conditions: ~1E15 molecules/cm2
Notes: Caroline
- Point out high levels over I-95

## Slide 10
First Light comm3 S001-S006
Cloud fraction
Cloud pressure
First Light: Cloud Products
Saturation causes some retrieval failure under cloudy conditions.

## Slide 11
Formaldehyde: First Results
Using radiance reference to reduce large systematic biases
Background correction
Typical fitting uncertainty for clear sky conditions: ~8E15 molecules/cm2
Notes: Caroline
- Describe sources (different from NO2, VOC oxidation, vegetation, industrial)
- Describe importance of HCHO for ozone/PM production
- How scientists use HCHO

## Slide 12
Total Ozone: First Results
Notes: Caroline
- Describe sources (different from NO2, VOC oxidation, vegetation, industrial)
- Describe importance of HCHO for ozone/PM production
- How scientists use HCHO

## Slide 13: Comparison of Working Diffuser Solar Irradiance at 30 Solar Angle
Trending solar to day 1 indicates inadequate solar azimuthal angle BTDF characterization similar to GEMS

## Slide 14: Evaluation of Working Diffuser Solar Irradiance on 8/17 (15 frames)
After accounting for variation, we verify :
  L1 Signal to Noise Ratio (SNR) calculation is correct
  We can meet the solar SNR requirement.

## Slide 15: Status Update and Plan
A new version of INR have been delivered last week, which can work very well for hourly scans to within a subpixel level.
We made the first SDPC update beyond first light changes: INR, L0-1b, O2-O2 cloud, NO2, and HCHO, and just processed 3 days of data.
  Close to document all the changes
  Need to make change request to the Change Control Board, perform additional testing and configuration management process to get it officially approved.
  Use official SDPC to process data to send to ASDC and share with the TEMPO validation and science team.
We plan to make another SDPC update (INR, L0-1b, O2-O2 cloud, NO2, and HCHO, ozone profile) before PLAR scheduled on October 18-19.

## Slide 16: Summary
TEMPO operation goes on very well, currently no major issues to prevent from nominal operation.
TEMPO first light and its NO2 images release show that the TEMPO instrument is working very well, and we have made a lot of progress in producing reasonably good L1b product and L2 data products at this early stage.
An SDPC update is being developed, waiting for approval to produce data products that can be sent to ASDC and shared with TEMPO validation and science team.

## Slide 19: Nitrogen Dioxide
Credit: NASA Scientific Visualization Studio
August 2, 2023
11:14 AM
3:24 PM
Notes: Caroline
- Mention previous studies over Houston that measured inequalities.

## Slide 20: Nitrogen Dioxide
Credit: NASA Scientific Visualization Studio
August 2, 2023
9:14 AM
1:25 PM
Notes: Caroline