## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
A New Era of Air Quality Monitoring from Space over North America with TEMPO: Mission Status from First Two Years in Orbit
Xiong Liu1, K. Chance1, C.R. Nowlan1, G. Gonzalez Abad1, R. Suleiman1, J. Houck1, J. Davis1, H. Wang1, H. Chong1, W. Hou1, J. Park1, M. Ghahremanloo1,
J. Bak1, C. Chan Miller1, J. Fitzmaurice1, L. Yatsuhashi1, A. Oppenheimer1, E. O’Sullivan1, K. Daugherty2, D.E. Flittner2, C. Fenn2, D. Rosenbaum2, C. Brown2, N. Mishra2, R.T. Neece2 , E. Roback2, J. Strickland2, L. Judd2, P. Rawat2, K. Travis2,
J. Carr3, J. Szykman4, B. Henderson4, L. Valin4, J. Joiner5, Z. Fasnacht5, S. Frith5,
D. Haffner5, E. Knowland5, N. Kramarova5, N. Krotkov5, C. Li5, W. Qin5,
G. Jaross5, C. Seftor5, A. Vasilkov5, E.-S. Yang5, J. Ziemke5, M. Newchurch6,
Naeger6, R. Cohen7, J. Geddes8, J. Herman9, B. Pierce10, R. Spurr11,
S. Kondragunta12, J. Wang13, O. Torres5, H. Zhang12, P. Ciren12,
X. Zhao14, and the TEMPO Team
1Smithsonian Astrophysical Observatory (SAO), CfA
2NASA LaRc 3Carr Astro. 4EPA 5NASA GSFC 6UAH 7UCB
8BU 9UMBC 10UWM 11RT Sol. Inc 12NOAA 13UI 14ECCC
DC Air Researchers Consortium
February 27, 2026

## Slide 2: TEMPO (Tropospheric Emissions: Monitoring of Pollution)
NASA’s first Earth Venture Instrument (EVI-1), selected in 2012
Led by Smithsonian Astrophysical Observatory (SAO) in partnership with NASA LaRC, with instrument built by Ball Aerospace (now part of BAE Systems)
NASA’s first GEO & host payload, launched on board IS-40e in April 2023 on to the GEO at 91 ∘ W
Hourly daytime air pollution over North America at neighborhood scale (2x4.75 km2 at the center of the field of regard)
Baseline products (L2):
  NO2, HCHO, Total Ozone, Ozone Profile, Clouds
Global Geo-Ring for Air Quality along with GEMS (2020) and Sentinel-4 (2025)
Credit: NASA’s Scientific Visualization Studio
TEMPO first light RGB and examples of spectra
Credit: Heesung Chong
293-494 nm
538-741 nm

## Slide 3: Geostationary Air Quality Constellation
GEMS: Launch Feb 2020
GEMS-2: Launch ~2032
Sentinel-4a: Launch 2025
Sentinel-4b: launch ~2035
Launch April 2023
Image Credit: NASA LaRC

## Slide 4: TEMPO Scanning
Nominal scans: hourly, 2.4M pixels
  2035 N/S pixels x 1181 E/W steps per hour
  2 x 4.75 km2 at center of field of regard
Optimized scans
  Higher temporal resolution scans in early AM and late PM over coasts (40 mins)
Twilights scans (science bonus & discovery)
  Performed during darkness (~Aug. 15-Apr. 15)
  City lights (lighting types), moonlights, Aurora, airglow, gas flaring, lightning, fires
Special observations to support TEMPO Green Paper & Cal/Val: 21 days in 2025 for wildfires, prescribed burning, lightning NOx, CO Front Range field campaigns, CAL/VAL
  High-frequency scans (~10 mins) over
  selected regions (alternate hourly
  scan / 1 hour high-frequency scans)
  Lunar collect (4/9/2025, 9/9/2025,
  11/3/2025, 12/10/2025, 2/3/2026)
  Railroad Valley (6/2024, 6/2025, 10/2025 (side slither)
Request Special Observations at TEMPO Early Adopter Website
Credit: Aaron Naeger
Radiance derivation  Post-processing (de-speckling, de-streaking, etc.)  Composite
Clearest-Sky City lights Composite 1–12 February 2024
Credit: Jim Carr

## Slide 5: TEMPO Timeline & Status
Successful commissioning & nominal operation. Instrument & spacecraft performing very well!
Date | Details
7 April 2023 | Launch
June-July 2023 | TEMPO power on + dry-out, cool down, etc.
2 August 2023 | First light
19 October 2023 | Nominal operations
18 June 2025 | Baseline mission ended (End-of-Prime Mission Review 12/11/2025)
September 2026 | First extended mission ends, further extension by NASA senior reviews (next in March 2026)
Credit: Heesung Chong & Dave Flittner
Very small degradation in 2 years even for short UV, correctable in future versions.

## Slide 6: TEMPO Data Products Public Release NASA’s Atmospheric Science Data Center (ASDC)
TEMPO data now publicly available at NASA’s ASDC (~6 hours latency, NRT with 2-3 hours latency).
Multiple tools (ASDC/Enabled by ASDC):
  Earthdata Search, OPeNDAP
  NASA Worldview: all data products (L2+L3)
  ArcGIS services (Earthdata & Living Atlas):
  L3 NO2 + HCHO + total ozone
  RSIG (EPA)
  TEMPO-Lite (CfA CosmicDS): L3 NO2
  NASA SPoRT Viewer
  Google Earth Engine (L3 NO2 & HCHO)
For more information check out:
  User Guides (known issues)
  Daily operation & commissioning logs
  Validation reports
  ATBD (drafts available upon request for L0-1 & O3 profile, released for total O3, cloud, NO2, & HCHO)
TEMPO V3/V4 download metrics (May 2024-December 2025)
5 PB, 170M files, >1300 unique user IPs
Worldview: >5300 unique user IPs, 6.2M records
ArcGIS Trop. NO2 (Living Atlas): >7800 unique user IPs
ASDC TEMPO
Public Release | Date | Details
V01 | 2/5/2024 | Limited 3 weeks released
V02 | 2/26/2024 | Level 1 (spectra) released
V03 | 5/20/2024 | L1, L2/3 cloud, NO2, H2CO, total O3 (provisional) V3 O3 profile (ASDC 6/9/2025, not for the public)
V04 | 9/17/2025 | Ozone Profile (beta), L1 + other L2/L3 (provisional) RADT (1/6/2026), Reprocessing started on (1/29/2026)
NRT V02 | 9/17/2025 | L1, L2/3 cloud, NO2, H2CO (funded by SNWG)

## Slide 7: Baseline TEMPO Data Products (V4)
*Beta: “minimally validated”, publication “not recommended and highly discouraged”
*Provisional: “performance demonstrated”, "suitable for scientific publication”
Level | V4 Product | Validation Status
L1 | Irradiance | Provisional
 | Radiance | Provisional
 | Radiance (twilight – city lights) | Provisional
L2 | Clouds | Provisional
 | NO2 | Provisional
 | HCHO | Provisional
 | O3 (total) | Provisional
 | O3 (profile) | Beta->Provisional in 6/2026
L3 | L2 gridded to 0.02° × 0.02° | Provisional
Work with the Validation Team and PEGASOS team to validate V4 and advance it to Full level
Reprocessing started on 1/29/2026, 2 days reprocessed in 1 day

## Slide 8: Expand Beyond TEMPO Baseline Products SNWG NRT + SNWG Enhanced + Research
Level | Product | Developer
L1 | Irradiance | SAO
 | Radiance NRT | SAO (Chong, ESS, accepted)
 | Radiance (twilight – city lights) | SAO (Carr, ESS, 2025)
L2 | Cloud NRT | SAO/GSFC (Wang, ESS, 2025)
 | NO2 NRT | SAO (Nowlan, ATBD, 2024)
 | H2CO NRT | SAO (Gonzalez Abad, ATBD,2024)
 | O3 (total) | SAO/GSFC
 | O3 (profile) | SAO
 | TEMPO/GOES-R aerosol products NRT | NOAA(released, ASDC, Zhang, JGR,2025)
 | C2H2O2 | SAO
 | H2O | SAO
 | BrO | SAO
 | SO2 NRT | NASA GSFC (Li, 2025, GRL)
 | UVAOD | NASA GSFC (under develop.)
 | Aerosol layer height | U. Iowa (under develop.)
 | UVB | NASA GSFC (under develop.)
Baseline Products
Satellite Needs Working Group (SNWG)
Cycle 3 NRT Products (~2-3 hours)
Public release (Sep. 17, 2025)
SNWG Cycle 4
TEMPO SO2 NRT & Enhanced Products
Public release in ~9/2028
Research Products
Ocean color (Fasnacht, 2025, ESS, NASA ROSES)
Vegetation (GPP) (Bandel @SSAI/NASA GSFC)
HNO2 (Theys @BIRA-IASB)
Free tropospheric NO2 (Dang, 2025, PNAS)
Surface Products (Ghahremanloo, JGR & many studies)
Emissions (Sun, JGR, Hsu, submitted @many studies)
JEDI Data Assimilation (Abdi-Oskouei, submitted)
TEMPO/GOES-R Synergy Radiance (Wang+Carr, ROSES)
Surface albedo/DLER (Zhang, JGR, NOAA)
IO, NO3, Solar induced fluorescence

## Slide 9
Algorithm Updates for TEMPO V4 (NRT V2)
GEOS-CF (meteorology / a priori): V1  V2
L1b: Improve absolute calibration (~10% overestimation in normalized radiance)
  Update BTDF by ~cos(30°) and scattering angle dependence, update to radiometric calibration coefficients based on ABI/VIIRS comparison
  Improve straylight correction (over correction in V3): improve PSF + background correction + reconstruct saturated pixels
  Improve wavelength calibration, and wavelength grid for rad. cal. coefficients
  Improve INR (geolocation)
Trace gases and clouds
  Greatly Improved GLER surface albedo climatology over land/snow (fix RAA clipping & BRDF clipping)
  NO2 / O2-O2 cloud de-striping
  Fix surface pressure anomaly (index shift by 1 in GEOS-CF surface pressure)
  Include clear-sky AMF & scattering weights for NO2/HCHO
TEMPO V3 in NASA ASDC
histogram peaks at ECF ~ 0.05,
suggesting an overestimate.
20240601 all scans
TEMPO V4*
20240601 all scans
ECF histogram peaks ~0.0, primary
due to L1b update & GLER
Histogram of Effective Cloud Fraction (ECF)

## Slide 10
Total O3: L1b improvement and
  Update LUTs with average on-orbit slit functions
  Perform additional soft calibrations using NPP OMPS data
  Quality flag updates.
Profile O3 : L1b improvement and
  Additional soft calibration
  Optimization in a priori, surface albedo, and measurement error constraint
Algorithm Updates for TEMPO V4
7/26/2024
V3: TEMPO-NPP
V4*: TEMPO-NPP
UVAI bias reduced from -2 in V3 to 0 in V4* (mostly from L1b)
Lat. depen. reduced from soft cal.
V3 soft cal.
7/26/2024
V4* soft cal.
7/26/2024
6/12/2024 S006
8/08/2024 S008
V4*: This version is subject to change before public release of V4.
Credit: Matthew Johnson
Credit: Matthew Johnson

## Slide 11: TEMPO V4 L2 Validation
Credit: Laura Judd
Los Angeles on August 22nd, 2023: Scans 9, 10
y=0.95x+2E14
r2=0.85
Median % difference: -1.7%
Median difference: -6E13
V4 shows a huge improvement over V3 in all regions measured during STAQS
r2 improved from 0.73 0.85 for all sites
0.490.62 for East Cost
GCAS
TEMPO
All GCAS data is collected within 30 minutes of the TEMPO scan
New York City on August 9th, 2023: Scans 2,3,4

## Slide 12: New TEMPO Study Published in GRL (Jin et al., 2025): Observing the Diurnal Variations of Ozone-NOx-VOC Chemistry Over the U.S. From the Geostationary TEMPO Instrument
Diurnal Variations of O3 Production Regime Derived from TEMPO
Xiaomeng Jin (xiaomeng.jin@rutgers.edu)
12

## Slide 13
TEMPO Cloud-Sliced Free Tropospheric (FT) NO2
Observations: Implications for Lightning Emissions
Ruijun Dang (rjdang@g.harvard.edu)
High observation density from TEMPO enables effective cloud slicing
Cloud Slicing to Derive Free Tropospheric (700-300 hPa) NO2
Large errors in model lightning NOx emissions: A yield of 150 mol N flash-1 appears most reasonable for NA.
First Diurnal Observation of FT NO2
New TEMPO Study published on PNAS
Dang et al., 2025

## Slide 14
TEMPO AGU Special Collection
Call for Papers
TEMPO Data Products, Science, and Applications
Submission Deadline: December 31, 2026
Currently, 28 papers submitted, 21 papers published so far!

## Slide 15: TEMPO Early Adopter Program for Science and Applications
NO2
HCHO
O3
UVAI
Boise
Boise
Boise
Boise
Cloud Fraction < 50%
Cloud Fraction < 50%
TEMPO Early Adopter program: ~650 Early Adopters including ~115 from local, state, and regional AQ agencies
TEMPO wildfire smoke monitoring in Idaho
TEMPO observed large NO2 and HCHO plumes associated with wildfires, mostly in Oregon
NO2 VCDs peaked during the afternoon with the wildfire intensity
Large HCHO VCDs were observed farther downstream from the wildfire locations
UVAI tracked the smoke transport shown by the strongly positive values tied to absorbing particles
Distinct increases in total O3 columns within the wildfire smoke plumes
Stakeholder quote “The new knowledge gained by TEMPO data will allow Idaho DEQ to document wildfire/ozone events in Exceptional Event demonstrations. We may be able to use the data to maintain situational awareness of enhanced precursors from fire and eventually improve our ozone forecasting. We have also been looking for a way to screen for ozone EE events - this may be a promising way to do it.”
Credit: Aaron Naeger

## Slide 16: Summary and Outlook
Successful commissioning & nominal operations; instrument performing very well.
Special observations capability to support TEMPO Green Paper & CAL/VAL
TEMPO at night capability provides bonus science and discovery
Successfully completed baseline mission. 1st extension to September 2026 & further extension via NASA Senior Reviews
Released significantly improved V4 data products including ozone profile and V2 NRT products on September 17, 2025.
Continue to improve data products (next version in ~2028)
Develop new data products (funded under SNWG)
Expand the wide usage of TEMPO data for science and applications
Thank you!
Acknowledgements: Funding from NASA (TEMPO, NNL13AA09C; SNWG TEMPO NRT, 80MSFC24CA004)