## Slide 1
ACAM/GCAS Measurements of NO2, CH2O, and O3 during Discover-AQ
GSFC
Scott Janz
Matt Kowalewski
Sam Xiong
Kent McCullough
Nickolay Krotkov
Lok Lamsal
SAO
Xiong Liu
Cheng Liu
Caroline Nowlan

## Slide 2: Original ACAM configuration MD and CA deployments

## Slide 3: Original ACAM configuration MD and CA deployments
Minimum Cell size
0.5km x 0.75km
Nadir Flight
Track
Scan Direction
10 steps per scan
1 Hz step rate
IFOV footprint
Spectrometers used (similar to PANDORA) sample each spatial location sequentially
6-7 km

## Slide 4
Houston/Denver Configuration [GCAS]
Short Pass
Filter
Telecentric
Foreoptics
UV/VIS
Offner
B/I
CCD
Hybrid-Wedge Depolarizer
Elphel Visible Video camera
PC/104
ADC
AD590 Support
Ethernet Switch
Wedged Housing Window
Purge Port
Purge Port
GPS Receiver
Outer Housing
Internal Environment
Dry nitrogen backfill
1 Atm
Data Connector
Power Connector
Wireless
(Bluetooth, USB)
Nadir view
GPS Antenna Feedthru
Wireless Antenna Feedthru
Custom designed 2-d spectrograph
45° instantaneous FOV. Vis/NIR not shown
VIS/NIR spectrograph not shown

## Slide 5: GCAS System Layout
Exploded view of entire assembly
UV/VIS
Telescope
VIS/NIR
Telescope
HD Video
Radiometric Calibration Fixture
Telescopes map vertical slit extent to a 6-7 km cross-track FOV at typical flight altitudes. Increases dwell time for each pixel by factor of 10 compared to previous configuration.
Camera is run at ~2Hz -> 20 images captured every 1.1 km of along-track movement.
In-field calibration fixture to track radiometric response
Spectral coverage and resolution similar to ACAM
  300-490 nm @0.2 nm/pixel
  480-890 nm @0.4 nm/pixel
System F/# the same, 7 meters/pixel GSD @8km
Nadir viewing only

## Slide 6: ACAM Spatial/Temporal Variability NO2 July 21st MD Deployment
Morning
Afternoon
0.005° x 0.005° grid of 3 km2 average, differential slant column abundance. “Clean scene” reference at cross.

## Slide 7
ACAM CH2O – July 21st
MD Deployment
1500-1630 Local
1630-1800 Local
0.005° x 0.005° grid of 3 km2 average, differential slant column abundance. “Clean scene” reference at cross. Hot spots correlate well with DFGAS integrated columns.

## Slide 8: GCAS NO2 Sept. 25th, O3 Pandora Comparisons Houston Deployment
Composite comparison with Pandora O3 overflights – all days/stations
Differential slant column abundance shows good correlation with Pandora slant column – absolute offset due to viewing different air mass.
Differential slant column abundance – example of large gradients. GCAS is 3x more sensitive than ACAM for a given spatial binning scheme.

## Slide 9: GCAS CH2O Sept. 24th Houston deployment
Morning
Afternoon
Highest levels of CH2O seen of the four deployments. Comparisons with DFGAS complicated by cloud interference.

## Slide 10
GCAS NO2 SCDs (SAO) – Houston Deployment
Preliminary results of GCAS NO2 SCDs at spatial resolution of 250 x 500 m2 show significant spatiotemporal variability.

## Slide 11: SAO ACAM Trace Gas Retrievals
July 22th Morning July 22th afternoon
11
July 20th Morning July 20th afternoon
July 20th Morning July 20th afternoon
NO2
HCHO
Perform ACAM Trace Gas Retrievals of NO2, HCHO, and total O3 columns using a two-step approach: SCDs, SCDs to VCDs.
Retrievals for the first campaign were archived at the DISCOVER-AQ data center.
Notes: 6/3/15
11

## Slide 12
Trace Gas Fitting
OMI/TEMPO trace gas fitting algorithm to derive Slant Colum Densities (SCDs, S) against average“clean” background (NO2, HCHO) or derived reference at the top of the atmosphere (for total O3)
  Basic Optical Absorption Spectroscopy (BOAS): Direct fitting of radiances using nonlinear least squares fitting (NLLS)
  NO2: 430-485 nm, average “clean” background, average fitting precision of ~6.3x1014 molecules/cm2
  HCHO: 324-357 nm, average “clean” background, average fitting precision of ~8.0x1015 molecules/cm2
  Total O3: 318-335 nm, derived TOA reference, BDM cross sections at 228 K (using 2 or more cross sections reduces residual, but increase fitting precision), fitting precision of ~3.5 DU.

## Slide 13
Air Mass Factor Calculation
    Merged ozone profile: CMAQ tropospheric O3 + OMI stratospheric O3
    Hourly CMAQ trace gas profiles (sz) of NO2 and HCHO in the troposphere and MACH stratospheric NO2 profiles
    MODIS BRDF/albedo climatology at 30 arc sec (~ 1km) derive blue sky albedo for NO2 at ~470 nm from black & white sky albedo weighted using the ratio of direct to total downwelling flux at the surface
    High-resolution MODIS albedo @470 nm scaled down to 342 nm based on ratio of coarse-resolution OMI albedo at @471 nm to that @342 nm for both HCHO and O3
    VLIDORT calculation of scattering weights wz at flight altitude weighted by CMAQ profiles to derive wavelength-dependent AMFs (Aλ)
    Weighted by cross sections to derive A for fitting window (for total O3)

## Slide 14
Convert from SCDs to VCDs
NO2 and HCHO: need to account for background reference as fitting against reference does not remove abundance above the aircraft
Derive total/tropospheric VCDs (e.g., comparison with Pandora/OMI) or VCDs below aircraft (comp. with P3B)
Approximate Vref and Vabv,ac based on CMAQ profiles and MACH stratospheric NO2, which can cause systematic biases.

## Slide 15: Comparison with PANDORA NO2
15
PANDORA total NO2 from direct-sun: high precision (~2.6E14 molecules cm-2), accuracy (~1.0E15 based on PANDORA performance inter-comparison (Tzortziou et al., 2013)
Collocation: within 3 km and 20 mins, average both data
Generally good agreement, higher correlation at stations more variability (with R > 0.86, e.g., UMBC, Essex, SERC), lower correlation at stations with less variability (e.g., Padonia, Aldino), large biases at Essex/Padonia
Notes: 6/3/15
15

## Slide 16
Generally good agreement with correlation of ~0.80 and slope of 0.98: mean biases of ~2.7E15 molecules cm-2 (1.5-4.5) and 1σ of 1.7E15 (0.9-1.6) with large biases at Essex and Padonia (3.9-4.5E15)
Comparison with PANDORA NO2
16
Notes: 6/3/15
16

## Slide 17: Comparison with P3B NO2
17
In situ P3B: column integration from spiral scaled to NO2 columns below aircraft with CMAQ profiles
Collocation: within 3 km and 30 mins, average ACAM data
Generally good correlation of ~0.81 with slope of 1.2.
Mean biases of 1.0E15 molecules cm-2 and 1σ of 2.1E15 molecules cm-2
Notes: 6/3/15
17

## Slide 18
OMI NO2 distribution agree well with ACAM NO2 considering the significant difference in spatial resolution.
Reasonably good correlation (R=0.62), with mean biases of 2.0E15 molecules cm-2 and 1σ of 1.4E15 molecules cm-2 except that OMI underestimates slope by 2/3 likely due to much larger footprints and differences in profile shapes
Comparison of ACAM and OMI NO2
18
Collocation: ±0.05° lat, ±0.20°lon, ~0.5 hr, average ACAM data
Notes: 6/3/15
18

## Slide 19: Comparison with P3B HCHO
19
In situ P3B: column integration from spiral data (~0.3 km-3 km) scaled to HCHO column below aircraft with CMAQ profiles
Collocation: within 3 km and 1 hour, average all ACAM data
P3B
ACAM
Overall, general good correlation of ~0.80.
Notes: 6/3/15
19

## Slide 20: Comparison with P3B HCHO
20
Generally good correlation of ~0.8 with slope of 1.1.
Large mean biases of ~1.0E16 molecules cm-2 and 1σ of 7.3E15 (5.2-8.5-E15) molecules cm-2
Notes: 6/3/15
20

## Slide 21: Comparison with OMI Total O3
OMTO3 V8.5: typically accurate to within 2%, negative biases of ~2% due to the use of Bass-Paur data.
Collocation: within 1° in longitude, 0.1 ° in latitude and 1 hour
Generally good agreement with a mean bias of 2.6 DU and 1σ of 4.4 DU.
21
Notes: 6/3/15
21

## Slide 22: Summary and Future Outlook
ACAM trace gases of NO2, HCHO, and total O3 for the Washington D.C.-Baltimore campaign were retrieved using a two-step approach and were archived at the DISCOVER-AQ data center.
Generally good agreement with other correlative measurements except for some large biases that need to be further investigated.
Apply the trace gas fitting algorithms to GCAS for Houston and Colorado campaigns
Optimize O3 profile retrieval algorithm from UV and UV/Visible.
Compare ACAM/GCAS retrievals between GSFC and SAO, and compare GCAS and GeoTASO retrievals, sort out the differences and improve the retrievals
22