## Slide 1
TEMPO Proxy & Operational Data Updates
Aaron Naeger & TEMPO Team
TEMPO Deputy Program Applications Lead
NASA / University of Alabama in Huntsville
May 1-5, 2023
Huntsville, AL
U.S. Government sponsorship acknowledged.
@NaegerAaron

## Slide 2
TEMPO Measurements & Baseline Products
2
TEMPO operational trace gas retrievals based on 2-step approach
  Derive slant column densities (SCD) – integrated number density of gas molecules in mean photon path from sun to instrument – by spectral fitting to measured radiances in known trace gas absorption windows
  Calculation of vertical column densities (VCD) using Air Mass Factors calculated offline with a radiative transfer model accounting for surface, atmospheric, and viewing geometry conditions
AQ relevant precision (ppb) assumes all gas molecules are contained over an area from the surface to 1 km
Vertical Column Density (VCD)
Slant Column Density (SCD)
TEMPO products will be of high accuracy and precision, particularly NO2
VCDs provide information on the trace gas in the vertical above the TEMPO footprint

## Slide 3
TEMPO L2+ Products: Baseline + SNWG TEMPO NRT
3
3
3
Level | Product | Key Variables | Resolution (km2) | Frequency/ SIze
L2 | Cloud | Cloud Fraction, Cloud Pressure | 2.0 x 4.75 | Hourly, granule
 | O3 (Ozone) profile | O3 profile, Tropospheric O3 column, Total O3 column, Stratosphere O3 column, Cloud Fraction, O3 a priori, O3 Averaging Kernel | >= 8.0 x 4.75 | Hourly, granule
 | Total O3 | Total column O3, Cloud Fraction, Aerosol Index | 2.0 x 4.75 | Hourly, granule
 | NO2 (Nitrogen Dioxide) | Slant Column Density (SCD), Tropospheric Vertical Column Density (VCD), Total VCD, Cloud Fraction, Air Mass Factor (AMF), Data Quality Flag | 2.0 x 4.75 | Hourly, granule
 | HCHO (Formaldehyde) | SCD, Total VCD, Cloud Fraction, AMF, Data Quality Flag | 2.0 x 4.75 | Hourly, granule
 | Aerosol | Ultraviolet & Visible Aerosol Optical Depth (AOD), Aerosol Optical Centroid Height (AOCH), Aerosol Absorption Index (AAI) | 8.0 x 4.75 (TBD) | Hourly, granule
L3 | Same as L2 (Gridded) | Same as L2 | ~2 x 2 (TBD) | Hourly, scan
** Center of Field of Regard
**
Level 3 product stitches together TEMPO Level 2 product granules for each scan
Near real-time (NRT) products: Latency 2 - 3 hours
Baseline (Offline) products: Latency 3 - 6 hours (except O3 profile ~24 hours)
SNWG: Satellite Needs Working Group

## Slide 4
TEMPO L2+ Products: Additional
Level | Product | Key Variables | Resolution (km2) | Frequency/ SIze
L2 | C2H2O2 (Glyoxal) | SCD, Total VCD, Cloud Fraction, AMF, Data Quality Flag | 2.0 x 4.75 | Hourly, granule
 | H2O (Water Vapor) |  | 2.0 x 4.75 | 2.0 x 4.75
 | BrO (Bromine) |  | 2.0 x 4.75 | 
 | SO2 (Sulfur Dioxide) | SCD, VCD (Total, Planetary Boundary Layer, & Lower / Middle / Upper Tropospheric, Lower Stratospheric) | 2.0 x 4.75 | Hourly, granule
 | TEMPO/GOES-R Synergistic | Aerosol, Fire / Hotspot, Cloud & Mask, Lightning, Snow / Ice, Precipitable Water, etc. | 2.0 x 4.75 | Hourly, granule
L3 | Same as L2 (Gridded) | Same as L2 | ~2 x 2 (TBD) | Hourly, scan
L4 | UVB | UV irradiance, erythemal irradiance, UVI | TBD | Hourly, scan
**
** Center of Field of Regard

## Slide 5
Mission Phases & Operational Timeline
5
5
Commissioning: July – Sept 2023
Launched: April 7, 2023
First light: Targeting June 26
TEMPO commissioning phase from July – Sept 2023
Nominal operation: ~6 months after launch (Oct 2023)
Baseline mission length: 20 months (Oct 2023 – May 2025) w/ possible 10+ year lifetime depending on senior reviews
Public release of Baseline Products at ASDC: Level 1b data ~Feb 2024, Level 2 & 3 data ~April 2024
Initial public release of NRT products at ASDC ~Oct 2024
Power On: June 6
ASDC: Atmospheric Science Data Center

## Slide 6
TEMPO Proxy Products
Level | Product | Major Outputs | Res km2 ** | Freq/Size
L2 | NO2 | SCD, strat./trop. VCD, error, AMFs, scattering weights | 2.0 x 4.75 | Hourly, granule
 | HCHO | SCD, VCD, error, AMFs, scattering weights | 2.0 x 4.75 | Hourly, granule
 | O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, a priori, averaging kernels | 8.0 x 4.75 | Hourly, granule
 | Aerosol | AAI, UVAOD, UVSSA, AOCH, VISAOD | 8.0 x 4.75 | Hourly, granule
L3 | Gridded L2 | Same as L2 | ~5 x 5 (TBD) | Hourly, scan
Green text: Available to Early Adopters and Science Team via Earthdata Search
Level 3 products will be available very soon!
** Center of Field of Regard
SCD: Slant Column Density
VCD: Vertical Column Density
AMF: Air Mass Factors
AAI: Aerosol Absorption Index
UVAOD: UV Aerosol Optical Depth
VISAOD: VIS Aerosol Optical Depth
UVSSA: UV Single Scatter Albedo
AOCH: Aerosol Optical Centroid Height
Pre-launch proxy products have been developed for the TEMPO early adopters to familiarize the community with the file format, data variables, download methods, and developing codes and tools

## Slide 7
Monitoring NO2 with TEMPO
7
TEMPO will observe rapidly varying NO2 columns within wildfire smoke plumes and across urban areas and traffic corridors.
OMI
Aug. 23, 2013
NASA Worldview
Terra MODIS
~7:40 AM
~12:50 PM
*Proxy data not intended to support operational decisions or scientific research studies
~8:40 AM
~10:40 AM
~11:40 AM
~12:40 PM
~1:40 PM
~5:40 PM
~3:40 PM
OMI NO2
TEMPO Proxy Level 2 NO2 data

## Slide 8
Multi-Pollutant Assessments with TEMPO
*Proxy data not intended to support operational decisions or scientific research studies
Worldview
28 – 31 Aug. 2013
29 Aug. 2013
Aqua MODIS
Multi-pollutant information from TEMPO will help better diagnose emission sources, pollutant transport, and health impacts
HCHO/NO2 ratios can help infer ozone sensitivity to precursors
Tropospheric NO2 VCD
Total HCHO VCD

## Slide 9
Monitoring Ozone Pollution with TEMPO
0-2 km (PBL) O3
Tropospheric O3
TEMPO instrument will be sensitive to O3 in the lower troposphere as shown by the proxy data
O3 profile will offer new capabilities to track and predict (assimilation) O3 concentrations and transport from the stratosphere to the planetary boundary layer (PBL)
Unprecedented monitoring of O3 pollution within the layer of air where people live and breathe
TEMPO O3 data will help fill the gaps in surface monitor coverage, especially the large gaps in the western region
20 July 2013 Use Case

## Slide 10
Summary of TEMPO Strengths (Non-Exhaustive)
O3 profile will offer new capabilities to monitor and distinguish ozone concentrations from the stratosphere to the planetary boundary layer (PBL)
High-resolution tracking of air pollutants during interstate and international transport, which will provide valuable information and support for exceptional event analyses
TEMPO will observe small-scale emission sources that have not been adequately resolved by current satellite missions, capability to quantify sub-urban emissions and pollutant gradients
TEMPO will monitor rapidly evolving pollutants from episodic events such as wildland fires
Diurnal information on HCHO / NO2 ratios for new understanding of sensitivity of local O3 production and assessments of O3 production regimes
Data will be valuable for surface monitor site analysis (selecting new site locations)
Robust monitoring of industrial operations, regulatory monitors may miss peak emissions!
Hourly scans for observing gaps in cloud cover, mitigate impact of clouds on satellite monitoring
Aerosol optical depth and aerosol layer height for aerosol plume monitoring and PM2.5 estimates
Low latent NO2, HCHO, and aerosol products for real-time monitoring & forecasting!

## Slide 11
Challenges Remain!
Space-borne spectrometers like TEMPO provide vertical column measurements, not nose-level concentration measurements
  Periods of persistent cloud cover will still cause gaps in TEMPO
Challenges associated with accessing, processing, and properly interpreting satellite data, especially noisy products such as HCHO and SO2
  Large increase in data volume with TEMPO
Adapting previous retrieval methods for low-earth orbiting instruments (TROPOMI) to account for new challenges associated with geostationary satellites
  Changing solar geometry throughout the day, surface reflectivity, and a priori input for retrievals
First-ever O3 PBL retrieval from space will be challenging, sensitivity to changes in O3 in the PBL will require detailed assessments
@NaegerAaron
aaron.naeger@nasa.gov