## Slide 1
TEMPO Training
Aaron Naeger & TEMPO Team
TEMPO Deputy Program Applications Lead
NASA / University of Alabama in Huntsville
May 1-5, 2023
Huntsville, AL
U.S. Government sponsorship acknowledged.
@NaegerAaron

## Slide 2
What will TEMPO measure?
TEMPO will measure the backscattered UV and visible (VIS) radiation
TEMPO retrieval algorithms use information on the absorption spectra of different trace gases in the UV & VIS bands to infer column density amounts of trace gases
Slant Column Density (SCD)
Vertical Column Density (VCD)
Land
Atmosphere
Spectral range of TEMPO
Clouds
Raw
Level 3

## Slide 3
Slant Column to Vertical Column Density
AMF converts slant columns into a vertical column (dimensionless quantity)
AMF - the relative length of mean light path at a certain wavelength for photons interacting with a certain absorber in the atmosphere relative to the vertical path
  Dependence on the vertical distribution of the trace gas, surface albedo, viewing geometry, clouds, aerosols, and the O3 column
  An increase in the light path through the atmosphere leads to an increase in AMF
Air Mass Factor (AMF)
Vertical Column Density (VCD)
Slant Column Density (SCD)

## Slide 4
How Can We Make Pre-Launch Products?
Use a Chemical Transport Model (CTM) to represent the atmosphere
Use radiative transfer calculations and known information on TEMPO instrument, sensitivities, trace gas absorption spectra, and auxiliary data to derive SCDs and VCDs
Slant Column Density (SCD)
Vertical Column Density (VCD)
Land
Spectral range of TEMPO
Model Atmosphere
Clouds
Vertical Column Density (VCD)
TEMPO Coming Soon!
Level 1
Level 3

## Slide 5
How Can We Make “Fast” Pre-Launch Products?
Use lookup tables to generate “Fast” Proxy products, rather than very “slow” computationally expensive radiative transfer calculations of the TEMPO radiance spectra
  Bypass Level 1 radiance calculations!
Slant Column Density (SCD)
Vertical Column Density (VCD)
Land
Spectral range of TEMPO
Model Atmosphere
Clouds
Vertical Column Density (VCD)
TEMPO Coming Soon!
Level 2
Level 3

## Slide 6
TEMPO “Fast” Proxy L2 Products
Proxy L2 products are being developed for the early adopter community to expand and enhance engagement activities with a diversity of stakeholders / end-users
  Files have similar format and structure as the planned operational files
Key uses of the proxy products include:
  Prepare decision support systems for immediate ingestion and application of operational TEMPO data once available after launch (e.g., prepare data assimilation systems)
  Understand best practices / methods of incorporating TEMPO products into applied (and fundamental) science studies
  Conduct qualitative assessments of how TEMPO data will enhance the application focus areas of the mission
Goal
Promote immediate and effective use of operational TEMPO data and enhance the applications value and societal benefit of the data products

## Slide 7
TEMPO Proxy Products
Level | Product | Major Outputs | Res km2 ** | Freq/Size
L2 | NO2 | SCD, strat./trop. VCD, error, AMFs, scattering weights | 2.0 x 4.75 | Hourly, granule
 | HCHO | SCD, VCD, error, AMFs, scattering weights | 2.0 x 4.75 | Hourly, granule
 | O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, a priori, averaging kernels | 8.0 x 4.75 | Hourly, granule
 | Aerosol | AAI, UVAOD, UVSSA, AOCH, VISAOD | 8.0 x 4.75 | Hourly, granule
L3 | Gridded L2 | Same as L2 | ~5 x 5 (TBD) | Hourly, scan
Green text: Available to Early Adopters and Science Team via Earthdata Search
Level 3 products will be available very soon!
** Center of Field of Regard
SCD: Slant Column Density
VCD: Vertical Column Density
AMF: Air Mass Factors
AAI: Aerosol Absorption Index
UVAOD: UV Aerosol Optical Depth
VISAOD: VIS Aerosol Optical Depth
UVSSA: UV Single Scatter Albedo
AOCH: Aerosol Optical Centroid Height

## Slide 8
“Fast” Proxy Method for NO2 & HCHO
Interpolate GEOS-NR-Chem (G5NR) model data onto TEMPO grid
Derive true SCDs from model concentration profiles and ω
AMF: Air Mass Factor
LUT: Lookup Table
SNR: Signal-to-Noise Ratio
Calculate scattering weights (ω) from LUT (function of view geometry, **surface reflectance, clouds)
Rederive SCDs and AMFs from model climatology profiles
Apply TEMPO SNR module to add noise to true SCDs & derive SCD error
Calculate VCD and errors from AMFs and true SCDs
**Surface reflectance from MODIS climatology
Output
G5NR simulation from July 2013 – June 2014

## Slide 9
Proxy Methods for Deriving Column Density
Scattering Weights (Lookup Table)
SCD (model)
Trace Gas Profile
(Model)
Fast proxy method starts from modeled trace gas concentration profile and scattering weights from lookup table to derive SCD
Scattering weights characterize the vertical measurement sensitivity to a trace gas
AMF (Climatology)
SCD (Climatology)
VCD (Climatology)
AMF (Climatology)
VCD
(Product)
SCD (Model)
Rederive SCD from climatology-based trace gas profile and scattering weights
dz
∫

## Slide 10
Wildfire Smoke - August 29, 2013
NASA Worldview
Aqua MODIS True Color imagery shows distinct smoke plumes from wildfires across western U.S.

## Slide 11
G5NR to TEMPO Grid
Interpolate G5NR fields (~12.5 x 12.5 km2) to native TEMPO pixel resolution (2 x 4.75 km2)
G5NR Grid
TEMPO Grid
G5NR Grid
TEMPO Grid

## Slide 12
Calculating SCDs
NO2 Scattering Weights
NO2 SCD
NO2 Model Profile
∫
dz

## Slide 13
Model “Truth” vs Climatology
G5NR simulation
NO2 Climatology
G5NR monthly hourly average
Notable differences between model truth and climatology associated with wildfire smoke in the western U.S.
G5NR
G5NR
NO2 Truth

## Slide 14
Model “Truth” vs Retrieval
G5NR
NO2 VCD product is different than model truth due to applying LUTs, noise, etc. in fast proxy method
NO2 VCD Product
NO2 Truth

## Slide 15
Cloud Filtering
NO2 VCD
Pre-cloud filtering
NO2 VCD
Filter NO2 pixels with cloud fraction > 0.3
Cloud Fraction

## Slide 16
Air Mass Factors
NO2 Climatology
NO2 Truth
AMF x VCD = SCD
SCD can be backed out from proxy product variables
NO2 SCD
NO2 VCD
Smaller AMFs in areas of high NO2 VCDs (e.g., cities, smoke plumes)
Proxy method does not account for influence of aerosols on AMFs!

## Slide 17
Instrument Errors
NO2 VCD Product
NO2 VCD Uncertainties
Instrument errors from TEMPO noise module reflected in VCD uncertainty

## Slide 18
NO2 and HCHO Proxy Products
Tropospheric NO2 VCD
Total HCHO VCD
Tropospheric NO2 VCD
Aug. 28 – Aug. 31
Proxy products show high NO2 and HCHO VCDs in wildfire smoke plumes
Enhanced NO2 VCDs from urban emission sources also shown

## Slide 19
Monitoring NO2 with TEMPO
19
TEMPO will observe rapidly varying NO2 columns within wildfire smoke plumes and across urban areas and traffic corridors.
OMI
Aug. 23, 2013
NASA Worldview
Terra MODIS
~7:40 AM
~12:50 PM
*Proxy data not intended to support operational decisions or scientific research studies
~8:40 AM
~10:40 AM
~11:40 AM
~12:40 PM
~1:40 PM
~5:40 PM
~3:40 PM
OMI NO2
TEMPO Proxy Level 2 NO2 data

## Slide 20
“Fast” Proxy Method for O3 profile
Interpolate G5NR model data onto TEMPO grid
Apply TEMPO SNR model to estimate instrument SNR
LUT: Lookup Table
SNR: Signal-to-Noise Ratio
Calculate radiances & weighting functions from multiwavelength LUT (function of view geometry, **surface reflectance, clouds)
Input a priori covariance matrix & TEMPO SNR into optimal estimation retrieval
Derive covariance matrix & averaging kernels from optimal estimation
Derive the retrieved O3 profile product and add random noise
**Surface reflectance from OMI climatology
Output

## Slide 21
TEMPO Proxy O3 Profile Product
O3 profile product reveals higher O3 columns in the tropospheric and 0-2 km layer, which are difficult to distinguish using the total O3 column alone
Tropospheric and 0-2 km O3 columns are particularly high over the eastern U.S.
Total O3
Tropospheric O3
0-2 km O3

## Slide 22
Model “Truth” vs Retrieval
Fast O3 proxy method introduces significant noise in the 0-2 km O3 product compared to the model truth
High O3 columns are still apparent across the east coast
Truth O3
Filtered O3 pixels with cloud fraction > 0.3
O3 profile product

## Slide 23
0-2 km O3 product
O3 profile product resolves the majority of the O3 column in the lower troposphere
  Demonstrates the sensitivity of the TEMPO instrument to the O3 pollution
TEMPO will provide new information on O3 pollution within the layer of air where people live
  Proxy product can provide early adopters an understanding of the expected information content from the operational product
Retrieved 0-2 km O3
Truth 0-2 km O3

## Slide 24
Hourly TEMPO Proxy O3 Profile
Hourly O3 profile product tracks O3 pollution in the tropospheric layer throughout the daytime
  A large area of higher O3 columns moves eastward
  Further enhancements in O3 pollution are shown over the U.S. east coast during the afternoon
0-2 km O3
Tropospheric O3

## Slide 25
“Fast” Proxy Method Overview
Advantages
Avoids need of radiative transfer model for calculating TEMPO spectra / radiances (very computationally expense!)
  Capable of generating a longer term archive of proxy TEMPO data for early adopters
Accounts for information (scattering weights, AMF, a priori profiles, averaging kernels) that characterizes the vertical sensitivity of the retrieval algorithms
Accounts for uncertainties from realistic instrument noise information
Disadvantage
Operational retrieval algorithms not applied due to bypassing radiance calculations
  Not useful for validating and optimizing TEMPO retrieval algorithms
Use of model truth data in the proxy product with coarser resolution than TEMPO can underrepresent the expected spatial information from operational TEMPO data
Realism of proxy data is ultimately dependent on model performance!

## Slide 26
Proxy Aerosol Product from EPIC data
Proxy aerosol products are developed from EPIC UV aerosol data
  Spatiotemporal interpolation to the TEMPO grid and repackaging to expected operational TEMPO aerosol file
EPIC is a good source for TEMPO proxy aerosol:
  Operational TEMPO aerosol retrievals will be similar to EPIC
  EPIC has high temporal resolution (1-2 hours)
Worldview
Sept. 16, 2020
UVAOD
AAI
UVSSA