## Slide 1
Publications
Lei et al., Retrieval of UVB aerosol extinction profiles from the ground-based Langley Mobile Ozone Lidar (LMOL) system, Atmospheric Measurement Techniques, 2022
Bernier et al.: Cluster-based characterization of multi-dimensional tropospheric ozone variability in coastal regions: an analysis of lidar measurements and model results, Atmos. Chem. Phys., 22, 15313–15331, https://doi.org/10.5194/acp-22-15313-2022, 2022. .
Torres-Vazquez, A., et al. Performance evaluation of the meteorology and air quality conditions from multiscale WRF-CMAQ simulations for the Long Island Sound Tropospheric Ozone Study (LISTOS). Journal of Geophysical Research: Atmospheres, 127, e2021JD035890, 2022
Gronoff et al., SO2 plumes observation with LMOL: Theory, Modeling, and Validation In 30th International Laser Radar Conference, Vol I. Springer International Publishing, Springer Atmospheric Sciences Series, 2023.
Zhao et al., Identification of the roles of urban plume and local chemical production in ozone episodes observed in Long Island Sound during LISTOS 2018: implications for ozone control strategies Environment International,2023, 107887, ISSN 0160-4120
Dreessen et al., (2023)VOC and trace gas measurements and ozone chemistry over the Chesapeake Bay during OWLETS-2, 2018,Journal of the Air & Waste Management Association,73:3,178-199
Berkoff et al., Langley Mobile Ozone Lidar: Instrument Updates and Results, Applied Optics (in progress)
Phoenix et al., Analysis of Atmospheric Conditions Responsible for an Ozone Exceedance Event in Southeast Virginia on June 15, 2022, Journal of Geophysical Research (in progress)
Gronoff et al., Observation of pollution events at low altitude during TRACER-AQ: the advantage of adaptive resolution lidar, AMT (in progress)
Personnel Updates
Tim Berkoff is still backfilling laser/trailer work until replacement can be identified
Randa Elhertani, Engineering Division, is providing temporary support
Langley Mobile Ozone Lidar Team Accomplishments
Tim Berkoff (PI), Guillaume Gronoff (Co-PI), Daniel Phoenix, Randa Elhertani, Claudia Bernier (NASA Fellow at U of H)
Field or Other Activities and Data Archived
1,676 hours of lidar operation in 2022 (approaching 1.0 FTE in data!)
four
Outlook
SOWLETS, SARP-E, & STAQS campaigns, new lab space, building-up sonde capability
Fully automated O3, aerosol system with SO2 capability (LaRC IRAD funded)
Experimental extreme near field testing underway (25-100 m altitude)
7 posters on display at this meeting!
Posters!
Poster!
Poster!
Posters!
Poster!
Frontal
passages
Strat O3
CF aloft,
low O3
High surface O3
Mid-level ridge
O3
streamers
(quick-look curtain)
shortwave
(also related
to strat)

## Slide 2
1Department of Earth and Atmospheric Science, University of Houston, 2NASA Langley Research Center, 3Science Systems and Application Inc., 4Global Modeling and Assimilation Office, NASA Goddard Space Flight Center, 5Goddard Earth Science Technology & Research, 6Joint Center for Earth Systems Technology, 7University of Maryland
Cluster-based characterization of multi-dimensional tropospheric ozone variability in coastal regions: an analysis of lidar measurements and model results
Background:
Coastal regions are subject to harmful ozone (O3) accumulation that are difficult to forecast due to a lack of measurements in these areas. Recent and planned NASA air quality campaigns have focused on this issue.
Method:
Developed a clustering method (left figure) based on a suite of multi-dimensional lidar O3 measurements from 3 recent air quality campaigns: OWLETS 1 & 2, LISTOS
By filtering/grouping the lidar measurements into associated clusters, we characterize coastal O3 behavior during high pollution months
Findings:
Derived lidar clusters used to evaluate the ability of two chemical transport models to simulate the distinct O3 cases (right figure b, c)
The clusters allowed us to easily highlight current model limitations e.g., both models fairly capture low-level/near surface O3 pattern and magnitude but fail to capture mid-level O3
This method can be used to understand air quality patterns for a specific region, more readily evaluate model performance, and for future work, investigate TEMPO retrievals vs. lidar and models to assess the ability of satellite retrievals (e.g., TEMPO) to monitor O3 over such complex environments
Significance:
NASA TOLNet lidar measurements provide crucial observations to better understand air quality behavior, comprehensively evaluate models, and improve satellite retrievals, resulting in forecast improvements of hazardous pollution conditions that impact human health, vegetation/agriculture, and related ecosystems.
Claudia Bernier1, Yuxuan Wang1, Guillaume Gronoff2,3, Timothy Berkoff2, K. Emma Knowland4,5, John T. Sullivan4, Ruben Delgado6,7, Vanessa Caicedo6,7, & Brian Carroll2,6
Work recently published: Bernier, C., Wang, Y., Gronoff, G., Berkoff, T., Knowland, K. E., Sullivan, J. T., Delgado, R., Caicedo, V., and Carroll, B.:, Atmos. Chem. Phys., 22, 15313–15331, https://doi.org/10.5194/acp-22-15313-2022, 2022.

## Slide 3
Analysis of Atmospheric Conditions Responsible for an Ozone Exceedance Event in Southeast Virginia on June 15, 2022
Daniel B. Phoenix1, Guillaume P. Gronoff1,2, Timothy A. Berkoff2, Daniel Salkovitz3, K. Emma Knowland4,5, John T. Sullivan4, Laurence W. Twigg4,6, Maurice Roots7, and Claudia Bernier8 1Science Systems and Applications, Inc., Hampton, VA 23666, 2NASA Langley Research Center, Hampton, VA 23666, 3Virginia Department of Environmental Quality, Richmond, VA, USA,
4NASA Goddard Space Flight Center, Greenbelt, MD, USA, 5Morgan State University, Baltimore, MD, USA, 6Science Systems and Applications, Inc., Greenbelt, MD, USA
7University of Maryland, Baltimore County, Baltimore, MD, USA, 8Department of Earth and Atmospheric Science, University of Houston, Houston, TX 77004
Background:
On June 15, 2022, the Virginia Department of Environmental Quality monitoring site at Suffolk/Holland, a rural site in southeast Virginia, recorded its first ozone exceedance since 2016. The Richmond DEQ site also recorded an ozone exceedance.
This is an unusual event because the Suffolk/Holland DEQ site is not located in an area with high vehicular traffic or local sources of primary pollutants.
NAAQS exceedance is rare for Virginia and must be addressed or risk being classified as a nonattainment area, which requires compliance to meet federal air quality standards.
TOLNet was able to assist the VA DEQ in understanding what happened and why this event occurred.
Analysis:
TOLNet lidars at Greenbelt, MD (TROPOZ, not shown) and Hampton, VA (LMOL, shown below) collected data during this period.
The lidars enable us to understand the temporal evolution of O3 that afternoon as well as evaluate the O3 representation in air quality models such as GEOS-CF.
We can use GEOS-CF and the HYSPLIT back-trajectory model to identify the source of the high O3 air.
Findings:
Model calculations reveal that much of the high O3 air in SE Virginia was transported from the I-95 traffic corridor (e.g., NYC, NJ, Philadelphia).
GEOS-CF model analysis shows air rich in O3, CO, and NOX traveling from NYC/NJ to SE Virginia. An upper-level ridge and large-scale anticyclonic circulation at the surface drives the transport.
This air mass arrives at sunrise on June 15 and quickly mixes into the PBL, contributing to the elevated O3 mixing ratios near the surface.
Significance:
NASA TOLNet lidar measurements provide crucial observations that allow us to better understand air quality behavior and comprehensively evaluate models with the goal of improving the forecasting of dangerous pollution events which can be harmful to humans, vegetation, and ecosystems.
TOLNet lidars also assist in evaluating air quality model forecast and satellite retrievals (e.g., TEMPO), and can assist state regulators for the benefit of society.
GEOS-CF (model)
LaRC (obs)
Percent Difference

## Slide 4
SOWLETS 2023 Technology Demonstration Campaign
2017, 2018: OWLETS, Ozone Water Land Environmental Transition Study
2023: SOWLETS, SO2 & Ozone Water Land Environmental Transition Study
OWLETS
SOWLETS
Background:
SOWLETS is a NASA Langley IRAD 2023 project to demonstrate a new lidar technology:
  Pulsed 4-wavelength laser for simultaneous O3, SO2, & aerosol profiles
  (Gronoff et al. poster)
Key Goal:
Intercompare lidar with O3/SO2 sonde launches operated by University of Houston & St. Edwards for validation of new SO2 lidar retrievals
Site:
NASA Langley campus (Building 1250 and/or CRAVE/CAPABLE site)
Adjacent Hampton Steam Incinerator emissions will serve as a source of SO2 and aerosol
Key Measurements:
Langley Mobile Ozone Lidar (May Test/June 2023)
Ten SO2 sonde launches (June 2023)
Pandora, Ceilometer, Wind lidar, Plume thermal imagery
Hampton University
Synergistic SARP-E SO2, aerosol, and wind measurements
LMOL lidar
SO2 sonde launch
Langley site
4-wav. laser spectrum