## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
TEMPO Products Updates
Xiong Liu1, Kelly Chance1, Raid M. Suleiman1, Kevin J. Daugherty2,
David E. Flittner2, John Houck1, John E. Davis1,
Gonzalo Gonzalez Abad1, Caroline Nowlan1, Huiqun Wang1,
Chistopher Chan Miller1,3, Juseon Bak4, Hyeong-Ahn Kwon1,5,
Jim Carr6, Weizhen Hou1, Hee-sung Chong1, Mike Newchurch7,
Jim Szykman8, Aaron Naeger7, The TEMPO Team
1CfA | Harvard & Smithsonian 2NASA LaRc
3Harvard University 4Pusan National University
5U. Suwon, 6Carr Astronautics 7UAH 8EPA
xliu@cfa.harvard.edu
TEMPO Science Team Meeting
Huntsville, AL
May 2, 2023

## Slide 2: Outline
Data Products (Enhanced & Research Data Products)
Algorithm Development Status
Test TEMPO algorithms with GEMS
Science Verification & Validation

## Slide 3: Baseline and Threshold Products (Variables) & Requirements
Species/Products | Required Precision | Temporal Revisit*
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
Aerosols, SO2, C2H2O2 were removed from baseline products during KDPC
Cloud product (cloud fraction, cloud pressure): used in trace gas/aerosol retrievals
* # of hourly measurements to be averaged to achieve required precision
Mission duration: 20 months for baseline, 12 months for threshold
Spatial resolution: < 60 km2 for baseline (4 native pixels coadded), < 300 km2 for threshold

## Slide 4: TEMPO Data Products Baseline + SNWG 2020 NRT + SNWG 2022 NRT/Enhanced
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted digital counts |  | 2.0 x 4.75 | Daily/hourly
L1-b | Irradiance NRT | SAO L0-1 | Calibrated & quality flags |  |  | daily
 | Radiance NRT | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule
L2 | Cloud NRT | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | Climatology + GEOS-CF | >= 8.0 x 4.75** | Hourly, granule
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule
 | NO2 NRT | SAO trace gas, BU strat/trop sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | HCHO NRT | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | C2H2O2 | SAO trace gas |  | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | H2O | SAO trace gas |  | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | BrO | SAO trace gas |  | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | Aerosol NOAA NRT | OMAERUV/UI AOCH | AAI, UVAOD, UVSSA, AOCH, VISAOD |  | 8.0 x 4.75 | Hourly, granule
 | SO2 NRT | OMSO2 PCA | SCD, VCD (PBL,TRL,TRM,TRU,STL) |  | 2.0 x 4.75 | Hourly, granule
 | UVB | GEMS/GSFC UVB | UV irradiance, erythemal irradiance, UVI |  | 2.0 x 4.75 | Hourly, scan
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 2 x 2 (?) | Hourly, scan
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
Satellite Needs Working Group (SNWG) will fund TEMPO NRT products (L2 products < 3 hours from observation time): 6/1/2023-5/30/2025
SNWG 2022 Survey has selected to produce TEMPO NRT/Enhanced Productions starting in 2025

## Slide 5: Research Products
TEMPO research products will greatly extend science and applications
  OClO, IO, HNO2, NO3, volcanic (SO2 plume height and Vertical Column Density)
  Additional/improved cloud with O2-O2 bands / O2 B band
  Additional aerosol products from hyperspectral spectra, O2 B and O2-O2-bands, and TEMPO + GOES-R synergy at @U Iowa, NOAA, GSFC
  Vegetation/Ocean Color products: vegetation indices, Growth Primary Productivity (GPP), Solar Induced Fluorescence (SIF), ocean color
  Surface albedo/Bidirectional Reflectance Distribution Function (BRDF) products
  Diurnal out-going shortwave radiation and cloud forcing
  Night lights: allows discrimination between lighting types
  Higher-level products: Near-real-time pollution/Air Quality indices

## Slide 6: Algorithm Development Status
Launch-ready Science Data Processing Center (SDPC) V4 software completed in Feb 2022
Algorithm mostly based on OMI heritage algorithms except for new L0-1b processor including Imagination Navigation and Registration (INR) using GOES-R by Carr Astronautics
L1-2 algorithms updates (O3 profile, total O3, NO2, HCHO, cloud) include:
  Add visible spectrum to UV O3 profile algorithm
  SAO trace gas algorithm with adapted NASA stratospheric/tropospheric separation for NO2
  New CLDO4: SAO O2-O2 fitting + GSFC’s O2-O2 cloud at ~477/466 nm (H. Wang, E.-S. Yang, A. Vasilkov)
  NASA GMAO’s GEOS-CF trace gas profiles and meteorology (E. Knowland and GMAO)
  Hourly resolved monthly mean Geometry-dependent Lambertian Equivalent Reflectivity (GLER) climatology (C. Chan Miller, W. Qin, Z. Fasnacht)
Development of non-baseline products
  CHOCHO, H2O, BrO: will use SAO’s trace gas algorithm
  SO2: OMI PCA SO2 algorithm adapted for TEMPO/GEMS from synthetic/GEMS data (Can Li)
  Aerosols: being adapted from OMI/TROPOMI AERUV algorithm (Omar’s team), from EPIC/TROPOMI Aerosol Layer Height algorithm using O2-A/B (Jun Wang’s team, funded by NASA Applied Science Program)

## Slide 7: Test TEMPO-like O3PROF Algorithm with OMI/TOPOMI/GEMS Data
Comparison of tropospheric ozone column (950-300 hPa) from several products over the GEMS domain on August 1, 2022 including TEMPO-like algorithm OMPROFOZ V2 applied to OMI, and S5p-TROPOMI, and GEMS
Apply TEMPO algorithm (OMPROFOZ v2, UV only) to GEMS data without soft calibration (BTDF correction via wavelength calibration) works reasonably well. Cross-track stripes can be seen.
OMI-PROFOZ
3 days-mean
Daily S5P-PROFOZ
GEMS-PROFOZ
04:45 UTC
Credit: Juseon Bak

## Slide 8: Test TEMPO NO2 Algorithm with GEMS Data
NO2 Slant Column Densities (SCDs) observed by GEMS (V1) on June 1, 2021 at 6:45 UTC are similar to SAO TEMPO NO2 SCDs from the same GEMS data except for some known positive biases in the GEMS V1 operational retrievals.
GEMS
SAO MEASURES/TEMPO
GEMS
GEMS-MEASURES
Credit: Hyeong-Ahn Kwon

## Slide 9: Test TEMPO HCHO Algorithm with GEMS Data
SAO’s GEMS formaldehyde retrievals on June 1, 2021 at 6:45 UTC, compare quite well with GEMS V2 retrievals
GEMS
SAO MEASURES
GEMS - MEASURES
GEMS V2 vs. SAO
HCHO SCDs
Credit: Hyeong-Ahn Kwon

## Slide 10: Calibration and L1b Validation
Verify and update image correction steps in the L0-1 processing during Commissioning Phase (~L+1~L+3 months, ~90 days)
  System linearity, zero-input, relative gains, saturation blooming, dark current variation and temperature-dependent correction, check quality flags, evolution of solar diffuser, noise calculation, straylight
Assess wavelength calibration and its performance
  Will assess performance of routine processing (wavelength calibration in both L0-1b & L1-2 via high-resolution solar reference and atmospheric absorption)
  Pre-launch measured instrument line shape will be compared with that derived from solar irradiance
Assess radiometric calibration using a multi-pronged approach
  Internal assessment of images, Assess performance of routine processing
  Comparison solar irradiance with solar reference and correlative contemporaneous sensors (e.g., OMPS, TROPOMI, GOME-2, EPIC, MODIS, VIIRS)
  Comparison with radiative transfer simulation
Assess geo-location methodology with Image Navigation and Registration (INR) during commissioning phase, accuracy and uncertainty
  Imagery: assess registration offset of fiducial points not used in INR, using other reference imagery
  L2: assess bias and variance in registration offset of known point sources of NO2

## Slide 11: TEMPO L2 Science Validation Plan
TEMPO PLRA has a bare minimum validation requirements (3 Pandoras, 1 month per season)
Jim Szykman has led the development of best-efforts basis validation plan: beta, provisional, full
Use satellite observations (i.e., LEO and EPIC/DSCOVR) for cross validations
Pandora & Pandonia Global Network (PGN): validate NO2, HCHO, total O3 and diurnal variation
TOLNet: 8 LIDAR instruments by time of launch to validate tropospheric O3 & 0-2 km O3 and diurnal variation
Airborne instruments: GEO-TASO, GCAS, HSRL-2, IAGOS, SeaRey UAV
Other instruments: ozonesonde, Dobson/Brewer, MAXDOAS, FTIR, AERONET, …
Planned flight campaigns AGES+ (e.g., STAQS, AEROMMA+CUPiDS, GOTHAAM) during June-Aug 2003, provide integrated approaches linking TEMPO science, applications, and validation
Indirect evaluation with chemistry transport models and data assimilation.
www-air.larc.nasa.gov/missions/TOLNet/
Nowlan et al. (2018) GCAS, DISCOVER-AQ, Texas, Sep 2013
https://www.pandonia-global-network.org/
~60 PGNs in TEMPO FoR, ~20 to add in 2 years

## Slide 12: Summary
Launch-ready SDPC software has been developed to produce baseline products meeting PLRA. Several major updates (new O2-O2 cloud, GEOS-CF, GLER) have been developed to significantly improve over heritage algorithms.
Applying our TEMPO algorithms to GEMS data agree quite well with operational GEMS products.
Post-launch science verification and validation activities have been planned to validate and improve the data products

## Slide 16: TEMPO Data Products Distribution
NASA Earthdata Search
  CMR Search ⚬ Metadata
NASA WorldView
  GIBS API ⚬ visualization
Harmony and OPeNDAP
  ⚬ transform ⚬ subsetting
  ⚬ reformatting ⚬ distribution
HTTPS data access
  ⚬ datapool
  ⚬ permanent URL/direct access
  ⚬ enables scripts/workflow
Geospatial Web Services
  ⚬ WCS ⚬ WMS ⚬ ArcGIS Image Service
Example scripts
  ⚬ Python/Jupyter Notebook
  ⚬ R scripts
  ⚬ contributed tutorials/scripts
ASDC Data Archival & Distribution: Tools and Services
Earthdata Login https://urs.earthdata.nasa.gov
Earthdata Forum https://forum.earthdata.nasa.gov/
ASDC User Support support-asdc@earthdata.nasa.gov
User Support and Other Resources
TEMPO data can be served directly through the EPA RSIG. https://www.epa.gov/hesc/remote-sensing-information-gateway
EPA RSIG3D Gateway
Slides from Jeff Walters, Tim Larson at TEMPO STM 2020 & EAWNov2021

## Slide 17: TEMPO Green Paper: Chemistry Experiments with TEMPO
NORMAL TIME RESOLUTION STUDIES | Volcanoes
Air quality and health | Socio-economic studies
Ultraviolet exposure | National pollution inventories
Biomass burning | Regional and local transport of pollutants
Synergistic GOES-16/17 Products | Sea breeze studies for Florida and Cuba
Advanced aerosol products | Transboundary pollution gradients
Soil NOx after fertilizer application and after rainfall | Transatlantic dust transport
Solar-induced fluorescence from chlorophyll | HIGH TIME RESOLUTION EXPERIMENTS
Foliage studies | Lightning NOx
Mapping NO2 and SO2 dry deposition at high resolution | Morning and evening higher-frequency scans
Crop and forest damage from ground-level ozone | Dwell-time studies and temporal selection to improve detection limits
Halogen oxide studies in coastal and lake regions | Exploring the value of TEMPO in assessing pollution transport during upslope flows
Air pollution from oil and gas fields | Tidal effects on estuarine circulation and outflow plumes
Night light measurements resolving lighting type | Air quality responses to sudden changes in emissions
Ship tracks, drilling platform plumes, and other concentrated sources. | Cloud field correlation with pollution
Water vapor studies | Agricultural soil NOx emissions and air quality
The TEMPO Green Paper living document at http://tempo.si.edu/publications.html
Early Adopters are key to building the TEMPO Green Paper!
High-time special observations can be requested at:
https://weather.msfc.nasa.gov/tempo/green_paper.html

## Slide 18: Including Visible to Improve Tropospheric Ozone Retrieval Sensitivity
This example is for solar zenith angle =25, viewing zenith angle 45, relative azimuthal angle 86, Signal to noise Ratio (SNR) with 4 pixels coadded
Add visible to improve retrieval sensitivity in the lower troposphere and help separate free tropospheric O3 from boundary layer O3
Under ideal conditions: 3-5 total Degree of Freedom for Signal (DFS) with up to ~1.5 in the troposphere, and up to ~0.5 DFS in 0-2 km
Adapted from OMI (Liu et al., 2010): Spectral fitting + VLIDORT + Optimal Estimation (OE) from Fitting windows: 293-345 nm, 540-650 nm
Retrieve partial O3 columns at ~24 layers (bottom layer is 0-2 km above the surface) as well as total, stratospheric, and tropospheric O3 columns, other trace gases, and auxiliary parameters.
A priori: a combination of tropopause-based climatology (Bak et al., 2013) with diurnally-resolved GEOS-CF data

## Slide 19: TEMPO Algorithm Teams
Operational Algorithm | Personnel
Raw to L0 | John Davis
L0-1b | John Houck, Xiong Liu, Dave Flittner, Weizhen Hou, Jim Carr, Chris Chan Miller
Ozone profile | Xiong Liu, Juseon Bak, Weizhen Hou
Total ozone | Dave Haffner, Joanna Joiner
Nitrogen dioxide | Caroline Nowlan, Gonzalo González Abad, Jeff Geddes, Chris Chan Miller
Formaldehyde | Gonzalo González Abad, Caroline Nowlan, Hyeong-Ahn Kwon, Chris Chan Miller
Glyoxal | Gonzalo González Abad, Hyeong-Ahn Kwon, Chris Chan Miller
Clouds | Huiqun Wang, Alexander Vasilkov, Eun-Su Yang, Joanna Joiner
Sulfur dioxide | Can Li, Nicolay Krotkov
Aerosols | Omar Torres, Jun Wang
Operational implementation and IT support @ SAO Science Data Processing Center (SDPC) by John Houck | 

## Slide 20: NRT vs. Off-line Trace Gas Products (if with additional NRT funding)
Implementing both NRT and off-line trace gas products (e.g., NO2, HCHO) for NO2, HCHO, aerosol, SO2, cloud
Major potential differences between NRT and offline
 | NRT | Off-line
Trace gas profiles/Met data | GEOS-CF | GEOS-CF Replay
Surface | GLER climatology | MODIS/VIIRS albedo/BRDF products
L1B | Skip wavelength calibration One-pass INR Default/No Pol. Correction | Two-pass Kalman Filter INR Improved pol. Correction with L2 retrievals?
L2 algorithms | Smaller fitting windows Avoid waiting for the entire hourly scan | More optimized fitting windows Improve radiance reference & cross-track correction
Data Latency | Within 2-3 hours upon receipt of raw data at SAO Ground System | + 8 days as MODIS BRDF is produced using data +/- 8 days

## Slide 21: L1b Requirements
Table of SNR req. and with Beginning of Life (BOL) as-built performance (4 Pixels coadded)
Radiometric Uncertainty: < 4% (1-sigma) for both irradiance & radiance
Albedo uncertainty: wavelength independent < 2%, dependent < 1%
Long-term (20 months) radiometric drift detection: < 0.9%
Nonlinearity: <2% of 98% well response, and knowledge (after corr.) < 0.5% from 2-98% of well response
Pre-launch Wavelength mapping uncertainty: < 0.02 nm
Spectral stability (within 24 hours): < 0.1 nm for radiance & irradiance
Spectral co-registration error: < 0.7 pixel between 2 bands, < 0.4 pixel within UV or visible bands
L1b products: Spectral Radiance, Irradiance and Uncertainty, Spectral Scale, Geo-location (lat/lon)
PLRA: no requirement for radiance or irradiance, geolocation accuracy < 4km
Instrument design & performance requirements were derived from L2 precision req.
Signal to Noise Ratio (SNR) was the dominate factor for radiance performance

## Slide 22: Test TEMPO Trace Gas Algorithms with GEMS Data
Comparison of GEMS HCHO Air Mass Factors (AMFs) with SAO calculated GEMS AMFs on June 1, 2021 at 6:45 UTC. Differences arise from using different a-priori profiles, and surface reflectance properties.
Credit: Hyeong-Ahn Kwon