## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
TEMPO Science Overview
Xiong Liu1, Kelly Chance1, Raid M. Suleiman1, Kevin J. Daugherty2,
David E. Flittner2, John Houck1, John E. Davis1,
Gonzalo Gonzalez Abad1, Caroline Nowlan1, Huiqun Wang1,
Chistopher Chan Miller1,3, Juseon Bak4, Hyeong-Ahn Kwon1,5,
Jim Carr6, Weizhen Hou1, Hee-sung Chong1, Mike Newchurch7,
Jim Szykman8, Aaron Naeger7, The TEMPO Team
1CfA | Harvard & Smithsonian 2NASA LaRc
3Harvard University 4Pusan National University
5U. Suwon, 6Carr Astronautics 7UAH 8EPA
xliu@cfa.harvard.edu
TEMPO Science Team Meeting
Huntsville, AL
May 2, 2023

## Slide 2: Outline
Science Overview
Measurement Requirements
Data Products (Baseline + SNWG NRT Solution)
Commissioning timeline, Distribution, and Data Release Plan

## Slide 3: Hourly daytime atmospheric pollution over North America from the GEO
NASA’s first Earth Venture Instrument (EVI) selected in 2012 & first hosted payload
PI: Kelly Chance, Smithsonian Astrophysical Observatory (SAO): Science team, ground systems, science data processing center
Instrument Development: Ball Aerospace
Instrument Project Management: Kevin Daugherty, NASA LaRC
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, UAH, U Iowa, Sitting Bull College, RT Solutions, Carr Astronautics
International collaboration: Mexico, Canada, Cuba, Korea, U.K., ESA, Spain
Mission Project Management: Kevin Daugherty, NASA LaRC
Host Satellite Provider: Maxar Technologies
Satellite Host: Intelsat (IS-40e)
Launch: SpaceX
Provides hourly daylight observations to capture rapidly varying emissions and chemistry important for air quality
  UV/visible grating spectrometer to measure key elements in tropospheric ozone and aerosol pollution
  Distinguishes boundary layer from free tropospheric & stratospheric ozone
Aligned with Earth Science 2007 Decadal Survey recommendations
  Makes many of the GEO-CAPE atmospheric measurements
  Responds to the phased implementation recommendation of GEO-CAPE mission design team

## Slide 4: North American Component of an International Geostationary Air Quality Constellation
Launched Feb 2020
Launch late 2024
Launched April 2023
Image Credit: NASA LaRC

## Slide 5: TEMPO Science Questions
What are the temporal and spatial variations of emissions of gases and aerosols important for air quality and climate?
How do physical, chemical, and dynamical processes determine tropospheric composition and air quality over scales ranging from urban to continental, diurnally to seasonally?
How does air pollution drive climate forcing and how does climate change affect air quality on a continental scale?
How can observations from space improve air quality forecasts and assessments for societal benefit?
How does intercontinental transport affect air quality?
How do episodic events, such as wildfires, dust outbreaks, and volcanic eruptions, affect atmospheric composition and air quality?

## Slide 6: TEMPO Instrument
Imaging grating spectrometer measuring solar irradiance and solar backscattered Earth radiance
  2 channels (1 focal plane but with 2 2-D 2 k 1k detectors ): ~293-494 + 538-741 nm
  ~0.6 nm FWHM, ~0.2 nm sampling
~293-494 nm
~538-741 nm
Examples of spectra based on GOME

## Slide 7: TEMPO Operation
Nominal: Scan Field of Regard (FOR) in 1 hour with 10 granules
  ~ 2K N/S pixels 1226 steps/hr, ~ 2.5 M pixels/hr, daily # spatial pixels ~TROPOMI
  2 4.75 km2 @center of FOR, from 8 km2 at Mexico City to 21 km2 at Canadian Tar Sands
  FOR: N/S +/-210 pixels, E/W +230/160 pixels
Optimized scan: in the early morning and late afternoon, daylight portion of FOR, higher temporal resolution
High-time scan (up to 25%): selected portion of FOR at higher temporal resolution (e.g., <= 10 mins)
Field of regard is optimized to cover both Puerto Rico and Canadian tar sands.
S5p-TROPOMI NO2 product oversampled by Kang Sun.
  Operate on geostationary communications satellite Intelsat 40e (IS-40e) at 91 ∘ W

## Slide 8: Baseline and Threshold Products (Variables) & Requirements
Species/Products | Required Precision | Temporal Revisit*
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
Aerosols, SO2, C2H2O2 were removed from baseline products during KDPC
Cloud product (cloud fraction, cloud pressure): used in trace gas/aerosol retrievals
* # of hourly measurements to be averaged to achieve required precision
Mission duration: 20 months for baseline, 12 months for threshold
Spatial resolution: < 60 km2 for baseline (4 native pixels coadded), < 300 km2 for threshold

## Slide 9: TEMPO Data Products
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted digital counts |  | 2.0 x 4.75 | Daily/hourly
L1-b | Irradiance | SAO L0-1 | Calibrated & quality flags |  |  | daily
 | Radiance | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule
L2 | Cloud | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | Climatology+GEOS-CF | >= 8.0 x 4.75** | Hourly, granule
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule
 | NO2 | SAO trace gas, BU strat./trop. sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | HCHO | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 2 x 2 (?) | Hourly, scan
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
Launch-ready SDPC software has been developed to produce baseline products meeting PLRA

## Slide 10: TEMPO Data Products Baseline + SNWG TEMPO NRT
Level | Product | Algorithm | Major Outputs | A Priori (L2) | Res km2 * | Freq/Size
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted digital counts |  | 2.0 x 4.75 | Daily/hourly
L1-b | Irradiance NRT | SAO L0-1 | Calibrated & quality flags |  |  | daily
 | Radiance NRT | SAO L0-1 | Geolocated, calibrated, viewing, geolocation & quality flags |  | 2.0 x 4.75 | Hourly, granule
L2 | Cloud NRT | OMI O2-O2 | Cloud fraction, cloud pressure | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | Climatology+GEOS-CF | >= 8.0 x 4.75** | Hourly, granule
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | Climatology | 2.0 x 4.75 | Hourly, granule
 | NO2 NRT | SAO trace gas, BU strat./trop. sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
 | HCHO NRT | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | GEOS-CF | 2.0 x 4.75 | Hourly, granule
L3 | Gridded L2 | SAO L2-3 | Same as L2 |  | 2 x 2 (?) | Hourly, scan
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
Satellite Needs Working Group (SNWG) will fund TEMPO NRT products (L2 products < 3 hours from observation time): 6/1/2023-5/30/2025, NOAA to produce NRT aerosol products

## Slide 11: Commissioning Timeline, Distribution, and Data Release Plan
Launch
TEMPO
Power On
First Light
TEMPO Commissioning
S/C Activity (TEMPO Off)
Activation
Outgassing
Instrument Characterization and Analysis
PLAR
Nominal Operations
L+60 days (6/6/23)
L+110 days (7/26/23)
L+178 days
(10/2/23)
L+0 (4/7/23)
*Dates are as of 4/25/23 and are subject to change
Nominal operation after Post Launch Acceptance Review (PLAR): ~10/2023
Baseline mission (Phase E, 20 months, 10/2023-5/2025), NASA senior/extension review
Data products sent to ASDC for archival and distribution
Plan for initial public release of baseline products at ASDC after algorithm verification, product validation, algorithm optimization/improvement: L1b, 2/2024; L2/3, 4/2024
Provide earlier access to validation team prior to the public release
Initial public release of NRT products at ASDC (~6 mos behind baseline products): ~10/2024

## Slide 12: Summary
TEMPO will provide revolutionary hourly daytime atmospheric pollution measurements at high spatial resolution over North America from the GEO via UV/visible imaging grating spectroscopic measurement technique
Launch-ready SDPC software has been developed to produce baseline products meeting PLRA. We were funded by SNWG to produce NRT products for L1b, cloud, NO2, and HCHO products.
After 4 months of TEMPO commissioning and PLAR, nominal operation starts in 10/2023, kicking off a 20-month baseline mission. Baseline L2 products is planned to be released to the public from ASDC in ~1 year after launch.

## Slide 16: Why geostationary? High temporal and spatial resolution
Hourly NO2 surface concentration and integrated column calculated by CMAQ air quality model: Houston, TX, June 22-23, 2005
June 22
Hour of Day (UTC)
June 23
LEO observations provide limited information on rapidly varying emissions, chemistry, & transport
GEO will provide observations at temporal and spatial scales highly relevant to air quality processes

## Slide 17
TEMPO Requirements and Science Questions are leveraged from the GEO-CAPE Science Traceability Matrix

## Slide 18: TEMPO Science Traceability Matrix

## Slide 19: TEMPO Data Products Distribution
NASA Earthdata Search
  CMR Search ⚬ Metadata
NASA WorldView
  GIBS API ⚬ visualization
Harmony and OPeNDAP
  ⚬ transform ⚬ subsetting
  ⚬ reformatting ⚬ distribution
HTTPS data access
  ⚬ datapool
  ⚬ permanent URL/direct access
  ⚬ enables scripts/workflow
Geospatial Web Services
  ⚬ WCS ⚬ WMS ⚬ ArcGIS Image Service
Example scripts
  ⚬ Python/Jupyter Notebook
  ⚬ R scripts
  ⚬ contributed tutorials/scripts
ASDC Data Archival & Distribution: Tools and Services
Earthdata Login https://urs.earthdata.nasa.gov
Earthdata Forum https://forum.earthdata.nasa.gov/
ASDC User Support support-asdc@earthdata.nasa.gov
User Support and Other Resources
TEMPO data can be served directly through the EPA RSIG. https://www.epa.gov/hesc/remote-sensing-information-gateway
EPA RSIG3D Gateway
Slides from Jeff Walters, Tim Larson at TEMPO STM 2020 & EAWNov2021

## Slide 20: TEMPO Green Paper: Chemistry Experiments with TEMPO
NORMAL TIME RESOLUTION STUDIES | Volcanoes
Air quality and health | Socio-economic studies
Ultraviolet exposure | National pollution inventories
Biomass burning | Regional and local transport of pollutants
Synergistic GOES-16/17 Products | Sea breeze studies for Florida and Cuba
Advanced aerosol products | Transboundary pollution gradients
Soil NOx after fertilizer application and after rainfall | Transatlantic dust transport
Solar-induced fluorescence from chlorophyll | HIGH TIME RESOLUTION EXPERIMENTS
Foliage studies | Lightning NOx
Mapping NO2 and SO2 dry deposition at high resolution | Morning and evening higher-frequency scans
Crop and forest damage from ground-level ozone | Dwell-time studies and temporal selection to improve detection limits
Halogen oxide studies in coastal and lake regions | Exploring the value of TEMPO in assessing pollution transport during upslope flows
Air pollution from oil and gas fields | Tidal effects on estuarine circulation and outflow plumes
Night light measurements resolving lighting type | Air quality responses to sudden changes in emissions
Ship tracks, drilling platform plumes, and other concentrated sources. | Cloud field correlation with pollution
Water vapor studies | Agricultural soil NOx emissions and air quality
The TEMPO Green Paper living document at http://tempo.si.edu/publications.html
Early Adopters are key to building the TEMPO Green Paper!
High-time special observations can be requested at:
https://weather.msfc.nasa.gov/tempo/green_paper.html

## Slide 21: Including Visible to Improve Tropospheric Ozone Retrieval Sensitivity
This example is for solar zenith angle =25, viewing zenith angle 45, relative azimuthal angle 86, Signal to noise Ratio (SNR) with 4 pixels coadded
Add visible to improve retrieval sensitivity in the lower troposphere and help separate free tropospheric O3 from boundary layer O3
Under ideal conditions: 3-5 total Degree of Freedom for Signal (DFS) with up to ~1.5 in the troposphere, and up to ~0.5 DFS in 0-2 km
Adapted from OMI (Liu et al., 2010): Spectral fitting + VLIDORT + Optimal Estimation (OE) from Fitting windows: 293-345 nm, 540-650 nm
Retrieve partial O3 columns at ~24 layers (bottom layer is 0-2 km above the surface) as well as total, stratospheric, and tropospheric O3 columns, other trace gases, and auxiliary parameters.
A priori: a combination of tropopause-based climatology (Bak et al., 2013) with diurnally-resolved GEOS-CF data

## Slide 22: TEMPO Science Team, U.S.
Team Member | Institution | Role | Responsibility
K. Chance | SAO | PI | Overall science development; Level 1b, H2CO, C2H2O2
X. Liu | SAO | Deputy PI | Science development, data processing; O3 profile, tropospheric O3
J. Al-Saadi | LaRC | Deputy PS | Project science development
J. Carr | Carr Astronautics | Co-I | INR Modeling and algorithm
M. Chin | GSFC | Co-I | Aerosol science
R. Cohen | U.C. Berkeley | Co-I | NO2 validation, atmospheric chemistry modeling, process studies
D. Edwards | NCAR | Co-I | VOC science, synergy with carbon monoxide measurements
J. Fishman | St. Louis U. | Co-I | AQ impact on agriculture and the biosphere
D. Flittner | LaRC | Project Scientist | Overall project development; STM; instrument cal./char.
J. Herman | UMBC | Co-I | Validation (PANDORA measurements)
D. Jacob | Harvard | Co-I | Science requirements, atmospheric modeling, process studies
S. Janz | GSFC | Co-I | Instrument calibration and characterization
J. Joiner | GSFC | Co-I | Cloud, total O3, TOA shortwave flux research product
N. Krotkov | GSFC | Co-I | NO2, SO2, UVB
M. Newchurch | U. Alabama Huntsville | Co-I | Validation (O3 sondes, O3 lidar)
R.B. Pierce | NOAA/NESDIS | Co-I | AQ modeling, data assimilation
R. Spurr | RT Solutions, Inc. | Co-I | Radiative transfer modeling for algorithm development
R. Suleiman | SAO | Co-I, Data Mgr. | Managing science data processing, BrO, H2O, and L3 products
J. Szykman | EPA | Co-I | AIRNow AQI development, validation (PANDORA measurements)
O. Torres | GSFC | Co-I | UV aerosol product, AI
J. Wang | U. Nebraska | Co-I | Synergy w/GOES-R ABI, aerosol research products
J. Leitch | Ball Aerospace | Collaborator | Aircraft validation, instrument calibration and characterization
D. Neil | LaRC | Collaborator | GEO-CAPE mission design team member

## Slide 23: TEMPO Science Team, non-U.S.
Team Member | Institution | Role | Responsibility
R. Martin | Dalhousie U. | Collaborator | Atmospheric modeling, air mass factors, AQI development
Chris McLinden | Environment Canada | Collaborator | Canadian air quality coordination
Michel Grutter de la Mora | UNAM, Mexico | Collaborator | Mexican air quality coordination
Gabriel Vazquez | UNAM, Mexico | Collaborator | Mexican air quality, algorithm physics
Amparo Martinez | INECC, Mexico | Collaborator | Mexican environmental pollution and health
J. Victor Hugo Paramo Figeuroa | INECC, Mexico | Collaborator | Mexican environmental pollution and health
Brian Kerridge | Rutherford Appleton Laboratory, UK | Collaborator | Ozone profiling studies, algorithm development
Paul Palmer | Edinburgh U., UK | Collaborator | Atmospheric modeling, process studies
J. Kim | Yonsei U. | Collaborators, Science Advisory Panel | Korean GEMS, CEOS constellation of GEO pollution monitoring
C.T. McElroy | York U. Canada |  | CSA PHEOS, CEOS constellation of GEO pollution monitoring
B. Veihelmann | ESA |  | ESA Sentinel-4, CEOS constellation of GEO pollution monitoring

## Slide 24: TEMPO Algorithm Teams
Operational Algorithm | Personnel
Raw to L0 | John Davis
L0-1b | John Houck, Xiong Liu, Dave Flittner, Weizhen Hou, Jim Carr, Chris Chan Miller
Ozone profile | Xiong Liu, Juseon Bak, Weizhen Hou
Total ozone | Dave Haffner, Joanna Joiner
Nitrogen dioxide | Caroline Nowlan, Gonzalo González Abad, Jeff Geddes, Chris Chan Miller
Formaldehyde | Gonzalo González Abad, Caroline Nowlan, Hyeong-Ahn Kwon, Chris Chan Miller
Glyoxal | Gonzalo González Abad, Hyeong-Ahn Kwon, Chris Chan Miller
Clouds | Huiqun Wang, Alexander Vasilkov, Eun-Su Yang, Joanna Joiner
Sulfur dioxide | Can Li, Nicolay Krotkov
Aerosols | Omar Torres, Jun Wang
Operational implementation and IT support @ SAO Science Data Processing Center (SDPC) by John Houck | 

## Slide 25: NRT vs. Off-line Trace Gas Products (if with additional NRT funding)
Implementing both NRT and off-line trace gas products (e.g., NO2, HCHO) for NO2, HCHO, aerosol, SO2, cloud
Major potential differences between NRT and offline
 | NRT | Off-line
Trace gas profiles/Met data | GEOS-CF | GEOS-CF Replay
Surface | GLER climatology | MODIS/VIIRS albedo/BRDF products
L1B | Skip wavelength calibration One-pass INR Default/No Pol. Correction | Two-pass Kalman Filter INR Improved pol. Correction with L2 retrievals?
L2 algorithms | Smaller fitting windows Avoid waiting for the entire hourly scan | More optimized fitting windows Improve radiance reference & cross-track correction
Data Latency | Within 2-3 hours upon receipt of raw data at SAO Ground System | + 8 days as MODIS BRDF is produced using data +/- 8 days