## Slide 1
Li, F., X. Zhang, S. Kondragunta, X. Lu, I. Csiszar, and C. Schmidt, Hourly biomass burning emissions product from blended geostationary and polar-orbiting satellites for air quality forecasting applications, RSE, 2022
Regional ABI and VIIRS based fire Emissions (RAVE)
Hourly fire emissions by fusing GOES-R ABI and VIIRS fire radiative power (FRP)
RAVE product provides hourly 3km emissions for 11 species (CO2, CO, PM2.5, BC, OC, SO2, NOx, NH3, VOCs, TPM, and CH4)
Operational RAVE product supports several NOAA air quality forecast models.

## Slide 2: RAVE Emissions Evaluated using TROPOMI CO
Identify fresh smoke plumes using VIIRS true color imagery and TROPOMI Aerosol Index
Analyze TROPOMI CO within the smoke plume ()
Calculate background TROPOMI CO ()
Calculate enhanced CO () due to fires and compare to RAVE CO
Li, F., X. Zhang, S. Kondragunta, X. Lu, I. Csiszar, and C. Schmidt, Hourly biomass burning emissions product from blended geostationary and polar-orbiting satellites for air quality forecasting applications, RSE, 2022

## Slide 3: Opportunities: Hourly TEMPO NO2
Apply hourly TEMPO NO2 observations to evaluate daytime hourly RAVE NOx emissions in a similar way as with TROPOMI CO observations.
Unlike CO, NO2 is not long-lived and amount of NO2 emitted depends on fuel type and fuel consumption.
Analysis of TROPOMI and TEMPO NO2 data will be carried for different types of fires prior to using in RAVE validation work.
2:25 PM
2:30 PM
TROPOMI NO2
Suomi NPP VIIRS
April 5th, 2021