## Slide 1
Assessing Diurnal Emissions with TEMPO
Panel Talk
Ken Pickering
University of Maryland

## Slide 2
Diurnal Variation of Emissions for Air Quality Modeling
Air quality models (e.g., CMAQ, CAMx, etc.) require emissions to be distributed realistically by hour of the day. EPA SMOKE-MOVES software contains diurnal emission profiles for various source types. How accurate are they?
Can TEMPO data be used to evaluate and improve these diurnal emission distributions?
- Hourly tropospheric columns of NO2 will be available each day during daylight hours at 2 x 4.75 km spatial resolution
- Should enable estimates of emission variation for major sources, major roadways, area sources
Examples of diurnal NOx emission profiles
from SMOKE-MOVES
Small EGUs
Airports
Prescribed
Fires
Onroad Vehicles

## Slide 3
Issues with Use of Tropospheric Columns in Estimating Emissions
Challenge for TEMPO:
NO2 tropospheric column retrievals are highly sensitive to
diurnal variation in model-derived a-priori profile shapes.
Model vertical mixing scheme plays a large role in determining
profile shapes.
Ranges displayed result from variation of
surface reflectivity, solar zenith angle,
and aerosol optical depth
DISCOVER-AQ data often showed surface
and column NO2 not well correlated. Vertical
mixing rate throughout the morning may
exceed emission rate, allowing columns to
increase, but surface NO2 to decrease.
Column increases should reflect magnitude
of emissions.
Jim Crawford
Lok Lamsal
DISCOVER-AQ
Colorado

## Slide 4
Free Tropospheric NO2 Complicates Satellite Emission Estimates
As anthropogenic NOx emissions have declined substantially over North America in the last 20 years, the fraction of the tropospheric column NO2 due to these emissions has also decreased, causing greater uncertainty in linking surface emissions to satellite-derived NO2 columns.
The need for accurate information on free tropospheric sources of NO2 (lightning, aviation, elevated wildfire plumes, aerosol nitrate photolysis) has therefore increased in importance (Silvern et al., 2019; Qu et al., 2021; Shah et al., 2023; Dang et al., 2023)
Wildfire contribution episodic, but has increased in the last decade; aviation contribution varies with economy
Lightning contribution: both diurnal variation and episodic occurrence; global long-term variation very small except 2020
Diurnal Variation of Lightning Flashes
Beirle et al, 2014
Füllekrug et al. (2022)
OMI, TROPOMI, GCAS NO2 data have been used in estimates of lightning NOx production per flash (Pickering et al., 2016;
Bucsela et al., 2019, Allen et al., 2019; Allen et al., 2021a; Allen et al., 2021b).
TEMPO “Green Paper” Lightning NOx Experiment in Summer 2023 – high time and spatial resolution; will reduce uncertainties
such as NOx lifetime in near field of convection; background NO2; diurnal variation of UT NO2