## Slide 1
Geostationary Environment Monitoring Satellite (GEMS)
Jongmin Yoon and Kyung-Jung Moon
Environmental Satellite Center
NIER

## Slide 2: Contents
01
02
03
04
Status of GEMS development
GEMS Level-2 data
GEMS ground system
Data validation plan
Notes: .

## Slide 3
Status of GEMS
1
2000 N-S x 697 E-W
x 8 times/day
= 11,152,000 spectrum/day
Measurement Concept

## Slide 4
Status of GEMS
1
Instrument tests
< Ready for vibration test >
< Result of vibration test >

## Slide 5
Status of GEMS
1
Measurement schedule and IOT plan
< Instrument activation and commissioning timeline >
GEMS-Specific Activation duration is 30 days out of 6 months of GK-2B IOT Phase to avoid the GEMS-GOCI II Mission Operation Confliction

## Slide 6
2
GEMS algorithm development
GEMS Level-2 data

## Slide 7
2
Data Processing (L0-L1-L2)
GEMS Level-2 data

## Slide 8
2
Level-2 Processor Interface
Processing step by step
Time limit (30 minutes)
Re-processing at night (TBD)
GEMS Level-2 data

## Slide 9
2
Num | Product | Importance | Min (cm-2) | Max (cm-2) | Nominal (cm-2) | Accuracy | Window (nm) | Spat Resol (km2)@Seoul | SZA (deg) | method
1 | Surface Prop. (LER, BRDF) | Environment | 0 | 1 | - | 20% | 300-500 | 3.5 x 8 | < 70 | Multi-l
3 | ECF CCP CRF | Retrieval Climate | 0 (COD) | 50 (COD) | 17 (COD) | 20% | 300-500 | 7 x 8 | < 70 | O2O2 RRS
4 | AOD AI SSA AEH | Air quality Climate | 0 (AOD) | 5 (AOD) | 0.2 (AOD) | 20% or 0.1@ 400nm | 300-500 | 3.5 x 8 | < 70 | Multi-l O2O2
3 | TropO3 StratO3 TotalO3 | Oxidant Pollutant O3 layer | 4x1017 | 2x1018 | 1x1018 | 3%(TOz) 5%(Stra) 20(Trop) | 300-340 | 7 x 8 | < 70 | OE TOMS
1 | HCHO | VOC proxy | 1x1015 | 3x1016 | 3x1015 | 1x1016 cm-2 | 328.5-356.5 | 7 x 8 x 4 pixels | < 50 | DF
1 | CHOCHO |  | 1x1014 | 1x1015 | 5x1014 | 1x1015 cm-2 | 435-461 | 7 x 8 x 4 px | < 50 | DF
2 | TropNO2 StratNO2 | O3 precursor | 3x1013 | 1x1017 | 1x1014 | 1x1015 cm-2 | 425-450 | 7 x 8 x 2 pixels | < 70 | DOAS
1 | SO2 | Aerosol precursor Volcano | 6x108 | 1x1017 | 6x1014 | 1x1016 cm-2 | 310-330 | 7 x 8 x 4 pixels x 3 hours | < 50 | DOAS PCA
4 | UVI VitaD dose rate DNA dose rate Plant dose rate | Public health | 0 | 12 62 25 48 | 6.8 33 mW/m2 12 mW/m2 25 mW/m2 | 20% | 300-360 | 7 x 8 | < 70 | Multi-l RTM
Level-2 Main Products (20)
GEMS Level-2 data

## Slide 10
GEMS ground system
3
Main concept of ground system operation
Operational Concept | Explanation
Non-stop Operation | Non-stop Operating ground station for 24hours and 365days Securing stability and non-stop automation through active-active high stability multiplexing Constructing an operation system in emergencies and at all times Establishment of back-up system for each sub system
Real-time Service | Acquisition in real-time and distribution in near-real-time Distribution within 1hour after receiving RAW data Improvement of processing efficiency through algorithm parallelization
Operation for 10years | Operating 10 years according to designed duration of GK2B operation Considering expansion possibilities of hardware, software, network, and new facilities
Data archive | Archiving all data in main storage, that is received and produced Building storage system that can expand and meet storage requirements
Back-up system | Constructing back-up system for data reliability Non-stop Operating with rapid substitution in case of failure Establishment of back-up system to meet system operation concept and requirements
High Availability | Achieving 99% or more operational availability for high-speed processing and customized services with Hot backup system

## Slide 11
GEMS ground system
  KARI
Related institutes
Individual users
  KIOST
  NMSC
Receiving system
  DMS
  (Data Management System)
  DAS
  (Data Analysis
  System)
  SDPS
  (Scientific Data
  Processing System)
  DVS
  (Data Verification
  System)
  PPS
  (data Pre-Processing
  System)
DPS
INR
  CMS
  (Control and Monitoring System)
  E-Portal_in
  (Environment-Portal)
PSS
(Product Service
System)
DVS Client
(Data Verification
System Client)
DAS Client
(Data Analysis
System Client)
Internal Network
External Network
Internal network
Internet
  Basic
  system
Advanced system
  KARI installation
  E-Portal_out
  (Environment-Portal)
3
Overview of ground system

## Slide 12
GEMS ground system
Data service web
Data storage
1. Search
2. Data request
3. Data transmission
4. Download
Data service to public
User
Data service to institution
Institution
Data service web
1. Setting for data request
2. Setting information
transmission
3. Data request/transmission
4. (Periodic) data transfer
Distribution module
Prior consultation
(agreement) is required
Providing web-based service that is easy to access for general users
Providing sftp-based service for periodic/large data
3
Data sharing

## Slide 13
2020.03
GK2B launch
2020.11
IOT end
In-Orbit Test (pre-processing)
L2 IOT
(tuning/improvement)
2019.12
Establishment of regulation and guide for operation and data distribution
2019.09
IOT plan
2021.03
L2 product
L2 validation +
Use (step by step)
Pre-launch test
Webpage open and operation
Network construction
3
Road ahead
GEMS ground system

## Slide 14
4
Data validation plan
Main products for validation

## Slide 15
4
Validation strategy
Data validation plan

## Slide 16
4
Validation network within GEMS domain
Data validation plan
[Kim et al., 2019]

## Slide 17
4
Pandora network
Data validation plan
~2018 (4) : YSU, PNU, SNU, UNIST
2019 (2) : China, Japan (LTP project)
2020~2021 (6) : Korea (ESC, TBD)
< Proposed Pandora network >

## Slide 18
4
Announcement of Opportunity for GEMS
Data validation plan
2019.8 : Outlines the CalVal requirements for GEMS AO
2019.9~11 : Draws up the first draft of GEMS AO and share it with GEMS science team
2019.11 : Opens the draft of GEMS AO at GEMS international science team meeting
~2020.1 : Completes the final version of GEMS AO
2020.1~2 : GEMS AO Call
2020.3~ : Launches GEMS and the GEMS CalVal activity

## Slide 19
Thank you for your attention~!!