## Slide 1: Status of Tropospheric Emissions: Monitoring of Pollution (TEMPO)
Xiong Liu1,*, Kelly Chance1, Raid M. Suleiman1, Kevin J. Daugherty2, David E. Flittner2, John Houck1, John E. Davis1, Gonzalo Gonzalez Abad1, Caroline Nowlan1, Huiqun Wang1, Chistopher Chan Miller1,3, Juseon Bak4, Hee-sung Chong1 and The TEMPO Team
1Center for Astrophysics (CfA) | Harvard & Smithsonian 2NASA LaRC 3Harvard University 4Pusan National University *xliu@cfa.harvard.edu
AGU Fall meeting 2022, December 12-16, 2022, Chicago, IL, USA
A55K-1233
Introduction: TEMPO, it is about time!
Introduction: TEMPO, it is about time!
  Provide revolutionary hourly daytime atmospheric pollution over North America from the GEO
  NASA’s first EVI selected in 2012 and first host payload.
    PI-led mission from SAO by PI Dr. Kelly Chance
    Instrument project management at NASA LaRC
    Instrument development at Ball Aerospace & Technologies.
    Science team includes other institutions, Universities, and companies with international collaboration.
    Mission project management also at NASA LaRC as designated by NASA to find host and launch vehicle for TEMPO.
    Host satellite provider by Maxar Technologies, host by Intelsat on Intelsat 40e (IS40e), launch on SpaceX Falcon 9
  North America component of an international geostationary air quality constellation.
Introduction: TEMPO, it is about time!
TEMPO Status
  Delivery by Ball in Nov. 2018
  Maxar selected in July 2019
  Intelsat selected in 02/2020.
  TEMPO sensor fully integrated onto IS40e on 6/30/2022.
  Spacecraft thermal vacuum testing completed in Oct. & spacecraft dynamic testing in mid-Dec.
  Operation/Mission Readiness Review (ORR/MRR) in late Jan./early Feb. 2022
  KDP-E in Feb. 2023
  Launch ~ 3/21/2023
Courtesy from Ball
Courtesy from Maxar
Courtesy from Maxar
Left: 1st fully integrated powered testing of TEMPO in July on IS40e.
Introduction: TEMPO, it is about time!
TEMPO Instrument & Measurements
  Imaging grating spectrometer measuring solar irradiance and solar backscattered Earth radiance
  Nominal: scan Field of Regard (FOR) within 1 hour in 10 granules with ~2.5 M pixels with native spatial resolution 2.0x4.75 km2 at center of FOR (from 8 km2 in Mexico City to 21 km2 at Canadian tar sands)
  Optimized scan: daylight portion of FOR in early AM/late PM at higher temporal resolution (~30 mins)
  High-time scan (up to 25%): selected portion of FOR at higher temporal resolution (e.g., <= 10 mins)
~293-494 nm
~538-741 nm
TEMPO instrument & measurement characteristics | 1.4 m x 1.1 m x 1.2 m, 137kg
Volume, Mass | 1.4 m x 1.1 m x 1.2 m, 137kg
Average operating power | 138 W
Detector size | Two 2048 (spatial) x 1028 (spectral)
Wavelength range | UV band: ~293 - 494 nm Visible band: 538 - 741 nm
Spectral resolution | ~0.6 nm @FWHM(0.54-0.63 nm)
Spectral sampling | ~0.2 nm or ~3 pixels /FWHM (2.7-3.2)
Spectral co-registration1 | < 0.1 pixel (for UV, visible, UV/visible)
Orbit | GEO (35786 km), 91.0°W above equator
Instantaneous FOV | 41.49 µrad (N/S) x 129.20 µrad (E/W)
MTF @Nyquist | 0.31-0.41 N/S x 0.38-0.49 E/W
Field of view2 | 4.92° N/S x 8.64° E/W
Spatial resolution | 2.0 km (N/S) x 4.75 km (E/W) km @center of FOR
Temporal resolution3 | ~1 hour, ~3s snapshot / mirror step
Spectra per hour2,3,4 | 2035 N/S (cross-track) x 1226 E/W (mirror step)
Maximum SNR5 | 1350 @ 330 - 340 nm, EOL
1Smile, keystone, and UV/visible co-alignment are within 0.1 pixel.
2Assume 123µrad E/W mirror step size (6.2µrad overlap) & 1226 steps as in left Fig.
3Nominal mode.
42035 out of 2048 spatial pixels are valid; 1016 out of spectral 1028 pixels are valid.
5For the nominal radiance.
An optimized TEMPO FOR. Actual FOR can extend by ~200 pixels in E/W, move by ~200 pixels in N/S.
Examples of typical TEMPO-like spectra (based on GOME). The boxes show the two TEMPO bands.
TEMPO Requirements
  TEMPO baseline requirements are specified for four pixels coadded with additional time-average
  Aerosols, SO2, C2H2O2 were removed from baseline products during KDPC (Key Decision Point before Phase C), working to add them back
  Cloud product (cloud fraction, cloud pressure): required for trace gas/aerosol retrievals
Species/Products | Required Precision | Temporal Revisit*
0-2 km O3 (Selected Scenes) Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
Aerosol Optical Depth | 0.10 | 1 hour
TEMPO baseline and threshold measurement requirements
* # of hours to be averaged to achieve required precision
Mission duration: 20 months for baseline, 12 mons for threshold
Spatial resolution: < 60 km2 for baseline (4 pixels coadded), < 300 km2 for threshold
Level | Product | Algorithm | Major Outputs | Res km2 * | Freq/Size
L0 | Digital counts | Raw to L0 | Reconstructed/reformatted digital counts | 2.0 x 4.75 | Daily/hourly
L1-b | Irradiance NRT | SAO L0-1 | Calibrated & quality flags |  | daily
 | Radiance NRT | SAO L0-1 | Geolocated,calibrated, viewing,geolocation&quality flags | 2.0 x 4.75 | Hourly, granule
L2 | Cloud NRT | OMI O2-O2 | Cloud fraction, cloud pressure | 2.0 x 4.75 | Hourly, granule
 | O3 profile | SAO O3 profile | O3 profile, total/strat/trop/0-2 km O3 column, errors, a priori, AKs | <= 8.0 x 4.75** | Hourly, granule
 | Total O3 | TOMS V8.5 | Total O3, AI, cloud fraction | 2.0 x 4.75 | Hourly, granule
 | NO2 NRT | SAO trace gas, BU strat/trop sep. | SCD, strat./trop. VCD, error, shape factor, scattering weights | 2.0 x 4.75 | Hourly, granule
 | H2CO NRT | SAO trace gas | SCD, VCD, error, shape factor, scattering weights | 2.0 x 4.75 | Hourly, granule
 | C2H2O2 | SAO trace gas |  | 2.0 x 4.75 | Hourly, granule
 | H2O | SAO trace gas |  | 2.0 x 4.75 | Hourly, granule
 | BrO | SAO trace gas |  | 2.0 x 4.75 | Hourly, granule
 | Aerosol NRT | OMAERUV+UI AOCH | AAI, UVAOD, UVSSA, AOCH, VISAOD | 8.0 x 4.75 | Hourly, granule
 | SO2 | OMSO2 PCA | SCD, VCD (PBL,TRL,TRM,TRU,STL) | 2.0 x 4.75 | Hourly, granule
 | TEMPO/GOES-R Synerg. product | GOES-R products on TEMPO pixels | Radiance, aerosol, cloud & mask, fire/hotspot, snow/ice, rainfall, precipitable water, land/sea surface T, lightning | 2.0 x 4.75 | Hourly, granule
L3 | Gridded L2 | SAO L2-3 | Same as L2 | 2 x 2 (?) | Hourly, scan
L4 | UVB | GEMS/GSFC UVB | UV irradiance, erythemal irradiance, UVI | TBD | Hourly, scan
Black: launch-ready baseline products; green/orange/purple: additional products
Proposed NRT (L1b <~1 hr, L2 cloud <~1.5 hr, L2/3 trace gas < ~2.5 hrs): from SNWG, NASA+NOAA OMB, NOAA to produce aerosol NRT
NRT data products timeline, 4-5 months behind baseline products (1/2024 start NRT processing, 6/2024: public release)
* Spatial resolution at center of FOR. ** Might be at 8 x 9.5 km2
TEMPO Data Products, Product Archival and Distribution
TEMPO data products including proposed NRT and additional products
  TEMPO data are sent to ASDC @NASA LaRC for archival/distribution with tools & services
  User support and other resources: Earthdata Login, Earthdata Forum, ASDC user support
  EPA RSIG3D Gateway: TEMPO data can be served directly through the EPA RSIG. https://www.epa.gov/hesc/remote-sensing-information-gateway
NASA Earthdata Search: CMR Search, Metadata
NASA WorldView: GIBS API, visualization
Harmony and OPeNDAP: transform, subsetting, reformatting, distribution
HTTPS data access: datapool, permanent URL/direct access, enables scripts/workflow
Geospatial Web Services: WCS, WMS, ArcGIS
Example scripts: Python/Jupyter Notebook, R scripts, contributed tutorials/scripts
TEMPO Algorithm Development Status and Plan
  Science Data Processing Center (SDPC) V3 (launch ready) completed early this year
  Algorithm mostly based on OMI heritage algorithms except for new L0-1b processor (including INR using GOES-R from Carr Astronautics), with main L1-2 updates shown below:
  Add visible to SAO UV O3 profile algorithm
  SAO trace gas algorithm with adapted NASA stratospheric/tropospheric separation for NO2
  CLDO4new: SAO O2-O2 fitting + GSFC’s O2-O2 cloud at ~477 nm (H. Wang, E.-S. Yang, A. Vasilkov)
  NASA GMAO’s GEOS-CF trace gas profiles and meteorology (E. Knowland and GMAO)
  Hourly resolved monthly mean GLER climatology (C. Chan Miller, W. Qin, Z. Fasnacht)
  Development of other products
  CHOCHO, H2O, BrO: will use SAO’s trace gas algorithm
  SO2: OMI PCA SO2 algorithm adapted for TEMPO/GEMS from synthetic/GEMS data (C. Li)
  Aerosols: being adapted from OMI/TROPOMI AEROUV algorithm (O. Torres’s team), and from EPIC/TROPOMI Aerosol Layer Height algorithm using O2-A/B (J. Wang’s team)
  Continue algorithm refinement/optimization during commissioning and nominal operation
Commissioning Plan Timeline and Data Release Plan
TEMPO Commissioning
S/C Activity (TEMPO Off)
Activation
Outgassing
Instrument Characterization and Analysis
PLAR
Nominal Operations
L+88 days
L+120 days
L+178 days
L+0
Launch
* L+# days are approximate
TEMPO Power on
TEMPO 1st light
Activity | Intelsat
LEOP: Orbit Transfer | 2 Weeks
Spacecraft Bus + Payload IOT | 1 + 4 Weeks
Drift to Location 60ºW-91ºW | 4 Weeks (TBD)
Commercial Services | 1 Week
TEMPO Commissioning Begins | L+12 Weeks
TEMPO comm.: 06/17-9/17/2023, first light ~7/17/2023
Nominal operation after PLAR: ~9/17/2023
Plan for initial public release of baseline products at ASDC (L1b in ~4 mons, 1/2024, L2/3 in ~6 mons, 3/2024):
Provide baseline data products to validation team priori to the public release via ASDC.
TEMPO Validation Plan
  TEMPO PLRA: bare minimum validation requirements (3 Pandoras, 1 month per season)
  Jim Szykman led the development of best-of-effort basis validation plan: beta, provisional, full
  Satellite observations (i.e., LEOs + EPIC/DSCOVR)
  Pandonia Global Network (PGN): NO2, HCHO, total O3
  TOLNet with 8 LIDARs: tropospheric O3 & 0-2 km O3
  Airborne instruments: GEO-TASO, GCAS, HSRL-2, SeaRey UAV, in-situ …
  Other ground-based instruments: ozonesonde, MAXDOAS, FTIR, Dobson/Brewer, AERONET, …
  Planned flight campaigns: AGES (STAQS, AEROMMA+ CUPiDs, GOTHAAM) in June-August 2023
  Indirect validation with CTMs and data assimilation
https://www.pandonia-global-network.org
www-air.larc.nasa.gov/missions/TOLNet
~60 in TEMPO FOR, ~20 to add in 2 yrs
TEMPO Green Paper: Chemistry Experiments
  Green paper is a living document at: http://tempo.si.edu/publications.html
  High-time special mode can be requested: https://weather.msfc.nasa.gov/tempo/green_paper.html
NORMAL TIME RESOLUTION STUDIES | Volcanoes
Air quality and health | Socio-economic studies
Ultraviolet exposure | National pollution inventories
Biomass burning | Regional and local transport of pollutants
Synergistic GOES-16/17 Products | Sea breeze studies for Florida and Cuba
Advanced aerosol products | Transboundary pollution gradients
Soil NOx after fertilizer application and after rainfall | Transatlantic dust transport
Solar-induced fluorescence from chlorophyll | HIGH TIME RESOLUTION EXPERIMENTS
Foliage studies | Lightning NOx
Mapping NO2 and SO2 dry deposition at high resolution | Morning and evening higher-frequency scans
Crop and forest damage from ground-level ozone | Dwell-time studies & temporal selection to improve detection limits
Halogen oxide studies in coastal and lake regions | Assessing pollution transport during upslope flows
Air pollution from oil and gas fields | Tidal effects on estuarine circulation and outflow plumes
Night light measurements resolving lighting type | Air quality responses to sudden changes in emissions
Ship tracks, drilling platform plumes, other concentrated sources | Cloud field correlation with pollution
Water vapor studies | Agricultural soil NOx emissions and air quality
Early Adopters are key to building the TEMPO Green Paper!
Summary
  We are currently on track for TEMPO launch onto the GEO at 91∘W in March 2023 and produce at-launch products, to provide hourly daylight observation of atmospheric pollution at high spatial resolution over North America.
  Acknowledgements: Thanks to NASA for funding (NNL13AA09C). Thanks to TEMPO instrument/mission management team @NASA LaRC, Ball, Maxar, Intelsat, and the TEMPO team.